| Input Contribution |
| --- |
| Meeting ID* | TP#26 |
| Title:* | Structure of catalogue |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd., Yinjiaxin@huawei.com |
| Uploaded Date:* | 2016-11-23 |
| Document(s) Impacted* | TR-0032 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to be incorporated into the document. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## 5.2	Structure of catalog

5.2.1	Introduction

Features of oneM2M are organized into a hierarchical structure and separated by Entity, Function and Feature Sets at each level. Entity and Function have their dedicated abbreviations. Feature is uniquely identified by Feature ID. Feature ID is a combination of abbreviation of Entity, Function the serial number of Feature Set and the serial number of Feature separated by dot “.” in the form as the following.

{Abbr of Entity}.{Abbr of Function}.{Serial number of Feature Set}.{Serial number of Feature}

5.2.2	Entity

Entity is oneM2M defined Entities which could be AE or CSE as feature is implemented differently from the perspective of AE and CSE. There may some other features that are common for both AE and CSE like the binding and serialization. It’s defined to have three Entity categories, AE, CSE and General.

- GE	-	Features that are supported by both CSE and AE

- CE	-	Features that are supported by CSE

- AE	-	Features that are supported by AE

5.2.3	Functions

In the document, oneM2M defined CSFs are used to categorize features. Besides, a new category is added to organize features that are shared between Functions or agnostic to both CSE and AE. The Functions are composed of oneM2M defined CSFs and one new Function called GENC that is general capability.

- GEN	-	General capability

- ASM	-	Application and Service Layer Management

- CMDH	-	Communication Management and Delivery Handling

- DMR	-	Data Management and Repository

- DMG	-	Device Management

- DIS	-	Discovery

- GMG	-	Group Management

- LOC	-	Location

- NSSE	-	Network Service Exposure, Service Execution and Triggering

- REG	-	Registration

- SEC	-	Security

- SCA	-	Service Charging and Accounting

- SUB	-	Subscription

Editor’s Note:  This list may be changed along with the definition in architecture. However, the definition of Feature as the composition of Function won’t be changed.

5.2.4	Feature Set

Function is composed of Feature Sets. Feature Set is a set of Features that are closely related. For example, in group management Function, the configuration of group and the fan out of operation can be regarded as two separate Feature Sets that belong to group management (GMG). Under each Function, Feature Set is identified by a five digit number starting from 00001.

5.2.5	Feature

Feature Set is composed of Features. Feature is the atomic procedure that is defined by oneM2M. On the consideration of service, it’s meaningless to divide the procedure anymore. For example, set the max number of instance of a container or application registration. Under each Feature Set, Feature is identified by a five digit number starting from 00001.