| CHANGE REQUEST |
| --- |
| Meeting:* | ARC26 |
| Source:* | Huawei Technologies Co., Ltd. |
| Date:* | 2016-11-27 |
| Contact:* | Jiaxin Yin, Yinjiaxin@huawei.com |
| Reason for Change/s:* |  |
| CR against: Release* | Three |
| CR against: WI* | Active WI-0034 and WI-0035 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 v3.0.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

In the study in WI-0034-Study_of_re-usable_service_layer_context_&Transaction_enablement and WI-0035-Action_Triggering, it’s well recognized that the function of action triggering, transaction and service layer context will be new features in Release 3 of oneM2M standard, there have been several potential solutions for each individual new feature provided and analysed in TR-0020 and TR-0021.

Technically speaking, action triggering and transaction is about the combination and orchestration of the existing services provided by the system. Action triggering is about how to connect the services together by predefined order, filers and rules to form sequences and dependencies. Transaction is about how to manipulate multiple separated operation into one atomic operation. It’s all about how to combine different services together and what to achieve by combining these services.

As a new feature that is going to be provided by oneM2M. It’s required to have a new CSF defined for this purpose.

### -----------------------Start of change 1-------------------------------------------

### 6.2.13	Service Combination

#### 6.2.13.1	General concept

#### The Service Combination CSF (SCB) is responsible for the combination of the existing services provided by the oneM2M system. Services of oneM2M are delivered by the CRUDN of oneM2M defined resources. The combination of services is about defining the dependencies, the order of execution, the input and output relationship, other kinds of relationship among multiple services. The combination also includes the maintaining and managing of context informatiofor the purpose of enforcement of service combination. Examples of service combination are: action triggering, transaction etc.

#### 6.2.13.2	Detailed Description

#### Service combination in oneM2M currently supports the management of actions and transactions.

#### Action management is to enable the oneM2M system to trigger operations towards dedicated resources based on pre-defined rules and contexts. The operation could be CRUDN operations. The rules and contexts are delegated service logic by applications. By doing this, applications could delegate the oneM2M CSEs for services that normally need applications involvement by standardized means. Applications could be exempt from the busy sequences of event handling of determination. The service logics delegated to oneM2M system could also be shared with others in this way.

#### Transaction management is to enable the oneM2M system to execute multiple operations in an atomic way. Multiple operations shall be either all successful or none of them is successfully executed. The CSF is providing context information management for the enforcement of transaction management by application such as the state of transaction, the commit or cancel of the transactions. The CSF also provides coordination if there are multiple transactions to be executed at the same resource to avoid confliction and dead lock to guarantee the consistency of oneM2M system.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?