| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 26.2 |
| Source:* | Huawei |
| Date:* | 2016-11-25 |
| Contact:* | Jessie, Huawei, lijing80@huawei.com Echo,Huawei,echo.xubei@huawei.com |
| Reason for Change/s:* | <exact change/s to be provided below> |
| CR against: Release* | Release 3 |
| CR against: WI* | Active < WI-0031> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001-V2.10.1 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

R03 change history:

- Update the multicast group creation condition: based on the multicast capability of registree member Hosting CSE to comply the oneM2M registration path.

Add the note: The group Hosting CSE should be the Registrar CSE for member Hosting CSEs

## Introduction

When an application wants to send a message to the members of a certain group, it may send the request to the <fanOutPoint> resource, then the request is fanned out to each of the members of the <group> resource indicated by the membersIDs attribute of the <group> resource. This is how the group message is transferred from the application to the group members defined by the current specification.

However, the existing method applied to M2M group message communication only saves the communication between the application and the group management server, but the group management server still needs to communicate with each group member separately. If the group management server or the network has limited capability or bandwidth, then the communication between the group management server and the group members will be a high cost and is not economical. The communication cost between the group server and the group members can be decreased by reusing the existing underlying network technologies, for example, 3GPP MBMS or IP multicast. But not all the M2M devices and networks support multicast, so it is necessary for oneM2M to extend the group related resources to manage and reuse the multicast capability of the underlying network, in order to make the group communication more efficient and economical.

### -----------------------Start of change 1-------------------------------------------

#### 10.2.7.2	Create <group>

This procedure shall be used for creating a <group> resource.

Table 10.2.7.2-1: <group> CREATE

| <group> CREATE |
| --- |
| Associated Reference Point | Mcc, Mca and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address of the <CSEBase>, <AE>, or <remoteCSE> where the <group> resource is intended to be Created Content: The representation of the <group> resource for which the attributes are described in clause 9.6.13 |
| Processing at Originator before sending Request | The Originator shall request to Create a <group> resource by using the CREATE operation. The request shall address <CSEBase>, <remoteCSE> or <AE> resource of a Hosting CSE. The Request shall also provide memberIDs and may provide expirationTime attributes. The Originator may be an AE or a CSE |
| Processing at Receiver | For the CREATE procedure, the Receiver shall: Check if the Originator has CREATE permissions on the target resource Check the validity of the provided attributes Validate that there are no duplicate members present in the memberIDs attribute Validate that the resource type of every member on each member Hosting CSE conforms to the memberType attribute in the request, if the memberType attribute of the <group> resource is not 'mixed'. Set the memberTypeValidated attribute to TRUE upon successful validation. Upon successful validation of the provided attributes, create a new group resource including the <fanOutPoint> child-resource in the Hosting CSE. If the CSE supports semantic discovery functionality, the Hosting CSE shall also set the semanticSupportIndicator attribute to TRUE and create the <semanticFanOutPoint> child-resource. If the registree member Hosting CSEs support the multicast capability, create <multicastGroup> child-resource in the group Hosting CSE. The Receiver shall perform the procedure as description in the Figure 10.2.7.x1-1. Conditionally, in the case that the group resource contains temporarily. unreachable Hosting CSE of sub-group resources as member resource, set the memberTypeValidated attribute of the <group> resource to FALSE Respond to the Originator with the appropriate generic Response with the representation of the <group> resource if the memberTypeValidated attribute is FALSE, and the address of the created <group> resource if the CREATE was successful As soon as any Hosting CSE that hosts the unreachable resource becomes reachable, the memberType validation procedure shall be performed. If the memberType validation fails, the Hosting CSE shall deal with the <group> resource according to the policy defined by the consistencyStrategy attribute of the <group> resource provided in the request. or by default if the attribute is not provided |
| Information in Response message | The representation of the <group> resource if the memberTypeValidated attribute is FALSE |
| Processing at Originator after receiving Response | None |
| Exceptions | No change from the basic procedure in clause 10.1.1 |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 10.2.7.4	Update <group>

This procedure shall be used for updating an existing <group> resource.

Table 10.2.7.4-1: <group> UPDATE

| <group> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address of the <group> resource |
| Processing at Originator before sending Request | The Originator shall request to update attributes of an existing <group> resource by using an UPDATE operation. The Request shall address the specific <group> resource of a CSE. The Originator may be an AE or a CSE |
| Processing at Receiver | The UPDATE procedure shall be: Check if the Originator has UPDATE permissions on the <group> resource. Check the validity of provided attributes Validate that there are no duplicated members present in the memberIDs attribute Validate that the resource type of every member on each member Hosting CSE conforms to the memberType attribute in the request, if the memberType attribute of the <group> resource is not 'mixed'. Set the memberTypeValidated attribute to TRUE upon successful validation Upon successful validation of the provided attributes, update the <group> resource in the Hosting CSE Conditionally, if the member IDs change and group or sub-group includes child-resource <multicastGroup>, update or delete the <multicastGroup> as the new group members. The Receiver shall perform the procedure as description in the Figure 10.2.7.x1-1. Conditionally, in the case that the <group> resource contains temporarily unreachable Hosting CSE of sub-group resources as members resource set the memberTypeValidated attribute of the <group> resource to FALSE Respond to the Originator with the appropriate generic response with the representation of the <group> resource if the memberTypeValidated attribute is FALSE, and the address of the created <group> resource if the UPDATE is successful As soon as any Hosting CSE that hosts unreachable resource becomes reachable, the memberType validation procedure shall be performed. If the memberType validation fails, the Hosting CSE shall deal with the <group> resource according to the policy defined by the consistencyStrategy attribute of the <group> resource provided in the request, or by default if the attribute is not provided |
| Information in Response message | The representation of the <group> resource if the memberTypeValidated attribute is FALSE |
| Processing at Originator after receiving Response | None |
| Exceptions | No change from the basic procedure in clause 10.1.3 |

#### 10.2.7.5	Delete <group>

This procedure shall be used for deleting an existing <group> resource.

Table 10.2.7.5-1: <group> DELETE

| <group> DELETE |
| --- |
| Associated Reference Point | Mcc, Mca and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address of the <group> resource |
| Processing at Originator before sending Request | The Originator shall request to delete an existing <group> resource by using the DELETE operation. The request shall address the specific <group> resource of a Hosting CSE. The Originator may be an AE or a CSE This operation shall also delete the child virtual resources <fanOutPoint> and <semanticFanOutPoint> |
| Processing at Receiver | Besides the basic procedure in clause 10.1.4, the receiver shall: Check if the group or sub-group includes <multicastGroup>, and perform the multicast message procedure to notify member resource Hosting CSE to delete the <parentGroup> as description in the Figure 10.2.7.x1-1. |
| Information in Response message | No change from the basic procedure in clause 10.1.4 |
| Processing at Originator after receiving Response | None |
| Exceptions | No change from the basic procedure in clause 10.1.4 |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

#### 10.2.7.7	Create <fanOutPoint>

This procedure shall be used for creating the content of all members resources belonging to an existing <group> resource.

Table 10.2.7.7-1: <fanOutPoint> CREATE

| <fanOutPoint> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address of the <fanOutPoint> virtual resource Content: The representation of the resource the Originator intends to create Group Request Identifier: The group request identifier Response Type: If the parameter is set to BlockingSynch, it indicates that the group CSE shall return the aggregated response once. Otherwise if the parameter is set to nonBlockingRequestSynch, nonBlockingRequestAsynch or flexBlocking, it indicates that the Group Hosting CSE shall return the aggregated response in a batched mode Result Expiration Time: Indicates the maximum time limit in which the Group Hosting CSE has to respond the aggregated response. |
| Processing at Originator before sending Request | The Originator shall request to create the resource that have the same content in all members resources belonging to an existing <group> resource by using a CREATE operation. The Request may address the virtual child resource <fanOutPoint> of the specific <group> resource of a group Hosting CSE. The request may also address the address that results from appending a relative address to the <fanOutPoint> address in order to create the resources that have the same content under the corresponding child resources represented by the relative address with respect to all members resources. The Originator may be an AE or CSE. |
| Processing at Group Hosting CSE | For the CREATE procedure, the Group Hosting CSE shall: Check if the Originator has CREATE privilege in the <accessControlPolicy> resource referenced by the membersAccessControlPolicyIDs in the <group> resource. In the case members membersAccessControlPolicyIDs is not provided the access control policy defined for the <group> resource shall be used Upon successful validation, obtain the IDs of all members resources from the attribute membersIDs of the addressed <group> resource If the group or sub-group includes <multicastGroup>, the group Hosting CSE shall perform the procedure as description in the Figure 10.2.7.x1-1. Generate fan out requests addressing the obtained address (appended with the relative address if any) to the other member hosting CSEs as indicated in figure 10.2.7.6-1 which are not in the multicast group. The From parameter in the fanout request is set to ID of the Originator from the request from the original Originator. The Response Type parameter in the fanout request may be set by the group hosting CSE differently according to its local policy In the case that a member resource is a <group> resource and the request to be fanned out does not contain a group request identifier already, generate a unique group request identifier, include the group request identifier in all the requests to be fanned out and locally store the group request identifier If the group Hosting CSE determines that multiple members resources belong to one CSE according to the IDs of the members resources, it may converge the requests accordingly before sending out. This may be accomplished by the group Hosting CSE creating a <group> resource on the members Hosting CSE to collect all the members on that members Hosting CSE After receiving the responses from the members hosting CSEs, respond to the Originator with the aggregated results and the associated members list. Depending on the Response Type, the Group Hosting CSE shall: - blockingRequest: respond with the aggregated responses before the Result Expiration Time reaches and discard the member responses received after - nonBlockingRequestSynch: prepare the operationResult of the <request> resource and indicate that if all the member responses have been aggregated by setting the requestStatus of the <request> resource before the Result Expiration Time reaches. There may be multiple updates of the operationResult attribute. - nonBlockingRequestAsynch: notify with the aggregated response from all or part of the members before the Result Expiration Time reaches. There may be more than one notifications. - flexBlocking: continue aggregate the member response until the group hosting CSE determines to send the aggregated responses, if all member responses has been aggregated, respond the aggregated response as in the blockingRequest case. Otherwise, respond an acknowledgement together with the current aggregated member responses and the reference to the created <request> resource. Then continue aggregate and deliver the remaining member response to the Originator as defined in the nonBlockingRequestSynch or the nonBlockingRequestAsynch case. - After the Result Expiration Time, there shall not be any further updates to the aggregated responses. (See note) |
| Processing at Member Hosting CSE | For the CREATE procedure, the Member Hosting CSE shall: Check if the request has a group request identifier. Check if the group request identifier is contained in the requested identifiers stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the group request identifier until the expiration of the request expiration time or local policy Check if the original Originator has the CREATE permission on the addressed resource. Upon successful validation, perform the create procedures for the corresponding type of addressed resource as described in other sub-clauses of clause 10.2 Send the corresponding response to the Group Hosting CSE |
| Information in Response message | Converged responses from members hosting CSEs |
| Processing at Originator after receiving Response | None |
| Exceptions | Same request with identical group request identifier received Originator does not have the CREATE permission to access the <fanOutPoint> resource |
| NOTE: If Result Expiration Time is not provide in the original request from the Originator, the group hosting CSE may decide the timer based on its local policy. |

#### 10.2.7.8	Retrieve <fanOutPoint>

This procedure shall be used for retrieving the content of all member resources belonging to an existing <group> resource.

Table 10.2.7.8-1: <fanOutPoint> RETRIEVE

| <fanOutPoint> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address of the <fanOutPoint> virtual resource Content: The representation of the resource the Originator intends to retrieve Group Request Identifier: The group request identifier Response Type: If the parameter is set to BlockingSynch, it indicates that the group hosting CSE shall return the aggregated response once. Otherwise if the parameter is set to nonBlockingRequestSynch or nonBlockingRequestAsynch, it indicates that the Group Hosting CSE shall return the aggregated response in a batched mode. Result Expiration Time: Indicates the maximum time limit in which the Group Hosting CSE has to respond the aggregated response. |
| Processing at Originator before sending Request | The Originator shall request to obtain the resource or specific attributes of all member resources belonging to an existing <group> resource by using a RETRIEVE operation. The request may address the virtual child resource <fanOutPoint> of the specific <group> resource of a group Hosting CSE. The request may also address the address that results from appending a relative address to the <fanOutPoint> address in order to retrieve the corresponding attributes or child resources represented by the relative address with respect to all members resources. The Originator may be an AE or CSE |
| Processing at Group Hosting CSE | For the RETRIEVE procedure, the Group Hosting CSE shall: Check if the Originator has RETRIEVE permission in the <accessControlPolicy> resource referenced by the membersAccessControlPolicyIDs in the addressed <group> resource. In the case membersAccessControlPolicyIDs is not provided, the access control policy defined for the group resource shall be used Upon successful validation, obtain the IDs of all members resources from the membersIDs attribute of the addressed <group> resource If the group or sub-group includes <multicastGroup>, the group Hosting CSE shall perform the procedure as description in the Figure 10.2.7.x1-1. Generate fan out requests addressing the obtained address (appended with the relative address if any) to the other members hosting CSEs as indicated in figure 10.2.7.6-1 which are not in the multicast group. The From parameter in the fanout request is set to ID of the Originator from the request from the original Originator. The Response Type parameter in the fanout request may be set by the group hosting CSE differently according to its local policy In the case that a member resource is a <group> resource, generate a unique group request identifier and the request to be fanned out does not contain a group request identifier already, include the group request identifier in all the requests to be fanned out and locally store the group request identifier If the group hosting CSE determines that multiple members resources belong to one CSE according to the IDs of the members resources, it may converge the requests accordingly before sending out. This may be accomplished by the group Hosting CSE creating a <group> resource on the members Hosting CSE to collect all the members on that members Hosting CSE After receiving the responses from the members hosting CSEs, respond to the Originator with the aggregated results and the associated members list. Depending on the Response Type, the Group Hosting CSE shall: - BlockingRequest: respond with the aggregated responses before the Result Expiration Time reaches and discard the member responses received after. - nonBlockingRequestSynch: prepare the operationResult of the <request> resource and indicate that if all the member responses have been aggregated by setting the requestStatus of the <request> resource before the Result Expiration Time reaches. There may be multiple updates of the operationResult attribute. - nonBlockingRequestAsynch: notify with the aggregated response from all or part of the members before the Result Expiration Time reaches. There may be more than one notifications. - flexBlocking: continue aggregate the member response until the group hosting CSE determines to send the aggregated responses. If all member responses has been aggregated, respond the aggregated response as in the blockingRequest case. Otherwise, respond an acknowledgement together with the current aggregated member responses and the reference to the created <request> resource. Then continue aggregate and deliver the remaining member response to the Originator as defined in the nonBlockingRequestSynch or the nonBlockingRequestAsynch case. - After the Result Expiration Time, there shall not be any further updates to the aggregated responses. (See note) |
| Processing at Member Hosting CSE | For the RETRIEVE procedure, the Member Hosting CSE shall: Check if the request has a group request identifier. Check if the group request identifier is contained in the requested identifier stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the request identifier until the expiration of the request expiration time or local policy Check if the original Originator has the RETRIEVE permission on the addressed resource. Upon successful validation, perform the retrieve procedures for the corresponding type of addressed resource as described in other sub-clauses of clause 10.2 Send the corresponding response to the group Hosting CSE |
| Information in Response message | Converged responses from members hosting CSEs |
| Processing at Originator after receiving Response | None |
| Exceptions | Same request with identical group request identifier received Originator does not have RETRIEVE permission to access the <fanOutPoint> resource |
| NOTE: If Result Expiration Time is not provide in the original request from the Originator, the group hosting CSE may decide the timer based on its local policy. |

#### 10.2.7.9	Update <fanOutPoint>

This procedure shall be used for updating the content of all member resources belonging to an existing <group> resource.

Table 10.2.7.9-1: <fanOutPoint> UPDATE

| <fanOutPoint> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address of the <group> resource Content: The representation of the resource the Originator intend to Update Group Request Identifier: The group request identifier Response Type: If the parameter is set to BlockingSynch, it indicates that the group hosting CSE shall return the aggregated response once. Otherwise if the parameter is set to nonBlockingRequestSynch or nonBlockingRequestAsynch, it indicates that the Group Hosting CSE shall return the aggregated response in a batched mode Result Expiration Time: Indicates the maximum time limit in which the Group Hosting CSE has to respond the aggregated response. |
| Processing at Originator before sending Request | The Originator shall request to update all member resources belonging to an existing <group> resource with the same data by using a UPDATE operation. The request may address the virtual child resource <fanOutPoint> of the specific <group> resource of a group Hosting CSE. The request may also address the address that results from appending a relative address to the <fanOutPoint> in order to update the corresponding child resources represented by the relative address with respect to all <members> resources. The Originator may be an AE or CSE. |
| Processing at Group Hosting CSE | For the UPDATE procedure, the Group Hosting CSE shall: Check if the Originator has UPDATE permission in the <accessControlPolicy> resource referenced by the membersAccessControlPolicyIDs in the group resource. In the case members membersAccessControlPolicyIDs is not provided the access control policy defined for the group resource shall be used Upon successful validation, obtain the IDs of all member resources from the attribute membersIDs of the addressed <group> resource If the group or sub-group includes <multicastGroup>, the group Hosting CSE shall perform the procedure as description in the Figure 10.2.7.x1-1. Generate fan out requests addressing the obtained address (appended with the relative address if any) to the other members hosting CSEs as indicated in figure10.2.7.6-1 which are not in the multicast group.The From parameter in the fanout request is set to ID of the Originator from the request from the original Originator. The Response Type parameter in the fanout request may be set by the group hosting CSE differently according to its local policy In the case that a member resource is a <group> resource and the request to be fanned out does not contain a group request identifier already, generate a unique group request identifier, include it in all the requests to be fanned out and locally store the group request identifier If the group Hosting CSE determines that multiple members resources belong to one CSE according to the IDs of the member resources, it may converge the requests accordingly before sending out. This may be accomplished by the group Hosting CSE creating a <group> resource on the member Hosting CSE to collect all the members on that members Hosting CSE After receiving the responses from the members hosting CSEs, respond to the Originator with the aggregated results and the associated members list. Depending on the Response Type, the Group Hosting CSE shall: - BlockingRequest: respond with the aggregated responses before the Result Expiration Time reaches and discard the member responses received after - nonBlockingRequestSynch: prepare the operationResult of the <request> resource and indicate that if all the member responses have been aggregated by setting the requestStatus of the <request> resource before the Result Expiration Time reaches. There may be multiple updates of the operationResult attribute. - nonBlockingRequestAsynch: notify with the aggregated response from all or part of the members before the Result Expiration Time reaches. There may be more than one notifications. - flexBlocking: continue aggregate the member response until the group hosting CSE determines to send the aggregated responses, if all member responses has been aggregated, respond the aggregated response as in the blockingRequest case. Otherwise, respond an acknowledgement together with the current aggregated member responses and the reference to the created <request> resource. Then continue aggregate and deliver the remaining member response to the Originator defined in the nonBlockingRequestSynch or the nonBlockingRequestAsynch case - After the Result Expiration Time, there shall not be any further updates to the aggregated responses. (See note) |
| Processing at Member Hosting CSE | For the UPDATE procedure, the Member Hosting CSE shall: Check if the request has a group request identifier. Check if the request identifier is contained in the requested identifier stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the request identifier until the expiration of the request expiration time or local policy Check if the original Originator has the UPDATE permission on the addressed resource. Upon successful validation, perform the update procedures for the corresponding type of addressed resource as described in other sub-clauses of clause 10.2 Send the corresponding response to the group Hosting CSE |
| Information in Response message | Converged responses from members hosting CSEs |
| Processing at Originator after receiving Response | None |
| Exceptions | Same request with identical group request identifier received Originator does not have the UPDATE permissions to access the <fanOutPoint> resource |
| NOTE: If Result Expiration Time is not provide in the original request from the Originator, the group hosting CSE may decide the timer based on its local policy. |

#### 10.2.7.10	Delete <fanOutPoint>

This procedure shall be used for deleting the content of all members resources belonging to an existing <group> resource.

Table 10.2.7.10-1: <fanOutPoint> DELETE

| <fanOutPoint> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address of the <fanOutPoint> virtual resource Content: The representation of the resource the Originator intends to delete Group Request Identifier: The group request identifier Response Type: If the parameter is set to BlockingSynch, it indicates that the group hosting CSE shall return the aggregated response once. Otherwise if the parameter is set to nonBlockingRequestSynch or nonBlockingRequestAsynch, it indicates that the Group Hosting CSE shall return the aggregated response in a batched mode Result Expiration Time: Indicates the maximum time limit in which the Group Hosting CSE has to respond the aggregated response. |
| Processing at Originator before sending Request | The Originator shall request to delete all members resources belonging to an existing <group> resource by using a DELETE operation. The request may address the virtual child resource <fanOutPoint> of the specific <group> resource of a group Hosting CSE. The request may also address the address that results from appending a relative address to the <fanOutPoint> in order to delete the corresponding child resources represented by the relative address with respect to all member resources. The Originator may be an AE or a CSE |
| Processing at Group Hosting CSE | For the DELETE procedure, the <group> Hosting CSE shall: Check if the Originator has DELETE permission in the <accessControlPolicy> resource referenced by the membersAccessControlPoliciIDs in the <group> resource. In the case membersAccessControlPolicyIDs is not provided the access control policy defined for the group resource shall be used Upon successful validation, obtain the IDs of all member resources from the attribute membersIDs of the addressed <group> resource If the group or sub-group includes <multicastGroup>, the group Hosting CSE shall perform the procedure as description in the Figure 10.2.7.x1-1. Generate fan out requests addressing the obtained address (appended with the relative address if any) to the other member hosting CSEs as indicated in figure 10.2.7.6-1 which are not in the multicast group. From parameter in the fanout request is set to ID of the Originator from the request from the original Originator. The Response Type parameter in the fanout request may be set by the group hosting CSE differently according to its local policy In the case that the members resources is a <group> resource and the request to be fanned out does not contain a group request identifier already, generate a unique group request identifier, include the group request identifier in all the requests to be fanned out and locally store the group request identifier If the <group> Hosting CSE determines that multiple members resources belong to one CSE according to the IDs of the members resources, it may converge the requests accordingly before sending out. This may be accomplished by the group Hosting CSE creating a <group> resource on the member Hosting CSE to collect all the members on that member Hosting CSE After receiving the responses from the members hosting CSEs, respond to the Originator with the aggregated results and the associated members list. Depending on the Response Type, the Group Hosting CSE shall: - BlockingRequest: respond with the aggregated responses before the Result Expiration Time reaches and discard the member responses received after - nonBlockingRequestSynch: prepare the operationResult of the <request> resource and indicate that if all the member responses have been aggregated by setting the requestStatus of the <request> resource before the Result Expiration Time reaches. There may be multiple updates of the operationResult attribute. - nonBlockingRequestAsynch: notify with the aggregated response from all or part of the members before the Result Expiration Time reaches. There may be more than one notifications. - flexBlocking: continue aggregate the member response until the group hosting CSE determines to send the aggregated responses, if all member responses has been aggregated, respond the aggregated response as in the blockingRequest case. Otherwise, respond an acknowledgement together with the current aggregated member responses and the reference to the created <request> resource. Then continue aggregate and deliver the remaining member response to the Originator as defined in the nonBlockingRequestSynch or the nonBlockingRequestAsynch case - After the Result Expiration Time, there shall not be any further updates to the aggregated responses (See note) |
| Processing at Member Hosting CSE | For the DELETE procedure, the Members Hosting CSE shall: Check if the request has a group request identifier. Check if the group request identifier is contained in the requested identifier stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the group request identifier until the expiration of the request expiration time or local policy Check if the original Originator has the DELETE permission on the addressed resource. Upon successful validation, perform the delete procedures for the corresponding type of addressed resource as described in other sub-clauses of clause 10.2 Send the corresponding response to the Group Hosting CSE |
| Information in Response message | Converged responses from members hosting CSEs |
| Processing at Originator after receiving Response | None |
| Exceptions | Same request with identical group request identifier received Originator does not have the DELETE permissions to access the <fanOutPoint> resource |
| NOTE: If Result Expiration Time is not provide in the original request from the Originator, the group hosting CSE may decide the timer based on its local policy. |

### -----------------------End of change 3-------------------------------------------

-----------------------Start of change 4-------------------------------------------

#### 10.2.7.x1	<multicastGroup> and <parentGroup> Management Procedures

Figure 10.2.7.x1-1 illustrates how the <multicastGroup> and <parentGroup> resource works on the group Hosting CSE and the group members Hosting CSEs.

Figure 10.2.7.x1-1: Multicast resource related procedures

001: The AE/CSE sends a group resource creation request to the group Hosting CSE.

For example, the member resources m11, m12, m21 and m22 are respectively located on two M2M devices ASN-CSE1 and ASN-CSE2. The access path of the member resources are:

m11 = coap://d1.example.org/xx1/aa

m12 = coap://d1.example.org/yy1/bb

m21 = coap://d2.example.org/xx2/cc

m22 = coap://d2.example.org/yy2/dd

002: The group Hosting CSE creates the group resource, and retrieves multicast capability of all member Hosting CSEs determine whether it is necessary to create a multicast group, based on the local configured criteria. If the group Hosting CSE determines to create multicast group, then perform the following steps, otherwise, end the process.

  - Note1: The group Hosting CSE and member Hosting CSE must be the registration relationship, the group Hosting CSE register on the member Hosting CSE, or the member Hosting CSE register on the group Hosting CSE. For example, the group Hosting CSE residing on IN-CSE can create multicast group for member Hosting CSE residing on MN-CSE, and can not create multicast group for member Hosting CSE residing on ASN-CSE which registers on the MN-CSE.

  - Note 2: The multicast group can be used which hosted CSE scenarios, and the Application Dedicated Node can not be supported.

003: The group Hosting CSE create <multicastGroup>, allocates multicast type based on multicast capability of the member Hosting CSEs and network and member list as the segmentation.

- If the multicast type is 3GPP_MBMS_group, the multicast Address should be the address of 3GPP group service server.

- If the multicast type is IP_multicast_group, allocates a multicast address to the member resources according to the member devices having the member resources and the access paths of the member resources on the member devices.

The group Hosting CSE establishes a mapping relationship between the multicast address and the fanout URI according to the access paths of the member resources on the member devices. If the access paths of all the members are different, a virtual fan out URI needs to be allocated, such as /wellknown/.

For a guide to an allocation scheme of IPv4 and IPv6 multicast address spaces, reference may be made to standard documents such as [RFC 3171] and [RFC 4291]. As a result, the group Hosting CSE create one or more <multicastGroup> resources as the child resources of the group resource requested by AE/CSE.

In this example, the attributes of the <multicastGroup> resources are illustrated in table 10.2.7.x1-1.

Table 10.2.7.x1-1: Group resource mapping

| Group resource | multicastGroup | multicastType | Member list | Multicast address | fanout URI |
| --- | --- | --- | --- | --- | --- |
| Grp1 | multicastGroup1 | IP_multicast_group | coap://d1.example.org/ coap://d2.example.org/ | [FF32:30:3FFE:FFFF:1::1234] | /wellknown/grp1 |

004: The group Hosting CSE sends a group advertisement for joining a multicast group and create parent group to the member Hosting CSE to instruct them to join the multicast group corresponding to the multicast address.  In this example, the group Hosting CSE should send one group advertisement message for the members.

005: The member Hosting CSE use a multicast management protocol such as MLD or IGMP according to the method of the prior art to join the multicast group corresponding to the multicast address indicated in the multicast group advertisement.

006: The member Hosting CSE create the < parentGroup > after successfully joining the multicast group.

In this example, the both ASN-CSE1 and ASN-CSE2 create one <parentGroup> resource to record to which multicast group its local member resources have joined.

Table 10.2.7.x1-2: parentGroup resource in member Hosting CSE

| parentGroup | Member list | Multicast address | fanout URI |
| --- | --- | --- | --- |
| multicastGroup1 | /xx1/aa /yy1/bb | [FF32:30:3FFE:FFFF:1::1234] | /wellknown/grp1 |
| multicastGroup1 | /xx2/cc /yy2/dd | [FF32:30:3FFE:FFFF:1::1234] | /wellknown/grp1 |

007: The member Hosting CSE send the response to the URI as the attribute responseURI of the <parentGroup>.

008: The AE/CSE sends a request for accessing member resources to group Hosting CSE, asking to access member resources. For example, access the m11 and m21 in the group resource Grp1.

009: The group Hosting CSE check the <multicastGroup>, according to the group resource identifier. If the group has multicast group or the group has a sub group which has the multicast group, check the multicast type:

Case A): The multicast type is 3GPP_MBMS_group.

- 009a then send the group message delivery to the SCEF to start the 3GPP MBMS group message procedure, as specified in 3GPP TS 23.682 [i.14] and 3GPP TS 23.468 [i.*]. The 3GPP MBMS group corresponds to the group concept used in 3GPP TS 23.682 [i.14] and the resourceID of the 3GPP MBMS group corresponds to the External Group ID used in 3GPP TS 23.682 [i.14].

Case B): The multicast type is IP_MBMS_group.

- 009b: a multicast mapping relationship is established for the member resources, constructs a member resource access request, and sends the member resource access request in multicast mode to the multicast address in the mapping relationship (namely, the multicast address).

- 010b: The member Hosting CSE receive the multicast access request, and access the local member resources by mapping the member list and fanout URI.

011: The member Hosting CSE return access results to the URI as the attribute responseURI of the <parentGroup>.

012: The group Hosting CSE aggregates the group member resource access results received from member Hosting CSE.

013: The group Hosting CSE returns the combined group member resource access result to the network application AE.

#### 10.2.7.x2	Create <multicastGroup>

This procedure shall be used for creating <multicastGroup> resource.

Table 10.2.7.x3-1: <multicastGroup> RETRIEVE

| <multicastGroup> RETRIEVE |
| --- |
| Associated Reference Point | Mcc, Mca and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address of the <multicastGroup> resource Content: The representation of the resource the Originator intends to create Group Request Identifier: The group request identifier Response Type: If the parameter is set to BlockingSynch, it indicates that the group Hosting CSE shall return the aggregated response once. Otherwise if the parameter is set to nonBlockingRequestSynch or nonBlockingRequestAsynch, it indicates that the Group Hosting CSE shall return the aggregated response in a batched mode. Result Expiration Time: Indicates the maximum time limit in which the Group Hosting CSE has to respond the aggregated response. |
| Processing at Originator before sending Request | The Originator shall request to obtain <multicastGroup> resource information by using the create operation. The request shall address the specific <multicastGroup> resource of a Hosting CSE. The Originator may be an AE or a CSE |
| Processing at Group Hosting CSE | Besides the generic create procedure defined in clause 10.1.1, the Receiver shall perform the procedure as description in the Figure 10.2.7.x1-1. |
| Processing at Member Hosting CSE | Besides the generic create procedure defined in clause 10.1.2, the Receiver shall perform the procedure as description in the Figure 10.2.7.x1-1 . |
| Processing at Receiver | No change from the basic procedure in clause 10.1.1 |
| Information in Response message | No change from the basic procedure in clause 10.1.1 |
| Processing at Originator after receiving Response | Converged responses from members Hosting CSEs |
| Exceptions | No change from the basic procedure in clause 10.1.1 |

#### 10.2.7.x3	Retrieve <multicastGroup>

This procedure shall be used for retrieving <multicastGroup> resource.

Table 10.2.7.x3-1: <multicastGroup> RETRIEVE

| <multicastGroup> RETRIEVE |
| --- |
| Associated Reference Point | Mcc, Mca and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address of the <multicastGroup> resource Content: The representation of the resource the Originator intends to retrieve Group Request Identifier: The group request identifier Response Type: If the parameter is set to BlockingSynch, it indicates that the group Hosting CSE shall return the aggregated response once. Otherwise if the parameter is set to nonBlockingRequestSynch or nonBlockingRequestAsynch, it indicates that the Group Hosting CSE shall return the aggregated response in a batched mode. Result Expiration Time: Indicates the maximum time limit in which the Group Hosting CSE has to respond the aggregated response. |
| Processing at Originator before sending Request | The Originator shall request to obtain <multicastGroup> resource information by using the RETRIEVE operation. The request shall address the specific <multicastGroup> resource of a Hosting CSE. The Originator may be an AE or a CSE |
| Processing at Group Hosting CSE | Besides the generic create procedure defined in clause 10.1.2, the Receiver shall perform the procedure as description in the Figure 10.2.7.x1-1. |
| Processing at Member Hosting CSE | Besides the generic create procedure defined in clause 10.1.2, the Receiver shall perform the procedure as description in the Figure 10.2.7.x1-1 . |
| Processing at Receiver | No change from the basic procedure in clause 10.1.2 |
| Information in Response message | No change from the basic procedure in clause 10.1.2 |
| Processing at Originator after receiving Response | Converged responses from members Hosting CSEs |
| Exceptions | No change from the basic procedure in clause 10.1.2 |

#### 10.2.7.x4 Update <multicastGroup>

This procedure shall be used for updating an existing <multicastGroup> resource.

Table 10.2.7.x4-1: <multicastGroup> DELETE

| <multicastGroup> DELETE |
| --- |
| Associated Reference Point | Mcc, Mca and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address of the <multicastGroup> resource Content: The representation of the resource the Originator intends to update Group Request Identifier: The group request identifier Response Type: If the parameter is set to BlockingSynch, it indicates that the group Hosting CSE shall return the aggregated response once. Otherwise if the parameter is set to nonBlockingRequestSynch or nonBlockingRequestAsynch, it indicates that the Group Hosting CSE shall return the aggregated response in a batched mode Result Expiration Time: Indicates the maximum time limit in which the Group Hosting CSE has to respond the aggregated response. |
| Processing at Originator before sending Request | The Originator shall request to delete an existing <multicastGroup> resource by using the DELETE operation. The request shall address the specific <multicastGroup> resource of a Hosting CSE. The Originator may be an AE or a CSE. |
| Processing at Group Hosting CSE | Besides the generic create procedure defined in clause 10.1.3, the group Hosting CSE shall: perform multicast message procedure to notify the member resource Hosting CSE to update the <parentGroup> as well; |
| Processing at Member Hosting CSE | The member Hosting CSE shall: Check if the request has a group request identifier. Check if the group request identifier is contained in the requested identifier stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the group request identifier until the expiration of the request expiration time or local policy Check if the original Originator has the UPDATE permission on the addressed resource. Upon successful validation, perform the updating the attributes as description in clause 9.6.y. Send the corresponding response to the response URI |
| Processing at Receiver | No change from the basic procedure in clause 10.1.3 |
| Information in Response message | No change from the basic procedure in clause 10.1.3 |
| Processing at Originator after receiving Response | Converged responses from members Hosting CSEs |
| Exceptions | No change from the basic procedure in clause 10.1.3 |

#### 10.2.7.x5	Delete <multicastGroup>

This procedure shall be used for deleting an existing <multicastGroup> resource.

Table 10.2.7.x4-1: <multicastGroup> DELETE

| <multicastGroup> DELETE |
| --- |
| Associated Reference Point | Mcc, Mca and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address of the <multicastGroup> resource Content: The representation of the resource the Originator intends to delete Group Request Identifier: The group request identifier Response Type: If the parameter is set to BlockingSynch, it indicates that the group Hosting CSE shall return the aggregated response once. Otherwise if the parameter is set to nonBlockingRequestSynch or nonBlockingRequestAsynch, it indicates that the Group Hosting CSE shall return the aggregated response in a batched mode Result Expiration Time: Indicates the maximum time limit in which the Group Hosting CSE has to respond the aggregated response. |
| Processing at Originator before sending Request | The Originator shall request to delete an existing <multicastGroup> resource by using the DELETE operation. The request shall address the specific <multicastGroup> resource of a Hosting CSE. The Originator may be an AE or a CSE. |
| Processing at Group Hosting CSE | Besides the generic create procedure defined in clause 10.1.4, the group Hosting CSE shall: perform multicast message procedure to notify the member resource Hosting CSE to leave the multicast group and delete the <parentGroup>; |
| Processing at Member Hosting CSE | The member Hosting CSE shall: Check if the request has a group request identifier. Check if the group request identifier is contained in the requested identifier stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the group request identifier until the expiration of the request expiration time or local policy Check if the original Originator has the DELETE permission on the addressed resource. Upon successful validation, perform the multicast group leave procedure and the delete <parentGroup> procedures. Send the corresponding response to the response URI |
| Processing at Receiver | No change from the basic procedure in clause 10.1.4 |
| Information in Response message | No change from the basic procedure in clause 10.1.4 |
| Processing at Originator after receiving Response | Converged responses from members Hosting CSEs |
| Exceptions | No change from the basic procedure in clause 10.1.4 |

#### 10.2.7.x6	Create <parentGroup>

This procedure shall be used for creating <parentGroup> resource.

Table 10.2.7.x6-1: <parentGroup> CREATE

| <parentGroup> CREATE |
| --- |
| Associated Reference Point | Mcc, Mca and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address the <parentGroup> resource. Content: The representation of the <parentGroup> resource for which the attributes are described in clause 9.6.13 |
| Processing at Originator before sending Request | The Originator should be a group management server. The <multicastGroup> resource should be created inside the group management server first, and then the group management server notice the group members to join the multicast group using the CREATE operation. |
| Processing at Receiver | Besides the basic procedures described in clause 10.1.1.1, the receiver shall also comply with the multicast management protocol such as MLD or IGMP to join the multicast group and create <parentGroup> as description in the Figure 10.2.7.x1-1. |
| Information in Response message | According to clause 10.1.1.1. |
| Processing at Originator after receiving Response | None |
| Exceptions | If the Receiver responds with an error, the originator should delete the receiver’s information from the <multicastGroup> resource locally stored. |

#### 10.2.7.x7	Update <parentGroup>

This procedure shall be used for updating <parentGroup> resource.

Table 10.2.7.x6-1: <parentGroup> UPDATE

| <parentGroup> UPDATE |
| --- |
| Associated Reference Point | Mcc, Mca and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address the <parentGroup> resource. Content: The representation of the <parentGroup> resource for which the attributes are described in clause 9.6.13 |
| Processing at Originator before sending Request | The Originator should be a group management server. The <multicastGroup> resource should be created inside the group management server first, and then the group management server notice the group members to join the multicast group using the CREATE operation. |
| Processing at Receiver | For the UPDATE procedure, the Member Hosting CSE shall: Check if the request has a group request identifier. Check if the request identifier is contained in the requested identifier stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the request identifier until the expiration of the request expiration time or local policy Check if the original Originator has the UPDATE permission on the addressed resource. Upon successful validation, perform the update procedures for attributes as described in other sub-clauses of clause 9.6.y Send the corresponding response to the group Hosting CSE. |
| Information in Response message | According to clause 10.1.3 |
| Processing at Originator after receiving Response | None |
| Exceptions | None |

#### 10.2.7.x8	Delete <parentGroup>

This procedure shall be used for deleting an existing <parentGroup> resource.

Table 10.2.7.x7-1: <parentGroup> DELETE

| <parentGroup> DELETE |
| --- |
| Associated Reference Point | Mcc, Mca and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address of the <parentGroup> resource |
| Processing at Originator before sending Request | The Originator shall request to delete an existing <parentGroup> resource by using the DELETE operation. The request shall address the specific <group> resource of a Hosting CSE. The Originator may be an AE or a CSE. |
| Processing at Receiver | Besides the basic procedures described in clause 10.1.4, the receiver shall also comply with the multicast management protocol such as MLD or IGMP to leave the multicast group and delete <parentGroup>as description in the Figure 10.2.7.x1-1 |
| Information in Response message | No change from the basic procedure in clause 10.1.4 |
| Processing at Originator after receiving Response | None |
| Exceptions | No change from the basic procedure in clause 10.1.4 |

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5-------------------------------------------

#### 2.2	Informative references

[i.*]	3GPP TS 23.468 3rd Generation Partnership Project;Technical Specification Group Services and System Aspects;Group Communication System Enablers for LTE (GCSE_LTE); Stage 2. (Release 13)

### -----------------------End of change 5---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?