| Input Contribution |
| --- |
| Meeting ID* | ARC#27 |
| Title:* | Features catalog |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd., Yinjiaxin@huawei.com Yang Xiao, Huawei Technologies Co., Ltd., xiaoyang.xiao@huawei.com Dong Wang, Huawei Technologies Co., Ltd., dong.wang@huawei.com |
| Uploaded Date:* | 2017-2-4 |
| Document(s) Impacted* | TR-0032 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to be incorporated into the document. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1-------------------------------------------

## 2.1	Normative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M TS-0001: "Functional Architecture".

[2]	oneM2M TS-0004: "Service Layer Core Protocol Specification"

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

# 4	Conventions,

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

The Optionality defined in the each of the Features means if the Feature is mandatory (M) of optional (O) if the implementor intends to implement the feature set. If the Implementation is to support a certain Feature Set, all Features marked M shall be supported by the Implementation.

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

# 6	oneM2M defined Functions

### 6.1	General capability (GEN)

#### 6.1.1	Binding and serialization

#### The Feature Set is about AE and CSE supporting binding oneM2M primitives to transport networks. At least one of the bindings shall be supported.

Table 6.1.1-1: Features of GE/GEN/00001

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| GE/GEN/00001/00001 | Support HTTP binding | O | 1,2 |
| GE/GEN/00001/00002 | Support CoAP binding | O | 1,2 |
| GE/GEN/00001/00003 | Support MQTT binding | O | 1,2 |
| GE/GEN/00001/00004 | Support Websocket binding | O | 2 |

#### The Feature Set is about AE and CSE supporting serializations. At least one of the serializations shall be supported.

#### Table 6.1.1-2: Features of GE/GEN/00002

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| GE/GEN/00002/00001 | Support XML serialization | O | 1,2 |
| GE/GEN/00002/00002 | Support JSON serialization | O | 1,2 |
| GE/GEN/00002/00003 | Support CBOR serialization | O | 2 |

#### 6.1.2	Resource Identification

The Feature Set is about CSE supporting resource identification.

Table 6.1.2-1: Features of GE/GEN/00003

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| GE/GEN/00003/00001 | Support Unstructured resource identifier | M | 1,2 |
| GE/GEN/00003/00002 | Support Structured resource identifier | M | 1,2 |

The Feature Set is about AE supporting resource identification. At least one of the Features shall be supported.

Table 6.1.2-2: Features of GE/GEN/00004

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| GE/GEN/00004/00001 | Support CSE-relative Unstructured resource identifier | O | 1,2 |
| GE/GEN/00004/00002 | Support SP-relative Unstructured resource identifie | O | 1,2 |
| GE/GEN/00004/00003 | Support Absolute Unstructured resource identifier | O | 1,2 |
| GE/GEN/00004/00004 | Support CSE-relative Structured resource identifier | O | 1,2 |
| GE/GEN/00004/00005 | Support SP-relative Structured resource identifier | O | 1,2 |
| GE/GEN/00004/00006 | Support Absolute Structured resource identifier | O | 1,2 |

### 6.1.3	Resource Addressing

The Feature Set is about CSE supporting resource addressing.

Table 6.1.3-1: Features of CE/GEN/00001

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/GEN/00001/00001 | Support blocking request with correct response status code | M | 1,2 |
| CE/GEN/00001/00002 | Support of request with result content | O | 1,2 |
| CE/GEN/00001/00003 | Support attribute addressing for Retrieve | O | 1,2 |

The Feature Set is about AE supporting resource addressing.

Table 6.1.3-2: Features of AE/GEN/00001

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/GEN/00001/00001 | Support Create request targeting one resource | O | 1,2 |
| AE/GEN/00001/00002 | Support Update request targeting one resource | O | 1,2 |
| AE/GEN/00001/00003 | Support Retrieve request targeting one resource | O | 1,2 |
| AE/GEN/00001/00004 | Support Delete request targeting one resource | O | 1,2 |
| AE/GEN/00001/00005 | Support requesting one attribute of a resource | O |  |
| AE/GEN/00001/00006 | Support of requesting attributes by setting Result Content | O | 1,2 |
| AE/GEN/00001/00007 | Support of requesting hierarchical address by setting Result Content | O | 1,2 |
| AE/GEN/00001/00008 | Support of requesting hierarchical address and attributes by setting Result Content | O | 1,2 |
| AE/GEN/00001/00009 | Support of requesting attributes and child resources by setting Result Content | O | 1,2 |
| AE/GEN/00001/00010 | Support of requesting child resources by setting Result Content | O | 1,2 |
| AE/GEN/00001/00011 | Support of requesting attributes and child resource references by setting Result Content | O | 1,2 |
| AE/GEN/00001/00012 | Support of requesting child resource references by setting Result Content | O | 1,2 |
| AE/GEN/00001/00013 | Support of requesting nothing by setting Result Content | O | 1,2 |

### 6.2	Registration (REG)

#### 6.2.1	CSE capability discovery

#### The Feature Set is about CSE supporting discovery of basic CSE capabilities.

Table 6.2.1-1: Feature set CE/REG/00001

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/REG/00001/00001 | Support <CSEBase> resource with attributes multiplicity equals 1[1]. | M | 1,2 |
| CE/REG/00001/00002 | Support the cseType attribute of <CSEBase> resource | O | 1,2 |
| CE/REG/00001/00003 | Support the nodeLink attribute of <CSEBase> resource. This is dependent on the feature set for <node> resource. | O | 1,2 |

Table 6.2.1-2: Feature set AE/REG/00001

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/REG/00001/00001 | The Retrival of <CSEBase> | O | 1,2 |

#### 6.2.2	AE registration

#### The Feature Set is about CSE supporting AE registration.

Table 6.2.2-1: Feature set CE/REG/00002

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/REG/00002/00001 | Support <AE> resource with attributes multiplicity equals 1[1] | M | 1,2 |
| CE/REG/00002/00002 | AE registration without pre-assigned AE-ID in the registration request. Possible cases are: The request includes AE-ID Stem as ‘C’. The request includes AE-ID Stem as ‘S’. The request does not include AE-ID Stem | M | 1,2 |
|  | AE registration with pre-assigned AE-ID | M | 1,2 |
| CE/REG/00002/00003 | Support the labels attribute of <AE> resource | O | 1,2 |
| CE/REG/00002/00004 | Support the applicationName attribute of <AE> resource | O | 1,2 |
| CE/REG/00002/00005 | Support the pointOfAccess attribute of <AE> resource | O | 1,2 |

The Feature Set is about CSE supporting allowed combination of IDs according to service subscriptions.

Table 6.2.2-2: Feature set CE/REG/00003

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/REG/00003/00001 | Support <m2mServiceSubscriptionProfile> resource with attribute multiplicity equals 1[1] | M | 1,2 |
| CE/REG/00003/00002 | Support the labels attribute of <m2mServiceSubscriptionProfile> resource | O | 1,2 |
| CE/REG/00003/00003 | Support the CRUD of <serviceSubscribedNode> with attribute multiplicity equals 1 | M | 1,2 |
| CE/REG/00003/00004 | Support the labels attribute of <serviceSubscribedNode> | O | 1,2 |
| CE/REG/00003/00005 | Support the CSE-ID attribute of < serviceSubscribedNode > | O | 1,2 |
| CE/REG/00003/00006 | Support the deviceIdentifier attribute of < serviceSubscribedNode > | O | 1,2 |
| CE/REG/00003/00007 | Support the ruleLinks attribute of < serviceSubscribedNode > | O | 1,2 |
| CE/REG/00003/00008 | Support the CRUD of < serviceSubscribedAppRule > with attribute multiplicity equals 1 | O | 1,2 |
| CE/REG/00003/00009 | Support the labels attribute of < serviceSubscribedAppRule > | O | 1,2 |
| CE/REG/00003/00010 | Support the allowedApp-IDs attribute of <serviceSubscribedAppRule > | O | 1,2 |
| CE/REG/00003/00011 | Support the allowedAEs attribute of <serviceSubscribedAppRule > | O | 1,2 |
| CE/REG/00003/00012 | Support the allowedRole-IDs attribute of <serviceSubscribedAppRule> | O | 1,2 |

Editor’s Note: contribution about announcement creation is needed.

The Feature Set is about AE supporting AE registration

Table 6.2.2-3: Feature set AE/REG/00002

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/REG/00002/00001 | Create <AE> with mandatory attributes[2] | O | 1,2 |
| AE/REG/00002/00002 | Create <AE> with resourceName attribute | O | 1,2 |
| AE/REG/00002/00003 | Create <AE> with expirationTime attribute | O | 1,2 |
| AE/REG/00002/00004 | Create <AE> with labels | O | 1,2 |
| AE/REG/00002/00005 | Create <AE> with applicationName | O | 1,2 |
| AE/REG/00002/00006 | Create <AE> with pointOfAccess | O | 1,2 |
| AE/REG/00002/00007 | Create <AE> with nodeLink | O | 1,2 |
| AE/REG/00002/00008 | Create <AE> with contentSerialization | O | 1,2 |
| AE/REG/00002/00009 | Update <AE> with expirationTime | O | 1,2 |
| AE/REG/00002/00010 | Update <AE> with labels | O | 1,2 |
| AE/REG/00002/00011 | Update <AE> with applicationName | O | 1,2 |
| AE/REG/00002/00012 | Update <AE> with pointOfAccess | O | 1,2 |
| AE/REG/00002/00013 | Update <AE> with nodeLink | O | 1,2 |
| AE/REG/00002/00014 | Update <AE> with requestReachability | O | 1,2 |
| AE/REG/00002/00015 | Update <AE> with contentSerialization | O | 1,2 |
| AE/REG/00002/00016 | Delete <AE> | O | 1,2 |
| AE/REG/00002/00017 | Retrieve <AE> | O | 1,2 |

#### 6.2.3	CSE registration

The Feature Set is about CSE supporting CSE registration as registrar CSE.

Table 6.2.3-1: Feature Set CE/REG/00006

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/REG/00006/00001 | Support <remoteCSE> resource with attributes multiplicity equals 1[1] | M | 1,2 |
| CE/REG/00006/00002 | Support the labels attribute of <remoteCSE> resource | O | 1,2 |
| CE/REG/00006/00003 | Support the cseType attribute of <remoteCSE> resource | O | 1,2 |
| CE/REG/00006/00004 | Support the pointOfAccess attribute of <remoteCSE> resource | O | 1,2 |
| CE/REG/00006/00005 | Support the nodeLink attribute of <remoteCSE> resource | O | 1,2 |

### The Feature Set is about CSE supporting CSE registration as registree CSE.

Table 6.2.3-2: Features of CE/REG/00007

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/REG/00007/00001 | The Creation with <remoteCSE> resource for CSE registration with mandatory attributes[2] for Create and locally create <remoteCSE> that represents the Regstree CSE | O | 1,2 |
| CE/REG/00007/00002 | Create the <remoteCSE> with resourceName attribute | O | 1,2 |
| CE/REG/00007/00003 | Create the <remoteCSE> with expirationTime attribute | O | 1,2 |
| CE/REG/00007/00004 | Create the <remoteCSE> with labels attribute | O | 1,2 |
| CE/REG/00007/00005 | Create the <remoteCSE> with cseType attribute | O | 1,2 |
| CE/REG/00007/00006 | Create the <remoteCSE> with pointOfAccess attribute | O | 1,2 |
| CE/REG/00007/00007 | Create the <remoteCSE> with nodeLink attribute | O | 1,2 |
| CE/REG/00007/00008 | Update the <remoteCSE> with labels | O | 1,2 |
| CE/REG/00007/00009 | Update the <remoteCSE> with expirationTime | O | 1,2 |
| CE/REG/00007/00010 | Update the <remoteCSE> with pointOfAccess attribute | O | 1,2 |
| CE/REG/00007/00011 | Update the <remoteCSE> with requestReachability | O | 1,2 |
| CE/REG/00007/00012 | Update the <remoteCSE> with nodeLink attribute | O | 1,2 |
| CE/REG/00007/00013 | Delete the <remoteCSE> resource on the Registrar, also delete the <remoteCSE> resource on the Registree | O | 1,2 |
| CE/REG/00007/00014 | Retrieve the <remoteCSE> resource | O | 1,2 |

## 6.3	Data Management and Repository (DMR)

#### 6.3.1	Configuration of container for data sharing

The Feature Set is about CSE supporting configuration of container.

Table 6.3.1-1: Feature Set CE/DMR/00001

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/DMR/00001/00001 | Support <container> resource with attributes multiplicity equals 1[1] | M | 1,2 |
| CE/DMR/00001/00002 | Support the labels attribute of <container> resource | O | 1,2 |
| CE/DMR/00001/00003 | Support the creator attribute of <container> resource | O | 1,2 |
| CE/DMR/00001/00004 | Support the maxNrOfInstances attribute of <container> resource | O | 1,2 |
| CE/DMR/00001/00005 | Support the maxByteSize attribute of <container> resource | O | 1,2 |
| CE/DMR/00001/00006 | Support the maxInstanceAge attribute of <container> resource | O | 1,2 |

The Feature Set is about AE supporting configuration of container.

Table 6.3.1-2: Feature Set AE/DMR/00001

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/DMR/00001/00001 | Create <container> with no attribute set | O | 1,2 |
| AE/DMR/00001/00002 | Create <container> with resourceName | O | 1,2 |
| AE/DMR/00001/00003 | Create <container> with expirationTime | O | 1,2 |
| AE/DMR/00001/00004 | Create <container> with labels | O | 1,2 |
| AE/DMR/00001/00005 | Create <container> with creator | O | 1,2 |
| AE/DMR/00001/00006 | Create <container> with maxNrOfInstances | O | 1,2 |
| AE/DMR/00001/00007 | Create <container> with maxByteSize | O | 1,2 |
| AE/DMR/00001/00008 | Create <container> with maxInstanceAge | O | 1,2 |
| AE/DMR/00001/00009 | Update <container> with expirationTime | O | 1,2 |
| AE/DMR/00001/00010 | Update <container> with labels | O | 1,2 |
| AE/DMR/00001/00011 | Update <container> with maxNrOfInstances | O | 1,2 |
| AE/DMR/00001/00012 | Update <container> with maxByteSize | O | 1,2 |
| AE/DMR/00001/00013 | Update <container> with maxInstanceAge | O | 1,2 |
| AE/DMR/00001/00014 | Delete <container> | O | 1,2 |
| AE/DMR/00001/00015 | Retrieve <container> | O | 1,2 |

#### 6.3.2	Managing data instance

#### The Feature Set is about CSE supporting managing data instance.

Table 6.3.2-1: Feature Set CE/DMR/00002

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/DMR/00002/00001 | Support <contentInstance> resource with attributes multiplicity equals 1[1] | O | 1,2 |
| CE/DMR/00002/00002 | Support the labels attribute of <contentInstance> resource | O | 1,2 |
| CE/DMR/00002/00003 | Support the creator attribute of <contentInstance> resource | O | 1,2 |
| CE/DMR/00002/00004 | Support the contentInfo attribute of <contentInstance> resource | O | 1,2 |
| CE/DMR/00002/00005 | Support the contentRef attribute of <contentInstance> resource | O | 1,2 |
| CE/DMR/00002/00006 | Retrieve and Delete of latest <contentInstance> resource by <latest> virtual resource | O | 1,2 |
| CE/DMR/00002/00007 | Retrieve and Delete of oldest <contentInstance> resource by <oldest> virtual resource | O | 1,2 |

The Feature Set is about AE supporting reporting of data instance.

Table 6.3.2-2: Feature Set AE/DMR/00002

| Feature ID | Feature Description | Category | Release |
| --- | --- | --- | --- |
| AE/DMR/00002/00001 | Create <contentInstance> with mandatory attributes[2] | O | 1,2 |
| AE/DMR/00002/00002 | Create <contentInstance> with resourceName | O | 1,2 |
| AE/DMR/00002/00003 | Create <contentInstance> with expirationTime | O | 1,2 |
| AE/DMR/00002/00004 | Create <contentInstance> with labels | O | 1,2 |
| AE/DMR/00002/00005 | Create <contentInstance> with creator | O | 1,2 |
| AE/DMR/00002/00006 | Create <contentInstance> with contentInfo | O | 1,2 |
| AE/DMR/00002/00007 | Create <contentInstance> with contentRef | O | 1,2 |
| AE/DMR/00002/00008 | Delete <contentInstance> | O | 1,2 |
| AE/DMR/00002/00009 | Retrieve <contentInstance> | O | 1,2 |

## 6.4	Device Management (DMG)

### 6.4.1	Configuration of node

The Feature Set is about CSE supporting configuration of node.

Table 6.4.1-1: Feature Set CE/DMG/00001

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/DMG/00001/00001 | Support <node> resource with attributes multiplicity equals 1[1] | M | 1,2 |
| CE/DMG/00001/00002 | Support the labels attribute of <node> resource | O | 1,2 |
| CE/DMG/00001/00003 | Support the hostedCSELink attribute of <node> resource | O | 1,2 |

The Feature Set is about AE supporting configuration of node.

Table 6.4.1-2: Feature Set AE/DMG/00001

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/DMG/00001/00001 | Create <node> resource with mandatory attributes[2] | O | 1,2 |
| AE/DMG/00001/00002 | Create <node> resource with resourceName | O | 1,2 |
| AE/DMG/00001/00003 | Create <node> resource with expirationTime | O | 1,2 |
| AE/DMG/00001/00004 | Create <node> resource with labels | O | 1,2 |
| AE/DMG/00001/00005 | Create <node> resource with hostedCSELink | O | 1,2 |
| AE/DMG/00001/00006 | Update <node> resource with expirationTime | O | 1,2 |
| AE/DMG/00001/00007 | Update <node> resource with labels | O | 1,2 |
| AE/DMG/00001/00008 | Update <node> resource with nodeID | O | 1,2 |
| AE/DMG/00001/00009 | Delete <node> | O | 1,2 |
| AE/DMG/00001/00010 | Retrieve <node> | O | 1,2 |

### 6.4.2	Configuration of mgmtObj for device management

The Feature Set is about CSE supporting configuration of <mgmtObj> for device management.

Table 6.4.2-1: Feature Set CE/DMG/00002

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/DMG/00002/00001 | Support <mgmtObj> resource with attributes multiplicity equals 1[1] | M | 1,2 |
| CE/DMG/00002/00002 | Support the labels attribute of <mgmtObj> resource | O | 1,2 |
| CE/DMG/00002/00003 | Support the description attribute of <mgmtObj> resource | O | 1,2 |
| CE/DMG/00002/00004 | Support the mgmtLink attribute of <mgmtObj> resource | O | 1,2 |

The Feature Set is about AE supporting configuration of <mgmtObj> for device management.

Table 6.4.2-2: Feature Set AE/DMG/00002

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/DMG/00002/00001 | Create <mgmtObj> with no attribute set | O | 1,2 |
| AE/DMG/00002/00002 | Create <mgmtObj> resource with mgmtDefinition | O | 1,2 |
| AE/DMG/00002/00003 | Create <mgmtObj> resource with resourceName | O | 1,2 |
| AE/DMG/00002/00004 | Create <mgmtObj> resource with expirationTime | O | 1,2 |
| AE/DMG/00002/00005 | Create <mgmtObj> resource with labels | O | 1,2 |
| AE/DMG/00002/00006 | Create <mgmtObj> resource with mgmtLink | O | 1,2 |
| AE/DMG/00002/00007 | Update <mgmtObj> resource with description | O | 1,2 |
| AE/DMG/00002/00008 | Update <mgmtObj> resource with mgmtLink | O | 1,2 |
| AE/DMG/00002/00009 | Update <mgmtObj> resource with expirationTime | O | 1,2 |
| AE/DMG/00002/00010 | Update <mgmtObj> resource with labels | O | 1,2 |
| AE/DMG/00002/00011 | Delete <mgmtObj> | O | 1,2 |
| AE/DMG/00002/00012 | Retrieve <mgmtObj> | O | 1,2 |

### 6.4.3	Software management

The Feature Set is about CSE supporting software management.

Table 6.4.3-1: Feature Set CE/DMG/00003

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/DMG/00003/00001 | Support the [software] specialization attributes multiplicity equals 1[1] | M | 1,2 |
| CE/DMG/00003/00002 | Support the activate attribute of [software] resource | O | 1,2 |
| CE/DMG/00003/00003 | Support the deactivate attribute of [software] resource | O | 1,2 |
| CE/DMG/00003/00004 | Support the activeStatus attribute of [software] resource | O | 1,2 |

The Feature Set is about AE supporting software management.

Table 6.4.3-2: Feature Set AE/DMG/00003

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/DMG/00003/00001 | Create [software] resource with mandatory [objectAttribute][2] | O | 1,2 |
| AE/DMG/00003/00002 | Update [software] resource with softwareName | O | 1,2 |
| AE/DMG/00003/00003 | Update [software] resource with URL | O | 1,2 |
| AE/DMG/00003/00004 | Update [software] resource with install | O | 1,2 |
| AE/DMG/00003/00005 | Update [software] resource with uninstall | O | 1,2 |
| AE/DMG/00003/00006 | Update [software] resource with activate | O | 1,2 |
| AE/DMG/00003/00007 | Update [software] resource with deactive | O | 1,2 |

### 6.4.4	Firmware management

The Feature Set is about CSE supporting firmware management.

Table 6.4.4-1: Feature Set CE/DMG/00004

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/DMG/00004/00001 | Support the [firmware] specialization attributes multiplicity equals 1[1] | M | 1,2 |

The Feature Set is about AE supporting firmware management.

Table 6.4.4-2: Feature Set AE/DMG/00004

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/DMG/00004/00001 | Create [firmware] resource with mandatory [objectAttribute][2] | O | 1,2 |
| AE/DMG/00004/00002 | Update [firmware] resource with version | O | 1,2 |
| AE/DMG/00004/00003 | Update [firmware] resource with firmwareName | O | 1,2 |
| AE/DMG/00004/00004 | Update [firmware] resource with URL | O | 1,2 |
| AE/DMG/00004/00005 | Update [firmware] resource with update | O | 1,2 |
| AE/DMG/00004/00006 | Update [firmware] resource with updateStatus | O | 1,2 |

### 6.4.5	Management of device information

The Feature Set is about CSE supporting management of information of a device.

Table 6.4.5-1: Feature Set CE/DMG/00005

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/DMG/00005/00001 | Support the [deviceInfo] specialization attributes multiplicity equals 1[1] | M | 1,2 |

The Feature Set is about AE supporting management of information of a device.

Table 6.4.5-2: Feature Set AE/DMG/00005

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/DMG/00005/00001 | Create [deviceInfo] resource with mandatory [objectAttribute][2] | O | 1,2 |
| AE/DMG/00005/00002 | Update [deviceInfo] resource with deviceLabel attribute | O | 1,2 |
| AE/DMG/00005/00003 | Update [deviceInfo] resource with manufacture attribute | O | 1,2 |
| AE/DMG/00005/00004 | Update [deviceInfo] resource with model attribute | O | 1,2 |
| AE/DMG/00005/00005 | Update [deviceInfo] resource with deviceType attribute | O | 1,2 |
| AE/DMG/00005/00006 | Update [deviceInfo] resource with fwVersion attribute | O | 1,2 |
| AE/DMG/00005/00007 | Update [deviceInfo] resource with swVersion attribute | O | 1,2 |
| AE/DMG/00005/00008 | Update [deviceInfo] resource with hwVersion attribute | O | 1,2 |

### 6.4.6	Management of device capability

The Feature Set is about CSE supporting device capability management.

Table 6.4.6-1: Feature Set CE/DMG/00006

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/DMG/00006/00001 | Support [deviceCapability] specialization attributes multiplicity equals 1[1] | M | 1,2 |
| CE/DMG/00006/00002 | Support the enable attribute of [deviceCapability] resource | O | 1,2 |
| CE/DMG/00006/00003 | Support the disable attribute of [deviceCapability] resource | O | 1,2 |

The Feature Set is about AE supporting device capability management.

Table 6.4.6-2: Feature Set AE/DMG/00006

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/DMG/00006/00001 | Create [deviceCapability] resource with mandatory [objectAttribute][2] | O | 1,2 |
| AE/DMG/00006/00002 | Create [deviceCapability] resource with enable | O | 1,2 |
| AE/DMG/00006/00003 | Create [deviceCapability] resource with disable | O | 1,2 |
| AE/DMG/00006/00004 | Update [deviceCapability] resource with capabilityName | O | 1,2 |
| AE/DMG/00006/00005 | Update [deviceCapability] resource with attached | O | 1,2 |
| AE/DMG/00006/00006 | Update [deviceCapability] resource with capabilityActionStatus | O | 1,2 |
| AE/DMG/00006/00007 | Update [deviceCapability] resource with currentState | O | 1,2 |
| AE/DMG/00006/00008 | Update [deviceCapability] resource with enable | O | 1,2 |
| AE/DMG/00006/00009 | Update [deviceCapability] resource with disable | O | 1,2 |

### 6.4.7	Reboot and factory reset

The Feature Set is about CSE supporting device reboot or factory reset.

Table 6.4.7-1: Feature Set CE/DMG/00007

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/DMG/00007/00001 | Support [reboot] specialization attributes multiplicity equals 1[1] | M | 1,2 |

The Feature Set is about AE supporting device reboot or factory reset.

Table 6.4.7-2: Feature Set AE/DMG/00007

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/DMG/00007/00001 | Create [reboot] resource with reboot attribute | O | 1,2 |
| AE/DMG/00007/00002 | Create [reboot] resource with factoryReset attribute | O | 1,2 |
| AE/DMG/00007/00003 | Update [reboot] resource with reboot attribute | O | 1,2 |
| AE/DMG/00007/00004 | Update [reboot] resource with factoryReset attribute | O | 1,2 |

### 6.4.8	Memory management

The Feature Set is about CSE supporting retrieval of information associated with the memory in use by a device.

Table 6.4.8-1: Feature Set CE/DMG/00008

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/DMG/00008/00001 | Support [memory] specialization attributes multiplicity equals 1[1] | M | 1,2 |

The Feature Set is about AE supporting retrieval of information associated with the memory in use by a device.

Table 6.4.8-2: Feature Set AE/DMG/00008

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/DMG/00008/00001 | Create [memory] resource with mandatory [objectAttribute][2] | O | 1,2 |
| AE/DMG/00008/00002 | Update [memory] resource with memAvailable attribute | O | 1,2 |
| AE/DMG/00008/00003 | Update [memory] resource with memTotal attribute | O | 1,2 |

6.4.9	Battery management

The Feature Set is about CSE supporting retrieval of information associated with the battery in use by a device.

Table 6.4.9-1: Feature Set CE/DMG/00009

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/DMG/00009/00001 | Support the [battery] specialization attributes multiplicity equals 1[1] | M | 1,2 |

The Feature Set is about AE supporting retrieval of information associated with the battery in use by a device.

Table 6.4.9-2: Feature Set AE/DMG/00009

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/DMG/00009/00001 | Create [battery] resource with mandatory [objectAttribute][2] | O | 1,2 |
| AE/DMG/00009/00002 | Update [battery] resource with batteyLevel attribute | O | 1,2 |
| AE/DMG/00009/00003 | Update [battery] resource with batteryStatus attribute | O | 1,2 |

### 6.4.10	Device Diagnostics and Monitoring

The Feature Set is about CSE supporting retrieval of event logs from a device.

Table 6.4.10-1: Feature Set CE/DMG/00010

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/DMG/00010/00001 | Support [eventLog] specialization attributes multiplicity equals 1[1] | M | 1,2 |

The Feature Set is about AE supporting retrieval of event logs from a device.

Table 6.4.10-2: Feature Set AE/DMG/00010

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/DMG/00010/00001 | Create [eventLog] resource with mandatory [objectAttribute][2] | O | 1,2 |
| AE/DMG/00010/00002 | Create [eventLog] resource with logStart attribute | O | 1,2 |
| AE/DMG/00010/00003 | Create [eventLog] resource with logStop attribute | O | 1,2 |
| AE/DMG/00010/00004 | Update [eventLog] resource with logTypeId attribute | O | 1,2 |
| AE/DMG/00010/00005 | Update [eventLog] resource with logData attribute | O | 1,2 |
| AE/DMG/00010/00006 | Update [eventLog] resource with logStatus attribute | O | 1,2 |
| AE/DMG/00010/00007 | Update [eventLog] resource with logStart attribute | O | 1,2 |
| AE/DMG/00010/00008 | Update [eventLog] resource with logStop attribute | O | 1,2 |

### 6.4.11	Configuration of mgmtObj for device Topology Managment

The Feature Set is about CSE supporting area network topology managment.

Table 6.4.11-1: Feature Set CE/DMG/00011

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/DMG/00011/00001 | Support [areaNwkInfo] specialization attributes multiplicity equals 1[1] | M | 1,2 |

The Feature Set is about AE supporting area netork topology managment.

Table 6.4.11-2: Feature Set AE/DMG/00011

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/DMG/00011/00001 | Create [areaNwkInfo] resource with mandatory [objectAttribute][2] | O | 1,2 |
| AE/DMG/00011/00002 | Update [areaNwkInfo] resource with areaNwkType | O | 1,2 |
| AE/DMG/00011/00003 | Update [areaNwkInfo] resource with listOfDevices | O | 1,2 |

The Feature Set is about CSE supporting retrieval of the information of  a device in the area network.

Table 6.4.11-3: Feature Set CE/DMG/00012

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/DMG/00012/00001 | Support [areaNwkDeviceInfo] specialization attributes multiplicity equals 1[1] | M | 1,2 |
| CE/DMG/00012/00002 | Support the sleepInterval attribute of [areaNwkDeviceInfo] resource | O | 1,2 |
| CE/DMG/00012/00003 | Support the sleepDuration attribute of [areaNwkDeviceInfo] resource | O | 1,2 |
| CE/DMG/00012/00004 | Support the status attribute of [areaNwkDeviceInfo] resource | O | 1,2 |

The Feature Set is about AE supporting retrieval of the information of a device in the area network.

Table 6.4.11-4: Feature Set AE/DMG/00012

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/DMG/00012/00001 | Create [areaNwkDeviceInfo] resource with mandatory [objectAttribute][2] | O | 1,2 |
| AE/DMG/00012/00002 | Create [areaNwkDeviceInfo] resource with sleepInterval | O | 1,2 |
| AE/DMG/00012/00003 | Create [areaNwkDeviceInfo] resource with sleepDuration | O | 1,2 |
| AE/DMG/00012/00004 | Create [areaNwkDeviceInfo] resource with devStatus | O | 1,2 |
| AE/DMG/00012/00005 | Update [areaNwkDeviceInfo] resource with devID | O | 1,2 |
| AE/DMG/00012/00006 | Update [areaNwkDeviceInfo] resource with devType | O | 1,2 |
| AE/DMG/00012/00007 | Update [areaNwkDeviceInfo] resource with areaNwkId | O | 1,2 |
| AE/DMG/00012/00008 | Update [areaNwkDeviceInfo] resource with sleepInterval | O | 1,2 |
| AE/DMG/00012/00009 | Update [areaNwkDeviceInfo] resource with sleepDuration | O | 1,2 |
| AE/DMG/00012/00010 | Update [areaNwkDeviceInfo] resource with devStatus | O | 1,2 |
| AE/DMG/00012/00011 | Update [areaNwkDeviceInfo] resource with listOfNeighbors | O | 1,2 |

### 6.4.12	Adapter of the technology specific protocol

The Feature Set is about CSE supporting adapter of the technology specific protocol.

Table 6.4.12-1: Feature Set CE/DMG/00013

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/DMG/00013/00001 | Support the objectIDs attribute of <mgmtObj> resource | M | 1,2 |
| CE/DMG/00013/00002 | Support the objectPaths attribute of <mgmtObj> resource | M | 1,2 |
| CE/DMG/00013/00003 | Support the mgmtLink attribute of <mgmtObj> resource | O | 1,2 |

## 6.5	Discovery (DIS)

### 6.5.1	Resource discovery

The Feature set is about CSE supporting resource discovery.

Table 6.5.1-1: Features of CE/DIS/00001

| Feature ID | Feature Description | Category | Release |
| --- | --- | --- | --- |
| CE/DIS/00001/00001 | Support the Discovery request with filterUsage equals to “Discovery” | M | 1,2 |
| CE/DIS/00001/00002 | Support discovery with filterCriteria (createdBefore, createdAfter, modifiedSince, unmodifiedSince, stateTagSmaller, stateTagBigger, expireBefore, expireAfter, labels, resourceType, sizeAbove, sizeBelow, contentType, limit, attribute, filterOperation, level, offset) | O | 1,2 |
| CE/DIS/00001/00003 | Support discovery with content filter (contentFilterSyntax, contentFilterQuery of filterCriteria) | O | 2 |

The Feature set is about AE supporting Discovery Request.

Table 6.5.1-2: Features of AE/DIS/00001

| Feature ID | Feature Description | Category | Release |
| --- | --- | --- | --- |
| AE/DIS/00001/00001 | Support discovery of resources without filterCriteria | O | 1,2 |
| AE/DIS/00001/00002 | Support filter according to creation time (createdBefore, createdAfter) | O | 1,2 |
| AE/DIS/00001/00003 | Support filter according to modified time (modifiedSince, unmodifiedSinse) | O | 1,2 |
| AE/DIS/00001/00004 | Support filter according to state tag (stateTagSmaller, stateTagBigger) | O | 1,2 |
| AE/DIS/00001/00005 | Support filter according to expiration time (expireBefore, expireAfter) | O | 1,2 |
| AE/DIS/00001/00006 | Support filter according to labels (labels) | O | 1,2 |
| AE/DIS/00001/00007 | Support filter according to resource type (resourceType) | O | 1,2 |
| AE/DIS/00001/00008 | Support filter according to resource size (sizeAbove, sizeBelow) | O | 1,2 |
| AE/DIS/00001/00009 | Support filter according to contentType (contentType) | O | 1,2 |
| AE/DIS/00001/00010 | Support limit the number of resources in the response (limit) | O | 1,2 |
| AE/DIS/00001/00011 | Support filter according to attributes (attribute) | O | 1,2 |
| AE/DIS/00001/00012 | Support the logical operation between multiple criterias (filterOperation) | O | 1,2 |
| AE/DIS/00001/00013 | Support limit the level of the discovery (level) | O | 1,2 |
| AE/DIS/00001/00014 | Support indicating the offset when returning the discovered results (offset) | O | 1,2 |
| AE/DIS/00001/00015 | Support content based discovery (contentFilterSyntax, contentFilterQuery) | O | 2 |

## 6.6	Group Management (GMG)

## 6.6.1	Configuration of group

The Feature Set is about CSE supporting configuration of group.

Table 6.6.1-1: Feature Set CE/GMG/00001

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/GMG/00001/00001 | Support the <group> resource with attributes multiplicity equals 1[1] | M | 1,2 |
| CE/GMG/00001/00002 | Support the labels attribute of <group> resource | O | 1,2 |
| CE/GMG/00001/00003 | Support the creator attribute of <group> resource | O | 1,2 |
| CE/GMG/00001/00004 | Support the groupName attribute of <group> resource | O | 1,2 |

## The Feature Set is about CSE supporting configuration of group with memberType other than MIXED.

Table 6.6.1-2: Feature Set CE/GMG/00002

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/GMG/00002/00001 | Support the memberTypeValidated attribute of <group> resource | M | 1,2 |
| CE/GMG/00002/00002 | Support the validation of member’s resource type and set the memberTypeValidated as well as the procedure to update the group according to consistencyStrategy | M | 1,2 |
| CE/GMG/00002/00003 | Support the consistencyStrategy attribute of <group> resource | M | 1,2 |

Editor’s Note: semanticSupportIndicator attribute of <group> resource will be listed in semantics related feature set

The Feature Set is about AE supporting configuration of group.

Table 6.6.1-3: Feature Set AE/GMG/00001

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/GMG/00001/00001 | Create <group> resource with mandatory attributes[2] | O | 1,2 |
| AE/GMG/00001/00002 | Create <group> resource with resourceName | O | 1,2 |
| AE/GMG/00001/00003 | Create <group> resource with expirationTime | O | 1,2 |
| AE/GMG/00001/00004 | Create <group> resource with labels | O | 1,2 |
| AE/GMG/00001/00005 | Create <group> resource with creator | O | 1,2 |
| AE/GMG/00001/00006 | Create <group> resource with memberType | O | 1,2 |
| AE/GMG/00001/00007 | Create <group> resource with membersAccessControlPolicyIDs | O | 1,2 |
| AE/GMG/00001/00008 | Create <group> resource with consistencyStrategy | O | 1,2 |
| AE/GMG/00001/00009 | Create <group> resource with groupName | O | 1,2 |
| AE/GMG/00001/00010 | Update <group> resource with expirationTime | O | 1,2 |
| AE/GMG/00001/00011 | Update <group> resource with labels | O | 1,2 |
| AE/GMG/00001/00012 | Update <group> resource with maxNrOfMembers | O | 1,2 |
| AE/GMG/00001/00013 | Update <group> resource with memberIDs | O | 1,2 |
| AE/GMG/00001/00014 | Update <group> resource with membersAccessControlPolicyIDs | O | 1,2 |
| AE/GMG/00001/00015 | Update <group> resource with groupName | O | 1,2 |
| AE/GMG/00001/00016 | Delete <group> resource | O | 1,2 |
| AE/GMG/00001/00017 | Retrieve <group> resource | O | 1,2 |

## 6.6.2	Fan out using group

The Feature Set is about CSE supporting fan out of requests through group.

Table 6.6.2-1: Feature Set CE/GMG/00003

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/GMG/00003/00001 | Fan out of request to all members and aggregate member responses | M | 1,2 |
|  | Support the membersAccessControlPolicyIDs attribute of <group> resource | O | 1,2 |
| CE/GMG/00003/00002 | Create sub group resource in case multiple members belong to same member CSE | O | 1,2 |
| CE/GMG/00003/00003 | Subscribe via group without aggregating notifications | O | 1,2 |
| CE/GMG/00003/00004 | Subscribe via group and aggregate notifications | O | 1,2 |

Feature Set AE/GMG/00002 is about AE supporting fan out of requests through group.

Table 6.6.2-2: Feature Set AE/GMG/00002

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/GMG/00002/00001 | Request by addressing fanOutPoint of group resource | O | 1,2 |
| AE/GMG/00002/00002 | Subscribe via group without aggregating notifications | O | 1,2 |
| AE/GMG/00002/00003 | Subscribe via group and aggregate notifications | O | 1,2 |

## 6.7	Subscription (SUB)

### 6.7.1	Configuration of subscription for data Notification

The Feature Set is about CSE supporting configuration of subscription.

Table 6.7.1-1: Features of CE/SUB/00001

| Feature ID | Feature Description | Category | Release |
| --- | --- | --- | --- |
| CE/SUB/00001/00001 | The Support of <subscription> resource with attributes multiplicity equals 1[1] | M | 1,2 |
| CE/SUB/00001/00002 | Support the labels attribute of <subscription> resource. | O | 1,2 |
| CE/SUB/00001/00004 | Support the creator attribute of <subscription> resource | O | 1,2 |
| CE/SUB/00001/00014 | Support the subscriberURI attribute of <subscription> resource | O | 1,2 |

The Feature Set is about CSE supporting configuration of policies related to notification.

Table 6.7.1-2: Features of CE/SUB/00002

| Feature ID | Feature Description | Category | Release |
| --- | --- | --- | --- |
| CE/SUB/00001/00003 | Support the eventNotificationCriteria attribute of <subscription> resource | O | 1,2 |
| CE/SUB/00002/00001 | Support the expirationCounter attribute of <subscription> resource | O | 1,2 |
| CE/SUB/00002/00002 | Support the batchNotify attribute of <subscription> resource | O | 1,2 |
| CE/SUB/00002/00003 | Support the rateLimit attribute of <subscription> resource | O | 1,2 |
| CE/SUB/00002/00004 | Support the preSubscriptionNotify attribute of <subscription> resource | O | 1,2 |
| CE/SUB/00002/00005 | Support the pendingNotification attribute of <subscription> resource | O | 1,2 |
| CE/SUB/00002/00006 | Support the notificationStoragePriority attribute of <subscription> resource | O | 1,2 |
| CE/SUB/00002/00007 | Support the latestNotify attribute of <subscription> resource | O | 1,2 |
| CE/SUB/00002/00008 | Support the notificationContentType attribute of <subscription> resource | O | 1,2 |
| CE/SUB/00002/00009 | Support the notificationEventCat attribute of <subscription> resource | O | 1,2 |

The Feature Set is about CSE supporting configuration of subscription through group.

Table 6.7.1-3: Features of CE/SUB/00003

| Feature ID | Feature Description | Category | Release |
| --- | --- | --- | --- |
| CE/SUB/00003/00001 | Support the groupID attribute of <subscription> resource | M | 1,2 |
| CE/SUB/00003/00002 | Support the notificationForwardingURI attribute of <subscription> resource. | M | 1,2 |

The Feature Set is about AE supporting configuration of subscription.

Table 6.7.1-4: Features of AE/SUB/00001

| Feature ID | Feature Description | Category | Release |
| --- | --- | --- | --- |
| AE/SUB/00001/00001 | Create <subscription> with mandatory attribute | M | 1,2 |
| AE/SUB/00001/00002 | Create <subscription> with labels attribute | O | 1,2 |
| AE/SUB/00001/00003 | Create <subscription> with expirationTime attribute | O | 1,2 |
| AE/SUB/00001/00004 | Create <subscription> with creator attribute | O | 1,2 |
| AE/SUB/00001/00005 | Create <subscription> with subscriberURI attribute | O | 1,2 |
| AE/SUB/00001/00006 | Update <subscription> with labels attribute | O | 1,2 |
| AE/SUB/00001/00007 | Update <subscription> with expirationTime attribute | O | 1,2 |
| AE/SUB/00001/00008 | Update <subscription> with creator attribute | O | 1,2 |
| AE/SUB/00001/00009 | Delete <Subscription> | O | 1,2 |
| AE/SUB/00001/00010 | Retrieve <Subscription> | O | 1,2 |

The Feature Set is about AE supporting configuration of policies related to subscription.

Table 6.7.1-5: Features of AE/SUB/00002

| Feature ID | Feature Description | Category | Release |
| --- | --- | --- | --- |
| AE/SUB/00002/00001 | Create <subscription> with eventNotificationCriteria attribute | O | 1,2 |
| AE/SUB/00002/00002 | Create <subscription> with expirationCounter attribute | O | 1,2 |
| AE/SUB/00002/00003 | Create <subscription> with batchNotify attribute | O | 1,2 |
| AE/SUB/00002/00004 | Create <subscription> with rateLimit attribute | O | 1,2 |
| AE/SUB/00002/00005 | Create <subscription> with preSubscriptionNotify attribute | O | 1,2 |
| AE/SUB/00002/00006 | Create <subscription> with pendingNotification attribute | O | 1,2 |
| AE/SUB/00002/00007 | Create <subscription> with notificationStoragePriority attribute | O | 1,2 |
| AE/SUB/00002/00008 | Create <subscription> with latestNotify attribute | O | 1,2 |
| AE/SUB/00002/00009 | Create <subscription> with notificationContentType attribute | O | 1,2 |
| AE/SUB/00002/00010 | Create <subscription> with notificationEventCat attribute | O | 1,2 |
| AE/SUB/00002/00011 | Update <subscription> with eventNotificationCriteria attribute | O | 1,2 |
| AE/SUB/00002/00012 | Update <subscription> with expirationCounter attribute | O | 1,2 |
| AE/SUB/00002/00013 | Update <subscription> with batchNotify attribute | O | 1,2 |
| AE/SUB/00002/00014 | Update <subscription> with rateLimit attribute | O | 1,2 |
| AE/SUB/00002/00015 | Update <subscription> with pendingNotification attribute | O | 1,2 |
| AE/SUB/00002/00016 | Update <subscription> with notificationStoragePriority attribute | O | 1,2 |
| AE/SUB/00002/00017 | Update <subscription> with latestNotify attribute | O | 1,2 |
| AE/SUB/00002/00018 | Update <subscription> with notificationContentType attribute | O | 1,2 |
| AE/SUB/00002/00019 | Update <subscription> with notificationEventCat attribute | O | 1,2 |

The Feature Set is about AE supporting configuration of subscription through group.

Table 6.7.1-6: Features of AE/SUB/00003

| Feature ID | Feature Description | Category | Release |
| --- | --- | --- | --- |
| AE/SUB/00001/00001 | Create <subscription> with notificationForwardingURI attribute | M | 1,2 |

### 6.7.2	Trigger notification pertaining to subscription

The Feature Set is about CSE supporting trigger notification pertaining to subscription.

Table 6.7.2-1: Features of CE/SUB/00004

| Feature ID | Feature Description | Category | Release |
| --- | --- | --- | --- |
| CE/SUB/00004/00001 | Notify the address indicated in notificationURI with notification elements multiplicity equals 1[2] | M | 1,2 |
| CE/SUB/00004/00002 | Notify with notificationEvent/representation | O | 1,2 |
| CE/SUB/00004/00003 | Notify with creator | O | 1,2, |

The Feature Set is about CSE supporting aggregation of notification pertaining to subscription configured through group.

Table 6.7.2-2: Features of CE/SUB/00005

| Feature ID | Feature Description | Category | Release |
| --- | --- | --- | --- |
| CE/SUB/00004/00001 | The aggregation of notification and notify the address indicated in notificationForwardingURI | M | 1,2 |

## 6.8	Security (SEC)

## 6.8.1	Configuration of access control policy

The Feature Set is about CSE supporting configuration of access control policy.

Table 6.8.1-1: Features of CE/SEC/00001

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/SEC/00001/00001 | Support <accessControlPolicy> resource with attributes multiplicity equals 1[1] | M | 1,2 |
| CE/SEC/00001/00002 | Support the labels attribute of <accessControlPolicy> resource | O | 1,2 |

The Feature Set is about AE supporting configuration of access control policy.

Table 6.8.1-2: Features of AE/SUB/00001

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| AE/SEC/00001/00001 | Create <accessControlPolicy> resource with mandatory attributes[2] | O | 1,2 |
| AE/SEC/00001/00002 | Create <accessControlPolicy> resource with resourceName | O | 1,2 |
| AE/SEC/00001/00003 | Create <accessControlPolicy> resource with expirationTime | O | 1,2 |
| AE/SEC/00001/00004 | Create <accessControlPolicy> resource with labels | O | 1,2 |
| AE/SEC/00001/00005 | Update <accessControlPolicy> resource with expirationTime | O | 1,2 |
| AE/SEC/00001/00006 | Update <accessControlPolicy> resource with labels | O | 1,2 |
| AE/SEC/00001/00007 | Update <accessControlPolicy> resource with privileges | O | 1,2 |
| AE/SEC/00001/00008 | Update <accessControlPolicy> resource with selfPrivileges | O | 1,2 |
| AE/SEC/00001/00009 | Delete <accessControlPolicy> resource | O | 1,2 |
| AE/SEC/00001/00010 | Retrieve <accessControlPolicy> resource | O | 1,2 |

The Feature Set is about CSE supporting access control to the addressed resources.

Table 6.8.1-3: Features of CE/SEC/00002

| Feature ID | Feature Description | Optionality | Release |
| --- | --- | --- | --- |
| CE/SEC/00002/00001 | Support accessControlPolicyIDs attribute for <resource> that the Implementation supports. | M | 1,2 |
| CE/SEC/00002/00002 | Support Access Control Decision making on the Hosting CSE | M | 1,2 |

### -----------------------End of change 3-------------------------------------------

# Comments

AE shall support one of the two: structured or unstructured. relativeness is not an option. when it wants to manipulate over Mcc, then it shall support SP-relative or absolute.

so suggestions are: separate CSE and AE for this feature set. and simplify 6 into two for AE (structured/unstructured). CSE is okay

I’d suggest to have one feature set for each param.

if an AE is registree he already knows this, if not, he shall know then it can send the retrieval using the ID. so it is already given to the app.

Delete ID and type of CSE

this is too kind wording =) we don’t do other hundreds of features. and it

simplify this to even with the other paragraphs

this should not be feature set as stand-alone. this is one of the feature of whole AE registration with other cases.

CSE relative one also can be SP relative. so this is tricky. suggest to merge 2-3, 2-4 to 2-1.

this is for “CE/GMG/00003”, only for fan-out

convention: lower case for the first letter

same comment

this “mandatory” is TS-0004, request mandatory for sure. let’s not confuse readers

there’s no mandatory elements, but different elements per subscription setting

notification receiver’s roll is to answer the question for verification, for example. these two are not valid.

NotificationForwardingURI和GroupID都放在一个单独的featureset中，专门关于通过群组进行订阅

AE行为的这个表按照TS-0004里面操作针对属性的MO来写

使用一般的通知流程即可，增加关于eventNotificationCriteria中的条件判断。notificationForwarding和GroupID都是用于通过群组订阅的，放在一个单独的feature set中。