| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC 27.1 |
| Source:* | Catalina Mladin, Convida, Mladin.Catalina@convidawireless.com Michael Starsinic, Convida, Starsinic.Michael@convidawireless.com |
| Date:* | 2017-02-23 |
| Reason for Change/s:* | Moves 3GPP-related text from TS-0001 to TS-0026 |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0058 MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0026 V0.1.1 |
| Clauses * | Clauses 6-8 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | TS-0001 Annex B |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This document makes proposals on how to map TS-0001 text pertaining to 3GPP interworking to TS-0026.

The table below shows the proposed text mapping for the TS-0001 3GPP-related annexes. The text move affects the existing TS-0026 section 6 (Interworking with CIoT network features exposed at the service layer), and it is proposed to add a new section focusing on connectivity establishment.

The main goal is to make sure that there is no loss of content. Text shows as “existing” to reflect existing content in TS-0001 and to easily identify content changes, see comments for clarifications. Where merges are needed they were provided with different change markings for ease of reading.

This document is meant to be used first for discussion, although it is structured (approximately) as a CR. Once there is a group decision the next version of this document can become the TR-0026 CR, with all text moved from TS-0001 shown as new.  A corresponding TS-0001 CR with the corresponding deletions will be provided.

| TS-0001 Section | TS-0001 Section Title | TS-0026 Section | TS-0026 Section Title | Comments |
| --- | --- | --- | --- | --- |
| B | oneM2M System and 3GPP MTC Underlying Network Interworking | N/A | N/A | No content |
| B.1 | 3GPP MTC Underlying Network Introduction | N/A (5) | oneM2M Architecture for 3GPP cellular IoT interworking with oneM2M | Proposed to be removed, content covered by TS-0026 clause 5 Alternatively, a merge with TS-0026 clause 5.1 may be considered |
| B.2 | 3GPP MTC Functionality | N/A | N/A | No content |
| B.2.1 | 3GPP Release-11 MTC Functionality | N/A (5) | oneM2M Architecture for 3GPP cellular IoT interworking with oneM2M | Proposed to be removed. Rel-13 content is covered in TS-0026 clause 5. Alternatively, figure B.2.1-2 and referring text to be merged to TR-0024 clause 5.3 |
| B.2.2 | 3GPP Release-13 MTC Interworking | N/A | N/A | No content |
| B.2.2.1 | General overview of 3GPP Release-13 MTC Interworking | N/A (5.3) | Cellular IoT Features and Services | Propose to delete B.2.2.1. Content is covered by TS-0026 sec 5.3 (except figure B2.2.1-1) |
| B.2.2.2 | 3GPP Release-13 MTC feature for Configuration of Device Communication Patterns | 7.6 (former 6.6) | 3GPP Release-13 MTC Procedure | Propose to include in TS-0026 Traffic Pattern section: former 6.6 (now 7.6) |
| B.3 | ASN/MN-CSE initiated connectivity establishment | New 6 | Connectivity Establishment | New title | Proposing a new section 6 in TS-0026 called “Connectivity Establishment”, as detailed in the body of this document Includes B3-B6 |
| B.3.0 | Overview | New 6.1 | Overview | Merge B3.0, B4 and B5 text into 7.1 |  |
| B.3.1 | Use of DHCP and DNS | New 6.2 | Use of DHCP and DNS | Maintain as 7.2 |  |
| B.3.2 | Pre-configuration | New 6.3 | Pre-configuration | Maintain as 7.3 |  |
| B.4 | Serving IN-CSE initiated connectivity establishment | New 6.1 | Overview | Merge B3.0, B4 and B5 text into 7.1 |  |
| B.5 | Connectivity between oneM2M Service Layer and 3GPP Underlying Network | New 6.1 | Overview | Merge B3.0, B4 and B5 text into 7.1 |  |
| B.6 | Connectivity Establishment Procedures | N/A | N/A | No content |  |
| B.6.1 | General | N/A | N/A | No content |  |
| B.6.1.0 | Overview | N/A | N/A | Propose to delete, only intro to B 6.1.1 and B 6.1.2 |  |
| B.6.1.1 | ASN/MN-CSE Initiated Connectivity Establishment Procedure | New 6.4 | ASN/MN-CSE Initiated Connectivity Establishment Procedure | Maintain as 7.4 |  |
| B.6.1.2 | IN-CSE initiated connectivity establishment procedure over Tsp | New 6.5 and 7.5 | SMS Based Device Triggering | Maintain heading as 6.5. and move to the Device triggering section 7.5 |  |

### -----------------------Start of Change 1 -------------------------------------------

# 6 Connectivity Establishment

## 6.1 Overview

ASN/MN-CSE and the serving IN-CSE communicate after completion of the Underlying Network bearer establishment and discovery of the serving IN-CSE. Data can then traverse between CSEs over the IP connection in the Underling Network over 3GPP Gi/SGi interface. In addition, the signalling connectivity between the two CSEs is also realized. Figure B.5-1 depicts the connectivity between the ASN/MN-CSE and the IN-CSE.

Figure 6.1-1: Connectivity Establishment between ASN/MN-CSE and IN-CSE

For ASN/MN initiated connectivity establishment, it is assumed that there is no connectivity previously established, i.e. no association between the ASN/MN-CSE or ADN-AE and the serving IN-CSE exists. When the ASN/MN-CSE or ADN-AE needs to send data to the serving IN-CSE it first discovers the serving IN-CSE, which is located in a packet data network, and establishes connection. Two methods can be used, as follows:

- Use of DHCP and DNS.

- Pre-configuration.

For serving IN-CSE initiated connectivity establishment, it is assumed that there is no connectivity previously established between the ASN/MN-CSE and the serving IN-CSE. When the serving IN-CSE needs to contact the ASN/MN-CSE to send data or request data, connectivity between them is established. This connectivity is triggered by the serving IN-CSE.

NOTE:	How the serving IN-CSE triggers a non-CSE capable M2M device (e.g. ADN) within the 3GPP Underlying Network is not specified in this release of the document.

## 6.2.	Use of DHCP and DNS

The ASN/MN-CSE or ADN-AE requests the DNS server address from the DHCP server followed by requesting the serving IN-CSE IP address from the DNS server.

## 6.3.	ASN/MN-CSE Pre-configuration

The ASN/MN-CSE or ADN-AE is preconfigured with the fully qualified domain name (FQDN) of the serving IN-CSE or the IP address of the serving IN-CSE. If the FQDN is known, DNS resolution is used to obtain the IP address.

### 6.4 ASN/MN-CSE or ADN-AE Initiated Connectivity Establishment Procedure

Figure 6.4-1: ASN/MN-CSE or ADN-AE initiated connectivity establishment

Step-0: Trigger

Subsequent procedures are triggered either when the ASN/MN-CSE or ADN-AE powers on or resulting from Device Triggering mentioned in clause B.6.1.2.

Step-1: Bearer Setup Procedure

Establish a 3GPP bearer(s) if not already available by using the procedures available in the 3GPP  network.

Step-2: DHCP Query & Response

The ASN/MN-CSE or ADN-AE sends a query to a DHCP server to find a particular DNS server IP address. The DHCP server responds with the IP address of a corresponding DNS server. Additionally, it is also possible to include one or a list of domain names, i.e. FQDNs of target IN-CSEs.

Step-3: DNS Query & Response

The ASN/MN-CSE or ADN-AE performs a DNS query to retrieve the IN-CSE(s) IP addresses from which one is selected. If the response does not contain the IP addresses, an additional DNS query is needed to resolve a Fully Qualified Domain Name (FQDN) of the serving IN-CSE to an IP address.

Step-4: Connection Establishment

After reception of domain name and IP address of an IN-CSE, the ASN/MN-CSE or ADN-AE can initiate communication towards the IN-CSE via the IP connection. The IN-CSE at this time shall be informed which Trigger Recipient ID of the ASN/MN-CSE or ADN-AE or the AE-PoA of the ADN-AE to use for establishing communication.

Step-5: CSE-PoA Update

Once the M2M Service Connection (Mcc) is established, in the IN-CSE the CSE-PoA of the ASN-CSE/MN-CSE or the AE-PoA of the ADN-AE shall be updated with the new established IP address.

The IN-CSE holds the state information and needs to be informed when the connection is closed.

### 6.5 IN-CSE initiated connectivity establishment procedure over Tsp

See clause 7.5. SMS Based Device Triggering.

# 7	Interworking with CIoT network features exposed to service layer

Editor’s Note: the signalling flows and resources specified in the following clauses should focus on the Mca and Mcn interfaces: CIoT features synergy with oneM2M service layer. At the time when this skeleton is drafted, the subclauses of clause 6 intend to capture all the 3GPP service capabilities exposure function categories. Once the subset of functions is fixed in subclause 5.3, some 3GPP service capabilities exposure functions may be removed in this TS.

## 7.1	Cellular IoT IP and non-IP data delivery

## 7.2	UE context information storage

## 7.3	High latency communications

## 7.4	Monitoring events

## 7.5	Device triggering

## 7.6	Configuration of Traffic Patterns

oneM2M uses the 3GPP Release-13 MTC feature for Configuration of Device Communication Patterns to configure Node Traffic Patterns in the Underlying Network (see section 8.3.5 Configuration of Node Traffic Patterns). 
To that purpose the IN-CSE translates the oneM2M Node Traffic Pattern (TP) into a 3GPP Device Communication Pattern.

A signalling sequence for provisioning of CP parameters is described in the sub-clause 5.10.2 of 3GPP TS 23.682 [i.14]. Following figure 7.6-1 provides the signalling sequence derived from the 3GPP specification. Figure B.2.2.2-2 illustrates the terminology mapping between 3GPP and oneM2M, where the SCS is mapped to IN-CSE and the SCEF is mapped to NSE. In case the SCS is 3GPP network operator controlled, the SCEF can be deployed co-located with the SCS.

Figure 7.6-1: Signalling sequence for provisioning of CP Parameters

Figure B.7.6 -2: 3GPP and oneM2M mapping

3GPP TS 23.682 [i.14] defines the request message of step 1 as below:

- The SCS/AS sends an Update Request (External Identifier or MSISDN, SCS/AS Identifier, SCS/AS Reference ID(s), CP parameter set(s), validity time(s), SCS/AS Reference ID(s) for Deletion) message to the SCEF.

NOTE 1:	The SCS/AS uses this procedure to add, change or delete some or all of the CP parameter sets of the UE, e.g. if the AS is aware that the UE has started or stopped moving for a significant time period, especially if the AS is instructing the UE to do so, then the SCS/AS provides the corresponding CP parameter set(s) and its validity time to the SCEF. The interface between SCEF and SCS/AS is outside the scope of 3GPP and the messages in the Figure are exemplary.

3GPP TS 23.682 [i.14] defines the request message of step 3 as below:

- The SCEF sends Update CP Parameter Request (External Identifier or MSISDN, SCEF Reference ID(s), SCEF Address, CP parameter set(s), validity time(s), SCEF Reference ID(s) for Deletion) messages to the HSS for delivering the selected CP parameter set(s) per UE. There may be multiple CP parameter sets included in this message where each CP parameter set for addition or modification has been determined to be non-overlapping with other CP parameter sets either included in the message or already provisioned for a given UE. The SCEF derives the SCEF Reference (IDs) for CP parameter sets to be sent to the HSS based on the SCS/AS Reference ID(s) from the SCS/AS.

NOTE 2:	A request for deletion of a CP parameter set from the SCS/AS may result in a request for modification of the non-overlapping CP parameter set by the SCEF.

EXAMPLE 1:	In the case that the selected server NSE is a 3GPP HSS, the protocol of the S6t reference point defined by 3GPP is used for the request. The S6t uses one of Diameter Application protocols defined by 3GPP. The request on the S6t reference point for the configuration of the CP parameter sets (a CIR command) must include a User-Identifier AVP (either an External Identifeir or a MSISDN of the UE), may include one or more AESE-Communication-Pattern AVP. An AESE-Communication-Pattern AVP must include a SCEF-ID AVP (represent the ID of the IN-CSE or M2M-SP-ID), may include a SCEF-Reference-ID AVP (assigned by the IN-CSE or M2M-SP to identify the configuration of CP parameter sets uniquely) , may include one or more Communication-Pattern-Set AVP. A Communication-Pattern-Set AVP may include AVPs for Periodic-Communication-Indicator, Communication-Duration-Time, Periodic-Time, one or more Scheduled-Communication-Time, Stationary-Indication, and Validity-Time. Refer to the 3GPP TS 29.336 [i.31] for the detailed protocol description.

3GPP TS 23.682 [i.14] defines the response message of step 5 as below:

- The HSS sends Update CP Parameter Response (SCEF Reference ID, Cause) message to the SCEF. The cause value indicates successful subscription update or the reason of failed subscription update.

- The actual parameters for the request and response messages in above steps 3 and 5 are defined by 3GPP TS 29.336 [i.31], clauses 7 and 8 for S6t reference point.

EXAMPLE 2:	In the case that the selected server NSE is a 3GPP HSS, the protocol of the S6t reference point defined by 3GPP is used for the response. The response on the S6t reference point for the configuration of the CP parameter sets (a CIA command) must include either Result-Code AVP or Experimental-Result AVP, may include a User-Identifier AVP if successful case, may include one or more AESE-Communication-Pattern-Config-Status AVP. An AESE-Communication-Pattern-Config-Status AVP must include the SCEF-Reference-ID AVP (same value in the request), may include the SCEF-ID (same value in the request) and an AESE-Error-Report AVP. Refer to the 3GPP TS29.336 for the detailed protocol description.

3GPP TS 23.682 [i.14] defines the response message of step 6 as below:

- The SCEF sends the Update Response (SCS/AS Reference ID, Cause) message to inform the SCS/AS whether the provision of the CP parameter set(s) was successful.

## 7.7	Group message delivery

## 7.8	Informing about Potential Network Issues

## 7.9	Setting up an AS session with required QoS procedure

## 7.10	Resource management of background data transfer

## 7.11	Change the chargeable party at session set-up or during the session procedure

### -----------------------End of Change 1 ---------------------------------------------

### -----------------------Start of Change 2 -------------------------------------------

## 7.5	SMS Based Device triggering

Connection Establishment between IN-CSE and ASN/MN-CSE or ADN-AE

Whenever the IN-CSE requires to establish a connection towards another entity (e.g. ASN/MN-CSE or ADN-AE, ADN-AE), Device Triggering procedure over the Tsp interface as described in 3GPP TS 23.682 [i.14] shall be used.

This procedure assumes the ASN/MN-CSE or ADN-AE is directly connected to 3GPP access network.

Figure 7.5.1-1: IN-CSE initiated connectivity establishment

Pre-condition

The IN-CSE checks the state information of the target device. Some of this state information is the result of provisioning or a previous connection establishment or triggering requests, such as the case of power-off, dormant and/or connected state. The IN-CSE decides its next action, e.g. if it needs to start device triggering or to report to IN-AE about the inability to perform the request.

The CSE-PoA for the ASN/MN-CSE or AE-PoA of the ADN-AE either already contains an IP address which is not valid anymore or no IP address at all, or FQDN does not resolve to a valid IP address. This is a pre-requisite for performing the device triggering procedure.

Step 1 (Optional): Request targeted to ASN/MN-CSE or ADN-AE

The IN-AE requests to perform one of the CRUD operation on a resource residing on the ASN/MN-CSE or ADN-AE, the request is sent via the Mca reference point to the IN-CSE. The request from IN-AE includes the address of the target resource.

Step 2: DNS Query/Response

The IN-CSE determines the need to trigger the ASN/MN-CSE or ADN-AE.

If the IN-CSE has no contact details for a contact MTC-IWF, it may determine the IP address(es)/port(s) of the MTC-IWF by performing a DNS query using the M2M-Ext-ID (M2M External Identifier) assigned to the target ASN/MN-CSE or ADN-AE, or using a locally configured MTC-IWF identifier.

Step-3: Device Triggering Request

The IN-CSE buffers the original request information and sends the Device Trigger Request message that contains information as specified in 3GPP TS 23.682 [i.14]. Such information includes:

- M2M-Ext-ID or MSISDN;

- SCS-Identifier, (is set to the IN-CSE ID);

- Trigger reference number (used to correlate the request with the response);

- Validity period, (which indicates how long the request is valid);

- Priority (this field allows to set the priority on or off);

- Application Port ID, (is set to the ASN/MN-CSE or ADN-AE Trigger-Recipient-ID since it is the triggering application addressed in the device from 3GPP point of view);

- Trigger payload, (optional information can be set to the payload).

NOTE 1:	In case that the Device Triggering request is for an M2M Service Connection setup request as in the present flow, it is assumed that when the target (i.e. ASN/MN-CSE or or ADN-AE) is woken up on receiving the trigger it initiates connection establishment with the IN-CSE with which it is registered. The information of the IN-CSE may be pre-stored in the target (i.e. ASN/MN-CSE or ADN-AE) or obtained from the payload.

Acknowledge

Once, 3GPP-MTC-IWF receives the Trigger Request, it asks the HSS to determine if the IN-CSE is authorized to perform the triggering to the target (i.e. ASN/MN-CSE or ADN-AE) and the HSS resolves the M2M-Ext-ID to IMSI (or MSISDN). Then the 3GPP MTC-IWF acknowledges to the IN-CSE with the confirmation of receiving Device Triggering Request.

Step-4: Device Triggering delivery procedure

The MTC-IWF initiates the T4 trigger delivery procedure according to the 3GPP TS 23.682 [i.14], based on the information received from HSS and local policy.

NOTE 2:	3GPP Network Entities (e.g. SMS-SC) can select appropriate device triggering mechanism (e.g. SMS based or SIP based via IP-SM-GW) according to the device capabilities.

Step 5: ASN/MN-CSE receives the trigger

As a result of the triggering procedure, the payload is delivered to the ASN/MN-CSE or ADN-AE trigger recipient.

NOTE 3:	In case the Device Trigger contains the optional part of the trigger payload, it is assumed that such trigger payload is forwarded to the application inside the ASN/MN-CSE or ADN-AE that is started as a result of device trigger.

Step 6: Device Triggering report

Request:

The MTC-IWF sends the Device Trigger Report message (containing the M2M-Ext-ID or MSISDN and trigger reference number) to the IN-CSE with a cause value indicating whether the trigger delivery succeeded or failed and the reason for the failure.

Acknowledge:

IN-CSE acknowledges to the MTC-IWF with the conformation of the received Device Triggering Report.

Step 7 (Optional): Connection establishment procedure

The ASN/MN-CSE or ADN-AE performs the Connection establishment procedure as described in clause 6.4 and oneM2M TS-0003 [2] for Secure Connection establishment.

As a result of this procedure the initial request over the reference point Mcc can be executed.

Step 8 (Optional): CSE-PoA/Reachability state updated

Once the connection over Mcc is established, the PoA of the ASN/MN-CSE or ADN-AE shall be updated at the IN-CSE with the new established IP address and the IN-CSE holds the reachability state of the ASN/MN-CSE or ADN-AE.

Step 9 (Optional): Re-sending of original request

As a result of step 7, the communication is established and now the initial request with the information stored in the buffer of the IN-CSE at Step 3 can be re-issued over the reference point Mcc.

### -----------------------End of Change 2 ---------------------------------------------

### -----------------------Start of Change 3 -------------------------------------------

## 8	Cellular IoT device management

## 8.1	sub-function of device management (e.g. Device Configuration)

### -----------------------End of Change 3 ---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause?

# Comments

Annex B.1 Proposed to be removed, since it is covered by TS-0026 clause 5.

Annex B.2 no content

Annex B2.1 Proposed to be removed since it is covered by TS-0026 clause 5.

Alternatively, figure B.2.1-2 and reffering text MAY be merged to TR-0024 clause 5.3

Annex B2.2 no content

Annex B.2.2.1. Propose to be deleted. Content is covered by TS-0026 sec 5.3 (except figure B2.2.1-1, however figure 5.2-1 was created to reflect it)

Annex B 2.2.2 Propose to be removed, since content is covered by TR-0024 clause 8.3.2

Annex B5 content merged here

Annex B 3.0 content stays

Annex B4 content merged here

This is no longer applicable

Should 6.2 and 6.3 be applied only to the ASM/MN-CSE or AND-AE initiated connectivity?

Annex B.4 Moved to 6.1 Overview

Annex B.5 Moved to 6.1 Overview

Annex B 6.1.0 Propose to be deleted, just intro to B6.1.1 and B6.1.2

Annex B 6.1.1

Annex B.6.1.2

Re-numbering of following clauses in TS-0026

Annex B2.2.2

Based on latest developments in 3GPP, this should be deleted.

Annex B.6.1.2.

# Text boxes

Application

Server

Application

Server

Application

Server

Operator

Network

Operator Network

UE

UE

UE

SCS

SCS

Operator

Boundary

A

.

Direct Model

B

.

Indirect Model

(MTC Service Provider

Controlled)

C

.

Indirect Model

(Mobile Network Operator

Controlled)

Operator

Network

Control plane

User plane

IN

-

CSE

IN

-

CSE

AE

AE

ASN/MN-CSE  or ADN-AE

ASN/MN-CSE  or ADN-AE