| Input Contribution |
| --- |
| Meeting ID* | ARC#28 |
| Title:* | TR-0028 OSGi Interworking |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd., Yinjiaxin@huawei.com |
| Date:* | 2017-03-19 |
| Input related to* | TR-0028 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TR-0028v0.0.1 |
| Decision requested or recommendation:* | Incorporated the texts to the TR. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

**************************start of change 1***************************************

## 2.2	Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules (http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf)

[i.2]	OSGi Residential (https://www.osgi.org/developer/downloads/release-6/)

[i.3]	OSGi Core (https://www.osgi.org/developer/downloads/release-6/)

**************************end of change 1***************************************

**************************start of change 2***************************************

# 8	oneM2M-OSGi Interworking

## 8.1	Requirement description

## OSGi Alliance defines services and interfaces for devices and functions provided by the devices[i.2]. Applications could utilize these services and interfaces to manipulate the device or read data from the device. End to end use cases and solutions can be produced in this way. The main purpose of oneM2M-OSGi Interworking is to enable the mutual service discovery and exposure of both standards. Which is to say, services and interfaces defined by OSGi can be mapped to oneM2M defined resources, and mutually, oneM2M defined resources can be mapped to OSGi defined services and interfaces. In this way, any OSGi compliant devices can be connected seamlessly to oneM2M system and viewed as a typical oneM2M entity by oneM2M defined CSEs and AEs. And vice versa, oneM2M compliant entities can be connected with OSGi devices as well. From the perspective of OSGi devices, oneM2M Entities are exposing OSGi defined services and interfaces.

## Figure 8.1-1: oneM2M-OSGi Interworking requirement

## 8.2	Potential solution and focus of oneM2M

## 8.2.1	General architecture

In order to achieve the requirements, an oneM2M-OSGi Interworking Bundle need to be defined. The service is in charge of all the mapping and translation of OSGi service and oneM2M resource.

The oneM2M-OSGi Interworking Bundle is running on the same OSGi Framework with the other OSGi services as well as the CSE Bundle that is implemented following the oneM2M specification.

From the OSGi perspective, the oneM2M-OSGi Interworking Bundle is defined as a Service with interfaces translated from oneM2M resource structures.

From the oneM2M perspective, the oneM2M-OSGi Interworking Bundle is defined with the purpose of mutual translation of OSGi services and oneM2M resource. The oneM2M-OSGi Interworking Bundle connects with a  Common Services Entity (CSE) to expose all OSGi services using oneM2M resources.

It’s well recognized that not all OSGi service and oneM2M resource may have one-to-one mapping. Some OSGi service may result in vancant oneM2M resources or procedures and vice versa. Some OSGi service may result in a combination of oneM2M resources and procedures and vise versa.The intention of the interworking to try to address to the best effort the largest common set of shared services.

Figure 8.2.1-1: oneM2M-OSGi Interworking architecture

8.2.2	Registration

The REG CSF of oneM2M is interworked with DAL (Device Abstraction Layer) in OSGi.

Editor’s Note: Detailes need to be further finalized.

8.2.3	Data Management and Repositary

The DMR CSF of oneM2M is interworked with DAL (Device Abstraction Layer) in OSGi.

Editor’s Note: Detailes need to be further finalized.

8.2.4	Subscription

The SUB CSF of oneM2M is interworked with DAL (Device Abstraction Layer) in OSGi.

Editor’s Note: Detailes need to be further finalized.

8.2.5	Device Management

The DMG CSF of oneM2M is interworked with Dmt Admin Service in OSGi.

Editor’s Note: Detailes need to be further finalized.

**************************end of change 2***************************************

# Text boxes

OSGi Device

oneM2M Entity