| Input Contribution |
| --- |
| Meeting ID* | ARC#28 |
| Title:* | IPE based Interworking |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd., Yinjiaxin@huawei.com |
| Date:* | 2017-03-20 |
| Input related to* | TS-0033 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TS-0033 |
| Decision requested or recommendation:* | Incorporate the texts if agreed. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## 6.2	Interworking through IPE

For devices that is not oneM2M compliant, an Interworking Proxy Entity (IPE) is defined for the purpose of connecting the device with oneM2M system. Interworking Proxy Entity is and AE that supports both oneM2M reference points as well as the protocol that the device support. IPE is in charge of the mapping and synchronization of services provided by the device and the resources defined by oneM2M.

Figure 6.2-1 Architecture of interworking through IPE

In this case, IPE could be deployed together with Device or oneM2M CSE or deployed separately. IPE understands the services provided by the Device and creates corresponding resources in oneM2M CSE. IPE at the same monitors the resources in oneM2M CSE and perform controlling to Device by invoke the service provided by Device.