| Input Contribution |
| --- |
| Meeting ID* | ARC#28 |
| Title:* | TS-0033 direct interworking |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd., Yinjiaxin@huawei.com |
| Date:* | 2017-03-20 |
| Input related to* | TS-0033 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TS-0033 v0.0.1 |
| Decision requested or recommendation:* | Incorporate the document if agreed. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## 6.3	Direct interworking

Other than the interworking through IPE, in direct interworking, devices are directly exposing oneM2M resources that can be address via Mcc or Mca reference point. In these cases, a device has its own service. The service could be data reporting for sensor, controlling for actuators or configuration. Instead of delegate the service to another oneM2M entity by an application entity in the middle to synchronize the state between the device and the oneM2M entity, the device could directly expose oneM2M defined CRUD interfaces by implementing an interworking service additional to the already existing service.

Figure 6.3-1 Architecture of direct interworking

In this case, the oneM2M Interworking Service acts as a translator between original device service and resources of oneM2M. The original services will be mapped to oneM2M defined resources and hosted by the oneM2M Interworking Service. Outside oneM2M entites will directly address the interface exposed by the oneM2M Interworking Service to invoke the services. The oneM2M Interworking Service is communicating with other original service using techniques that is implementation specific and out of scope of the specification.