| Input Contribution |
| --- |
| Meeting ID* | ARC#29 |
| Title:* | TR-0044 Use cases analysis |
| Source:* | Yuan Tao, CNICG, taoyuan@cnicg.cn; Ye Tian, CNIC, tianye@cnic.cn; Bo Yuan, CNIC, yuanbo@cnic.cn; Yang Liu, CAICT, liuyang1@ritt.cn. |
| Date:* | 2017-05-22 |
| Input related to* | TR-0044 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TR-0044 v0.0.1 |
| Decision requested or recommendation:* | To agree on the new text in TR-0044. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 7	Use cases analysis

Heterogeneous identification service is a common technology and widely used in the various IoT industries, for example, supply chain management and logistics, product traceability, energy management and so on. The TR-0001 collects the use case “Intelligence agricultural product traceability” in the section 12.20. And another use case “Heterogeneous identification service” has been discussed and approved.

There are three requirements related to the heterogeneous identification service that are not yet implemented by the 	specification.

| Requirement ID | Description | Release |
| --- | --- | --- |
| OSR-111 See REQ-2017-0018R01 | The oneM2M system shall be able to support heterogeneous identification services, the recognition of external identification systems and converting an object identifier to a compatible identifier recognized by the oneM2M system. |  |
|  | The oneM2M system shall be able to support the traceability linking service which provides a mapping that relates a product identifier to product related traceability information. Traceability information consists of: Logs Information on ID service nodes, such as: servers that provide access to traceability information, and devices (sensors and gateways) that gather traceability information |  |
|  | The oneM2M system shall be able to enable applications to retrieve the traceability information related to product identifiers. |  |