| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC #29 |
| Source:* | Echo, Huawei, echo.xubei@huawei.com Sarah, Huawei, changhongna@huawei.com |
| Date:* | 2017-05-22 |
| Reason for Change/s:* | Provides resources and flows for solution for DDS based direct change of data between oneM2M entities |
| CR against: Release* | Release 3 |
| CR against: WI* | Active < WI-0047> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0027 V0_2_0 |
| Clauses * | 7.2 (new) |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This solution’s aim is that how to make full use of the distinct features of DDS in oneM2M system.

As we mentioned in TR 00027, The Data Distribution Service (DDS) is a middleware protocol for data-centric connectivity, providing many-to-many communication, extreme reliability, and a scalable architecture. DDS has many distinct features, such as, data centricity, rich QoS, dynamic discovery, and so on. Especially, its dynamic discovery mechanism enables the applications flexible and extensible. In the dynamic discovery mechanism, every device can multicast its topics to the global data space. Once the device receives the topics from the global data space, it will match the topics and decide whether to establish the publish-subscribe relationship with other devices. The establishment of publish-subscribe relationship only depends on the DDS not the application.

DDS is used by many industries developing mission and business-critical smart applications, for example, transportation, industrial automation, military, aerospace, and so on. It has a relatively mature ecosystem.

So full using of the distinct features of DDS in oneM2M network is meaningful for oneM2M system.

we propose one solution. The main purpose of the solution is realizing the dynamic discovery and subscription of resource by using DDS in the oneM2M system.

### -----------------------Start of change 1-------------------------------------------

## 7.2	Solution 1

### 7.2.1	Introduction

DDS provides a dynamic discovery service by which entities can discover and possibly keep track of the presence of remote entities. The establishment of communication entirely depends on the dynamic discovery mechanism, which lead to the unauthorized devices could access to the oneM2M network.

In order to better discovery the resources and manage the communication relationship between oneM2M parties, the DDS Repository function is introduced. The DDS Repository function can be considered as an optional common service function which can be contained inside the MN-CSE or/and IN-CSE. The DDS Repository function can discovery the resources which can be permitted to subscribe to for the subscriber and identify the communication list for the publishers (AEs and CSEs) according to the resource matching and other information (e.g. group information , semantic). The oneM2M parties can establish the pub-sub relationship with other entities which are listed in the communication list by using the dynamic discovery mechanism of DDS.

### 7.2.2	Protocol segment

Figure 7.2.2-1: Protocol segment

Figure 7.2.2-1 shows a protocol segment view. In this scenario, all oneM2M nodes (ADN, ASN, MN, IN) include one or more DDS middlewares. The DDS Repository function is contained inside MN-CSE and/or IN-CSE. The green rectangle represents the CSE that contains the DDS Repository function.

An oneM2M entity sends its topics which are defined by DDS middleware to the CSE which includes DDS Repository function. The blue dotted line represents the reporting path. The block solid line indicates the data exchange among oneM2M entities.

### 7.2.3	Procedure for resource discovery and communication management

#### 7.2.3.1	Introduction

The DDS middlewares are deployed in the oneM2M device. The protocol stack is shown in figure 6.2.1-1. The pub-sub relationship between oneM2M parties is determined by the DDS Repository function. After accessing to the oneM2M network, the oneM2M parties need to send the topics which are defined by DDS middleware to the CSEs which contain the DDS Repository function through oneM2M network. It is worth noting that registration has been completed before the entity sends topics to the CSEs (e.g. IN-CSE). Once receiving the topics of parties, the IN-CSE matches the topics and then creates the communicable address list for the parties.

#### 7.2.3.2	Procedure

Figure 7.2.3.2-1: General Procedure for Resource Discovery and Communication Management

Step-1: Initiating creation of the <topicDirectory> resource

The topics defined by the DDS middleware can be considered a specialization of <topicDirectory> resource. The topicDirectory resource includes a sub-resource <topicList> and is used to represent the information that can be published or subscribed. The structure of <topicDirectory> resource and the sub-resource <topicList> are depicted respectively in figure 7.2.3.2-1 and figure 7.2.3.2-2.

Figure 7.2.3.2-2: Structure of <topicDirectory> resource

Figure 7.2.3.2-3: Structure of <topicList> resource

The <topicDirectory> resource shall contain the child resource specified in table 7.2.3.2-1.

Table 7.2.3.2-1: Child resource of <topicDirectory> resource

| Child Resources of <topicDirectory > | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <topicList> | 0..n | The <topicList> resource represents a topic instance in the <topicDirectory> resource. |

The <topicDirectory> resource shall contain the attributes specified in table 7.2.3.2-2.

Table 7.2.3.2-1: Attributes of <topicDirectory> resource

| Attributes of <topicDirectory> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 in TS-0001. |
| resourceID | 1 | RO | See clause 9.6.1.3 in TS-0001. |
| resourceName | 1 | WO | See clause 9.6.1.3 in TS-0001. |
| parentID | 1 | RO | See clause 9.6.1.3 in TS-0001. |
| expirationTime | 1 | RW | See clause 9.6.1.3 in TS-0001. |
| creationTime | 1 | RO | See clause 9.6.1.3 in TS-0001. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 in TS-0001. |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3 in TS-0001. |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3 in TS-0001. |

The <topicList> resource shall contain the attributes specified in table 7.2.3.2-3.

Table 7.2.3.2-1: Attributes of <topicList> resource

| Attributes of <topicDirectory> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 in TS-0001. |
| resourceID | 1 | RO | See clause 9.6.1.3 in TS-0001. |
| resourceName | 1 | WO | See clause 9.6.1.3 in TS-0001. |
| parentID | 1 | RO | See clause 9.6.1.3 in TS-0001. |
| expirationTime | 1 | RW | See clause 9.6.1.3 in TS-0001. |
| creationTime | 1 | RO | See clause 9.6.1.3 in TS-0001. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 in TS-0001. |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3 in TS-0001. |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3 in TS-0001. |
| topicName | 1 | RO | The name of the topic. |
| pubsubAttribute | 1 | RO | The attribute of the topic is used to indicate that the topic can be published or subscribed. This attribute shall be set to 'Publish' or ‘Subscribe’. |
| addressingInfo | 0..1 | RO | Represents the addresses to be used by other CSEs to connect to this CSE (e.g. IP address, Globally Unique Identifier (GUID defined by DDS). This attribute should be added when the pubsubAttribute of this resource is set to ‘Subscribe’. |
| topology | 1 | RW | Records the URIs of the AE/CSEs which are included in all topics discovery procedure. When the <topicDirectory> resource is created successfully, this attribute is updated. The CSE adds its identifier to this attribute and uses the ';' character to separate its identifier from the identifier of the previous one. The following is an example. IN-CSE;CSE0001;AE0001 |
| peerList | 0..1 (L) | RW | Represents a list of addresses of remote CSEs/AEs which subscribe to this resource. The address of one party can include the party’s identifier and the IP address, or Globally Unique Identifier (GUID defined by DDS). The following is an example. CSE0001, 10.144.115.11; or CSE0001, 68655CD60000005900000001000001C1; |

The Originator of a Request for initiating resource creation can be either an AE or a CSE which can be as the publisher or subscriber. The originator initiates creation of the <topicDirectory> resource request to its registrar CSE. All parameters defined in table 8.1.2-3 in TS-0001are applicable as indicated in that table. If the pubsubAttribute attribute is set to ‘Subscribe’, the addressingInfo attribute can be included in the request primitive. The addressingInfo attribute is used to identify the originator, e.g. IP address and Globally Unique Identifier (GUID defined in DDS).

Step-2: Local Processing

Once the Originator has been successfully authorized, its registrar CSE shall grant the Request after successful validation of the Request.

If the registrar CSE has registered to another CSE and hasn’t the DDS Repository function, the registrar CSE shall perform the basic procedure (clause 10.1.2 in TS-0001) for the Receiver of the CREATE Request apply, then follow the step-3.

If the registrar has the DDS Repository function, the registrar CSE shall follow the step-5.

If the registrar CSE hasn’t registered to another CSE and hasn’t the DDS Repository function, the registrar CSE shall reject the request with a “DDS_REPOSITORY_HAS_NOT_FOUND” response status code parameter value (4116).

Step-3: Create request of <topicDirectory> resource

After creating the requested resource, the registrar CSE adds its identifier to the topology attribute of the created resource and uses the ';' character to separate its identifier from the identifier of the Originator.

The registrar CSE sends a CREATE request of <topicDirectory> resource to its Registrar CSE. All parameters defined in table 8.1.2-3 in TS-0001 are applicable as indicated in that table.

Step-4: Local Processing

Same as the step-2.

Step-5: Local Processing

Once the target CSE has been successfully create the requested resource, the target CSE shall check whether the DDS Repository function is inside.

- If the receiver hasn’t DDS Repository function, the receiver shall initiate the creation request of <topicDirectory> resource to its registrar CSE.

- If the receiver has DDS Repository function, the receiver matches the topics according to the principle of string matching, the pubsubAttribute, and other information which can be pre-configured according to the actual deployment scenario requirement, e.g. whether or not allowing two nodes without registration relation establish pub-sub relationship. Then the receiver creates the address list of matching parties and updates the peerList attribute of the <topicList> resource.  After that, the receiver sends the UPDATE request to the requestor.

Step-6: Local Process

The receiver updates the peerList attribute of the <topicList> resource.

Step-7: Create UPDATE request of <topicDirectory> resource

The receiver initiates the update procedure to the originator according to the topology attribute of the requested resource.

Step-8: Local process

The originator updates the peerList attribute of the <topicList>  resource and configures the DDS middleware configuration according to the peerList attribute through the check_remote_participant API defined by the DDS Security[i.4]. Then the originator will initiate the dynamic discovery procedure to establish the pub-sub relationship with the other oneM2M parties which are listed in the address list. Once the pub-sub relationship is established, the publisher exchanges data with subscriber directly.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?