| Input Contribution |
| --- |
| Meeting ID* | ARC#29 |
| Title:* | Device representation in oneM2M |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd., yinjiaxin@huawei.com |
| Date:* | 2017-5-15 |
| Input related to* | TS-0033 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TS-0033 v0.0.2 |
| Decision requested or recommendation:* | Incorporated the contribution if agreed. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 6	Architecture of Interworking

## 6.1	Device Representation

## Device Representation is the representation of device or gateway in oneM2M system. oneM2M uses more than one resources and their mutual relationship to represent real world devices as well as services provided by the device.

## The Device Representation is synchronized with the device via various of ways to guarantee the state of the device is correctly reflected by the Device Representation and all requests to the Device Representation is passed to the device.

Device Representation is used to represent both oneM2M native device (ASN, ADN, MN) and oneM2M legacy device (NoDN). In both cases, devices shall be represented in oneM2M following the same principle so that when the corresponding device representation is exposed to applications, they have uniformed structure and usage.