| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC #29.4 |
| Source:* | Catalina Mladin, Convida Wireless, Mladin.Catalina@ConvidaWireless.com Dale Seed, Convida Wireless, Seed.Dale@ConvidaWireless.com Mike Starsinic, Convida Wireless, Starsinic.Michael@ConvidaWireless.com |
| Date:* | 2017-07-02 |
| Reason for Change/s:* | Provide UE Reachability functionality |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <WI-0058> - 3GPP & Cellular IoT Interworking MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0026 v0.0.2 |
| Clauses * | 7.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes a description of the UE Reachability monitoring flow.

### -----------------------Start of change 1-------------------------------------------

## 7.4 Monitoring events

### 7.4.x UE Reachability monitoring

The 3GPP SCEF functionality described in 3GPP TS 23.682 [2] supports APIs for monitoring specific events such as UE Reachability status. This allows M2M Servers to request to receive reports when a device becomes reachable for receiving either SMS or downlink data.

In the 3GPP interworking architecture of oneM2M, the UE can host an ADN-AE or an ASN/MN-CSE. The UE Monitoring flow in Figure 7.4.x-1 takes place after the UE has attached to the 3GPP Network and the ADN-AE or ASN/MN-CSE is registered with the IN-CSE.

Figure 7.4.x -1: UE Reachability monitoring

Step 0: UE Attach and oneM2M Registration Procedures.

The UE attaches to the 3GPP network and  the ADN-AE or ASN/MN-CSE hosted on the UE performs the oneM2M registration procedure, as detailed in clause 6.5. The IN-CSE hosts the corresponding <AE> or <remoteCSE> resource for the registree. During this procedure, <schedule> resources are created as children of the <AE> or <remoteCSE> and the UE hosted ADN-AE or ASN/MN may subscribe to their respective <schedule> resources.

If an IN-AE is interested in the reachability status of the UE, it may subscribe to the <schedule> resources (step 0b, optional).

Step 1: IN-CSE (SCS) sends a Monitoring Request to SCEF to monitor the UE reachability.

This step may be triggered by IN-CSE based on implementation options, for example after a certain number of communication failures have occurred. The creation of one or more subscriptions to the <schedule> (step 0b, optional) may also be used to trigger the monitoring request.

The monitoring request from the IN-CSE to the SCEF contains information as specified in 3GPP TS 23.682 [3]. Such information includes (but is not limited to):

- SCS Identifier shall be set to a value that is prearranged between the Service Provider and MNO.

- T8 Destination Address is set to the IP Address of the IN-CSE.

- TTRI is used to correlate this request with future responses. It shall be assigned based on internal IN-CSE policies.

- TLTRI is used to identify the monitoring request.  It shall be assigned based on internal IN-CSE policies.  Later, when reports are received, the value shall be used to associate them to the original request

- Maximum Number of Reports or Monitoring Duration shall be optionally set according to IN-CSE pre-provisioning if  continuous monitoring is supported.

- Chargeable Party identifier shall be optionally set according to IN-CSE pre-provisioning

- External Identifier shall be set to the M2M-Ext-ID of the UE

- Monitoring Type shall be set to “UE Reachability”

- Reachability Type shall be set to “Reachability for Data”

- Idle Status Indication shall be set according to IN-CSE pre-provisioning. It is recommended that Idle Status Indication set in order to provide a more accurate status via the <schedule> resource.

This information uses the values pre-provisioned at the IN-CSE, attributes of the <schedule> resource or is derived from local policies.

Step 002: -Step 003: Monitoring Request Handling in the Underlying Network.

The SCEF handles the Monitoring Request together with the Mobile Core Network, as described in 3GPP TS23.682[3]. The SCEF sends a Monitoring Response (TLTRI, Cause) message to the IN-CSE (SCS) to acknowledge acceptance of the Monitoring Request of the identified monitoring event configuration.

Step 004: Detection of UE changing from Idle mode and reporting to SCEF.

Later, the UE changes to connected mode (for a UE using Power Saving Mode or extended idle mode DRX) or the UE will becomes reachable for paging (for a UE using extended idle mode DRX). The Underlying Network detects the condition and sends a Monitoring Report (Idle Timestamp, Subscribed Periodic RAT/TAU timer, Active Timer) is sent to SCEF.

Step 005: SCEF sends UE Reachability Monitoring Report to IN-CSE (SCS).

The SCEF sends a Monitoring Report to the IN-CSE when receiving the Monitoring Report from MME that contains information as specified in 3GPP TS 23.682 [3]. Such information includes:

- External Identifier (M2M-Ext-ID of the UE)

- TLTRI (same as in the request)

If the Idle Status Indication was set, the Monitoring Report also includes:

- Idle Timestamp (start time of the ADN-AE or ASN/MN-CSE hosting UE becoming idle)

- Periodic RAT/TAU timer (optional)

- Active Time (optional)

Step 006: UE Reachability Monitoring Handling at the IN-CSE (SCS).

The IN-CSE uses the information provided in the Monitoring Report as follows:

- If the monitored UE hosts an ADN-AE, the information is used to update the <schedule> child resource of the corresponding <AE> resource

- If the monitored UE hosts an ASN/MN-CSE, the information is used to update the <schedule> child resource of the corresponding <remoteCSE> resource

The IN-CSE changes the <schedule> resource to indicate that communications are currently available at the monitored UE. If the Idle Status Indication was set and the corresponding additional information is provided in the report, the IN-CSE changes the scheduleElement such that the element duration indicates the Active Time value and the beginning of the next communication period is the end of the TAU timer. The changes may be activated at the time provided by the Idle Timestamp.

Step 007: (Optional) If IN-AEs have subscribed to changes in the <schedule> resources, a notification will be sent to the subscribers. Notifications will also be sent to the UE hosted UE hosted ADN-AE or ASN/MN, if indicated by subscriptions to their respective <schedule> resources.

NOTE: The UE Reachability Monitoring API described by TS 23.682 [2] also supports providing optional parameters for configuration purposes, such as: Maximum Latency, Maximum Response Time and Suggested number of downlink packets, to be used along with the “configuration” Monitoring Type. However, as of v.15.1.0 of TS 23.682, the Network Parameter Configuration API is recommended instead, therefore the use of these parameters is not described here.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?