| CHANGE REQUEST |
| --- |
| Meeting:* | ARC TP30 |
| Source:* | BeiXu，Huawei，Echo.xubei@huawei.com |
| Date:* | 2017-06-02 |
| Contact:* | BeiXu，Huawei，Echo.xubei@huawei.com |
| Reason for Change/s:* | Add new section about UE location reporting |
| CR against: Release* | <Release> Only ONE Release shall be indicated |
| CR against: WI* | Active <WI-0058 - 3GPP & Cellular IoT Interworking> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0026-V-0.3.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

For 3GPP Only One-time Reporting is supported for the Last Known Location. One-time and Continuous Location Reporting are supported for the Current Location. For Continuous Location Reporting the serving node(s) sends a notification every time it becomes aware of a location change. oneM2M only supports location procedure based on one-time retrieve or periodically update when the locationSource of <locationPolicy> is Network Based.  So oneM2M should support update the location container when receiving the location reporting from 3GPP to reduce the retrieve location messages.

Attributes of <locationPolicy> resource

| Attributes of <locationPolicy> | Multiplicity | RW/ RO/ WO | Description | <locationPolicyAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3. | NA |
| Parented | 1 | RO | See clause 9.6.1.3. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. | NA |
| Labels | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3. | OA |
| locationSource | 1 | RW | Indicates the source of location information: Network Based; Device Based; Sharing Based. | OA |
| locationInformationType | 1 | RW | Indicate the types of location information: Position fix (e.g. longitude and latitude); Geo-fence event (e.g. entering and leaving). | OA |
| locationUpdatePeriod | 0..1(L) | RW | Indicates the period for updating location information. If the value is marked '0' or not defined, location information is updated only when a retrieval request is triggered. If the attribute has more than one value and the hosting CSE of the resource is the target device, the value could be selected within listed values depending on device's local context information(e,q,, velocity, status of battery, range of the location etc). Zero('0') shall not be stored with non zero value(s). When the value is read, the first value in the list is the current active update period. | OA |
| locationTargetID | 0..1 | RW | The identifier to be used for retrieving the location information of a remote Node and this attribute is only used in the case that location information is provided by a location server. | OA |
| locationServer | 0..1 | RW | Indicates the identity of the location or Geo-fence server. This attribute is only used in that case location information is provided by a location server or Geo-fence server. | OA |
| locationContainerID | 1 | RO | ID of the <container> resource where the actual location information or event result of a M2M Node is stored. | OA |
| locationContainerName | 0..1 | RW | A name of the <container> resource where the actual location information of a M2M Node is stored. If it is not assigned, the Hosting CSE automatically assigns a name of the resource (see note). | OA |
| locationStatus | 1 | RO | Contains the information on the current status of the location request (e.g. location server fault). | OA |
| geographicalTargetArea | 0..1 | RW | Indicates area information where the Geo-fence feature is applied. | OA |
| geofenceEventCriteria | 0..1 | RW | Indicate the event type of Geo-fence feature: Entering; Leaving; Inside; Outside. | OA |
| aggregationForward | 0..1 | RW | Indicate how Geo-fence relevant information (e.g. measurement or position fix) from the target node is forwarded to Geo-fence server: True/False; Number of Events; Time-based Accmulation. | OA |
| M2M-Ext-ID | 0..1 | RW | Indicates the identity of the application which retrieves the location information of a remote node. This attribute is only used in the case that location information is provided by a location server. See clause 7.1.8 where this attribute is described. | OA |
| NOTE: The created <container> resource related to this policy shall be stored only in the Hosting CSE. |

oneM2M how to support the location information when the locationSource is Network Based:

Case a) locationUpdatePeriod >0, the procedure is the same as before: location information is updated periodically.

Case b) locationUpdatePeriod is not defined and locationUpdateEventCriteria is not defined, the procedure is the same as before: location information is updated only when a retrieval request is triggered.

Case c) locationUpdatePeriod is not defined and locationUpdateEventCriteria is LocationChanging, the procedure is 3GPP Continuous Location Reporting for Current Location;

Case d) locationUpdatePeriod = 0, locationUpdateEventCriteria should be not defined.

IN-AE retrieves <lastest> of <Container>, IN-CSE performs the procedure which is 3GPP one-time current location. If result of 3GPP one-time current location failed, then IN-CSE performs the procedure which is 3GPP one-time last known location based on the retrieveLastKnownLocation.

This contribution is focus on Case c), Case d).

### -----------------------Start of change 1-------------------------------------------

## 7.5	Monitoring event(Location Reporting)

### 7.5.1 Introduction

For 3GPP Only One-time Reporting is supported for the Last Known Location. One-time and Continuous Location Reporting are supported for the Current Location. For Continuous Location Reporting the serving node(s) sends a notification every time it becomes aware of a location change. oneM2M only supports location procedure based on one-time retrieve or periodically update when the locationSource of <locationPolicy> is Network Based.  So oneM2M should support update the location container when receiving the location reporting from 3GPP to reduce the retrieve location messages.

### 7.5.2 Resource Structure

Refer to the clause 9.6.10 Resource Type locationPolicy of TS-0001[1]

### 7.5.3 ServiceFlow

#### 7.5.3.1 Location updating triggered by retrieval

Figure 7.5.3.1-1: Service Flow of Location updating triggered by retrieving

Step 001-002: The IN-AE sends < locationPolicy> create request to IN-CSE. The detail of creating <locationPolicy> is specified in clause 10.2.9 of oneM2M TS-0001[i.9].The < locationPolicy > should include the attributes:

LocationSource(Which is defined as Network Based)

locationUpdatePeriod (Which is defined as 0)

locationTargetID (Which is defined M2M-Ext-ID as target ASN/MN-CSE or ADN-AE)

locationServer(Which is defined as SCEF address)

locationContainerID (Which is defined as the location container ID of target ASN/MN-CSE or ADN-AE )

locationInformationType(which is set to position fix)

retrieveLastKnownLocation(Which is defined according to IN-AE need)

Step 003: The IN-AE sends a <latest> of <container> Retrieve request of location container ID of target ASN/MN-CSE or ADN-AE to IN-CSE.

Step 004: The IN-CSE checks the locationSource of the < locationPolicy >, if the locationSource is Network Based and locationUpdatePeriod is zero, and then IN-CSE sends Monitoring Request to SCEF. The request contains information as specified in 3GPP TS 23.682 [i.5]. Such information includes:

External Identifier(which is locationTargetID)

SCS Identifier (which is IN-CSE ID)

SCS Reference ID (which is a parameter created by the IN-CSE to refer to a specific transaction initiated by the IN-CSE towards the SCEF; SCS Reference ID is stored by the SCEF.)

Monitoring Type (which is set to “Location Reporting”)

Monitoring Destination Address (which is IN-CSE address)

Location Type (which is set to” current location”).

Accuracy (Which is set to locationInformationType)

Step 005-006: 3GPP interworking handling the Monitor Request Information and performs the current location reporting procedure, more detail can reference 3GPP TS23.682 [i.5].

Step 007: The SCEF sends the Monitor Indication to the IN-CSE.

Step 008: The IN-CSE sends the retrieve response to IN-AE if the result of Step 007 is successful.

Step 009: The IN-CSE creates the new  <contentInstance> of  <container> according to the locationContainerID of <locationPolicy> for target ASN/MN-CSE or ADN-AE.

Step 009b: IN-CSE sends Monitoring Request to SCEF to get last known location if the result of Step 007 is failed and retrieveLastKnownLocation is TRUE.

The request contains information as specified in 3GPP TS 23.682 [i.5]. Such information includes:

External Identifier(which is locationTargetID),

SCS Identifier (which is IN-CSE ID)

SCS Reference ID (which is a parameter created by the IN-CSE to refer to a specific transaction initiated by the IN-CSE towards the SCEF; SCS Reference ID is stored by the SCEF.)

Monitoring Type (which is set to “Location Reporting”)

Monitoring Destination Address (which is IN-CSE address)

Location Type (which is set to” last known location”).

Accuracy (Which is set to locationInformationType)

Step 010b-011b: 3GPP interworking handling the Monitor Request Information and performs the last known location reporting procedure, more detail can reference 3GPP TS23.682 [i.5].

Step 012b: The SCEF sends the Monitor Indication to the IN-CSE.

Step 013b: The IN-CSE sends the retrieve response to IN-AE

Step 014b: The IN-CSE creates the new  <contentInstance> of  <container> according to the locationContainerID of <locationPolicy> for target ASN/MN-CSE or ADN-AE.

#### 7.5.3.2 Location updating triggered by location change

Figure 7.5.3.2-1: Service Flow of location updating triggered by location change

Step 001-002: The IN-AE sends <locationPolicy> create request to IN-CSE. The detail of creating <locationPolicy> is specified in clause 10.2.9 of oneM2M TS-0001[i.9].The < locationPolicy > should include the attributes:

locationSource (which is defined as Network Based)

locationTargetID (which is defined M2M-Ext-ID as target ASN/MN-CSE or ADN-AE)

locationServer (which is defined as SCEF address )

locationContainerID (which is defined as the location container ID of target ASN/MN-CSE or ADN-AE)

locationUpdateEventCriteria (which is set to LocationChange)

locationInformationType (which is set to position fix)

Step 003: The IN-CSE sends Monitoring Request to SCEF. The request contains information as specified in 3GPP TS 23.682 [i.5]. Such information includes:

External Identifier (which is locationTargetID)

SCS Identifier (which is IN-CSE ID)

SCS Reference ID (which is a parameter created by the IN-CSE to refer to a specific transaction initiated by the IN-CSE towards the SCEF; SCS Reference ID is stored by the SCEF.)

Monitoring Type (which is set to “Location Reporting”)

Monitoring Destination Address (which is IN-CSE address)

Location Type (which is set to “current location”).

Accuracy (Which is set to locationInformationType)

Step 004-Step 005: 3GPP interworking handling the MonitorRequest Information, and more detail can reference 3GPP TS23.682 [i.5]

Step 006: The SCEF (NSE) sends a Monitoring Response (SCS Reference ID, Cause) message to the IN-CSE (SCS) to acknowledge acceptance of the Monitoring Request of the identified monitoring event configuration.

Step 007: The 3GPP sends a Monitoring Indication to SCEF when detecting the location change of target ASN/MN-CSE or ADN-AE. The more detail can reference 3GPP TS23.682 [i.5]

Step 008: The SCEF (NSE) sends a Monitoring Indication message to the IN-CSE (SCS) to notify the IN-CSE the new location information of target ASN/MN-CSE or ADN-AE.

Step 009: IN-CSE creates the new  <contentInstance> of  <container> according to the locationContainerID of <locationPolicy> for target ASN/MN-CSE or ADN-AE.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?