| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC #29.4 |
| Source:* | Dale Seed, Convida Wireless, Seed.Dale@ConvidaWireless.com Mike Starsinic, Convida Wireless, Starsinic.Michael@ConvidaWireless.com Catalina Mladin, Convida Wireless, Mladin.Catalina@ConvidaWireless.com James Hu, ATT, james.hu@att.com |
| Date:* | 2017-07-02 |
|  | See Introduction |
| Reason for Change/s:* | Rel-3 |
| CR against: Release* | Active <WI-0058> - 3GPP & Cellular IoT Interworking MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: WI* | TS-0026 Version 0.0.2 |
| CR against: TS/TR* | 7.4.1 |
| Clauses * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Type of change: * | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Impacted other TS/TR(s) | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

As part of the SCEF Event Monitoring functionality an API is exposed that allows the IN-CSE to be informed when the SIM card of one physical device is placed in another physical device.  This condition is detected by the underlying 3GPP network when the association between the International Mobile Subscriber Identity (IMSI) and International Mobile Equipment Identity (IMEI/IMEISV) changes.

For example, consider the use case where numerous sensors are deployed throughout a city.  Many of the sensors are deployed in places where a thief, criminal or hacker could steal or tamper with the device.  For example, someone could remove the SIM card from a device and place it in another device that generates false values, place the SIM card in another device that will generate large volumes of illegitimate traffic, or place the SIM card in their smart phone.

This contribution proposes that upon receiving a report of a change in IMSI-IMEI(SV) association, the IN-CSE stops servicing requests from any ASN/MN-CSEs or ADN-AEs having an M2M-Ext-ID matching the one indicated by the report.   To block these requests, the IN-CSE tears down any active security associations (e.g. D/TLS sessions)  between the IN-CSE and these ADN-AEs or ASN/MN-CSEs.  In addition, the IN-CSE also denies new security association establishment requests from any ADN-AEs or ASN/MN-CSEs that have an M2M-Ext-ID matching the one indicated in the report. The restrictions may later be removed via administrative means.

### -----------------------Start of change 1-------------------------------------------

## 7.4	Monitoring events

## 7.4.1	Detecting Change of IMSI-IMEI(SV) Association

The 3GPP SCEF Event Monitoring functionality described in 3GPP TS 23.682 [2] supports an API that allows the IN-CSE to be informed when the SIM card of one physical device is placed in another physical device.  This condition is detected by the underlying 3GPP network when the association between the International Mobile Subscriber Identity (IMSI) and International Mobile Equipment Identity (IMEI/IMEISV) changes.

An IN-CSE may request to receive notifications from an underlying 3GPP network when the association between the IMSI and IMEI(SV) changes for a given UE that hosts one or more ASN/MN-CSEs or ADN-AEs registered to the IN-CSE.  Based on this notification, the IN-CSE may then ignore incoming requests from these ASN/MN-CSEs or ADN-AEs.

## 7.4.1.1	Change of IMSI-IMEI(SV) Association Request and Notification

Figure 7.4.1-1: Change of IMSI-IMEI(SV) Association Monitoring Request and Notification

Pre-conditions:

There is a relationship in place between the IN-CSE and MNO allowing the IN-CSE to request notifications for IMSI-IMEI(SV) association changes

An ASN/MN-CSE or ADN-AE registers with the IN-CSE and configures the M2M-Ext-ID attribute of its <remoteCSE> or <AE> resource. The IN-CSE examines the M2M-Ext-ID and recognizes that it is associated with an MNO that it has a relationship with.  The relationship allows the IN-CSE to request notifications when the device’s IMSI-IMEI(SV) association changes.

Step 1: IN-CSE Requests notification for changes in IMSI-IMEI(SV) association

The IN-CSE determines whether it wants a notification if the IMSI-IMEI(SV) association of a particular UE hosting one or more ASN/MN-CSEs or ADN-AEs changes.  This determination may be based on whether the IN-CSE has an established relationship with the underlying 3GPP network operator that supports this capability and provisioned policies.

Step 2 (Optional): DNS Query/Response

The IN-CSE may determine the IP address(es)/port(s) of the proper SCEF to contact by performing a DNS query using the M2M-Ext-ID (M2M External Identifier) assigned to the target ASN/MN-CSE or ADN-AE.  Alternatively, an IN-CSE may use a pre-configured SCEF identifier.  The method for pre-configuring a SCEF identifier into the IN-CSE is outside the scope of the present document.

Step 3: Monitoring Request

The IN-CSE sends a request to be notified when the device’s IMSI-IMEI(SV) association changes.  The Monitoring Request contains information as specified in 3GPP TS 23.682 [2] which includes the following:

- External Identifier shall be set to the M2M-Ext-ID of the UE hosting an ADN-AE or ASN/MN-CSE, which may have been provided during ADN-AE or ASN/MN-CSE registration.

- SCS Identifier shall be set to a value that is prearranged between the Service Provider and MNO.

- T8 Destination Address is set to the IP Address of the IN-CSE.

- TTRI is used to correlate this request with future responses. It shall be assigned based on internal IN-CSE policies.

- TLTRI is used to identify the Change of IMSI-IMEI(SV) Association Request.  It shall be assigned based on internal IN-CSE policies.  Later, when a report is received, the value will be used to reference the original request so that the IN-CSE knows what M2M-Ext-ID the report pertains to.

- Monitoring Type shall be set to "Change of IMSI-IMEI(SV) Association".

- Association Type shall be set to IMEI or IMEISV.  The type that is used is based on IN-CSE policies which may be based on the relationship between the Service Provider and MNO.

- Maximum Number of Reports and Monitoring Duration shall not be configured; thus indicating that a monitoring request may be cancelled after receiving one report.

- TLTRI for Deletion shall not be provided.

Step 4: Process Monitoring Request

The SCEF processes the request

Step 5: Monitoring Response

The SCEF responds to the request with a Cause value that indicates if the request was accepted or not and the TTRI that was provided in the Monitoring Request so that the IN-CSE can correlate the response with the original request.

Step 6: Detect change in IMSI-IMEI(SV) association

The underlying 3GPP network monitors and detects a IMSI-IMEI(SV) association change.

Step 7: Monitoring Indication

The SCEF sends a Monitoring Indication to the corresponding T8 Destination Address of the IN-CSE that was configured in the Monitoring Request.  The indication includes a report containing a TTRI value that is assigned by the SCEF and that will be provided back to the SCEF when the IN-CSE responds.  The report also includes the TLTRI value that was provided by the IN-CSE in the Monitoring Request so that the IN-CSE can correlate the indication with the original request and determine what UE the report pertains to.

Step 8: Monitoring Indication Response

The IN-CSE shall acknowledge the Monitoring Indication by returning a Monitoring Indication Response. The response shall include the TTRI that was provided by the SCEF in the Monitoring Indication.

Step 9: Process Notification

Using the TLTRI, the IN-CSE shall determine the corresponding M2M-Ext-ID.  The IN-CSE shall stop servicing requests from any ASN/MN-CSEs or ADN-AEs having an M2M-Ext-ID matching the one indicated in the report.   To block these requests, the IN-CSE may take an action such as tear down any active security associations (e.g. D/TLS sessions) between the IN-CSE and these ADN-AEs or ASN/MN-CSEs.  In addition, the IN-CSE may also deny new security association establishment requests from any ADN-AEs or ASN/MN-CSEs that have an M2M-Ext-ID matching the one indicated in the report until the restriction is removed via administrative means which are outside the scope of the present document.

## 7.4.1.2	Canceling IMSI-IMEI(SV) Association Change Monitoring Requests

If an ASN/MN-CSE or ADN-AE de-registers from the IN-CSE, the IN-CSE should cancel the corresponding Change of IMSI-IMEI(SV) Association Monitoring Request.  The IN-CSE shall cancel this request by sending a request to the SCEF’s Monitoring Request API that includes the following:

- SCS Identifier shall be set to a value that is prearranged between the Service Provider and MNO.

- TLTRI for Deletion shall be set to the value of the TLTRI configured in the Monitoring Request that is to be deleted. This value is used by the SCEF and the mobile core network to determine what request should be cancelled.

- TTRI is used to correlate this request with the SCEF’s response to the cancellation request. It shall be assigned based on internal IN-CSE policies.

Note, External Identifier, T8 Destination Address, Monitoring Type, Association Type, Maximum Number of Reports and Monitoring Duration shall not be included in this request.

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?