| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#30 |
| Source:* | Shuling Wang , Chinaunicom；Bei Xu, HuaWei |
| Date:* | 2017-06-20 |
| Contact:* | Shuling Wang, Chinaunicom, wangsl49@chinaunicom.cn Bei Xu, Huawei, echo.xubei@huawei.com |
| Reason for Change/s:* | Session QoS configuration |
| CR against: Release* | Release 3 |
| CR against: WI* | Active <WI-0046> MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0024 |
| Clauses/Sub Clauses* | Clause8 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides the process for session QoS requirement.

### -----------------------Start of change 1-------------------------------------------

## 8.12 Support for Session QoS configuration

### 8.12.1 Description

Session QoS configuration is the means by which a SCS sends information to the 3GPP network to guarantee the service quanlity for a specific application session.

### 8.12.2 Feature Gap Analysis

OneM2M uses the 3GPP Release-13 MTC feature for setting up required session  QoS process to provide corresponding session QoS requirement specified by oneM2M applications.

The signalling flow for setting up QoS configuration is described in th clasuse  5.11  of 3GPP TS23.682[]. Figure 8.12.2-1 provides the signalling sequence derived from 3GPP specification with oneM2M terminologies mapping (3GPP TS 23.682 [i.5], figure 5.11-1 )

Figure8.12.2-1 Signalling sequence for provisioning of CP Parameters

NOTE 1:	Step 1 and 5 are outside of 3GPP scope, but are shown for informative purposes only.

- When setting up the connection between SCS/AS and the UE with required QoS for the service, the SCS/AS sends an On-demand QoS request message (UE IP address, SCS/AS Identifier, SCS/AS Reference ID, Description of the application flows reference to a pre-defined QoS) to the SCEF. Optionally, a period of time or a traffic volume for the requested QoS can be included in the SCS/AS request.

NOTE 2:	Step 1 and 5 are outside of 3GPP scope, but are shown for informative purposes only.

2.	The SCEF authorizes the SCS/AS request and may apply policies to control the overall amount of pre-defined QoS authorized for the SCS/AS.

NOTE 3:	The pre-defined QoS here indicates the oneM2M applications’ unawareness of the QoS complexity of the  network level, and provides a simple way for the applications to specific QoS requirement. The pre-defined QoS can be a fuzzy QoS level, Gold, Silver, Bronze, for example. The QoS level requirement is mapping to specific Rx parameter of in the 3rd steps.

3.	The SCEF maps the UE IP address, the SCS/AS Identifier, the Description of the application flows and the reference to pre-defined QoS information to existing Rx parameters (including the optionally received period of time or traffic volume which is mapped to sponsored data connectivity information). The SCEF acts as an AF defined in TS 23.203 [27].

NOTE 4:	Before the reference to pre-defined QoS information is mapped to Rx parameters, the SCEF can perform a mapping from the name space of the 3rd party SCS/AS to the name space of the operator.

4.	The SCEF interacts with the PCRF via the Rx interface and triggers a PCRF initiated IP-CAN Session Modification as described in clause 7.4.2 of TS 23.203 [27]. The SCEF shall request to be notified about the transmission resource status.

The PCRF derives the required QoS based on the information provided by the SCEF and determines whether this QoS is allowed (according to the PCRF configuration for this 3rd party SCS/AS), and notifies the result to the SCEF.

The PCRF notifies the SCEF whether the transmission resources corresponding to the QoS request are established or not.

5.	The SCEF sends an On-demand QoS response message (SCS/AS Identifier, SCS/AS Reference ID, Result) to the SCS/AS. Result indicates whether the QoS request is granted or not.

## 8.12.3 Key Issues and Requirements

#### 8.12.3.1 Key SCEF NorthBound API Requirements

| Number | Description | Notes |
| --- | --- | --- |
| REQ-8.12-01 | Session QoS Request |  |
| REQ-8.1.2-02 | Session QoS response |  |

#### 8.12.3.2 Key SCEF SouthBound API Requirements

N/A

#### 8.12.3.3 Further 3GPP Requirements and Clarifications

N/A

#### 8.12.3.4 oneM2M Key Issues

Provide support for session QoS requirement functionality.

## 8.12.4 Solution(s)

#### 8.12.4.1 Proposed Resource types and attributes

This clause provides information of new resource types and new attributes including relationship with existing resource types and attributes.

Proposed new resource types are as below:

Resource Type <sessionQos>

Resource Type <qosProfile>

Note: It is child resource of existing Resource Type <AE>.

8.12.4.1.1 Resource Type <sessionQos>

The <sessionQos> resource represents the session QoS requirement of a certain AE and it is a child resource of AE. It is used to share information about a specific AE’s QoS requirement with the IN-CSE.

Figure8.12.4.1.1-1 Structure of <sessionQos> resource

The <sessionType> resource shall contain the attributes specified in table 8.12.4.1.1 -1.

Table 8.12.4.1.1-1: Attributes of <sessionQos> resource

| Attributes of <trafficPattern> | Multiplicity | RW/ RO/ WO | Description | <trafficPatternAnnc> Attributes |
| --- | --- | --- | --- | --- |
| ueId | 0..1 | RO | It indicate the originator ue of request if it is specified. Or else it indicates all the ues that are attach to the AE. | O |
| qosProfile | 1 | RW | Provides the qos requirement. Detail information is described in clause 8.12.4.1.2 | M |

#### 8.12.4.1.2 Resource Type <qosProfile>

#### The new resource type <qosProfile> illustrate the detail information about a qos request oraginated from a ue or an AE.

Figure8.12.4.1.2-1 Structure of <qosProfile> resource

The <qosProfile> resource shall contain the attributes specified in table 8.12.4.1.1 -1.

Table 8.12.4.1.2-1: Attributes of <qosProfile> resource

| Attributes of <trafficPattern> | Multiplicity | RW/ RO/ WO | Description | <trafficPatternAnnc> Attributes |
| --- | --- | --- | --- | --- |
| requiredQosLevel | 1 | RW | It provides the predefined QoS level, which can be gold, silver, copper, premium.. | M |
| Start | 0..1 | RW | It indicates the start of the QoS modification. If it is not present the service starts immediately. | O |
| End | 0..1 | RW | This element indicates the end of the session. If it is indicated, the service is stopped at the date indicated in this parameter. | O |

#### 8.12.4.2 Proposed Flow

This clause describes the procedure for session QoS configuration.

Figure 8.3.4.1.2-1 depicts a general procedure for setting up a QoS requirement in oneM2M architecture.

Figure8.12.4.2-1 QoS configuration Procedure between oneM2M and 3GPP

Step-1 QoS request

An IN-AE/UE  requests IN-CSE for a certain predefined QoS level with detailed requirement illustrated in resource <qosProfile>. The predefined Qos level can be gold, silver, copper, premium, and so on, which is defined by CSE. The request can be initiated by an AE or a specific UE with a certain event. Take a smartwatch for example, in the suitation of a seemly fall-down of an old man, the data to be transferred need a higher QoS level.

The request includes the following infornation:

AE-ID: the originator of the requesting AE,a profile of QoS requirement and a specific UE, which are respectively indicated by the <qosProfile> and <ueId> defined in clause 8.12.4.1 The value of the varialbes are decided by the AE according to the offline aggrement with network operators.

If the IN-CSE has received a request from an IN-AE to  create, update QoS requirement checks if the request from the IN-AE is valid.

Step-2 Generate QoS request message

The IN-CSE sends a request message to the NSE for parameter mapping and negotiation. The request massage is generated as 3GPP TS 23.682 specified according to the information derived from the resource <qosProfile>.

Step-3 parameter mapping and negotiation

The Underlying Network determines the Rx parameters and accomplish the configurate process.

Step-4 Response for transfer policies

The NSE responds to the IN-CSE with the QoS setting up result.

### -----------------------End of change 2 ------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause?

# Comments

这两个接口和图上不对应啊？图上是两个查询接口，这两个接口是平台北向接口吧？这里是SCEF和平台之间的接口

这个可以在oneM2M operation里体现，oneM2M operation包括C(Create)R（Retrieve）U（Update）D（Delete）N（Notify）

这一步是IN-AE创建QoS吗？创建之后，立刻网络就需要用吗？这个Session QoS在3GPP里是针对单个UE的，这里创建之后是针对整个IN-AE的吗？

Description of the application flows reference to a pre-defined QoS)--- 这个参数IN-CSE怎么获取呢？