| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC #29.4 |
| Source:* | Dale Seed, Convida Wireless, Seed.Dale@ConvidaWireless.com Mike Starsinic, Convida Wireless, Starsinic.Michael@ConvidaWireless.com Catalina Mladin, Convida Wireless, Mladin.Catalina@ConvidaWireless.com James Hu, ATT, james.hu@att.com |
| Date:* | 2017-07-02 |
|  | See Introduction |
| Reason for Change/s:* | Rel-3 |
| CR against: Release* | Active <WI-0058> - 3GPP & Cellular IoT Interworking MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: WI* | TS-0026 Version 0.0.2 |
| CR against: TS/TR* | 7.4.1 |
| Clauses * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Type of change: * | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Impacted other TS/TR(s) | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

As part of the SCEF functionality described in 3GPP TS 23.682, an API is exposed that allows the IN-CSE to change the chargeable party associated with traffic flows originating or terminating to UEs. For example, UEs hosting ADN-AEs or ASN/MN-CSEs.  This feature allows an IN-CSE to change the chargeable party to itself and sponsor (i.e. pay for) these traffic flows.

For example, consider the use case where an IoT Service Provider has a pre-established relationship with an MNO that allows the IoT Service Provider to sponsor traffic generated by its customer’s applications and devices.  As a sponsor, the IoT Service Provider has authorized the MNO to charge it for specific traffic flows.  In turn, the IoT Service Provider can pass these charges onto its customers.  For example, as part of the subscription plans that it offers to its customers, an IoT Service Provider can incorporate these underlying sponsorship costs.

This contribution proposes to introduce the capability to allow an IN-CSE to change the chargeable party in order to sponsor traffic flows originating or terminating to UEs.  For example, UEs hosting its registree ADN-AEs or ASN/MN-CSEs.

### -----------------------Start of change 1-------------------------------------------

## 7.11 Changing the chargeable party

The SCEF API described in 3GPP TS 23.682 [2] allows an IN-CSE to change the chargeable party for specified 3GPP traffic flows.  This capability allows the IN-CSE to sponsor specified traffic flows over the MNO’s 3GPP network that are either initiated by or targeted towards UEs.  For example, UEs hosting ADN-AEs or ASN/MN-CSEs registered to the IN-CSE.

Figure 7.11-1 Changing Chargeable Party

Pre-conditions:

There is a relationship in place between an IoT Service Provider and MNO allowing the IoT Service Provider’s IN-CSE to specify sponsors of traffic flows over the MNO’s underlying network that are either initiated by or targeted towards UEs.  As part of the relationship with the MNO, the IN-CSE may be provisioned with one or more instances of Sponsor Information which identifies a sponsor.  As far as the MNO is concerned, all instances of Sponsor Information are associated with the IN-CSE.  However, each instance of Sponsor Information may be used by the IN-CSE to uniquely identify and track different sponsors for different flows within the IN-CSE.

Step 1: ADN-AE or ASN/MN-CSE Registration

When registration of an ADN-AE or ASN/MN-CSE to an IN-CSE occurs, the IN-CSE may issue a request to the SCEF to configure the chargeable party for any traffic flowing to/from the UE hosting the ADN-AE or ASN/MN-CSE to a specified sponsor.

Note – An IN-CSE may also sponsor traffic flowing from NoDNs.

Step 2 (Optional): DNS Query/Response

The IN-CSE determines whether it wants to sponsor traffic for the UE. For example, a UE hosting the ASN/MN-CSE or ADN-AE.  This determination may be based on whether the IN-CSE has an established relationship with the underlying 3GPP network operator that supports this capability or via provisioned policies.  If the IN-CSE determines that it wants to sponsor traffic, the IN-CSE may determine the IP address(es)/port(s) of the proper SCEF to contact by performing a DNS query using the M2M-Ext-ID (M2M External Identifier) assigned to the target UE.  Alternatively, an IN-CSE may use a pre-configured SCEF identifier.  The method for pre-configuring a SCEF identifier into the IN-CSE is outside the scope of the present document.

Step 3: Set Chargeable Party Request

The IN-CSE sends a Set Chargeable Party Request to the SCEF.  The request contains information as specified in 3GPP TS 23.682 [2] which includes the following:

- SCS Identifier shall be set to a value that is prearranged between the Service Provider and MNO.

- TTRI is used to correlate this request with future responses. It shall be assigned based on internal IN-CSE policies.

- TLTRI shall be assigned based on internal IN-CSE policies.  The value will be used to reference the original request for cases where the IN-CSE wants to update the chargeable party.

- Description of the application flows.  Each flow includes a direction (uplink or downlink), source and destination IP address, protocol, and source and destination ports.  Depending on the direction of the flow, the IN-CSE shall configure the source and destination IP address and ports.  For example,  the IP address and port of an ADN-AE or ASN/MN-CSE hosted on a UE.  The IN-CSE shall configure the protocol based on the corresponding protocol binding used between the source and destination.

NOTE: To meet 3GPP requirements, the UE IP Address needs to be the non NAT’d IP Address and Port Number.

- Sponsor Information identifies the sponsor and shall be configured with an identifier that is prearranged between the Service Provider and MNO.

- Sponsoring Status shall be configured by the IN-CSE to start sponsoring.

- Reference ID is not used in this message

Step 4: Process Set Chargeable Party Request

The SCEF interacts with the PCRF within the 3GPP Network to determine whether to authorize the IN-CSE to start sponsoring traffic for the specified application flow(s).

Step 5: Set Chargeable Party Response

The SCEF responds to the request with a Cause value that indicates if the request was accepted and the TTRI that was provided in step 3 so that the IN-CSE can correlate the response with the original request.

Step 6: Trigger to Disable / Change sponsor

The IN-CSE may issue a request to the SCEF to notify it that the specified sponsor is no longer the chargeable party for traffic flowing to/from the UE.  For example, when an ADN-AE or ASN/MN-CSE hosted on a UE de-registers from an IN-CSE.

Alternatively, when an IP Address  of a UE changes ((e.g. and thus the PoA of an ADN-AE or ASN/MN-CSE hosted on the UE changes), the IN-CSE may issue a request to the SCEF to notify it that the current sponsor is no longer the chargeable party for traffic flowing to/from the UE and to re-configure the chargeable party.

Alternatively, based on a policy setting, the IN-CSE may issue a request to the SCEF to notify it that the current sponsor is no longer the chargeable party for traffic flowing to/from the UE.   For example, a sponsorship policy may define a maximum number of requests allowed.  If this limit is reached an IN-CSE may initiate a request to the SCEF to disable the current sponsorship.  The definition of this policy is outside the scope of the current specification.

Step 7: Monitoring Indication

The IN-CSE may determine the IP address(es)/port(s) of the proper SCEF to contact by performing a DNS query using the M2M-Ext-ID (M2M External Identifier) assigned to the target UE.  Alternatively, an IN-CSE may use a pre-configured SCEF identifier.  The method for pre-configuring a SCEF identifier into the IN-CSE is outside the scope of the present document.

Step 8: Set Chargeable Party Request

The IN-CSE sends a Set Chargeable Party Request to the SCEF.  The request contains information as specified in 3GPP TS 23.682 [2] which includes the following:

- SCS Identifier shall be set to a value that is prearranged between the Service Provider and MNO.

- TTRI is used to correlate this request with future responses. It shall be assigned based on internal IN-CSE policies.

- TLTRI shall be assigned based on internal IN-CSE policies.  The value will be used to reference the original request so that the IN-CSE knows what M2M-Ext-ID the report pertains to.

- Description of the application flows.  Each flow includes a direction (uplink or downlink), source and destination IP address, protocol, and source and destination ports.  Depending on the direction of the flow, the IN-CSE shall configure the source and destination IP address and ports. For example, with the IP address and port of an ADN-AE or ASN/MN-CSE hosted on a UE.  The IN-CSE shall configure the protocol based on the corresponding protocol binding used between the source and destination

NOTE - To meet 3GPP requirements, the UE IP Address needs to be the non NAT’d IP Address and Port Number.

- Sponsor Information identifies the sponsor and shall be configured with an identifier that is prearranged between the Service Provider and MNO.

- Sponsoring Status shall be configured by the IN-CSE to stop sponsoring.

- Reference ID is not used in this message

Step 9: Process Set Chargeable Party Request

The SCEF interacts with the PCRF within the 3GPP Network to determine whether to authorize the IN-CSE to stop sponsoring traffic for the specified application flows.

Step 10: Set Chargeable Party Response

The SCEF responds to the request with a Cause value that indicates if the request was accepted or not and the TTRI that was provided in step 8 so that the IN-CSE can correlate the response with the original request.

### -----------------------End of change 1-------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?