| CHANGE REQUEST |
| --- |
| Meeting:* | ARC TP29 |
| Source:* | BeiXu，Huawei，Echo.xubei@huawei.com |
| Date:* | 2017-04-24 |
| Contact:* | BeiXu，Huawei，Echo.xubei@huawei.com |
| Reason for Change/s:* | Add new section about 3GPP MBMS solution |
| CR against: Release* | <Release3> |
| CR against: WI* | Active <WI-0058 - 3GPP & Cellular IoT Interworking> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0026 - 3GPP_interworking-V0_3_0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The resource <schedule> updating refer to the contribution ARC-2017-0227-TS-0001-schedule_updating_for_MonitoringEvent (UE_Reachability)

### -----------------------Start of change 1-------------------------------------------

## 7.7 Group message delivery using MBMS

### 7.7.1 Overview

The Group Management (GMG) CSF is responsible for handling group related requests. The requests are sent to manage a group and its membership as well as to perform fanout operations to group member resources. When the same content is sent to the members of a group that are located in a particular geographical area, 3GPP provides MBMS capabilities that may be used to efficiently distribute the message to the group members using multicasting.

7.7.2 Resource StructureRefer to the clause 9.6.9 Resource Type <schedule>,9.6.13 Resource Type <group>  and 9.6.44 Resource Type < localMulticastGroup > of TS-0001[1].

### 7.7.3 ServiceFlow

#### 7.7.3.1 Create MBMS Group

Figure 7.7.3.1-1: Service Flow of MBMS Group Creating

Pre-conditions:

1) The MBMS service area information provided by operator is configured in the oneM2M System;

2) External Group Identifiers for the devices have been pre-provisioned in the oneM2M System.

Step 1: The IN-AE sends a <group> create request to the Group Hosting CSE.

Step 2: The Group Hosting CSE checks if the multicastCapability of more than two member Hosting CSEs are MBMS and have the same externalGroupID, then checks if the <schedule> of <group> in the request which indicates the start time and end time of group message delivery:

- if the <schedule> is not in the request, the Group hosting CSE creates the multicast group, the multicastType is 3GPP_MBMS_group;

- if the <schedule> is in the request, the Group Hosting CSE checks the <schedule> resource ACPs of  all the Member Hosting CSEs:

  - if  the Group Hosting CSE is allowed to update the <schedule> of  <node> for all the Member Hosting CSEs, the Group Hosting CSE creates the multicast group, creates the <schedule> of the <group>,and the multicastType is 3GPP_MBMS_group;

  - if the Group Hosting CSE is not allowed to update the <schedule> of <node> for all the Member Hosting CSEs, the Group Hosting CSE checks the existing <schedule>s of <node> for all the Member Hosting CSEs. If there is no time intersection of the existing <schedule>s, or the <schedule> in the request is not in the scope of the time intersection of the existing <schedule>s  of <node> for all the Member Hosting CSEs, then go to Step 3 and no multicast procedure is eligible. If the <schedule> in the request is in the scope of the time intersection of the existing  <schedule>s of  <node> for all the Member Hosting CSEs, then the Group Hosting CSE creates the multicast group, creates the <schedule> of the <group>,and the multicastType is 3GPP_MBMS_group;

Step 3: The Group Hosting CSE sends the response to the IN-AE/CSE.

Step 4: The Group Hosting CSE sends the Allocate TMGI Request to the SCEF.The request shall contain the following information as specified in 3GPP TS 23.682 [i.5].

External Group ID shall be set to the externalGroupID of Member Hosting CSEs.

TTRI is used to correlate this request with future responses. It shall be assigned based on internal Group Hosting CSE policies.

SCS Identifier shall be set to a value that is prearranged between the Service Provider and MNO.

location information (optional) shall be set to location information of Member Hosting CSEs according to the accuracy policy.

Accuracy shall be set by the Group Hosting CSE (e.g. based on a pre-provisioned policy setting)

Step 5: The Allocate TMGI is processed by the Underlying 3GPP Network based on the procedure defined in 3GPP TS 23.682 [i.5].

Step 6: The SCEF sends the Allocate TMGI Response to the Group Hosting CSE. The response shall contain the information Cause, TMGI and TMGI expiration as specified in 3GPP TS 23.682 [i.5].

Step 7: The Group Hosting CSE stores the TMGI and TMGI expiration  in the Multicast Group Information locally and sends <localMulticastGroup> creation request  to the Member Hosting CSEs via unicast which contains mandatory attributes specified in clause 9.6.44 of TS-0001[1]. If the multicastType is 3GPP_MBMS_group, the request contains the TMGI, responseTimeWindow and <schedule> if it is present in the child resource of  the <group> resource.

Step 8-9: These steps are specified in clause 10.2.7.14 Create <localMulticastGroup> of TS-0001[1].

#### 7.7.3.2 Group message delivery using MBMS

Figure 7.7.3.2-1: Service Flow of MBMS Group Message Delivery

Step 1: Before the TMGIExpiration of the multicast group, the Group Hosting CSE may send an Allocate TMGI Request to renew the expiration time for already allocated TMGIs.

Step 2-Step 3: The Allocate TMGI is processed by the Underlying 3GPP Network based on the procedure defined in 3GPP TS 23.682 [i.5].

Step 4: The SCEF sends the Allocate TMGI Response to the Group Hosting CSE. The response shall contain the information Cause, TMGI, TMGI expiration as specified in 3GPP TS 23.682 [i.5]. The Group Hosting CSE shall replace the new  TMGIExpiration in the Multicast Group Information locally.

Note: Step1- Step4 are optional if the TMGI expiration does not expire.

Step 5: If the multicastType is 3GPP_MBMS_group and <schedule> is included in the <group>, the group Hosting CSE shall send the Group Message Request to the SCEF to activate the MBMS bearer to provide MBMS communication network resources for MBMS members from the latest start time defined in the <schedule> child resource of the <group> resource. The request shall contain the following information as specified in 3GPP TS 23.682 [i.5].

External Group Identifier shall be set to the same value as the externalGroupID of Member Hosting CSEs.

SCS Identifier shall be set to a value that is prearranged between the Service Provider and MNO.

TMGI shall be set to the value assigned in the Allocate TMGI Response for the Multicast Group.

Message Delivery Start Time shall be set to the latest start time defined in the <schedule> child resource of the <group> resource.

Step 6-Step 7: The Activate MBMS Bearer Procedure is processed by the Underlying 3GPP Network based on the procedure defined in 3GPP TS 23.682 [i.5].

Step 8: The SCEF sends the Group Message Response to the Group Hosting CSE. The response shall contain the TTRI, TMGI and Acceptance Status as specified in 3GPP TS 23.682 [i.5].

Step 9: If the<schedule> is included in the < localMulticastGroup>, the Member Hosting CSEs shall listen for incoming multicast requests based on the <schedule> child resource of <localMulticastGroup> resource.

Step 10: The IN-AE/CSE sends a request carrying the group resource identifier for accessing member resources to Group Hosting CSE.

Note: This request could be sent either in the scope of the <schedule> or other time.Step 11: The Group Hosting CSE shall check if the Operation Execution Time in the scope of <schedule> of the <group> when Operation Execution Time is included in the request and <schedule> is included in the <group>. If not, the Group Hosting CSE shall return error to the IN-AE/CSE.

If the Operation Execution Time in the scope of <schedule> of the <group>, the Group Hosting CSE shall send the Group Message Request to SCEF. If the<schedule> is included in the < group>, this request should be sent in the scope of the <schedule> of the <group>.The request shall contain the following information as specified in 3GPP TS 23.682 [i.5].

External Group Identifier shall be set to the same value as the externalGroupID of the Member Hosting CSEs.,

SCS Identifier shall be set to a value that is prearranged between the Service Provider and MNO.

TLTRI is used to correlate this group message delivery request with future responses. It shall be assigned based on internal Group Hosting CSE policies.

TMGI shall be set to the value assigned in the Allocate TMGI Response. It is used to specific the MBMS bearer of network communication resource by 3GPP network to send the access member resources request from IN-AE/CSE to the MBMS group members.

Group Message Payload shall be set to the value specified in the request of access member resources from the IN-AE/CSE.

location information shall be set to location information of Member Hosting CSEs according to the accuracy policy.

Accuracy shall be set set by the Group Hosting CSE (e.g. based on a pre-provisioned policy setting)

Message Delivery Start Time shall be set to the Operation Execution Time if the<schedule> is not included in the <group> and Operation Execution Time is included in the request from IN-AE/CSE.

Step 11a-Step 12a: The Activate MBMS Bearer Procedure is processed by the Underlying 3GPP Network based on the procedure defined in 3GPP TS 23.682 [i.5].

Step 13a: The SCEF sends the Group Message Response to the Group Hosting CSE. The response shall contain the information TTRI, TMGI and Acceptance Status as specified in 3GPP TS 23.682 [i.5].

Note: Step 11a- Step 13a are optional only if the MBMS bearer activation is not performed

Step 13: The Group Message Delivery by MBMS Procedure is processed by the Underlying 3GPP Network based on the procedure defined in 3GPP TS 23.682 [i.5].

Step 14: The SCEF sends a Group Message Delivery to the Group Hosting CSE. The message shall contain the information TTRI, TLTRI, TMGI and Delivery Trigger Status as specified in 3GPP TS 23.682 [i.5].

Step 15: The Member Hosting CSE shall send the response message within the scope of responseTimeWindow. The more details are specified in clause 10.2.7.13.2 of TS-0001[1].

Step 16: The Group Hosting CSE shall receive the response messages from Member Hosting CSEs  until responseTimeWindow  expires and returns the aggregated group member resource access result to the IN-AE/CSE.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?