| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC 32 |
| Source:* | Albert Zhao, BOE, zhaojunjie111@boe.com.cn Max Zhang, BOE, zhangqiancto@boe.com.cn |
| Date:* | 2017-10-30 |
| Reason for Change/s:* | Resource table and figure are inconsistent |
| CR against: Release* | Release 3 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V2.16.0 |
| Clauses * | 9.6.39 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

After reviewing the resource type defination, there are several inconsistences between the resource type figure and resource type talbe, the detail as follows:

|  |  | Resource Type Figure | Resource Type Table | suggestion |
| --- | --- | --- | --- | --- |
| 1 | 9.6.4 Resource Type remoteCSE | has a <scheduleAnnc> sub-resource with multiplicity 0..1 | has no <scheduleAnnc> sub-resource consistent with TS-0004 | change figure |
| 2 | 9.6.8 Resource Type subscription | <notificationTargetMgmtPolicyRef> with multiplicity 0..1 <notificationTargetSelfReference> with multiplicity 0..1 | <notificationTargetMgmtPolicyRef> with multiplicity 0..n consistent with TS-0004 <notificationTargetSelfReference> with multiplicity 1 consistent with TS-0004 | change figure |
| 3 | 9.6.10 Resource Type locationPolicy | M2M-Ext-ID | authID consistent with TS-0004 | change figure |
| 4 | 9.6.20 Resource Type serviceSubscribedNode | niddRequired with multiplicity 0..1(L) | niddRequired with multiplicity 0..1 | change figure |
| 5 | 9.6.29 Resource Type serviceSubscribedAppRule | allowedAppIDs attribute allowedRoleIDs attribute | allowedApp-IDs attribute consistent with TS-0004 allowedRole-IDs attribute consistent with TS-0004 | change figure |
| 6 | 9.6.31 Resource Type notificationTargetMgmtPolicyRef | notificationTargetURI with multiplicity 1 notificationlPolicyID with multiplicity 1 | notificationTargetURI with multiplicity 1(L) consistent with TS-0004 notificationlPolicyID with multiplicity 0..1 consistent with TS-0004 | change figure |
| 7 | 9.6.33 Resource Type policyDeletionRules | deletionRules with multiplicity 1(L) | deletionRules with multiplicity 0..1(L) consistent with TS-0004 | change figure |
| 8 | 9.6.35 Resource Type flexContainer | no timeseries | timeSeries with multiplicity 0..n not update in TS-0004 | change figure |
| 9 | 9.6.39 Resource Type token | notBefore with multiplicity 0..1 consistent with TS-0004 | notBefore with multiplicity 1 | change table |

R01:refter to the above talbe,  we only resolve the table issues, since we agree to delete the figure in TS-0001 Rlease 3.

| 9 | 9.6.39 Resource Type token | notBefore with multiplicity 0..1 consistent with TS-0004 | notBefore with multiplicity 1 | change table |
| --- | --- | --- | --- | --- |

### -----------------------Start of change 9---------------------------------------------

### 9.6.39	Resource Type token

The <token> resource is used for storing a token that is issued to an AE or CSE. Details of the token may also be stored here in plaintext.

Figure 9.6.39-1: Structure of <token> resource

The <token> resource shall contain the child resources specified in table 9.6.39-1.

Table 9.6.39-1: Child resources of <token> resource

| Child Resources of <token> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |
| [variable] | <transcaction> | 0..n | See clause 9.6.48 |

The <token> resource shall contain the attributes specified in table 9.6.39-2.

Table 9.6.39-2: Attributes of <token> resource

| Attributes of <token> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. |
| resourceID | 1 | RO | See clause 9.6.1.3. |
| resourceName | 1 | WO | See clause 9.6.1.3. |
| parentID | 1 | RO | See clause 9.6.1.3. |
| expirationTime | 1 | RW | See clause 9.6.1.3. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3. |
| creationTime | 1 | RO | See clause 9.6.1.3. |
| labels | 0..1 (L) | RW | See clause 9.6.1.3. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3. |
| tokenID | 1 | WO | The identifier of the token. |
| tokenObject | 1 | WO | Used to store the token. See clause TS-0003 [2] for further details of a token. |
| version | 0..1 | WO | Version of the token. |
| issuer | 0..1 | WO | The identifier of the entity that is responsible for issuing the token to the AE or CSE. |
| audience | 0..1 (L) | WO | List of identifiers of the CSEs expected to accept the token. |
| holder | 0..1 | WO | The identifier of the AE or CSE to which the token is issued. |
| notBefore | 0..1 | WO | Start time of the token can be used for access control. |
| notAfter | 0..1 | WO | End time of the token can be used for access control. |
| tokenName | 0..1 | WO | Human readable name of the <token>.. |
| permissions | 0..1 (L) | WO | List of token permissions associated with the token. The structure of token permission is specified in the table 9.6.39-3. |
| extension | 0..1 | WO | Extension information held by the token, e.g. application-specific information. |

The structure of token permission is specified in the table 9.6.39-3.

Table 9.6.39-3: Structure of token permission

| Element | Multiplicity | Description | Note |
| --- | --- | --- | --- |
| resourceIDs | 0..1 | The resources to which this permission applies. If the privileges element is present, then this element shall be present. |  |
| privileges | 0..1 | A set of access control rules applicable to the identified resources (for the identified holder) | At least one of these must be present. |
| roleIDs | 0..1 | A set of role IDs applicable to the identified resources (for the identified holder) |  |

### -----------------------End of change 9---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?