| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#6 WG MAS |
| Title:* | OMA DM new requirements gap analysis |
| Source:* | Huawei Technologies UK (ETSI) Huawei Technologies Co., Ltd (CCSA) |
| Contact: | Jiaxin Yin, yinjiaxin@huawei.com |
| Date:* | 2013-07-26 |
| Abstract:* |  |
| Agenda Item:* | TBD |
| Work item(s): | WI0004 |
| Document(s) Impacted* | Technical Report - Study of Management Capability Enablement Technologies for Consideration by oneM2M |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text in the TR if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## *******change 1***************

## 6.1	Management related requirements gap analysis reference

Editor’s Note: The table below gives cross reference to the requirements and the technologies. The matrix represents whether or not the technology can fulfil the requirement. At the same time, in the following chapters, detailed description of the depth of how well the technology can fulfil the requirement should be shown.

Some MGR requirements (e.g., MGR-004) target functionality outside the scope of the existing technology (e.g., TR-069, OMA-DM). In those cases the analysis of the technology against the requirement determines if the the functionality that is outside the scope of the technology is allowed.

The definitions for the values in below table are:

FULL: the requirement can be fulfilled by the technology alone

PARTIAL: the requirement can be partially fulfilled by the technology

ALLOWED: Adopting this technology will allow this requirement to be implemented

NOT ALLOWED: This technology does not fulfill the requirement AND adopting this technology would not allow the requirement to be implemented

| Requirement Support |
| --- |
|  | OMA DM 1.3 | BBF TR069 | OMA DM LWM2M | OMA DM 2.0 |
| MGR-001 | Partial | Partial | Full | Partial |
| MGR-002 | Full | Full | Full | Full |
| MGR-003 | Full | Full | Full | Full |
| MGR-004 | Allowed | Allowed | Allowed | Allowed |
| MGR-005 | Partial | Partial | Partial | Partial |
| MGR-006 | Full | Full | Full | Full |
| MGR-007 | Full | Full | Full | Full |
| MGR-008 | Full | Full | Partial | Full |
| MGR-009 | Full | Full | Full | Full |
| MGR-010 | Partial | Partial | Partial | Partial |
| MGR-011 | Full | Full | Full | Full |
| MGR-012 | Full | Full | Partial | Full |
| MGR-013 | Allowed |  |  |  |
| MGR-014 | Full |  |  |  |
| MGR-015 | Full |  |  |  |
| MGR-016 | Full |  |  |  |

Table 6.1.1: Requirements fulfilment reference

## *******change 2***************

## 6.14	MGR-013

### 6.14.1	Requirement Description

The M2M System shall be able to identify and manage M2M Service status of M2M Devices. [i.23]

### 6.14.2	OMA DM 1.3

OMA DM 1.3 ALLOWS fulfilment of the requirement by development of a oneM2M Service Layer data model for management purposes.

DCMO defined in OMA DM can be used to enable or disable device capabilities, such as hardware, IO and connectivity. These capabilities correspond to the service status in the underlying network. OMA DM cannot support service status in the service layer, butallows the requirement to be fulfilled by modeling the service layer.

## 6.15	MGR-014

### 6.15.1	Requirement Description

The M2M System shall be able to retrieve events and information logged by M2M Gateways/ Devices and other devices in M2M Area Networks. [i.23]

### 6.15.2	OMA DM 1.3

OMA DM 1.3 can FULL fulfil the requirements.

Related technologies are defined in DiagMon:Trap which describes how the DM Client monitors the performance of the device. The DiagMon Client can send notification to DM Server or collect trap event together to response the retrieve request. As a result, OMA DM 1.3 can fully fulfill the requirement.

With regard to devices in the M2M Area Network, DiagMon is combined with GwMO to fulfill the requirement.

## 6.16	MGR-015

### 6.16.1	Requirement Description

The M2M System shall be able to support firmware management (e.g. update) of M2M Gateways/ Devices and other devices in M2M Area Networks.. [i.23]

### 6.16.2	OMA DM 1.3

OMA DM 1.3 can FULLY fulfil the requirement.

It is defined in FUMO about how to support firmware management. FUMO defined in OMA DM can be used to initiate firmware update, exchange device information, download update package, install update package, notify firmware update.

With regard to devices in the M2M Area Network, FUMO is combined with GwMO to fulfill the requirement.

## 6.17	MGR-016

### 6.17.1	Requirement Description

The M2M System shall be able to retrieve information related to the Static and Dynamic Device/Gateway Context for M2M Gateways/Devices as well as Device Context for other devices in M2M Area Networks. [i.23]

### 6.17.2	OMA DM 1.3

OMA DM 1.3 can FULLY fulfil the requirement.

DiagMon defined by OMA DM 1.3 enable the DM Server to acquire information related to the devices local context including battery level, available memory as well as some network capabilities.

DiagMon also defines Trap method which can be used to collect events related to the change of dynamic context in the device. The collected events can be retrieved by the DM Server.

ClientAPI defined in OMA DM 1.3 also provides interfaces that can be used to retrieve MO information from DM Client which can be static device context.