| INPUT CONTRIBUTION |
| --- |
| Group Name:* | MAS WG |
| Title:* | LWM2M Gap Analysis for Additional Requirements |
| Source:* | LG Electronics |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2013-07-29 |
| Abstract:* | The contribution provides gap analysis of OMA DM LWM2M and additional management requirement from requirement TS. |
| Agenda Item:* | TBD |
| Work item(s): | WI0004 |
| Document(s) Impacted* | Technical Report - Study of Management Capability Enablement Technologies for Consideration by oneM2M |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text in TR0006 if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

====================== 1st Change========================

## 6.1	Management related requirements gap analysis reference

Editor’s Note: The table below gives cross reference to the requirements and the technologies. The matrix represents whether or not the technology can fulfil the requirement. At the same time, in the following chapters, detailed description of the depth of how well the technology can fulfil the requirement should be shown.

Some MGR requirements (e.g., MGR-004) target functionality outside the scope of the existing technology (e.g., TR-069, OMA-DM). In those cases the analysis of the technology against the requirement determines if the the functionality that is outside the scope of the technology is allowed.

The definitions for the values in below table are:

FULL: the requirement can be fulfilled by the technology alone

PARTIAL: the requirement can be partially fulfilled by the technology

ALLOWED: Adopting this technology will allow this requirement to be implemented

NOT ALLOWED: This technology does not fulfill the requirement AND adopting this technology would not allow the requirement to be implemented

| Requirement Support |
| --- |
|  | OMA DM 1.3 | BBF TR069 | OMA DM LWM2M | OMA DM 2.0 |
| MGR-001 | Partial | Partial | Full | Partial |
| MGR-002 | Full | Full | Full | Full |
| MGR-003 | Full | Full | Full | Full |
| MGR-004 | Allowed | Allowed | Allowed | Allowed |
| MGR-005 | Partial | Partial | Partial | Partial |
| MGR-006 | Full | Full | Full | Full |
| MGR-007 | Full | Full | Full | Full |
| MGR-008 | Full | Full | Partial | Full |
| MGR-009 | Full | Full | Full | Full |
| MGR-010 | Partial | Partial | Partial | Partial |
| MGR-011 | Full | Full | Full | Full |
| MGR-012 | Full | Full | Partial | Full |
| MGR-013 |  |  | Allowed |  |
| MGR-014 |  |  | Full |  |
| MGR-015 |  |  | Full |  |
| MGR-016 |  |  | Full |  |

Table 6.1.1: Requirements fulfilment reference

====================== 2nd Change========================

## 6.14	MGR-013

### 6.14.1	Requirement Description

The M2M System shall be able to identify and manage M2M Service status of M2M Devices. [i.23]

### 6.14.4	OMA DM LWM2M

OMA DM LWM2M is ALLOWED to support the requirement.

LWM2M has capability to disconnect underlying network but LWM2M cannot support service status in the service layer. As a result, LWM2M is allowed to fulfill the requirement.

## 6.15	MGR-014

### 6.15.1	Requirement Description

The M2M System shall be able to retrieve events and information logged by M2M Gateways/ Devices and other devices in M2M Area Networks. [i.23]

### 6.15.4	OMA DM LWM2M

OMA DM LWM2M is FULLY support the requirement.

## The LWM2M Client has capability to collect error or event information such as GPS module failure, out of memory, SMS failure, and low battery power. The LWM2M has functionality to collect data to be notified due to subscription when the LWM2M Client is offline or the LWM2M Server is temporarily disabled.6.16	MGR-015

### 6.16.1	Requirement Description

The M2M System shall be able to support firmware management (e.g. update) of M2M Gateways/ Devices and other devices in M2M Area Networks.. [i.23]

### 6.16.4	OMA DM LWM2M

OMA DM LWM2M is FULLY support the requirement.

LWM2M has Firmware Object to update firmware of the LWM2M Client. LWM2M supports two download mechanisms: directly write firmware package, and give URI and let the LWM2M Client download firmware package. After updating firmware, LWM2M has capability to inform the connected LWM2M Servers of what functionalities are added in the LWM2M Client.

## 6.17	MGR-016

### 6.17.1	Requirement Description

The M2M System shall be able to retrieve information related to the Static and Dynamic Device/Gateway Context for M2M Gateways/Devices as well as Device Context for other devices in M2M Area Networks. [i.23]

### 6.17.4	OMA DM LWM2M

OMA DM LWM2M is FULLY support the requirement.

LWM2M has Static Context such as manufacturer, model number, and serial number, and Dynamic Context such as battery level, memory free, location, time, IP address, current network (e.g., WCDMA, GSM, LTE, Bluetooth, WiFi), and serving cell id. LWM2M has capability to expose parent IP address, which can make topology of M2M Area Network.