| INPUT CONTRIBUTION |
| --- |
| Group Name:* | MAS WG |
| Title:* | TR-069 Gap Analysis for Additional Requirements from TP6 |
| Source:* | Timothy Carey, Alcatel-lucent, timothy.carey@alcatel-lucent.com |
| Contact: | Timothy Carey, Alcatel-lucent, timothy.carey@alcatel-lucent.com |
| Date:* | 2013-08-29 |
| Abstract:* | The contribution provides gap analysis of TR-069 and additional management requirement from requirement TS from TP6. |
| Agenda Item:* | TBD |
| Work item(s): | WI0004 |
| Document(s) Impacted* | Technical Report - Study of Management Capability Enablement Technologies for Consideration by oneM2M |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text in TR0006 if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

====================== 1st Change========================

## 6.1 	Management related requirements gap analysis reference

Editor’s Note: The table below gives cross reference to the requirements and the technologies. The matrix represents whether or not the technology can fulfil the requirement. At the same time, in the following chapters, detailed description of the depth of how well the technology can fulfil the requirement should be shown.

Some MGR requirements (e.g., MGR-004) target functionality outside the scope of the existing technology (e.g., TR-069, OMA-DM). In those cases the analysis of the technology against the requirement determines if the the functionality that is outside the scope of the technology is allowed.

The definitions for the values in below table are:

FULL: the requirement can be fulfilled by the technology alone

PARTIAL: the requirement can be partially fulfilled by the technology

ALLOWED: Adopting this technology will allow this requirement to be implemented

NOT SUPPORTED: This technology does not fulfill the requirement AND adopting this technology would not allow the requirement to be implemented

| Requirement Support |
| --- |
|  | OMA DM 1.3 | BBF TR069 | OMA DM LWM2M | OMA DM 2.0 |
| MGR-001 | Partial | Partial | Full | Partial |
| MGR-002 | Full | Full | Full | Full |
| MGR-003 | Full | Full | Full | Full |
| MGR-004 | Allowed | Allowed | Allowed | Allowed |
| MGR-005 | Partial | Partial | Partial | Partial |
| MGR-006 | Full | Full | Full | Full |
| MGR-007 | Full | Full | Full | Full |
| MGR-008 | Full | Full | Partial | Full |
| MGR-009 | Full | Full | Full | Full |
| MGR-010 | Partial | Partial | Partial | Partial |
| MGR-011 | Full | Full | Full | Full |
| MGR-012 | Full | Full | Partial | Full |
| MGR-013 | Allowed | Allowed | Allowed | Allowed |
| MGR-014 | Full | Full | Full | Full |
| MGR-015 | Full | Full | Full | Full |
| MGR-016 | Full | Full | Full | Full |
| MGR-017 |  | Not Supported |  |  |

====================== 2nd Change========================

## 6.18	MGR-017

### 6.18.1	Requirement Description

The M2M system shall support the capability to map M2M service subscription role(s) to roles used within technology specific Device Management protocols. [i.23]

6.18.3	TR-069

This requirement is not NOT SUPPORTED by the TR-069 family of specifications.

The TR-069 family of specifications does provide security capabilities (ACLs) within the CPE to ensure authorized parties are permitted access control of an Object. However this ACL mechanism doesn’t discern different management roles within the ACS. The ACL mechanism in the CPE treats the ACS as the one authorized party. In addition, a CPE can only report to one ACS at a time. As such, the TR-069 ACS mechanism does not provide security authorization of resources to various roles within the ACS as expectation is, since a CPE can only be managed by 1 ACS, that this function is the responsibility of the ACS.

Likewise the ACL capability, while specified, isn’t widely supported in CPEs. In fact the BBF certification program does not include ACLs in its current certifications suite of tests.

Also the TR-069 family of specifications does not specify an interface northbound of the ACS except that TR-131 [i.32] does provide guidance to northbound systems such as M2M systems. If an interface with associated Service Layer to Device Management Layer security mechanisms are required, the expectation would be that oneM2M would either specify an interface between the ACS or work collaboratively with the Broadband Forum to specify a northbound interface from an ACS for the purposes of M2M Service Layer interaction.

====================== 3rd Change========================

## 2.2	Informative references

[i.32]	BBF TR-131 ACS Northbound Interface Requirements, Issue:1, November 2009