| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG5 |
| Title:* | DM Management Resource Lifecycle |
| Source:* | Tim Carey, Alcatel-Lucent, timothy.carey@alcatel-lucent.com |
| Contact: | Tim Carey, Alcatel-Lucent, timothy.carey@alcatel-lucent.com |
| Date:* | 2013-09-39 |
| Abstract:* | Detail Description of the Lifecycle of a Device Management Resource. |
| Agenda Item:* |  |
| Work item(s): | Architecture TS |
| Document(s) Impacted* | Architecture TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to request Architecture to include in the Functional Architecture TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

##### 6.2.4.x	Device Management Resource Lifecycle

##### 6.2.4.x.1	Overview

The lifecycle of a Management Resource is implemented using the resource management defined in Section 9. In addition a Management Resource maintains information and relationships that are specific Management Resources. This information is used to:

- Manage the technology specific objects via a Device Management Server which requires the information necessary identify and access the Device Management Server.

- Invoke the security mechanism of the Device Management Server in order to authorize access to the technology specific objects.

##### 6.2.4.x.2	Creation, Update and Deletion of Device Management Resources

Management Resources are either created, updated or deleted:

- By administrative means using the X reference point

- Directly by a CSE based on a discovery or another event within the CSE

- Indirectly by the Device Management Server or Device Management Client when an event (firmware update, fault notification) occurs within the Device Management Server or Client

Regardless of the Create, Update or Delete operation, the issuer of the operation shall be authorized to perform the operation. In addition, at most one Device Management Server shall be able to Create, Delete or Update addressible elements of a Management Resource.