| CHANGE REQUEST |
| --- |
| Group Name:* | WG5 (MAS) |
| Source:* | Ericsson |
| Format:* | TP #10 Face-to-Face Meeting |
| Date:* | 2014-04-01 |
| Contact:* | Shelby Kiewel (skiewel@iconectiv.com) |
| Reason for Change/s:* |  |
| CR against: Release* | 1.0 |
| CR against: TS/TR* | oneM2M-TS 0001 Technical Architecture v 0.4.2 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

When the Application ID (App-ID) was approved as a part of the the TS-0001 document, it was noted that further clarity was needed as to the structure of this identifier.

This contribution/suggested change is to provide a level of structure to this identifier for release 1, allowing for further development and detail shortly after release 1.

In change noted below, additional text is provided to establish more structure to the Application Identifier.  This will provide greater clarity in release 1 as to what this identifier was established to designate.

### ----------------------- Start of change 1 -----------------------

### 7.1.3	Application Identifier (App-ID)

This is equivalent to the application name and is not guaranteed to be globally unique on its own.

This identifier is to be supported via a single or multiple registries.

Editor's Note:  Who assigns the App-ID is FFS.  Detailed format and structure of the value(s) is FFS.

For discussion, an example semantic structure of this identifier could contain values such as:

- By Registrar (e.g. ABC, FYX)

  - Where ABC is known as ‘registar #1’

  - Where FYX is known as ‘registar #2’

- By vertical (e.g. XB5 = transportation)

- By functional grouping (e.g. where rail, sea, land, road, etc associate to another set of characters )

- By function (e.g. speed)

  - Sub-function (e.g. static, dynamic, real-time)

  - Additional sub-functions possible, but not required

  - Maximum 3 sub-functions per function

- By version (e.g. aaa)

### ----------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?