| CHANGE REQUEST |
| --- |
| Group Name:* | MAS#10 |
| Source:* | Thierry GARNIER, Gemalto N.V, thierry.garnier@gemalto.com Seongyoon Kim, LG Electronics, Seongyoon.kim@lge.com |
| Format:* | Plenary |
| Date:* | 2014-4-01 |
| Contact:* | Thierry GARNIER, Gemalto N.V, thierry.garnier@gemalto.com |
| Reason for Change/s:* | This contribution is to provide the mapping for OMA LWM2M regarding of data types and identifiers. |
| CR against: Release* | Release1 |
| CR against: TS/TR* | TS-0005, Management Enablement (OMA) ver 0.0.1 |
| Clauses/Sub Clauses* | 6 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution is to provide the texts regarding the general mapping described in the section 6.

### -----------------------Start of change 1-------------------------------------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M TS-0001: “oneM2M Functional Architecture”

[6]	"OMA LightweightM2M”, Version 1.0, Open Mobile Alliance™, http://www.openmobilealliance.org/

# 6. OMA  Lightweight M2M 1.0

## 6.1	Mapping of basic data types

oneM2M has defined the data types that describe the format of the value stored at the attribute. Those oneM2M data types are listed in the below table, and mapped to the data types specified by OMA Lightweight M2M 1.0 (shortened in LWM2M)

| oneM2M Data Types | description | Mapping to data types in OMA LWM2M |
| --- | --- | --- |
| TBD |  | Boolean |
| TBD |  | Float |
| TBD |  | Integer |
| TBD |  | Opaque |
| TBD |  | String |
| TBD |  | Time |

## 6.2	Mapping of Identifiers

| The LWM2M 1.0 enabler defines specific identifiers for entities (e.g. End Point Client Name, Server Identifier, Objects identifiers ..) To enable the device management using OMA LWM2M enabler, oneM2M identifiers needs to be mapped to identifiers specified by OMA LWM2M [6]. Below table shows the oneM2M identifiers that needs to be mapped to OMA LWM2M identifiers: oneM2M | Mapping to LWM2M Identifiers | Description |
| --- | --- | --- |
| M2M-Node-ID. | Endpoint Client Name | A unique identifier for the device. This value is globally unique and MUST be formatted as a URN. |
| The objectID attribute in <mgmtObj> resource. | Object ID | A unique identifier of Object. Each Object is characterized by a unique Object, which is represented as an integer. and the registered URN : urn:oma:lwm2m:oma:{Object ID} |
| URI as specified in the section 9.3. | URI | Each Object, Object Instance, Resource or Resource Instance is uniquely addressed by a URI. |

## 6.3	Mapping of resources

This section describes how to map the <mgmtObj> resources specified in the Annex D of [1] to the relevant Objects specified  in OMA LWM2M [6] enabler.

## 6.3.1 General Mapping Assumptions

OMA LWM2M Enabler implements the functionalities of the device management and M2M service enablement as  Objects.  An Object is a collection of resources which are related to a specific management functionality. For example the Firmware Update Object contains all the Resources used for firmware update purpose. Before to be able of  fulfilling its role, an Object shall be firstly instantiated into an Object Instance. Since oneM2M <mgmtObj> Resources are for providing specific management functionalities, oneM2M <mgmtObj> Resources shall be mapped to Object Instances specified by OMA LWM2M [6]. The attributes of a oneM2M <mgmtObj> Resource shall be mapped to the resources of the  associated LWM2M Object Instance.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?