| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG#5 |
| Title:* | mgmtCmd input for TS-0006-Management Enablement (BBF)-V0_2_0 |
| Source:* | InterDigital Communications |
| Contact: | Catalina.Mladin@InterDigital.com Chonggang.Wang@InterDigital.com |
| Date:* | 2014-05-25 |
| Abstract:* | mgmtCmd inputs to TS-0006 |
| Agenda Item:* | xxx |
| Work item(s): | MAS BBF TS |
| Document(s) Impacted* | TS-0006 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 1	Introduction

This contribution proposes TS-0006 text for mgmtCmd use for BBF management procedures. The R02 proposal includes

- In chapter 7: a few editorial updates, along with a sections on mgmtCmd and execInstance resources

- Section 8.3  is new text linking mgmtCmd  and execInstance primitives mapping

The changes are proposed such that there is less duplication and easier mapping between management procedures and primitives. For example,  a software installation procedure is described using the relevant BBF RPCs in section 8.10. Sections 9.1.3.6 and  9 show how <mgmtObj> and <mgmtCmd> primitives, respectively, can be mapped to perform such software installation procedures.

Major changes to MAS-2014-0400R03:

- Updated resource mapping for mgmtCmd and execInstance.

- Removed “Create <mgmtCmd>” and “Retrieve <mgmtCmd>” since both have no mapping to BBF.

- Removed “Retrieve <execInstance>” since it has no mapping to BBF.

### -----------------------Start of proposed text 1 -------------------------------------------

# 7	Mapping of resources

This clause contains all information on how to map management resources to  managed objects and parameters as defined in the TR-181 [6] data model or the Remote Procedure Calls (RPCs) in TR-069 [4].

Editors Note: Resource attributes need to be rechecked to ensure all attribles of the mgmtObj management resources are in the mapping tables (e.g., DeviceInfo:deviceId).

## 7.1	General mapping assumptions

TR-069 [4] specifies a protocol for communication between a CPE (Customer Premises Equipment) and an ACS (Auto-Configuration Server).  Any TR-069 enabled device has to follow the data model as described in the TR-106 [5] and TR-181 [6] as well as RPCs described in TR-069 [4].

As TR-181 [6] is the model that the Resources are mapped, all Resources shall have the objectId of the TR-181[6] namespace (e.g., "urn:broadband-forum-org:TR-181-2-7-0”).

## 7.2	Resource deviceInfo

The Resource deviceInfo is a read-only Resource that shall map to the Device.DeviceInfo object of TR-181 [6].

The information shall be retrieved using the GetParameterValues RPC of TR-069 [4].

| Attribute Name of deviceInfo | TR-181 Parameter |
| --- | --- |
| deviceLabel | Device.DeviceInfo.Description |
| Manufacturer | Device.DeviceInfo.Manufacturer |
| model | Device.DeviceInfo.ModelNumber |
| deviceType | Device.DeviceInfo.ProductClass |
| fwVersion | Device.DeviceInfo.SoftwareVersion if the device supports only 1 software version. If the device support multiple software versions this would map to Device.DeviceInfo.AdditionalSoftwareVersion |
| swVersion | Device.DeviceInfo.SoftwareVersion |
| hwVersion | Device.DeviceInfo.HardwareVersion |

## 7.3	Resource memory

The Resource memory is a read-only Resource that shall map to the Device.DeviceInfo.MemoryStatus object of TR-181 [6].

The information shall be retrieved using the GetParameterValues RPC of TR-069 [4].

Attempts to modify the attributes of the memory Resource causes an error code “operation unsupported” to be returned.

| Attribute Name of memory | TR-181 Parameter |
| --- | --- |
| memAvailable | Device.DeviceInfo.MemoryStatus.Free |
| memTotal | Device.DeviceInfo.MemoryStatus.Total |

## 7.4	Resource battery

The Resource battery  is a read-only Resource that shall map to an instance of Device.DeviceInfo.X_oneM2M_BatteryStatus.Battery.{i} object.

The information shall be retrieved using the GetParameterValues RPC of TR-069 [4].

| Attribute Name of battery | TR-181 Parameter |
| --- | --- |
| batteryLevel | Device.DeviceInfo.X_oneM2M_BatteryStatus.Battery.{i}.Level |
| batteryStatus | Device.DeviceInfo.X_oneM2M_BatteryStatus.Battery.{i}.Status |

## 7.5	Resource areaNwkInfo

The Resource areaNwkInfo is a multi-instance Resource where each instance of the Resource shall map to an instance of Device.X_oneM2M_CSE.{i}.M2MAreaNetwork.{i} object.

As the areaNwkInfo Resource is a multi-instance Resource, the M2MAreaNetwork object is an multi-object instance that can be created and deleted.

The M2MAreaNetwork instance shall be created  using the Add Object RPC of TR-069 [4].

The M2MAreaNetwork instance shall be deleted  using the Delete Object RPC of TR-069 [4].

The information of a M2MAreaNetwork shall be retrieved using the GetParameterValues RPC of TR-069 [4].

The information of a M2MAreaNetwork shall be modified using the SetParameterValues RPC of TR-069 [4].

| Attribute Name of areaNwkInfo | X_oneM2M Parameter |
| --- | --- |
| areaNwkType | Device.X_oneM2M_CSE.{i}.M2MAreaNetwork.{i}.Type |
| listOfDevices | Device.X_oneM2M_CSE.{i}.M2MAreaNetwork.{i}.ListOfDevices |

## 7.6	Resource areaNwkDeviceInfo

The Resource areaNwkDeviceInfo is a multi-instance Resource where each instance of the Resource shall map to an instance of Device.X_oneM2M_CSE.{i}.AreaNetworkDevice.{i} object.

As the areaNwkDeviceInfo Resource is a multi-instance Resource, the AreaNetworkDevice object is an multi-object instance that can be created and deleted.

Instances of the areaNwkDeviceInfo Resource is referenced in the listOfDevices attribute of the associated AreaNwkInfo Resource.

The M2MAreaNetworkDevice instance shall be created  using the Add Object RPC of TR-069 [4].

The M2MAreaNetworkDevice instance shall be deleted  using the Delete Object RPC of TR-069 [4].

The information of a M2MAreaNetworkDevice shall be retrieved using the GetParameterValues RPC of TR-069 [4].

The information of a M2MAreaNetworkDevice shall be modified using the SetParameterValues RPC of TR-069 [4].

| Attribute Name of areaNwkDeviceInfo | X_oneM2M Parameter |
| --- | --- |
| devId | Device.X_oneM2M_CSE.{i}.M2MAreaNetworkDevice.{i}.Host |
| devType | Device.X_oneM2M_CSE.{i}.M2MAreaNetworkDevice.{i}.Type |
| areaNwkId | Reference to Device.X_oneM2M_CSE.{i}.M2MAreaNetworkDevice.{i}.M2MAreaNetwork |
| sleepInterval | Device.X_oneM2M_CSE.{i}.M2MAreaNetworkDevice.{i}.SleepInterval |
| sleepDuration | Device.X_oneM2M_CSE.{i}.M2MAreaNetworkDevice.{i}.SleepDuration |
| status | Device.X_oneM2M_CSE.{i}.M2MAreaNetworkDevice.{i}.Status |
| listOfNeighbors | Device.X_oneM2M_CSE.{i}.M2MAreaNetworkDevice.{i}.Neighbors |

## 7.7	Resource eventLog

The Resource eventLog is a multi-instance Resource where each instance of the Resource shall map to an instance of Device.DeviceInfo.VendorLogFile.{i} object.

While the eventLog Resource is a multi-instance Resource, the VendorLogFile is a read-only object where only the CPE is able to create and delete instances of the VendorLogFile.

The contents of a VendorLogFile instance shall be retrieved using the Upload RPC of TR-069 [4].

The VendorLogFile.Name parameter does not support the capability to set the name. Attempts to modify the TypeId attribute of the eventLog Resource causes an error code “operation unsupported” to be returned.

The VendorLogFile object instance does not support action capabilities to start or stop the log. As such, the following mappings are used:

logStart: The value shall be set to “True” when the Resource is created. An error code “unsupported value” shall be returned for an attempt to set the values of logStart attribute to any other value.

logStop: When set to “True” the CSE shall initiate the “Upload” operation where the results of the VendorLogFile are placed in the logData attribute. When the logStop attribute is set to “True”, the CSE shall initiate the “Upload” operation where the results of the Upload operation are placed in the logData attribute.  Once the logStop attribute is set to “True” it cannot be set to “False”. An attempt to set the logStop attribute to “False” once it has been set to “True” shall result in an  error code “operation unsupported” to be returned.

logActionStatus: The value shall be set to “Started” when the Resource is created and shall be set to “Stopped” when the logStop is set to “True”

| Attribute Name of eventLog | TR-181 Parameter |
| --- | --- |
| logTypeId | Device.DeviceInfo.VendorLogFile.{i}.Name |
| logData | Upload RPC using the Device.DeviceInfo.VendorLogFile.{i} as the FileType. Results are placed in this attribute. |
| logActionStatus | Always returns the value of “Started” upon creation and the value “Stopped” upon a success transfer of the VendorLogFile.{i} Instance. |
| logStart | Set to “True” upon creation of the Resource. |
| logStop | Invoke the Upload RPC when set to “True”. |

RPC Upload Argument

URL: URL of the Server that M2M Node uses to uplod the event log in order to retrieve the contents of the eventLog.

FileType: “4 Vendor Log File <i>”

Username: Username credential of the Server that the M2M Node uses to receive the event log.

Password: Password credential of the Server that the M2M Node uses to receive the event log.

CommandKey: Automatically set by the M2M node in order to correlate the TransferComplete response.

DelaySeconds: 0 (immediate)

## 7.8	Resource deviceCapability

The deviceCapability Resource represents a capabilility of device that can be administratively enabled or disabled. The list of capabilities that are managed are defined in the enumeration of the capabilityName attribute.  The TR-181 [6] data model defines a subset of capabilities listed in the deviceCapability enumeration. The supported device capabilities within TR-181 [6] include:

LAN Interfaces: USB, Wi-Fi, HomePlug, MoCA, UPA

Hardware Capabilities: SmartCardReader

The information shall be retrieved using the GetParameterValues RPC of TR-069 [4].

The capabilities shall be enabled and disabled using the SetParameterValues RPC of TR-069 [4].

| Attribute Name of capabilityInstance | TR-181 Parameter |
| --- | --- |
| capabilityName | This attribute is fixed based on the value of the capablityName attribute. |
| attached | Returns “True” |
| capabilityActionStatus | No direct mapping exists. The progress indicator of the capabilityActionStatus is set to 0% as soon as the request to enable or disable the capability is performed by the M2M Service Layer. After completion of the request, the progress indicator is set to 100%. |
| enable | USB: Device.USB.Interface.(i).Enable WiFi: Device.WiFi.Radio.{i}.Enable HomePlug: Device.HomePlug.Interface.{i}.Enable MoCA: Device.MoCA.Interface.{i}.Enable UPA: Device.UPA.Interface.{i}.Enable SmartCardReader: Device.SmartCardReaders.SmartCardReader.{i}.Enable |
| disable | Same parameter is used to disable a capability as the enable attribute. |

## 7.9	Resource firmware

The firmware Resource represents a firmware instance and  is not considered a TR-069 managed entity within the device until the the firmware Resource’s update attribute has been written a value of “True”. When this occurs, the TR-069 Download RPC shall be invoked.

Note: In many instances, the server from which the firmware is downloaded requires authentication in the form of Username and Password credentials. The CSE that executes firmware download shall maintain the a mapping of the username and password of the download server needed to download the firmware outside the lifecycle of the specific firmware

| Attribute Name of firmware | RPC Download Arguments |
| --- | --- |
| URL | URL |
| update | When set to the value of “True” executes the Download operations with a FileType “1 Firmware Upgrade Image” is performed. |
|  | Username: Received from the CSE for the download server where the update is set to “True”. |
|  | Password: Received from the CSE for the download server where the update is set to “True”. |
|  | CommandKey: Automatically set by the CSE where the update is set to “True” in order to correlate the TransferComplete response. |
|  | FileSize: 0 (not used) |
|  | TargetFileName: <empty> (not used) |
|  | DelaySeconds: 0 (immediate) |
|  | SuccessURL: <empty> (not used) |
|  | FailureURL: <empty> (not used) |

## 7.10	Resource software

The Resource software is a multi-instance Resource where each instance of the Resource maps directly to an instance of Device.SoftwareModules.DeploymentUnit.{i} object for the deployment aspects (install, remove) of the software Resource.  The install and uninstall operation of software Resource is performed using a combination of the ChangeDUState and ChangeDUStateComplete RPCs.

Once a software Resource has been installed, the Resource shall be mapped to the associated Device.SoftwareModules.ExecutionUnit.{i} objects in order to activate and deactivate the associated execution unit.

The software Resource version and name shall be retrieved using the GetParameterValues RPC of TR-069 [4].

The activate and deactive operations of the software Resource shall be performed by manipulating the Device.SoftwareModules.ExecutionUnit.{i}.RequestedState parameter using the SetParameterValues RPC.

| Attribute Name of software | Description |
| --- | --- |
| version | Device.SoftwareModules.DeploymentUnit.{i.Version |
| name | Device.SoftwareModules.DeploymentUnit.{i}.Name |
| URL | Device.SoftwareModules.DeploymentUnit.{i}.URL |
| install | Use the ChangeDUState:InstallOpStruct |
| installStatus | Status is defined as 0% if the install operation has not been initiated or has failed. If the install operation has completed successfully, the value of 100% is used in indicate a successful completion of the installation. |
| activate | The action that activates software previously installed. |
| deactivate | The action that deactivates software. |
| activeStatus | Status is defined as 0% if the last operation has not been has failed or a new operation has been initiaited. If the current operation has completed successfully, the value of 100% is used in indicate a successful completion of the operation. |

RPC ChangeDUState:InstallOpStruct Argument

URL: URL of the Server that M2M Node uses to download the DU.

Username: Username credential of Server that the CPE uses to download the DU – Supplied by the CSE.

Password: Password credential of Server that the CPE uses to download the DU – Supplied by the CSE.

UUID: Supplied by the CSE and used to correlate the DU for the uninstall operation.

ExecurtionEnvRef: <empty> not used

RPC ChangeDUState:Uninstall OpStruct Argument

UUID: UUID of the DU that was installed – Maintained by the CSE.

ExecutionEnvRef: <empty> not used

## 7.11	Resource reboot

The Resource reboot maps to either the Reboot RPC or FactoryReset RPC of TR-069 [4].

When the reboot attribute of the reboot Resource is set to “True”, the CSE shall execute the Reboot RPC of TR-069[4].

When the factoryReset attribute of reboot Resource is set to “True”, the CSE shall execute the FactoryReset RPC of TR-069[4].

| Attribute Name of reboot | Description |
| --- | --- |
| reboot | Executes the Reboot RPC |
| factoryReset | FactoryReset RPC |

RPC Reboot Arguments

CommandKey: Automatically set by the CSE where the reboot is set to “True” in order to correlate the “M-Reboot” Event from the next Inform.

## 7.12	Resource mgmtCmd

Each mgmtCmd Resource shall map to BBF TR-069 RPC commands based on the value of cmdType. Accordingly, execReqArgs shall contain arguments related to the corresponding BBF TR-069 RPCs. The details about corresponding procedure mapping are described in section 8.3.

| Attribute cmdType of mgmtCmd | Attribute execReqArgs of mgmtCmd |
| --- | --- |
| cmdType = RESET | Shall include all arguments related to BBF FactoryReset RPC |
| cmdType = REBOOT | Shall include all arguments related to BBF Reboot RPC |
| cmdType = UPLOAD | Shall include all arguments related to BBF Reboot RPC |
| cmdType = DOWNLOAD | Shall contain all arguments related to BBF Reboot RPC |
| cmdType = SOFTWAREINSTALL | Shall contain all arguments related to BBF ChangeDUState RPC which shall contain “InstallOpStruct” structure. |
| cmdType = SOFTWAREUNINSTALL | Shall contain all arguments related to BBF ChangeDUState RPC which shall contain “UninstallOpStruct” structure. |

## 7.13 Resource execInstance

The execInstance Resource shall map to BBF Cancel RPC commands when it is disabled/cancelled using a Update operation or deleted using a Delete operation. The details are described in section 8.3.

### ----------------------- End of proposed text 1 -------------------------------------------

### ----------------------- Start of proposed text 2 -------------------------------------------

## 8.3	MgmtCmd and ExecInstance primitive mappings

Editors Note: Need to flesh out the error codes for procedures.

### 8.3.1 Update (Execute) <mgmtCmd>

When the Update primitive for <mgmtCmd> addresses the execEnable attribute of the <mgmtCmd> , it effectively triggers an Execute <mgmtCmd> procedure. This in turn triggers the BBF RPC procedures represented by the <execInstance> sub-resources to be started.

The Hosting CSE performs command coversion of its  <execInstance> sub-resources. The mapping between the <execInstance> parameters and the RPC procedures triggered is based on the value of the  cmdType as described in TS-004 and is detailed in Table 8.3.1.-1

Table 8.3.1.-1 Mapping of Execute <mgmtCmd> primitives to BBF TR-069 RPC

| cmdType value | BBF TR-069 RPCs |
| --- | --- |
| “DOWNLOAD” | Download RPC (see section 8.3.1.1) and TransferComplete RPC (section 8.3.1.3) |
| “UPLOAD” | Upload RPC (section 8.3.1.2) and TransferComplete RPC (section 8.3.1.3) |
| “SOFTWAREINSTALL” | ChangeDUState RPC (section 8.3.1.4) and ChangeDUStateComplete RPC (section 8.3.1.5) |
| “SOFTWAREUNINSTALL” | ChangeDUState RPC (section 8.3.1.4) and ChangeDUStateComplete RPC (section 8.3.1.5) |
| “REBOOT” | Reboot RPC (section 8.3.1.6) |
| “RESET” | Factory reset RPC (section 8.3.1.7) |

#### 8.3.1.1	Execute File Download

The download file transfer operation may use the Download mechanism defined in TR-069 [4]. The Download mechanism is an asynchronous command which returns a successful response or one of the following fault codes in Table 8.3.5.1-1. A successful response means that the CPE has accepted the Download RPC.

Table 8.3.5.1-1: Download Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9000 | Method not supported |  |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9003 | Invalid arguments |  |
| 9004 | Resources exceeded (when used in association with SetParameterValues, this MUST NOT be used to indicate Parameters in error) |  |
| 9010 | File transfer failure (associated with Download, ScheduleDownload, TransferComplete or AutonomousTransferComplete methods). |  |
| 9012 | File transfer server authentication failure (associated with Upload, Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods, not associated with Scheduled Download method). |  |
| 9013 | Unsupported protocol for file transfer (associated with Upload, Download, ScheduleDownload, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |

#### 8.3.1.2 Execute File Upload Operations

The upload file transfer operation shall use the Upload mechanism defined in TR-069 [4]. The Upload mechanism is an asynchronous command that consists of the synchronous Upload RPC for the Upload and the asynchronous TransferComplete RPC.  The Upload RPC returns a successful response or one of the following fault codes in Table 8.3.5.2-1. A successful response means that the CPE has accepted the Upload RPC.

Table 8.3.5.2-1: Upload Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9000 | Method not supported |  |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9003 | Invalid arguments |  |
| 9004 | Resources exceeded (when used in association with SetParameterValues, this MUST NOT be used to indicate Parameters in error) |  |
| 9011 | Upload failure (associated with Upload, TransferComplete or AutonomousTransferComplete methods). |  |
| 9012 | File transfer server authentication failure (associated with Upload, Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9013 | Unsupported protocol for file transfer (associated with Upload, Download, ScheduleDownload, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |

#### 8.3.1.3	Report Results using TransferComplete RPC

After a File Download or Upload has been attempted,  the result of the operation is reported using the TransferComplete RPC. The TransferComplete RPC indicates a successful operation or one of the following fault codes in Table 8.3.5.3-2.

Table 8.3.5.3-2: TransferComplete Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9010 | File transfer failure (associated with Download, ScheduleDownload, TransferComplete or AutonomousTransferComplete methods). |  |
| 9011 | Upload failure (associated with Upload, TransferComplete or AutonomousTransferComplete methods). |  |
| 9012 | File transfer server authentication failure (associated with Upload, Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9014 | File transfer failure: unable to join multicast group (associated with Download, TransferComplete or AutonomousTransferComplete methods). |  |
| 9015 | File transfer failure: unable to contact file server (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9016 | File transfer failure: unable to access file (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9017 | File transfer failure: unable to complete download (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9018 | File transfer failure: file corrupted or otherwise unusable (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9019 | File transfer failure: file authentication failure (associated with Download, TransferComplete or AutonomousTransferComplete methods). |  |
| 9020 | File transfer failure: unable to complete download within specified time windows (associated with TransferComplete method). |  |

#### 8.3.1.4 Execute Software Operations with ChangeDUState RPC

The software installation and uninstall operations shall use the ChangeDUState mechanism defined in TR-069 [4]. The ChangeDUState mechanism is an asynchronous command that consists of the synchronous ChangeDUState RPC and returns a successful response or one of the following fault codes in Table 8.3.5.4.-1. A successful response means that the CPE has accepted the ChangeDUState RPC.

Table 8.3.5.4-1: ChangeDUState Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9000 | Method not supported |  |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9004 | Resources exceeded (when used in association with SetParameterValues, this MUST NOT be used to indicate Parameters in error) |  |

#### 8.3.1.5 Report Results with ChangeDUStateComplete RPC

After software installation and uninstall operations using a ChangeDUState mechanism  asdefined in TR-069 [4], the result of the state change operation is retrieved using the ChangeDUStateComplete RPC. The ChangeDUStateComplete RPC indicates a successful operatoin or one of the following fault codes in Table 8.3.5.5.-1.

Table 8.3.5.5-1: ChangeDUStateComplete Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9001 | Request denied (no reason specified) |  |
| 9003 | Invalid arguments |  |
| 9012 | File transfer server authentication failure (associated with Upload, Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9013 | Unsupported protocol for file transfer (associated with Upload, Download, ScheduleDownload, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9015 | File transfer failure: unable to contact file server (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9016 | File transfer failure: unable to access file (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9017 | File transfer failure: unable to complete download (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9018 | File transfer failure: file corrupted or otherwise unusable (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9022 | Invalid UUID Format (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install, Update, and Uninstall) |  |
| 9023 | Unknown Execution Environment (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install only) |  |
| 9024 | Disabled Execution Environment (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install, Update, and Uninstall) |  |
| 9025 | Deployment Unit to Execution Environment Mismatch (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install and Update) |  |
| 9026 | Duplicate Deployment Unit (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install only) |  |
| 9027 | System Resources Exceeded (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install and Update) |  |
| 9028 | Unknown Deployment Unit (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update and Uninstall) |  |
| 9029 | Invalid Deployment Unit State (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install, Update and Uninstall) |  |
| 9030 | Invalid Deployment Unit Update – Downgrade not permitted (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update only) |  |
| 9031 | Invalid Deployment Unit Update – Version not specified (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update only) |  |
| 9032 | Invalid Deployment Unit Update – Version already exists (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update only) |  |

#### 8.3.1.6	Execute Reboot operation

The reboot operation shall use the Reboot RPC defined in TR-069 [4]. The Reboot RPC is a synchronous command.  The Reboot RPC returns a successful response or one of the following fault codes in Table 8.3.5.6-1.

Table 8.3.5.6-1: Reboot Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9003 | Invalid arguments |  |

#### 8.3.1.7  Execute Factory Reset operation

The factory reset operation shall use the FactoryReset RPC defined in TR-069 [4]. The FactoryReset RPC is a synchronous command.  The FactoryReset RPC returns a successful response or one of the following fault codes in Table 8.3.5.7-1.

Table 8.3.5.7-1: FactoryReset Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9000 | Method not supported |  |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9003 | Invalid arguments |  |

| 8.3.1.8 |  |  |
| --- | --- | --- |

### 8.3.2	Delete <mgmtCmd>

The Delete primitive for <mgmtcmd> may map into zero or several BBF RPC commands as follows:

If  there there are no initiated <execInstance> sub-resouces  under the <mgmtCmd>  the receipt of the Delete primitive reults in the deletion of the resource without mapping into any BBF RPC commands.

If there are <execInstance> sub-resources which initiated  BBF File Upload and File Download operations which are cancelable, a BBF CancelTransfer RPC, as defined in TR-069 [4], shall be initiated for each cancealable operation. Upon completion of the cancellation operation, the <mgmtcmd> resource will be deleted.

Each CancelTransfer RPC returns a successful response or one of the following fault codes in Table 8.3.2-1.

Table 8.3.2-1: CancelTransfer Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9000 | Method not supported |  |
| 9001 | Request denied (no reason specified) |  |
| 9004 | Resources exceeded (when used in association with SetParameterValues, this MUST NOT be used to indicate Parameters in error) |  |
| 9021 | Cancelation of file transfer not permitted in current transfer state |  |

### 8.3.3 Update (Cancel) <execInstance>

When the Update primitive for an <execInstance>  sub-resource addresses the execDisable attribute of the < execInstance > , it effectively triggers a cancel <execInstance> procedure.

The hosting CSE determines if the operation has been initiated, if it is canceable and if it has been completed. Currently, only the BBF File Upload and File Download operations are cancellable.

If  the <execInstance> attribute execStatus reflects that the operation has not been started, that it is not cancealable or that the operation has been completed, corresponding error codes should be returned and no BBF RPC procedures are triggered.

If the <execInstance> sub-resource initiated BBF File Upload and File Download operations which are cancellable, the BBF CancelTransfer RPC, as defined in TR-069 [4], shall be initiated. The CancelTransfer RPC returns a successful response or one of the following fault codes in Table 8.3.3-1.

Table 8.3.3-1: CancelTransfer Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9000 | Method not supported |  |
| 9001 | Request denied (no reason specified) |  |
| 9004 | Resources exceeded (when used in association with SetParameterValues, this MUST NOT be used to indicate Parameters in error) |  |
| 9021 | Cancelation of file transfer not permitted in current transfer state |  |

### 8.3.4 Delete <execInstance>

The Delete primitive for an <execInstance>  sub-resource may map into zero or several BBF RPC procedures as follows:

The hosting CSE determines if the operation has been initiated, if it is canceable and if it has been completed. Currently, only the BBF File Upload and File Download operations are cancealable.

If  the <execInstance> sub-resouce status reflects that no operation has been initiatedor that it has been completed, it shall delete the sub-resource and  no BBF RPC procedures are triggered.

If the <execInstance> sub-resource initiated  BBF File Upload and File Download operations which are cancelable and have not been completed, the BBF CancelTransfer RPC as defined in TR-069 [4],   shall be initiated. The CancelTransfer RPC returns a successful response or one of the following fault codes in Table 8.3.4-1.

Table 8.3.4-1: CancelTransfer Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9000 | Method not supported |  |
| 9001 | Request denied (no reason specified) |  |
| 9004 | Resources exceeded (when used in association with SetParameterValues, this MUST NOT be used to indicate Parameters in error) |  |
| 9021 | Cancelation of file transfer not permitted in current transfer state |  |

### ----------------------- End of proposed text 2 -------------------------------------------