| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG#5 |
| Title:* | TS-0001 Editors notes to Action Items |
| Source:* | Tim Carey, ALU, timothy.carey@alcatel-lucent.com |
| Contact: | Tim Carey, ALU, timothy.carey@alcatel-lucent.com |
| Date:* | 2014-06-15 |
| Abstract:* | Create action items from leftover management release editors notes. |
| Agenda Item:* | xxx |
| Work item(s): | Functional Architecture TS |
| Document(s) Impacted* | TS-0001 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate Editors notes as action items. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

In TP11, the MAS WG decided to incorporate outstanding management related editors notes from TS-0001 into MAS action items.

9.6.16 <mgmtCmd>

[9.6.17.a]   Editor's Note: The types of management operations (e.g., cmdType) to be used by mgmtCmd are FFS.

Editor’s Note: It is FFS for how to use execTarget for group management

10.2.7.6 Execute <mgmtObj>

[10.2.7.6.b]  Editor's note: The definition of Execute is to be for FFS in clause 10.1.

10.2.8 External Management Operations through <mgmtCmd>

[10.2.8.a]  Editor's Note: Add external references (BBF etc)

10.2.8.3 Retrieve <mgmtCmd>

[10.3.8.3.a]  Editor's Note: We need to agree on a terminology on how to refer to a specific instance of a resource type.

10.2.8.6 10.2.8.6	Execute <mgmtCmd>

[10.2.8.6.a]  Editor's note: The definition of Execute is to be for FFS in clause 10.1.

Table 10.2.8.6-1: <mgmtCmd> EXECUTE

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | Originator needs to retrieve a resource. |
| Information on Request message | op: U. fr: Originator AE-ID or CSE-ID. to: Receiver CSE-ID. cn: <mgmtCmd>/execEnbale The UPDATE request shall address to <mgmtCmd>/execEnable without any payload. The mandatory and/or optional attributes defined in clause 9.6.15, as needed. |
| Local processing on Hosting CSE | (a) If the execution is allowed, Hosting CSE will do command conversion and mapping. (b) The Hosting CSE shall trigger existing device management procedures (i.e. BBF TR-069 [i.4]) to execute the corresponding management command on the remote entity. (c) The Hosting CSE shall perform local processing: if Step b is successful, the IN-CSE shall create an <execInstance> resource under the triggered <mgmtCmd> to maintain status and results for this execution. |
| Information on Response message | No change from the basic procedures. |
| Post-Conditions | The following processing on the Hosting CSE is dependent on the type of the command and execution status and may occur after the Response message has been sent. (a) After the command execution is finished, the remote entity sends response including execution results to the Hosting CSE, who will store the execution results in corresponding <execInstance> resource. This step may occur any time after the Response message has been sent and might occur after step b below. (b) The AE may use normal RETRIEVE procedure to retrieve the execution results or status of an <execInstance>. (c) After receiving the RETRIEVE request from the AE, the Hosting CSE can retrieve the execution status or results on the remote entity using existing management protocol. If step d. occurs before step e, step f. may not be needed. (d) A response shall be returned to the AE. |
| Exceptions | If the execution is not allowed or the specified <mgmtCmd> resource or its attribute/sub-resource does not exist in the IN-CSE, no further processing is required in the Hosting CSE and a proper error code shall be returned to AE in the Message response. If the corresponding management command cannot be executed in remote entity due to some reason, step 004 <??> shall be skipped and a proper error code shall be returned to AE in step 005 <??>. |

[10.2.8.6.b]  Editor's Note: Reference to setps 004 and 005 needed.

10.2.8.7	Cancel <execInstance>

[10.2.8.7.a]  Editor's Note: The Cancel flow shall be updated based on the definition of EXEC procedure.

10.2.14.4	Delete <node>

Table 10.2.14.4-1: <node> DELETE

| Description |
| --- |
| Pre-Conditions | The targeted <node> has been already created |
| Information on Request message | All parameters defined in table 8.1.2.1-1 are applicable as indicate in the table. |
| Local processing on Hosting CSE | No change from the generic procedure from clause 10.1.4. |
| Information on Response message | No change from the generic procedure from clause 10.1.4. |
| Post-Conditions | The targeted resource and all the children resources shall not exist anymore. Also all the related credential shall be deleted. [10.2.14.4.a] Editor's Note: if and how credentials are cleaned is FFS, in scope of WG4. |
| Exceptions | All exception described in the basic procedure (clause 10.1.4) are applicable. |

D.1	oneM2M Management Functions

[D.1.a]  Editor's Note: The notation for addressing the resources in this clause still need to be further studied.

D.7	Resource Type battery

[D.7a,]  Editor's Note: Using [battery] notation needs more discussion with WG2.

[D.7.b]  Editor's Note: The notation used for describing [battery] needs to be discussed and to be added to the Guidelines clause 9.1.

D.8	Resource Type deviceInfo

D.8.a]  Editor's Note: The notation used for describing [deviceInfo] needs to be discussed and to be added to the Guidelines clause 9.1

D.10	Resource Type reboot

[D.10.a] Editor's Note: The notation used for describing [reboot] needs to be discussed.

D.11	Resource Type eventLog

[D.11.a]  Editor's Note: The notation used for describing [eventLog] needs to be discussed.