| Input contribution Use case |
| --- |
| Use Case Title:* | MAS-2014-0409R01 Home Energy Management Use Case |
| Group Name:* | WG5 |
| Source:* | Orange (ETSI) |
| Contact: | Gilles Privat, gilles.privat@orange.com Patricia Martigne, patricia.martigne@orange.com |
| Date:* | 2014-06-10 |
| Abstract:* | This proposal proposes a home appliance control use case leveraging the semantic enablement capability. |
| Agenda Item:* |  |
| Work item(s): | oneM2M-WI-0005-Abstraction_&_Semantics_Capability_Enablement |
| Document(s) Impacted* | oneM2M-TR-0007-Study_on_Abstraction_and_Semantics_Enablement V0_10_0 + MAS-2014-0443 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include the use case into Annex A, and consequently modify Table in section 5.2. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## ******************start of change 1 ****************************

## 5.2	Use Case Analysis

The Annex A introduces several use cases for abstraction and semantics to identify key functionalities and potential requirements. The following table summarizes key functionalities and potential requirements for all use cases described in the Annex.

Table 1 Use Cases Analysis

|  | Name | Key functionalities | Potential requirements |
| --- | --- | --- | --- |
| … |  |  |  |
| 7 | Smart Home load control | Context-based reasoning Semantic query | The M2M System shall provide the capability for entities of the M2M system (e.g. AEs, or CSEs) to publish semantic descriptions within the M2M system. The M2M System shall support parsing and interpreting semantic descriptions. The M2M System shall support resource discovery based on semantics. |

## ******************end of change 1 ****************************

## ******************start of change 2 ****************************

## A.7 Smart Home load control use case

## A.7.1	Description

This use case is a key constituent of home energy management. Fine-grain control of all electrical appliances, be they connected to a communication network or not, makes it possible for the home to be fully integrated in a smart grid, where supply does not merely follow variations of aggregate loads , but a two-way mutual adaptation is possible to support a much better overall efficiency and a better matching  of available energy resources to the needs of consumers.

Two variants of this use case are, respectively, power-based or energy-based load shedding.

In power-based load shedding, a threshold on aggregate power may vary on different time-scales and requires instant adaptation by either shedding(turning off) or deferring loads. This corresponds to the case where the home is connected to a regular distribution grid where demand management is dictated by the distribution system operator.

In energy-based load control, the home operates on a limited energy budget for a given time span (e.g. 24 hours) and loads may be shed or shifted to stay within these limits. This corresponds to the case where the home is part of a microgrid that sets a priority on the use of limited local energy resources, with recourse to the external distribution grid used only as a last resort.

## A.7.2	Source

### Orange Labs (ETSI)

## A.7.3	 Actors

- Energy distribution operator or microgrid management system

- Home energy management system

- Individual home appliances that can be controlled either directly or indirectly

- Home M2M platform

- Home users

### Home context

## A.7.4	Pre-conditions

## A.7.5	Triggers

### • Change of power threshold set for home electricity consumption by energy distribution operator (for power-based variant)

### •	Turn on appliance that leads to exceed set aggregate power threshold

### •	Change of energy budget for target time-span(for energy variant) : this may be due to e.g. better than predicted solar generation from PV panel

### •	Deviation from predict use that leads to significantly deviate from allocated resources.

## A.7.6	Normal Flow

### In both variants of this use case, appliances whose use can be deferred are deferred in order of decreasing priority, then appliances that can be turned off are shed in order of decreasing priority, according to the category they belong to :comfort, entertainment, non-critical assistance, security, safety& critical assistance  (the latter category shall in principle never be turned off), until the constraints are met. Closed loop control can be applied iteratively to individual appliances.

### In case the power threshold or energy budget increases, a similar iterative procedure can be applied in reverse order by turning on appliances whose use might have been previously deferred.

## A.7.7	Post-conditions

- Aggregate power  returned under threshold

- Aggregate energy within budget in target time span

## A.7.8	High Level Illustration

## A.7.9	Potential requirements

- The M2M System shall provide the capability for entities of the M2M system (e.g. AEs, or CSEs) to publish semantic descriptions within the M2M system.

- The M2M System shall support parsing and interpreting semantic descriptions.

- The M2M System shall support resource discovery based on semantics.

******************end of change 2 ****************************