| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG#5 |
| Title:* | Mapping of cmdhPolicy resources for TS-0005 |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-07-21 |
| Abstract:* | This contribution provides text for clauses 5 an 6 of TS-0005 on mapping between cmdhPolicy resources and both OMA-DM and OMA-LWM2M objects. R01: Cleanup of text after first discussion at MAS#11.2 Addition of Annex A.x.1 Note this revision is not complete. R02 will be uploaded shortly. |
| Agenda Item:* | MAS#12 |
| Work item(s): | MAS Management Enablement (OMA) TS |
| Document(s) Impacted* | TS-0005 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Add proposed text to clauses 5 and 6 and of TS-0005v0.2.0 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction

Following text is proposed to be added to clauses 5.3 and 6.3 of TS-0005v0.2.0 (Management Enablement OMA).

For OMA-DM it is proposed to specify a new OMA DM Management Object, denoted  “M2M cmdhPolicies MO (MCMDHMO)” compliant with the best practices described in OMA-WP-Management_Object_Design_Guidelines-20130129-A.  This is not in the scope of this contribution.  However, the structure of this MCMDHMO assumed here is essentially the same as assumed in TS-0006.

For OMA LWM2M also a respective root object  needs to be defined. The text proposed here for clause 6.3 is very preliminary

## ----------------------- start of text addition 1 ---------------

## 5.3.x	Resource Type [cmdhPolicy]

The Resource Type [cmdhPolicy] represents a set of rules defining which CMDH parameters will be used by default when a request issued by a local originator contains the ec (event category) parameter but not all other CMDH parameters, see clause D.12 of TS-0001 [1].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource Type [cmdhPolicy] is a multi-instance Resource where each instance of the Resource shall map to an instance of a cmdhPolicies/<[cmdhPolicy]>+/ node.

The attributes of an instance of [cmdhPolicy] shall be mapped to nodes of MCMDHMO as follows.

Table 5.3.x-1: Resource Type [cmdhPolicy]

| Attribute Name of [cmdhPolicy] | Mapping to Nodes in Management Object |
| --- | --- |
| name | cmdhPolicies/<[cmdhPolicy]>+/name |
| cmdhDefaults | cmdhPolicies/<[cmdhPolicy]>+/defaultRule |
| cmdhLimits | cmdhPolicies/<[cmdhPolicy]>+/limitRules |
| cmdhNetworkAccessRules | cmdhPolicies/<[cmdhPolicy]>+/networkAccessECRules |
| cmdhBuffer | cmdhPolicies/<[cmdhPolicy]>+/bufferRules |

### 5.3.x.1	Resource Type [activeCmdhPolicy]

The Resource Type [activeCmdhPolicy] provides a link to the currently active set of CMDH policies, see clause D.12.1 of TS-0001 [1].

The Resource Type [activeCmdhPolicy]  is mapped to the enable parameter of the cmdhPolicies/<[cmdhPolicy]> nodes.

Table 5.3.x.1-1: Resource Type [activeCmdhPolicy]

| Attribute Name of [activeCmdhPolicy] | Mapping to Nodes in Management Object |
| --- | --- |
| cmdhPolicy | cmdhPolicies/<[cmdhPolicy]>+/enable At most one <[cmdhPolicy]> instance shall be enabled at a time. As such the <[cmdhPolicy]> instance that has the enable parameter with a value of “True” is the active CMDH policy. |

### 5.3.x.2	Resource Type [cmdhDefaults]

The Resource Type [cmdhDefaults] defines default CMDH policy values, see clause D.12.2 of TS-0001 [1].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource Type [cmdhDefaults] is a multi-instance Resource where each instance of the Resource shall map to an instance of the cmdhPolicies/<[cmdhDefaults]>+/ node.

The attributes of an instance of [cmdhDefaults] shall be mapped to nodes of MCMDHMO as follows.

Table 5.3.x.2-1: Resource Type [cmdhDefaults]

| Attribute Name of [cmdhDefaults] | Mapping to Nodes in Management Object |
| --- | --- |
| cmdhDefEcValue | cmdhPolicies/<[cmdhDefaults]>+/defaultECRules |
| cmdhEcDefParamValues | cmdhPolicies/<[cmdhDefaults]>+/defaultECParamRules |

### 5.3.x.3	Resource Type [cmdhDefEcValues]

The Resource Type [cmdhDefEcValues] represents a value for the ec (event category) parameter of an incoming request, see clause D.12.3 of TS-0001 [1].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource Type [cmdhDefEcValues] is a multi-instance Resource where each instance of the Resource shall map to an instance of the cmdhPolicies/<[cmdhDefEcValues]>+/ node.

The attributes of an instance of [cmdhDefEcValues] shall be mapped to nodes of MCMDHMO as follows.

Table 5.3.x.3-1: Resource Type [cmdhDefEcValues]

| Attribute Name of [cmdhDefEcValues] | Mapping to Nodes in Management Object |
| --- | --- |
| order | cmdhPolicies/<[cmdhDefEcValue]>+/order |
| defEcValue | cmdhPolicies/<[cmdhDefEcValue]>+/defEcValue |
| requestOrigin | cmdhPolicies/<[cmdhDefEcValue]>+/requestOrigin |
| requestContext | cmdhPolicies/<[cmdhDefEcValue]>+/requestContext |
| requestContextNotification | cmdhPolicies/<[cmdhDefEcValue]>+/requestContextNotification |
| requestCharacteristics | cmdhPolicies/<[cmdhDefEcValue]>+/requestCharacteristics |

### 5.3.x.4	Resource Type [cmdhEcDefParamValues]

The Resource Type [cmdhEcDefParamValues] represents a specific set of default values for the CMDH related parameters rqet (request expiration timestamp), rset (result expiration timestamp), oet (operational execution time), rp (response persistence) and da (delivery aggregation) that are applicable for a given ec (event category) if these parameters are not specified in the request, see clause D.12.4 of TS-0001 [1].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource Type [cmdhEcDefParamValues] is a multi-instance Resource where each instance of the Resource shall map to an instance of the cmdhPolicies/<[cmdhEcDefParamValues]>+/ node.

The attributes of an instance of [cmdhEcDefParamValues] shall be mapped to nodes of MCMDHMO as follows.

Table 5.3.x.4-1: Resource Type [cmdhEcDefParamValues]

| Attribute Name of [cmdhEcDefParamValues] | Mapping to Nodes in Management Object |
| --- | --- |
| applicableEventCategory | cmdhPolicies/<[cmdhEcDefParamValues]>+/applicableEventCategory |
| defaultRequestExpTime | cmdhPolicies/<[cmdhEcDefParamValues]>+/defaultRequestExpTime |
| defaultResultExpTime | cmdhPolicies/<[cmdhEcDefParamValues]>+/defaultResultExpTime |
| defaultOpExecTime | cmdhPolicies/<[cmdhEcDefParamValues]>+/defaultOpExecTime |
| defaultRespPersistence | cmdhPolicies/<[cmdhEcDefParamValues]>+/defaultRespPersistence |
| defaultDelAggregation | cmdhPolicies/<[cmdhEcDefParamValues]>+/defaultDelAggregation |

### 5.3.x.5	Resource Type [cmdhLimits]

The Resource Type [cmdhLimits] represents limits for CMDH related parameter values, see clause D.12.5 of TS-0001 [1].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource Type [cmdhLimits] is a multi-instance Resource where each instance of the Resource shall map to an instance of the cmdhPolicies/<[cmdhLimits]>+/ node.

The attributes of an instance of [cmdhLimits] shall be mapped to nodes of MCMDHMO as follows.

Table 5.3.x.5-1: Resource Type [cmdhLimits]

| Attribute Name of [cmdhLimits] | Mapping to Nodes in Management Object |
| --- | --- |
| order | cmdhPolicies/<[cmdhLimits]>+/order |
| requestOrigin | cmdhPolicies/<[cmdhLimits]>+/requestOrigin |
| requestContext | cmdhPolicies/<[cmdhLimits]>+/requestContext |
| requestContextNotification | cmdhPolicies/<[cmdhLimits]>+/requestContextNotification |
| requestCharacteristics | cmdhPolicies/<[cmdhLimits]>+/requestCharacteristics |
| limitsEventCategory | cmdhPolicies/<[cmdhLimits]>+/limitsEventCategory |
| limitsRequestExpTime | cmdhPolicies/<[cmdhLimits]>+/limitsRequestExpTime |
| limitsResultExpTime | cmdhPolicies/<[cmdhLimits]>+/limitsResultExpTime |
| limitsOpExecTime | cmdhPolicies/<[cmdhLimits]>+/limitsOpExecTime |
| limitsRespPersistence | cmdhPolicies/<[cmdhLimits]>+/limitsRespPersistence |
| limitsDelAggregation | cmdhPolicies/<[cmdhLimits]>+/limitsDelAggregation |

### 5.3.x.6	Resource Type [cmdhNetworkAccessRules]

The Resource Type [cmdhNetworkAccessRules] defines the usage of underlying networks for forwarding information to other CSEs during processing of CMDH-related requests in a CSE, see clause D.12.6 of TS-0001 [1].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource Type [cmdhNetworkAccessRules] is a multi-instance Resource where each instance of the Resource shall map to an instance of the cmdhPolicies/<[cmdhNetworkAccessRules]>+/ node.

The attributes of an instance of [cmdhNetworkAccessRules] shall be mapped to nodes of MCMDHMO as follows.

Table 5.3.x.6-1: Resource Type [cmdhNetworkAccessRules]

| Attribute Name of [cmdhNetworkAccessRules] | Mapping to Nodes in Management Object |
| --- | --- |
| applicableEventCategories | cmdhPolicies/<[cmdhLimits]>+/applicableEventCategories |
| cmdhNwAccessRule | cmdhPolicies/<[cmdhLimits]>+/NetworkAccessRules |

### 5.3.x.7	Resource Type [cmdhNwAccessRule]

The Resource Type [cmdhNwAccessRule] define limits in usage of specific underlying networks for forwarding information to other CSEs during processing of CMDH-related requests, see clause D.12.7 of TS-0001 [1].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource Type [cmdhNwAccessRule] is a multi-instance Resource where each instance of the Resource shall map to an instance of the cmdhPolicies/<[cmdhNwAccessRule]>+/ node.

The attributes of an instance of [cmdhNwAccessRule] shall be mapped to nodes of MCMDHMO as follows.

Table 5.3.x.7-1: Resource Type [cmdhNwAccessRule]

| Attribute Name of [cmdhNwAccessRule] | Mapping to Nodes in Management Object |
| --- | --- |
| targetNetwork | cmdhPolicies/<[cmdhNwAccessRule]>+/targetNetwork |
| minReqVolume | cmdhPolicies/<[cmdhNwAccessRule]>+/minReqVolume |
| backOffParameters | cmdhPolicies/<[cmdhNwAccessRule]>+/backOffParameters/backoffTime |
|  | cmdhPolicies/<[cmdhNwAccessRule]>+/backOffParameters/backoffTimeIncrement |
|  | cmdhPolicies/<[cmdhNwAccessRule]>+/backOffParameters/maximumBackoffTime |
| otherConditions | cmdhPolicies/<[cmdhNwAccessRule]>+/otherConditions/condition |
| allowedSchedule | cmdhPolicies/<[cmdhNwAccessRule]>+/allowedSchedule |

- Editors Note: The otherConditions parameter needs to be specified in TS-0004 before we can determine how to map the attribute.

- Editors Note: The backOffParameters needs to be specified in TS-0004 before we can determine how to map the attribute of this complex type.

- Editors Note: The allowed schedule parameter should have the same format as the <schedule> resource type. It needs to be specified in TS-0004 before we can determine how to map the attribute of this complex type

### 5.3.x.8	Resource Type [cmdhBuffer]

The Resource Type [cmdhBuffer] represents limits in usage of buffers for temporarily storing information that needs to be forwarded to other CSEs during processing of CMDH-related requests in a CSE, see clause D.12.8 of TS-0001 [1].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource Type [cmdhBuffer] is a multi-instance Resource where each instance of the Resource shall map to an instance of the cmdhPolicies/<[cmdhBuffer]>+/ node.

The attributes of an instance of [cmdhBuffer] shall be mapped to nodes of MCMDHMO as follows.

Table 5.3.x.7-1: Resource Type [cmdhBuffer]

| Attribute Name of [cmdhBuffer] | Mapping to Nodes in Management Object |
| --- | --- |
| applicableEventCategory | cmdhPolicies/<[cmdhNwAccessRule]>+/applicableEventCategory |
| maxBufferSize | cmdhPolicies/<[cmdhNwAccessRule]>+/maxBufferSize |
| storagePriority | cmdhPolicies/<[cmdhNwAccessRule]>+/storagePriority |

## ------------------------ end of text addition 1 ----------------

## ------------------------ start of text addition 2 ----------------

## 5.3.x	Resource Type [cmdhPolicy]

For OMA LWM2M  this resource shall be mapped to a unique instance of an LWM2M object for cmdhPolicies (urn:oma:mo:ext-onem2m:x).

Editor’s note:  LWM2M object and ObjectID for cmdhPolicies and for all resources in the following subsections 5.3.x.1 to 5.3.x.8 need to be defined.

The Resource Type [cmdhPolicy] is a multi-instance Resource where each instance shall map to an instance of a cmdhPolicies/<[cmdhPolicy]>+/ node.

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:x |
| objectPath | /x/0 |

The attributes of this Resource shall be mapped to specific resources of the LWM2M cmdhPolicies Object Instance as follows:

| Attribute Name of [memory] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| name |  |
| cmdhDefaults |  |
| cmdhLimits |  |
| cmdhNetworkAccessRules |  |
| cmdhBuffer |  |

### 6.3.x.1	Resource Type [activeCmdhPolicy]

The Resource Type [activeCmdhPolicy]  is mapped to the enable parameter of the cmdhPolicies/<[cmdhPolicy]> nodes.

At most one <[cmdhPolicy]> instance shall be enabled at a time. As such the <[cmdhPolicy]>  instance that has the enable parameter with a value of “True” is the active CMDH policy.

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:x |
| objectPath |  |

The attributes of this Resource shall be mapped to specific resources of the LWM2M cmdhPolicies Object Instance as follows:

| Attribute Name of [activeCmdhPolicy] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| cmdhPolicy |  |

### 6.3.x.2	Resource Type [cmdhDefaults]

The Resource Type [cmdhDefaults] is a multi-instance Resource where each instance of the Resource shall map to an instance of the cmdhPolicies/<[cmdhDefaults]>+/ node.

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:x |
| objectPath |  |

The attributes of this Resource shall be mapped to specific resources of the LWM2M cmdhPolicies Object Instance as follows:

| Attribute Name of [cmdhDefaults] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| cmdhDefEcValue |  |
| cmdhEcDefParamValues |  |

### 6.3.x.3	Resource Type [cmdhDefEcValues]

The Resource Type [cmdhDefEcValues] is a multi-instance Resource where each instance of the Resource shall map to an instance of the cmdhPolicies/<[cmdhDefEcValues]>+/ node.

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:x |
| objectPath |  |

The attributes of this Resource shall be mapped to specific resources of the LWM2M cmdhPolicies Object Instance as follows:

| Attribute Name of [cmdhDefEcValues] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| order |  |
| defEcValue |  |
| requestOrigin |  |
| requestContext |  |
| requestContextNotification |  |
| requestCharacteristics |  |

### 6.3.x.4	Resource Type [cmdhEcDefParamValues]

The Resource Type [cmdhEcDefParamValues] is a multi-instance Resource where each instance of the Resource shall map to an instance of the cmdhPolicies/<[cmdhEcDefParamValues]>+/ node.

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:x |
| objectPath |  |

The attributes of this Resource shall be mapped to specific resources of the LWM2M cmdhPolicies Object Instance as follows:

| Attribute Name of [cmdhEcDefParamValues] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| applicableEventCategory |  |
| defaultRequestExpTime |  |
| defaultResultExpTime |  |
| defaultOpExecTime |  |
| defaultRespPersistence |  |
| defaultDelAggregation |  |

### 6.3.x.5	Resource Type [cmdhLimits]

The Resource Type [cmdhLimits] is a multi-instance Resource where each instance of the Resource shall map to an instance of the cmdhPolicies/<[cmdhLimits]>+/ node.

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:x |
| objectPath |  |

The attributes of this Resource shall be mapped to specific resources of the LWM2M cmdhPolicies Object Instance as follows:

| Attribute Name of [cmdhLimits] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| order |  |
| requestOrigin |  |
| requestContext |  |
| requestContextNotification |  |
| requestCharacteristics |  |
| limitsEventCategory |  |
| limitsRequestExpTime |  |
| limitsResultExpTime |  |
| limitsOpExecTime |  |
| limitsRespPersistence |  |
| limitsDelAggregation |  |

### 6.3.x.6	Resource Type [cmdhNetworkAccessRules]

The Resource Type [cmdhNetworkAccessRules] is a multi-instance Resource where each instance of the Resource shall map to an instance of the cmdhPolicies/<[cmdhNetworkAccessRules]>+/ node.

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:x |
| objectPath |  |

The attributes of this Resource shall be mapped to specific resources of the LWM2M cmdhPolicies Object Instance as follows:

| Attribute Name of [cmdhNetworkAccessRules] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| applicableEventCategories |  |
| cmdhNwAccessRule |  |

### 6.3.x.7	Resource Type [cmdhNwAccessRule]

The Resource Type [cmdhNwAccessRule] is a multi-instance Resource where each instance of the Resource shall map to an instance of the cmdhPolicies/<[cmdhNwAccessRule]>+/ node.

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:x |
| objectPath |  |

The attributes of this Resource shall be mapped to specific resources of the LWM2M cmdhPolicies Object Instance as follows:

| Attribute Name of [cmdhNetworkAccessRule] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| targetNetwork |  |
| minReqVolume |  |
| backOffTime |  |
| backoffTimeIncrement |  |
| maximumBackoffTime |  |
| otherConditions |  |
| allowedSchedule |  |

- Editors Note: The otherConditions parameter needs to be specified in TS-0004 before we can determine how to map the attribute.

- Editors Note: The backOffParameters needs to be specified in TS-0004 before we can determine how to map the attribute of this complex type.

- Editors Note: The allowed schedule parameter should have the same format as the <schedule> resource type. It needs to be specified in TS-0004 before we can determine how to map the attribute of this complex type

### 6.3.x.8	Resource Type [cmdhBuffer]

The Resource Type [cmdhBuffer] is a multi-instance Resource where each instance of the Resource shall map to an instance of the cmdhPolicies/<[cmdhBuffer]>+/ node.

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:x |
| objectPath |  |

The attributes of this Resource shall be mapped to specific resources of the LWM2M cmdhPolicies Object Instance as follows:

| Attribute Name of [cmdhBuffer] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| applicableEventCategory |  |
| maxBufferSize |  |
| storagePriority |  |

## ------------------------ end of text addition 2 ----------------

## ------------------------ start of text addition 3 ----------------

Annex X (Normative):

OMA DM compatible Management Objects for oneM2M

X.1	M2M CMDH Policies MO (MCMDHMO)

The M2M CMDH Policies MO (MCMDHMO) resides in the Management Tree of any ASN or MN which support Device Management via OMA DM 1.3 and OMA DM 2.0. This MO corresponds to instances of the cmdhPolicy resource and its child resources which all represent subtypes of the mgmtObj resource type, as specified in Annex D.12 of the oneM2M functional architecture TS-0001 [x].

This MO maintains information regarding the remote provisioning and management of CMDH policies.

Figure A.x.1-1 gives the pictorial description of the MCMDHMO.

The various nodes within this MO are described as follows.

| cmdhPolicies |
| --- |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This node is the root node for the MCMDHMO which includes all MOs related to CMDH Policy management. The parent node of this node defines the location of this MO in the Management Tree. The Management Object Identifier for the MCMDHMO shall be: "urn:oma:mo:ext-onem2m-mcmdhmo:1.0". |
| cmdhPolicies/cmdhPolicy |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of instances of cmdhPolicy MOs. |
| cmdhPolicies/cmdhPolicy/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | node | Get |  |
|  | This placeholder interior node is the parent node of a specific instance of cmdhPolicy. |
| cmdhPolicies/cmdhPolicy/<x>/name |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |

| cmdhPolicies/cmdhPolicy/<x>/defaultRule |
| --- |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node includes a reference to a cmdhDefaults node. |

| cmdhPolicies/cmdhPolicy/<x>/limitRules |
| --- |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | This leaf node includes a reference to a cmdhDefaults node. |

| cmdhPolicies/cmdhPolicy/<x>/NetworkAccessECRules |
| --- |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | This leaf node includes a reference to a cmdhNetworkAccess node. |

| cmdhPolicies/cmdhPolicy/<x>/bufferRules |
| --- |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | This leaf node includes a reference to a cmdhBuffer node. |

Figure A.x.1-1: Structure of OMA-DM compatible M2M CMDH Policies MO (MCMDHMO)

| cmdhPolicies/activeCmdhPolicy |
| --- |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of an activeCmdhPolicy MO instance. |
| cmdhPolicies/activeCmdhPolicy/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of the activeCmdhPolicy MO instance. |
| cmdhPolicies/activeCmdhPolicy/<x>/enable |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node includes a reference to the currently active instance of cmdhPolicy MO. |
| cmdhPolicies/cmdhDefaults |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of instances of cmdhPolicy MOs. |
| cmdhPolicies/cmdhDefaults/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | node | Get |  |
|  | This placeholder node is the parent node of a specific instance of cmdhDefaults MOs. |
| cmdhPolicies/cmdhDefaults/<x>/defaultECRules |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | This leaf node includes a reference to an instance of cmdhDefEcValue MO. |
| cmdhPolicies/cmdhDefaults/<x>/defaultECParamRules |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | This leaf node includes a reference to an instance of cmdhEcDefParamValue MO. |  |
| cmdhPolicies/cmdhDefEcValue |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | node | Get |  |
|  | This interior node is the parent node of cmdhDefEcValue MOs. |
| cmdhPolicies/cmdhDefEcValue/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | Node | Get |  |
|  | This interior placeholder node is the parent node of the cmdhDefEcValue MO instances. |
| cmdhPolicies/cmdhDefEcValue/<x>/order |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | Int | Get |  |
|  | This leaf node includes the index indicating in which order the cmdhDefEcValue resource will be treated by the CSE to determine a value for the ec parameter. |
| cmdhPolicies/cmdhDefEcValue/<x>/defEcValue |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | Chr | Get |  |
|  | This leaf node includes the value to use for the ec parameter if the conditions expressed in the requestOrigin, requestContext and requestCharacteristics all match. If none of these attributes are defined, then the defEcValue shall be applied. |
| cmdhPolicies/cmdhDefEcValue/<x>/requestOrigin |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | Node | Get |  |
|  | This leaf node includes .... |
| cmdhPolicies/cmdhDefEcValue/<x>/requestContext |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | Chr | Get |  |
|  | This leaf node includes … |
| cmdhPolicies/cmdhDefEcValue/<x>/requestContextNotification |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | Bool | Get |  |
|  | This leaf node includes … |  |
| cmdhPolicies/cmdhDefEcValue/<x>/requestCharacteristics |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | Chr | Get |  |
|  | This leaf node includes … |
| cmdhPolicies/cmdhEcDefParamValues/ |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | Node | Get |  |
|  | This interior node is the parent node of the cmdhEcDefParamValues MO. |
| cmdhPolicies/cmdhEcDefParamValues/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This interior placeholder node is the parent node of the cmdhEcDefParamValues MO instances. |
| cmdhPolicies/cmdhEcDefParamValues/<x>/applicableEventCategory |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node includes … |
| cmdhPolicies/cmdhEcDefParamValues/<x>/defaultRequestExpTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node includes … |
| cmdhPolicies/cmdhEcDefParamValues/<x>/defaultResultExpTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node includes a reference to an instance of cmdhDefEcValue MO. |
| cmdhPolicies/cmdhEcDefParamValues/<x>/defaultOpExpTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node includes … |  |
| cmdhPolicies/cmdhEcDefParamValues/<x>/defaultResponsePersistence |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node includes … |
| cmdhPolicies/cmdhLimits |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of the cmdhLimits MO. |
| cmdhPolicies/cmdhLimits/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This interior placeholder node is the parent node of the cmdhLimits MO instances. |
| cmdhPolicies/cmdhLimits/<x>order |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node includes the value to use for the ec parameter if the conditions expressed in the requestOrigin, requestContext and requestCharacteristics all match. If none of these attributes are defined, then the defEcValue shall be applied. |
| cmdhPolicies/cmdhLimits/<x>/RequestOrigin |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node includes .... |
| cmdhPolicies/cmdhLimits/<x>/RequestContext |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrMore | chr | Get |  |
|  | This leaf node includes … |
| cmdhPolicies/cmdhLimits/<x>/RequestContextNotification |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node includes …. |  |
| cmdhPolicies/cmdhLimits/<x>/RequestCharacteristics |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | node | Get |  |
|  | This leaf node includes …. |
| cmdhPolicies/cmdhLimits/<x>/limitsEventCategory |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node includes …. |
| cmdhPolicies/cmdhLimits/<x>/limitsRequestExpTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node includes …. |
| cmdhPolicies/cmdhLimits/<x>/limitsResultExpTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node includes …. |
| cmdhPolicies/cmdhLimits/<x>/limitsOpExecTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node includes …. |
| cmdhPolicies/cmdhLimits/<x>/limitsRespPersistence |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node includes …. |
| cmdhPolicies/cmdhLimits/<x>/limitsDelAggregation |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | bool | Get |  |
|  | This leaf node includes …. |  |
| cmdhPolicies/cmdhNetworkAccessRules |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | node | Get |  |
|  | This interior node is the parent node of cmdhNetworkAccessRules MOs. |
| cmdhPolicies/cmdhNetworkAccessRules/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | node | Get |  |
|  | This interior placeholder node is the parent node of the cmdhDefEcValue MO instances. |
| cmdhPolicies/cmdhNetworkAccessRules/<x>/applicableEventCategories |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | Int | Get |  |
|  | This leaf node includes …. |
| cmdhPolicies/cmdhDefEcValue/<x>/cmdhNwAccessRules |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrMore | chr | Get |  |
|  | This leaf node includes a reference to an instance of cmdhNwAccessRules. |
| cmdhPolicies/cmdhNwAccessRules |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | Node | Get |  |
|  | This interior node is the parent node of cmdhNetworkAccessRules MOs. |
| cmdhPolicies/cmdhNwAccessRules/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This interior placeholder node is the parent node of the cmdhNwAccessRules MO instances. |
| cmdhPolicies/cmdhNwAccessRules/<x>targetNetwork |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node includes … |  |
| cmdhPolicies/cmdhNwAccessRules/<x>targetNetwork |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node includes … |
| cmdhPolicies/cmdhNwAccessRules/<x>minReqVolume |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node includes … |
| cmdhPolicies/cmdhNwAccessRules/<x>backOffParameters |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | Int | Get |  |
|  | This leaf node includes … |
| cmdhPolicies/cmdhNwAccessRules/<x>otherConditions |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node includes … |
| cmdhPolicies/cmdhNwAccessRules/<x>allowedSchedule |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node includes … |
| cmdhPolicies/cmdhBuffer |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | node | Get |  |
|  | This interior node is the parent node of the cmdhBuffer MO. |
| cmdhPolicies/cmdhBuffer/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneorMore | node | Get |  |
|  | This interior placeholder node is the parent node of the cmdhBuffer MO instances. |
| cmdhPolicies/cmdhBuffer/<x>/applicableEventCategory |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | Int | Get |  |
|  | This leaf node includes … |
| cmdhPolicies/cmdhBuffer/<x>/maxBufferSize |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node includes ... |
| cmdhPolicies/cmdhBuffer/<x>/storagePriority |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | one | int | Get |  |
|  | This leaf node includes … |

## ----------------------- end of text addition 3 ----------------

# Comments

for consistency with TS-0006 we should refer to "resource type" rather than "resource". This requires corresponding editorial changes for all other resources in clause 5.3.

to be defined as external MO compliant with OMA-WP-AC-MO-20090127-A

for consistency with TS-0006 we should refer to "resource type" rather than "resource". This requires corresponding editorial changes for all other resources in clause 5.3.