| CHANGE REQUEST |
| --- |
| Group Name:* | MAS#5 |
| Source:* | Thierry GARNIER, Gemalto N.V, thierry.garnier@gemalto.com |
| Format:* | Plenary |
| Date:* | 2014-07-18 |
| Contact:* | Thierry GARNIER, Gemalto N.V, thierry.garnier@gemalto.com |
| Reason for Change/s:* | This contribution updates Mapping of resources 6.3 section : reflect the flexible rootpath capability available in LWM2M update battery status codes |
| CR against: Release* | Release1 |
| CR against: TS/TR* | TS-0005, Management Enablement (OMA) ver 0.1.2 |
| Clauses/Sub Clauses* | 6.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution updates Mapping of resources 6.3 section in OMA LWM2M :

- reflect  the flexible rootpath capability available in LWM2M

- update battery status codes

### -----------------------Start of change 1-------------------------------------------

# 6.	OMA Lightweight M2M 1.0

## 6.3	Mapping of resources

### 6.3.1	General Mapping Assumptions

In case the objectPath is multiple (several Object Instances  are referenced in that Resource), a specified couple composed of one element of the objectId list and one element of objectPath list will be associated to a given Resource attribute for realizing the final mapping to the targeted OMA LWM2M [6] resource.

In OMA LWM2M, the Objects Instances are  located under the default  rootpath  (i.e.  “/”) when this rootpath  is not explicitly specified,. However, devices might be hosting other resources, that’s why the LWM2M has the capability to assign the LWM2M rootpath  to an alternative path . In oneM2M this alternate path will be part of a Resource objectPath  attribute (e.g. “/lwm2mPath /3/0”).

### 6.3.2	Resource [memory]

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:3 |
| objectPath | /3/0 (instance 0 of Object 3) |

### 6.3.3	Resource [battery]

The context of this Resource is the following

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:3 |
| objectPath | /3/0 |

The attributes of this  Resource shall be mapped to specific resources of the LWM2M Device Object Instance  as follows:

| Attribute Name of [battery] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| batteryLevel | 9 : current battery level as percentage |
| batteryStatus , oneM2M Status Codes “NORMAL” “CHARGING” “CHARGE-COMPLETE” “DAMAGED” “LOW-BATTERY” “NOT-INSTALLED” “UNKNOWN” | 20 : contains the battery status Battery Status Description 0 The battery is operating normally and not on power. 1 The battery is currently charging. 2 The battery is fully charged and still on power. 3 The battery has some problem. 4 The battery is low on charge. 5 The battery is not installed. 6 The battery information is not available. |

### 6.3.4	Resource [deviceInfo]

The context of this Resource is the following

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:3 |
| objectPath | /3/0 |

### 6.3.5	Resource [reboot]

The context of this Resource is the following

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:3 |
| objectPath | /3/0 |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?