| CHANGE REQUEST |
| --- |
| Group Name:* | MAS#12 |
| Source:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Format:* | Plenary / Teleconference |
| Date:* | 2014-7-16 |
| Contact:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Reason for Change/s:* | This contribution provides the Notify primitive mapping for OMA DM 1.3/2.0. |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0005, ver 0.2.0 |
| Clauses/Sub Clauses* | 5.4.1.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides the Notify primitive mapping for OMA DM 1.3/2.0

### -----------------------Start of New Text 1-------------------------------------------

#### 5.4.1.5	Notify Primitive Mapping

The Notify Request and Response primitives permit notifications to AE or CSEs that have subscribed to a Resource. When the AE and CSE have been subscribed to the <mgmtObj> Resource, the <mgmtObj> Resource hosting CSE will send the notification to the subscriber if the <mgmtObj> Resource has been changed according to the notification policy. For the notification, the <mgmtObj> resource hosting CSE has the responsibility to update the <mgmtObj> by monitoring the management objects in the device.

#### 5.4.1.5.1	Subscribe	Procedure Mapping for OMA DM 1.3

OMA DM 1.3 does not have the subscription mechanism that notifies the DM Server when the management objects in the device have been changed. The optional alerts DM_TREE_UNCHANGED_ALERT and the DM_TREE_CHANGED_ALERT can indicate the changes occurred in the DM Tree, but those alerts is not sent to the DM Server at the time the changes occurs. The DM Server may use periodic retrieval to monitor changes in management objects. Vendor specific extensions may also be used for the subscription mechanism such as that any changes in management objects can be reported to the DM Server using the generic alerts. In this way, the <mgmtObj> Resource hosting CSE updates the <mgmtObj>, and can send the notification to the subscribers upon changes in the <mgmtObj> Resource.

When a <subscription> Resource for a <mgmtObj> Resource is Created or Updated, the <mgmtObj> Resource hosting CSE shall monitor the changes in the corresponding management objects by using the mechanism described above. In case of the <subscription> Resource deletion, the <mgmtObj> Resource hosting CSE might stop monitoring the management objects in the device. Note that this is not the primitive mapping since there is no such subscribe primitive in OMA DM 1.3.

#### 5.4.1.5.2	Subscribe	Procedure Mapping for OMA DM 2.0

OMA DM 2.0 provides the SUB command that subscribe to any change occurring in a certain part of the DM Tree. When a change occurs, the DM Client will send a notification message with the changed management objects that has been subscribed. The <mgmtObj> Resource hosting CSE can use the SUB command to detect the changes in the management object and update the <mgmtObj> Resource. The optional SUB command might not be supported by the device, and in this case, the <mgmtObj> Resource hosting CSE periodically retrieve the management objects.

When a <subscription> Resource for a <mgmtObj> Resource is Created, Deleted or Updated the CSE shall perform the following procedures:

- The <subscription> Resource creation and update shall be mapped to the SUB command if the SUB command is supported. If the SUB command is not supported, the <mgmtObj> Resource hosting CSE shall monitor the changes in the relevant management objects by any means (e.g., the periodic retrieval).

- The <subscription> Resource deletion should be mapped to the UNSUB command if the UNSUB command is supported. In case that the corresponding management objects need to keep to be monitored, the UNSUB command may not be performed. If the UNSUB command is not supported, the <mgmtObj> Resource hosting CSE might stop monitoring the corresponding management objects in the device.

The status code mappings for the SUB/UNSUB commands are described in the following table.

| oneM2M Primitive Stauts Code | OMA DM 2.0 Status Code | Description |
| --- | --- | --- |
| success | (200) OK | The DM command completed successfully |
| error – bad request | (400) Bad Request | The requested command could not be performed because of malformed syntax in the command. |
| error - no privilege | (403) Forbidden | The requested command failed because the sender does not have adequate access rights on the recipient. |
| error – not found | (404) Not Found | The requested target was not found |
| error – internal error | (500) Internal Error | The recipient encountered an unexpected condition which prevented it from fulfilling the request |
| error – not implemented | (501) Not Implemented | The recipient does not support the features to fulfil the request. This is the appropriate response when the recipient does not recognize the requested command and is not capable of supporting it for any resource. |
| error – service unavailable | (503) Service Unavailable | The recipient is currently unable to handle the request due to a temporary overloading or maintenance of the recipient. The implication is that this is a temporary condition; which will be alleviated after some delay. |
| error – user rejected | (507) User Rejected | The request is not executed since the user rejected the request. |

#### 5.4.1.5.3	Notification	Procedure Mapping for OMA DM 1.3 and OMA DM 2.0

After the subscription procedures are mapped as described in the clause 5.4.1.5.1 and 5.4.1.5.2, the <mgmtObj> Resource hosting CSE is being capable of monitoring changes for management objects in the device. By monitoring those changes for management objects, the <mgmtObj> Resource hosting CSE keeps the <mgmtObj> updated. Those modifications of the <mgmtObj> Resource will trigger the notification message to be sent to the subscribers according to the <subscription> Resource as specified by the [PRO-TS]. This notification procedure is defined by the oneM2M service layer and independent on the underlying management technologies.

### -----------------------End of New Text 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?