| CHANGE REQUEST |
| --- |
| Group Name:* | MAS#12 |
| Source:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Format:* | Plenary / Teleconference |
| Date:* | 2014-7-31 |
| Contact:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Reason for Change/s:* | To propose the LWM2M Server Interactions |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0005, ver 0.2.0 |
| Clauses/Sub Clauses* | 6.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution is to provide the LWM2M Server Interactions.

### -----------------------Start of change 1-------------------------------------------

## 6.5	LWM2M Server Interactions

This clause describes how the IN-CSE interacts with a LWM2M Server in order to manage the devices. The interaction between the IN-CSE and the LWM2M Server includes the followings:

- Communication session establishment

- Translations for requests/responses and notifications between the oneM2M service layer and the LWM2M protocol

- Discovery of the LWM2M Objects in the device and Management Resources in the IN-CSE.

Note: The LWM2M Server interaction is applicable to the case that the LWM2M Server is external to the IN-CSE.

### 6.5.1	Communication Session Establishment

The communication session can be initiated by the IN-CSE or by the LWM2M Server. The IN-CSE can initiate the communication session if the IN-CSE needs to interact with the LWM2M Objects in the device through the LWM2M Server (e.g., an IN-AE sends firmware update Requests by using the [firmware] Resource in the IN-CSE). On the other hands, the LWM2M Server can initiate the communication session if the LWM2M Server detects changes of LWM2M Objects that the LWM2M Server manages or needs to notify events to the IN-CSE that occurred in the device. In this case, the notifications of LWM2M Object changes or events can be limited to the cases that the IN-CSE has expressed interests.

The multiple communication sessions can be established between the IN-CSE and the LWM2M Server depending on the communication environments and the protocols to be used for the communication session.

Note: LWM2M protocol does not support the concept of the management session, hence the established communication session between the IN-CSE and the LWM2M Server shall not imply that there are active communications between the LWM2M Server and the LWM2M Client.

### 6.5.2	Translation of Requests and Responses between IN-CSE and LWM2M Server

This specification specifies how oneM2M service layer protocol regarding the device management shall be mapped to OMA LWM2M protocol. The interaction between the IN-CSE and the LWM2M Server lies between these two protocols and the Requests/Responses from those two protocols shall be properly translated by the interactions between the IN-CSE and the LWM2M Server. The Requests/Responses translations between the IN-CSE and the LWM2M Server may be done in any way that satisfies the procedure mappings specified at the clause 6.4.

Note: When the translated Request is delivered to the LWM2M Server via the communication session, the LWM2M Server may try to deliver the received Request to the device according to the policy of LWM2M Server.

### 6.5.3	Discovery and Subscription for LWM2M Objects

Being triggered by oneM2M service layer, the interactions between the IN-CSE and the LWM2M Server can provide the following functionalities:

- Discovery of LWM2M Objects in the devices of interest

- Subscription to LWM2M Objects for being notified for the interested events

With the discovery and the subscription to the LWM2M Objects in the device, the IN-CSE can be capable to synchronize the <mgmtObj> Management Resources with LWM2M Objects in the device.

### 6.5.4	Access Control Management

For a device under managements, the IN-CSE can have multiple LWM2M Servers that can connect to the device. Among those LWM2M Servers, when receiving the oneM2M service layer Requests, the IN-CSE needs to select the proper LWM2M Server that can successfully perform the received Request based on the access rights that each LWM2M Server has. The interaction between the IN-CSE and the LWM2M Server may be used to discover the access control that the LWM2M Server has for the target device.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?