| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG#5 |
| Title:* | Update Resource mapping to OMA -LWM2M |
| Source:* | Gemalto N.V (ETSI) |
| Contact: | Thierry GARNIER, Gemalto N.V, thierry.garnier@gemalto.com |
| Date:* | 2014-07-11 |
| Abstract:* | This contribution is to upgrade the Resource mapping for OMA LWM2M |
| Agenda Item:* | MAS#12 |
| Work item(s): | MAS Management Enablement (OMA) TS |
| Document(s) Impacted* | TS-0005 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Add proposed text to clauses 6. of TS-0005v0.2.0 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction

This contribution is to upgrade  the  Resource   mapping between oneM2M and OMA LWM2M

## ----------------------- start of text addition 1 ---------------

### 6.3.2	Resource [firmware]

The resource [firmware] is for firmware management in the service layer.

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:5 Firmware Update Object |
| objectPath | /5/0 |

The attributes of this Resource shall be mapped to specific resources of the LWM2M Firmware Update Object Instance  as follows:

| Attribute Name of [firmware] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| version | has to be assigned by Management Adapter when Package installed |
| name | has to be assigned by Management Adapter when Package installed |
| URL | 1 PackageURI |
| update | 2 Update |
| updateStatus | 3 UpdateResult |

### 6.3.3	Resource [software]

The resource [software] is for software management in the service layer.

Note : The OMA LWM2M Software Management Object is currently under specification at OMA. This resource mapping is provided as an example (Informations here are preliminary ones). “X” Object Identifier will be replaced when the official one will be registered in OMNA.

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:X |
| objectPath | /X/0 |

The attributes of this Resource shall be mapped to specific resources of the LWM2M Software Management Object when  publicly available

| Attribute Name of [software] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| version | 0 Version of the software package |
| name | 1 Name of the software package |
| URL | 2 Package URI |
| install | 4 Install / Update |
| uninstall | 6 Unisntall |
| installStatus | 9 Update Result |
| activate | Editor’s Note : has to be provided when OMA work is completed |
| deactivate | Editor’s Note : has to be provided when OMA work is completed |
| activeStatus | Editor’s Note : has to be provided when OMA work is completed |

### 6.3.5	Resource [areaNwkInfo]

The resource [areaNwkInfo] is for managing the area network.

Notes : There is currently no defined  LWM2M object yet This mapping is not available in this current specification .

Editor’s Note : It could be specified  under the oneM2M authority. Such an Object shall have to be OMNA-registered and specified in this document  “clause 6.6 New LWM2M Objects”.

### 6.3.6	Resource [areaNwkDeviceInfo]

The resource [areaNwkDeviceInfo] is for managing the device of the area network as well as acquiring information about devices in the area network.

Notes : There is currently no defined  LWM2M object yet This mapping is not available in this current specification .

Editor’s Note : It could be specified  under the oneM2M authority. Such an Object shall have to be OMNA-registered and specified in this document  “clause 6.6 New LWM2M Objects”.

The context of this Resource is the following:

### 6.3.9	Resource [deviceCapability]

The Resource [deviceCapability] is to manage the device capabilities such USB, camera, etc. The Resource [deviceCapability] is mapped to the LWM2M Device Capability Object specified in the clause 6.6.

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext:420x Editor’s Note: 4200 could be registered in OMNA as oneM2M SDO |
| objectPath | /420x/0 |

The attributes of this Resource shall be mapped to specific resources of the LWM2M Device Capability Object  as follows::

| Attribute Name of [deviceCapability] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| capabilityName | 0 Name |
| attached | 3 Attached |
| capabilityActionStatus | has to be assigned by Management Adapter |
| Enable | 5 opEnable |
| Disable | 6 op Disable |

### 6.3.11	Resource [eventLog]

The Resource [eventLog] is to record the event log for the device.

Editor’s Note:this Resource may be mapped to several LWM2M Objects according to the logTypeId attribute of this Resource as follows:

- Trap Event Logging Function  Object  if the logTypeId attribute is set to "TBD"

- Trace Logs  Object if the logTypeId attribute is set to "TBD"

- Panic Logs Object if the logTypeId attribute is set to "TBD"

Notes : There is currently no defined  LWM2M object yet This mapping is not available in this current specification

Editor’s Note : It could be specified  under the oneM2M authority. Such an Object shall have to be OMNA-registered and specified in this document  “clause 6.6 New LWM2M Objects”.

::

## ------------------------ end of text addition 1 ----------------

## ----------------------- start of text addition 2 ---------------

## New LWM2M Objects

    - LWM2M Device Capability Object

Editor’s Note : oneM2M will have to be register under  OMNA authority as an external SDO provider for  OMA LWM2M Objects.The allocated  range  used here (4200-42XX ) for oneM2M SDO is only  given as an example

| Description This LWM2M Object is dedicated to manage the device capabilities of a device e.g. USB, camera, etc. Object definition Name Object ID Instances Mandatory Object URN DevCapability 4200 Multiple Optional urn:oma:lwm2m:ext:4200 Resource definitions ID Name Operations Instances Mandatory Type Range or Enumeration Units Description 0 Property R Single Mandatory String Property name 1 Group R Single Optional String Group name of of Device Capabilities 2 Description R Single Optional String Device Capability Description 3 Attached R Single Optional Boolean This resource indicates whether the Device Capability is removable and whether it is currently attached to the device. If the leaf exists then the Device Capability is removable. If the value of this node is “True” the Device Capability is currently attached to the device; if the value of this node is “False” the Device Capability is currently detached from the device; 4 Enabled R Single Mandatory Boolean This resource indicates whether the Device Capability is enabled regardless whether the Device Capability is attached or not. If the value of this resource is “True” the Device Capability is in Enabled State. If the value of is “False” the Device Capability is in Disabled State; The ‘Attached’ property is independent of ‘Enabled’ property. A Device Capability MAY have ‘True’ as value for ‘Enabled’ node while having ‘False’ as value for the ‘Attached’ node. That means the Device Capability is still not available and can’t be used until it is attached to the Device, but will be useable once the Device Capability is attached. 5 opEnable E Single Mandatory This command is used to enable the Device Capability to transfer the Device Capability from Disabled State to Enabled state. In Enabled State, the Device Capability is allowed to work when it is attached to the Device. 6 opDisable E Single Mandatory This command is used to disable the Device Capability to transfer the Device Capability from Enabled State to Disabled State. In Disabled state the Device Capability is not allowed to work. 7 DenyUserEn Single Optional Boolean This resource specifies whether the user is able to enable a Device Capability. If this resource is not present or the value is False, the user is allowed to enable the Device Capability. If this resource is present and the value is True, the user is not allowed to enable the Device Capability. 8 NotifyUser Single Optional Boolean This resource specifies whether the user is notified when enable/disable Primitive is executed. If the resource is not present or the value is ‘False’, the user will not be notified about the result of the operation. If the node is present and the value is ‘True’, the user will be notified about the result of the operation. |  |
| --- | --- |

## ------------------------ end of text addition 2 ----------------