| CHANGE REQUEST |
| --- |
| Group Name:* | MAS#12 |
| Source:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Format:* | Plenary / Teleconference |
| Date:* | 2014-7-31 |
| Contact:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Reason for Change/s:* | to propose the status code maping for LWM2M |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0005, ver 0.2.0 |
| Clauses/Sub Clauses* | 6.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

to propose the status code maping for LWM2M

### -----------------------Start of change 1-------------------------------------------

## 6.4	Mapping of procedures for management

In this section, the oneM2M Primitives (i.e, Create, Retrieve, Update and Delete) are mapped to logical operations defined in OMA LWM2M.The LWM2M operations involved in that mapping  (i.e. Create, Read, Write, Execute and Delete operations ) are mapped on CoAP methods [7] . which are all carried as  Confirmable CoAP message . In LWM2M the responses to  these operations  are  carried directly in the Acknowledgement message that acknowledges the request

### 6.4.1	Create primitive for <mgmtObj> Resource

Depending on the mgmtDefinition attribute of the <mgmtObj> Resource (i.e. [memory], [battery], [deviceInfo], etc.), an instance of  the associated LWM2M Object as specified in the clause 6.3 should be created.

Receiving Create Request primitive does not imply that the LWM2M Create operations shall be always performed since, on receiving the Create Request primitive, the corresponding LWM2M Object Instance  may already exist in the device.

In case that the LWM2M Object Instance is  successfully created after receiving the Create Request primitive, then the objectID and objectPath attributes should be properly set based on the LWM2M Object.

The  Create primitive shall map to the OMA LWM2M Create operation and shall return one of the codes described in the following Table.

Table 6.4.1-1 Create Returned Codes Mapping

| Primitive Codes | Description | Returned Codes |
| --- | --- | --- |
| success | “Create” operation is completed successfully | 2.01 Created |
| error - already exists | Target (i.e., Object) already exists Mandatory Resources are not specified | 4.00 Bad Request |
| error – no priviledge | Access Right Permission Denied | 4.01 Unauthorized |
| error – not found | URI of “Create” operation is not found | 4.04 Not Found, |
| error – not allowed | Target is not allowed for “Create” operation | 4.05 Method Not Allowed |

### 6.4.2	Retrieve primitive for <mgmtObj> Resource

Depending on the mgmtDefinition attribute of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated LWM2M Object resources  as specified in the clause 6.3 shall be retrieved.

The  Retrieve primitive shall map to the LWM2M Read operation and shall return one of the codes described in the following Table.

Table 6.4.2-1 : Retrieve Returned Codes Mapping

| Primitive Codes | Description | Returned Codes |
| --- | --- | --- |
| success | “Retrieve” operation is completed successfully | 2.05 Content |
| error – no priviledge | Access Right Permission Denied | 4.01 Unauthorized, |
| error – not found | Target of “Retrieve” operation is not found | 4.04 Not Found, |
| error – not allowed | Target is not allowed for “Retrieve” operation | 4.05 Method Not Allowed |

### 6.4.3	Update primitive for <mgmtObj> Resource

The Update Request Primitive for <mgmtObj> Resource can be used to modify the resources of a LWM2M Object instance  or to execute the action related to a resource of a LWM2M Object instance.

The mapping in either cases shall be different.

### 6.4.3.1	Update primitive for replacing data

Depending on the mgmtDefinition attribute of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated  resource(s) of  the LWM2M Object instance as specified in the clause 6.3 shall be updated.

The  Update  primitive shall map to the LWM2M Write operation and shall return one of the codes described in the following table.

Table 6.4.3.1-1 : Update Returned Codes Mapping

| Primitive Codes | Description | Returned Codes |
| --- | --- | --- |
| success | “Update” operation is completed successfully | 2.04 Changed |
| error – bad request | The format of data to be updated is different | 4.00 Bad Request, |
| error – no priviledge | Access Right Permission Denied | 4.01 Unauthorized |
| error – not found | Target of ”Update“ operation is not found | 4.04 Not Found, |
| error – not allowed | Target is not allowed for “Update” operation | 4.05 Method Not Allowed |

### 6.4.3.2	Update primitive for execution operation

This is the case that the Update Primitive targets the attribute that is mapped to a  LWM2M resource that supports the Execute operation.

The  Update  primitive shall map to the LWM2M Execute operation and shall return one of the codes described in the following table

Table 6.4.3.2-1 : Execute Returned Codes Mapping

| Primitive Codes | Description | Returned Codes |
| --- | --- | --- |
| success | “Update” (“Execute”) operation is completed successfully | 2.04 Changed |
| error – bad request | Some issue with the “Update” argument | 4.00 Bad Request, |
| error – no privilege | Access Right Permission Denied | 4.01 Unauthorized |
| error – not found | Target of “Update” (“Execute”) operation is not found | 4.04 Not Found, |
| error – not allowed | Target is not allowed for “Update” (“Execute”) operation | 4.05 Method Not Allowed |

### 6.4.4	Delete  primitive for <mgmtObj> Resource

Depending on the mgmtDefinition attribute of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated LWM2M Object instance as specified in the clause 6.3 should be deleted.

Receiving Delete Request primitive does not imply that the corresponding LWM2M Object Instance  shall be always deleted.

The  Delete  primitive shall map to the LWM2M Delete operation and shall return one  of the codes described in the following table.

Table 6.4.4-1 : Delete Returned Codes Mapping

| Primitive Codes | Description | Returned Codes |
| --- | --- | --- |
| success | “Delete” operation is completed successfully | 2.02 Deleted |
| error – not allowed | Target (i.e., Object Instance) is not allowed for “Delete” operation | 4.00 Bad Request, |
| error – no privilege | Access Right Permission Denied | 4.01 Unauthorized, |
| error – not found | Target of “Delete” operation is not found | 4.04 Not Found, |
| error – not allowed | Target is not allowed for “Delete” operation | 4.05 Method Not Allowed |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?