| CHANGE REQUEST |
| --- |
| Group Name:* | MAS#12 |
| Source:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Format:* | Plenary / Teleconference |
| Date:* | 2014-7-31 |
| Contact:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Reason for Change/s:* | To cleanup TS-0005 |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0005, ver 0.2.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

To clean up TS-0005

### -----------------------Start of change 1-------------------------------------------

## 5.1	Mapping of basic data types

oneM2M has defined the data types that describe the format of the value stored with the attribute. Those oneM2M data types are listed in the below table, and mapped to the data types specified by OMA DM Protocol [4], [5]. Note that OMA DM 1.3 [4] and OMA DM 2.0 [5] uses the same data types.

| oneM2M Data Types | Mapping to data types in OMA DM | description |
| --- | --- | --- |
| TBD | null | OMA DM Nodes with null data type shall not store any value. |
| xs:base64Binary | b64 | Data type for Base64-encoded binary data |
| xs:base64Binary | bin | Data type for binary data. |
| xs:boolean | bool | Data type for Boolean. |
| xs:string | chr | Data type for text. The length limitation should be considered for the mapping. |
| xs:integer | int | Data type for 32-bit signed integer |
| xs:date | date | Data type for date in ISO 8601 [13] format with the century being included in the year |
| xs:time | time | Data type specifying that the Node value is a time in ISO 8601 format |
| xs:float | float | Data type for a single precision 32-bit floating point type as defined in XML Schema 1.0 [14] as the float primitive type |
| The mgmtLink attribute in the <mgmtObj> Resource |  | The OMA DM 'node' data type describes the format of the Interior Node that can have child Nodes. The mgmtLink attribute in the <mgmtObj> Resource supports the hierarchy of <mgmtObj> Resource. Note that this is not data type mapping. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 5.3.6	Resource [areaNwkDeviceInfo]

The resource [areaNwkDeviceInfo] is for managing the device of the area network as well as acquiring information about devices in the area network. Regardless of OMA DM 1.3 and OMA DM 2.0, the resource shall be mapped to MANDMO (urn:oma:mo:ext-etsi-mandmo:1.0). The attributes of the resource shall be mapped to nodes of the MO as follows.

| Attribute Name of [areaNwkDeviceInfo] | Mapping to Nodes in Management Object |
| --- | --- |
| devId | DevInfo/DevId |
| devType | DevDetail/DevType |
| areaNwkId | <x>/AreaNwks/<x>/AreaNwkID |
| sleepInterval | <x>/AreaNwks/<x>/SleepInterval |
| sleepDuration | <x>/AreaNwks/<x>/SleepDuration |
| status | <x>/AreaNwks/<x>/Status |
| listOfNeighbors | <x>/AreaNwks/<x>/Groups/ListOfDeviceNeighbors |

Here first instance of <x> is the interior node that is the root node for the MANDMO. Second instance of <x> is the interior node that contains information related to a specific M2M Area Network that the device is associated with.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 5.3.11	Resource [eventLog]

The Resource [eventLog] is to record the event log for the device. Regardless of OMA DM 1.3 and OMA DM 2.0, this Resource shall be mapped to several Management Objects according to the logTypeId attribute of this Resource as follows:

- Trap Event Logging Function Management Object (MOID: "urn:oma:mo:oma-diag:trapeventlogging:1.1") if the logTypeId attribute is set to "trap"

- Trace Logs Management Object (MOID: "urn:oma:mo:oma-diag:tracelog:1.0") if the logTypeId attribute is set to "trace"

- Panic Logs Management Object (MOID: "urn:oma:mo:oma-diag:paniclog:1.1") if the logTypeId attribute is set to "panic"

The attributes of this Resource shall be mapped to Nodes in above Management Objects as follows:

| Attribute Name of [eventLog] | Mapping to Nodes in Management Object |
| --- | --- |
| logTypeId | This attribute is not mapped to Nodes in Management Object. Instead, this attribute specifies the log type, and based on the log type, the actual Management Object mapped to this Resource is decided. |
| logData | "<x>/DiagMonData/log" Node for Trap Event Logging Function MO and Trace Logs MO. "<x>/DiagMonData/PanicLog" Node for Panic Logs MO |
| logActionStatus | "<x>/Status" Node for Trap Event Logging Function MO, Trace Logs MO and Panic Logs MO |
| logStart | "<x>/Operations/Start" Node for Trap Event Logging Function MO, Trace Logs MO and Panic Logs MO |
| logStop | "<x>/Operations/Stop" Node for Trap Event Logging Function MO, Trace Logs MO and Panic Logs MO |

Here <x> is the interior node that acts as a placeholder for the respective Management Objects.

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

## 6.1	Mapping of basic data types

oneM2M has defined the data types that describe the format of the value stored at the attribute. Those oneM2M data types are listed in the below table, and mapped to the data types specified by OMA Lightweight M2M 1.0 [6] (shortened in OMA LWM2M)

| oneM2M Data Types | Mapping to data types in OMA LWM2M | description |
| --- | --- | --- |
| xs:string | String | UTF-8 string |
| xs:integer | Integer | ASCII signed integer 1, 2,4, or 8 bytes |
| xs:boolean | Boolean | Data type for BooleanASCII value 0 or 1 |
| xs:float | Float | A 32 or 64-bit floating point value. The valid range of the value for a Resource SHOULD be defined. |
| xs:base64Binary | Opaque | A sequence of binary octets, the minimum and/or maximum length of the octets MAY be defined. |
| xs:dateTime | Time | Unix Time. A signed integer representing the number of seconds since Jan 1st, 1970 in the UTC time zone. |

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5-------------------------------------------

### 6.3.7	Resource [battery]

The Resource [battery] provides battery related information. For  OMA LWM2M, this Resource shall be mapped to the unique Instance of LWM2M Device Object (LWM2M ObjectID: 3).

The context of this Resource is as follows

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:3 |
| objectPath | /3/0 |

The attributes of this  Resource shall be mapped to specific resources of the LWM2M Device Object Instance  as follows:

| Attribute Name of [battery] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| batteryLevel | 9 : current battery level as percentage |
| batteryStatus m2m:batteryStatus [2] “NORMAL” “CHARGING” “CHARGE-COMPLETE” “DAMAGED” “LOW-BATTERY” “NOT-INSTALLED” “UNKNOWN” | 20 : contains the battery status Battery Status Description 0 The battery is operating normally and not on power. 1 The battery is currently charging. 2 The battery is fully charged and still on power. 3 The battery has some problem. 4 The battery is low on charge. 5 The battery is not installed. 6 The battery information is not available. |

### -----------------------End of change 5---------------------------------------------

### -----------------------Start of change 6-------------------------------------------

### 6.3.11	Resource [eventLog]

The Resource [eventLog] is to record the event log for the device.

Notes : There is currently no defined  LWM2M object yet This mapping is not available in this current specification

Editor’s Note : It could be specified  under the oneM2M authority. Such an Object shall have to be OMNA-registered and specified in this document  “clause 6.6 New LWM2M Objects”.

### -----------------------End of change 6---------------------------------------------

### -----------------------Start of change 7-------------------------------------------

### -----------------------End of change 7---------------------------------------------

### -----------------------Start of change 8-------------------------------------------

### -----------------------End of change 8---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?