| Input contribution Use case |
| --- |
| Use Case Title:* | MAS-2014-0474R01-Intelligent Indoor Air Cleaning Use Case |
| Group Name:* | WG5 |
| Source:* | Haier (CCSA), Huawei (CCSA) |
| Contact: | Jun Zhang, Haier, zhangjun@haierubic.com Yongjing Zhang, Huawei, zhangyongjing@huawei.com Jiaxin Yin, Huawei, yinjiaxin@huawei.com |
| Date:* | 2014-09-18 |
| Abstract:* | This proposal proposes an intelligent indoor air cleaning use case with semantic mash-up and device-control functions. |
| Agenda Item:* |  |
| Work item(s): | oneM2M-WI-0005-Abstraction_&_Semantics_Capability_Enablement |
| Document(s) Impacted* | oneM2M-TR-0007-Study_on_Abstraction_and_Semantics_Enablement V0_11_0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include the use case into Annex A, and consequently modify Table in section 5.2. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## ******************start of change 1 ****************************

## 5.2	Use Case Analysis

The following other use cases from TR-0001 [i.29] have semantic aspects:

-	Use Case on Devices, Virtual Devices and Things  (see [i.29], Section 8.2)

-	Semantic Home Control (see [i.29], Section 9.6).

-	Semantic Device Plug and Play (see [i.29], Section 9.7)

-	Vehicle Diagnostic & Maintenance Report (see [i.29], Section 10.1)

The Annex A introduces several use cases for abstraction and semantics to identify key functionalities and potential requirements. The following table summarizes key functionalities and potential requirements for all use cases described in the Annex.

Table 1 Use Cases Analysis

| Section | Name | Key functionalities | Potential requirements |
| --- | --- | --- | --- |
| A.1 | Home Environment Monitoring Service using semantic mash-up | Sematic mash-up | - |
| A.2 | Semantic Home Control [NOTE-1] | Ontology model (ThingType, DeviceType) Semantic query | - |
| A.3 | Gym Use Case | Ontology model of treadmills Semantic query | The M2M System shall provide the capability to publish semantic descriptions. The M2M System shall support parsing and interpreting semantic descriptions. The M2M System shall support resource discovery based on semantics. |
| A.4 | Intelligent Alarm Service using Semantic Discovery and Mash-up | Semantic discovery Semantic mash-up Ontology model | The M2M System shall provide capabilities to represent device and service information using ontology for service discovery, mash-up and data analysis. |
| A.5 | Semantic Home Automation Control | Semantic appliance template Home automation ontology model Semantic query | The M2M system shall be able to support semantic modelling device template for diverse M2M devices (e.g. household appliances). The M2M System shall support common ontology to model the semantic information of M2M devices and the real-world entities (e.g. rooms) that associate with M2M devices. The M2M System shall support semantic query to enable the discovery of target M2M devices based on their semantic information. |
| A.6 | Semantic smart building light control | Semantic annotation Triple stores with the relationship of multiple ontologies Semantic query Reasoning | The oneM2M systems shall support the reasoning capability for deriving implicit knowledge from semantically annotated information according to referenced ontologies. |
| A.7 | Smart Home load control | Context-based reasoning Semantic query | The M2M System shall provide the capability for entities of the M2M system (e.g. AEs, or CSEs) to publish semantic descriptions within the M2M system. The M2M System shall support parsing and interpreting semantic descriptions. The M2M System shall support resource discovery based on semantics. |
| A.8 | Intelligent Indoor Air Cleaning Use Case | Semantic mash-up Device control | The M2M System shall provide the capability of mashing up virtual device resources based on existing device resources using semantic description and reasoning. The M2M System shall provide the capability of data analytics (e.g. processing, calculation) through semantic mash-up. The M2M System shall provide the capability of applying pre-defined service logics (e.g. trigger operations upon other resources or attributes according to the change of the monitoring resource) using semantic rules and ontology. |

## ******************end of change 1 ****************************

## ******************start of change 2 ****************************

## A.8 Intelligent Indoor Air Cleaning Use Case

## A.8.1	Description

In the newly decorated house, building materials and furniture may release volatile organic compounds (VOC) such as CH2O, which is harmful to health. Thus, people usually spend several months to ventilate the house after decoration in order to reduce the VOC level. However, the volatilization rate of VOC decreases significantly with the drop of temperature and humidity indoors. In winter, it is not efficient to reduce the VOC just by opening windows.

Therefore, an intelligent indoor air cleaning system based on home automation appliances is proposed as shown in Figure 1. The air cleaning system is composed of the following appliances: IntelligentAirCleaning APP (IN-AE locates in smart phone), M2M Service Platform (IN-CSE), heating device (ASN) such as smart air-conditioner, air cleaning device (ASN) such as smart air cleaner or fresh air system, humidification device (ASN) such as smart humidifier, and  air quality monitoring device (ASN).

Figure 1. Intelligent Indoor Air Cleaning System

- IntelligentAirCleaning APP  (IN-AE)

  - Generates semantic query for existing home automation appliances involved in the pre-defined intelligent air cleaning system (such as air cleaning device, air quality monitoring device , heating device, humidification device), and send it to M2M Service Platform;

  - Allows users to define the detailed intelligent air cleaning service logic based on existing appliances, including appliances involved, and the threshold of air quality index (AQI) /temperature/humidity to switch on/off the air cleaning device/ heating device/ humidification device;

  - Send the details of user-defined intelligent air cleaning service logic (such as appliances involved, the threshold of AQI/temperature/humidity) to M2M Service Platform;

  - Receives data (such as current AQI value) from M2M Service Platform.

- M2M Service Platform  (IN-CSE with Semantics CSF)

  - Discovers and selects existing appliances according to semantic annotations when receiving semantic query, and returns the information (such as URIs of semantic data and functions) of selected appliances to IntelligentAirCleaning APP;

  - Generates virtual AQI Calculation Device resource and virtual Air Quality Control Device resource according to user-defined intelligent air cleaning service logic through the mash-up function of itsSemantics CSF;

  - Calculates AQI with collected air quality data according to the virtual AQI Calculation Device resource description, and pushes it to IntelligentAirCleaning APP;

  - Monitors the change of AQI, starts air cleaning device when AQI exceeds the user-defined threshold, meanwhile starts the heating device and the humidification device respectively if the indoor temperature and humidity exceeds the user-defined threshold, according to the virtual Air Quality Control Device resource description.

- Air Cleaning Device (ASN)

  - Offers air cleaning service according to received command.

- Air Quality Monitoring Device (ASN)

  - Monitors the temperature, humidity, VOC, CO2 and PM 2.5/10 indoors, reports the data to the M2M service platform periodically.

- Heating Device (ASN)

  - Offers heating service according to received command, to ensure that the indoor temperature is high enough for the VOC to volatilize in relatively high speed.

- Humidification Device (ASN)

  - Offers humidification service according to received command, to ensure that the indoor humidity is high enough for the VOC to volatilize in relatively high speed.

Figure 2 shows the ontology model for Intelligent Indoor Air Cleaning System.

Figure 2. Ontology Model for Intelligent Indoor Air Cleaning System

The service mapping relationships between virtual resources and home automation appliances is shown in figure 3.

- AQI Calculation Device

  - Takes the data of abstract device VOC/CO2/PM2.5/PM10 Sensors as inputs, calculates the AQI value with given service logic.

- Air Cleaning System

  - AirCleaning Service: takes AQI as input, and generates device-control message to call the functions of abstract device AirCleaning when AQI exceeds the user-defined threshold;

  - Humidity Control Service: takes AQI and data of abstract device Humidity Sensor as inputs, and generates device-control message to call the function of abstract device Humidification when AQI exceeds the user-defined threshold and the humidity is below the user-defined threshold;

  - Temperature Control Service: takes AQI and data of abstract device Temperature Sensor as inputs, and generates device-control message to call the function of abstract device Heating when AQI exceeds the user-defined threshold and the temperature is below the user-defined threshold.

Figure 3. Service Mapping Relationships

## A.8.2	Source

Haier (CCSA)

Huawei (CCSA)

## A.8.3	 Actors

- Home Automation APP

- M2M Service Platform

- Air Cleaning Device

- Air Quality Monitoring Device

- Heating Device

- Humidification Device

## A.8.4	Pre-conditions

The M2M Service Platform contains all the necessary information to manage the whole home automation appliances. It contains a Semantics CSF to support semantic functions such as mash-up and reasoning.

The IntelligentAirCleaning APP can generate semantic query to retrieve the appliance information from M2M Service Platform.

The home automation appliances can interact with the M2M Service Platform which can execute the appliance control command and report the appliance status to IntelligentAirCleaning APP.

## A.8.5	Triggers

None

## A.8.6	Normal Flow

Figure 4 displays the flow diagram of Intelligent Indoor Air Cleaning System.

- Step 0: The smart home service provider creates the ontology model and profile for the types of mentioned home automation appliances in M2M Service Platform in advance.

- Step 1: All nodes register resources to both local ASN-CSEs and ontology repository in M2M Service Platform respectively.

- Step 2: The IntelligentAirCleaning APP generates semantic queries for existing home automation appliances based on the pre-defined intelligent air cleaning system(e.g. gets air cleaning devices, gets air quality monitor devices, gets heating devices, gets humidification devices), and send it to M2M Service Platform.

- Step 3: The Semantic CSF of M2M Service Platform obtains the required appliances through semantic discovery, and returns the information (such as URIs of semantic data and functions) of obtained appliances to IntelligentAirCleaning APP.

- Step 4: The user defines the detailed intelligent air cleaning service logic based on existing appliances, including appliances involved, and the threshold of AQI/temperature/humidity.

- Step 5: The IntelligentAirCleaning APP sends the user-defined intelligent air cleaning service logic to M2M Service Platform.

- Step 6: The Semantic CSF of M2M Service Platform mashes up a virtual AQI Calculation Device resource and a virtual Air Quality Control Device resource according to user-defined intelligent air cleaning service logic.

- Step 7: The virtual resources of AQI Calculation Device and Air Quality Control Device offer intelligent air cleaning service for users. For example, it periodically calculates AQI and reports to IntelligentAirCleaning APP; starts air cleaning service (locates in the smart air cleaner) when AQI exceeds the user-defined threshold; starts heating service (locates in the smart air-conditioner) when the temperature is below the user-defined threshold; starts the humidification service (locates in the smart humidifier) when the humidity is below the user-defined threshold.

Figure 4. High Level Flow Diagram of Intelligent Indoor Air Cleaning System

## A.8.7	Post-conditions

None

## A.8.8	High Level Illustration

See Figure 1 and Figure 3 in A.8.1

## A.8.9	Potential requirements

- The M2M System shall provide the capability of mashing up virtual device resources based on existing device resources using semantic description and reasoning.

- The M2M System shall provide the capability of data analytics (e.g. processing, calculation) through semantic mash-up.

- The M2M System shall provide the capability of applying pre-defined service logics (e.g. trigger operations upon other resources or attributes according to the change of the monitoring resource) using semantic rules and ontology.

******************end of change 2 ****************************