| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG#5 |
| Title:* | LWM2M mapping Resources minor updates |
| Source:* | Gemalto N.V (ETSI) |
| Contact: | Thierry GARNIER, Gemalto N.V, thierry.garnier@gemalto.com |
| Date:* | 2014-23-09 |
| Abstract:* | This contribution is to bring updates to Mapping of Resources regarding OMA LWM2M |
| Agenda Item:* | MAS#13 |
| Work item(s): | MAS Management Enablement (OMA) TS |
| Document(s) Impacted* | TS-0005 vo.3.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To agree proposed text to clauses 6. of TS-0005v0.3.0 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## ----------------------- start of text addition 1 ---------------

### 6.3.2	Resource [firmware]

The resource [firmware] is for firmware management in the service layer.

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:5 Firmware Update Object |
| objectPath | /5/0 |

The attributes of this Resource shall be mapped to specific resources of the LWM2M Firmware Update Object Instance  as follows:

| Attribute Name of [firmware] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| version | 6 PkgVersion |
| name | 7 Pkgname |
| URL | 1 PackageURI |
| update | 2 Update |
| updateStatus | 3 UpdateResult |

## ------------------------ end of text addition 1 ----------------

## ----------------------- start of text addition 2 ---------------

### 6.3.3	Resource [software]

The resource [software] is for software management in the service layer.

Note: The OMA LWM2M Software Management Object is currently under specification at OMA. This resource mapping is provided as an example (Information here are preliminary ones). “X” Object Identifier will be replaced when the official one will be registered in OMNA.

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:X |
| objectPath | /X/0 |

The attributes of this Resource shall be mapped to specific resources of the LWM2M Software Management Object when publicly available

| Attribute Name of [software] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| version | 0 Version of the software package |
| name | 1 Name of the software package |
| URL | 2 Package URI |
| install | 4 Install / Update |
| uninstall | 6 Unisntall |
| installStatus | 9 Update Result |
| activate | 10 Activate |
| deactivate | 11 Deactivate |
| activeStatus | 12 ActivationResult |

## ------------------------ end of text addition 2 ----------------

## ----------------------- start of text addition 3 ---------------

### 6.3.9	Resource [deviceCapability]

The Resource [deviceCapability] is to manage the device capabilities such USB, camera, etc. The Resource [deviceCapability] is mapped to the LWM2M Device Capability Object specified in the clause 6.6.

Note: The LWM2M Device capability Object specification is currently under the process to be endorsed by OMA SDO; it exempts specific oneM2M  involvement on that topic . This resource mapping is provided as an example (Information here are preliminary ones). “X” Object Identifier will be replaced when the official one will be registered in OMNA.

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:X |
| objectPath | /X/0 |

The attributes of this Resource shall be mapped to specific resources of the LWM2M Device Capability Object  as follows::

| Attribute Name of [deviceCapability] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| capabilityName | 0 Name |
| attached | 3 Attached |
| capabilityActionStatus | has to be assigned by Management Adapter |
| Enable | 5 opEnable |
| Disable | 6 op Disable |

## ------------------------ end of text addition 3 ----------------

## ----------------------- start of text addition 4 ---------------

## ------------------------ end of text addition 4 ----------------

## ----------------------- start of text addition 5 ---------------

### 6.4.6 	Management Resource Specific Procedure Mapping

#### 6.4.6.1		Resource [firmware]

The generic <mgmtObj> mappings described in the clause 6.4.1 – 6.4.5 shall apply, and no specific mapping is necessary.

In addition to the status code mapping for the <mgmtObj> CRUD Operations, no [firmware] specific status code is defined in [6].

#### 6.4.6.2		Resource [software]

The generic <mgmtObj> mappings described in the clause 6.4.1 – 6.4.5 shall apply, and no specific mapping is necessary.

In addition to the status code mapping for the <mgmtObj> CRUD Operations, no [software] specific status code is defined in [6].

#### 6.4.6.6		Resource [deviceCapability]

The generic <mgmtObj> mappings described in the clause 6.4.1 – 6.4.5 shall apply, and no specific mapping is necessary.

In addition to the status code mapping for the <mgmtObj> CRUD Operations, no [deviceCapability] specific status code  is defined in [6].

## ----------------------- start of text addition 4 ---------------