| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG#5 |
| Title:* | Resource mapping of CMDH Policy to OMA -LwM2M |
| Source:* | Gemalto N.V (ETSI) |
| Contact: | Thierry GARNIER, Gemalto N.V, thierry.garnier@gemalto.com |
| Date:* | 2015-01-08 |
| Abstract:* | This contribution is to upgrade the Resource mapping for OMA LwM2M regarding the CMDH Policy Resource |
| Agenda Item:* | MAS TP#15 |
| Work item(s): | MAS Management Enablement (OMA) TS |
| Document(s) Impacted* | TS-0005 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Add proposed text to clauses 6.3. of TS -0005-v0.5.0 Add proposed new LwM2M Objects to clause 6.6 of TS -0005-v0.5.0 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction

This contribution is to upgrade  the  Resource   mapping between oneM2M and OMA LwM2M

## ----------------------- start of text addition 1 ---------------

### 6.3.12	Resource [cmdhPolicy]

The Resource Type [cmdhPolicy] represents a set of rules associated with a specific CSE that govern the behaviour of that CSE regarding rejecting, buffering and sending request or response messages via the Mcc reference point. See clause D.12 of TS-0001 [1] for a detailed high-level description of the overall structure of the [cmdhPolicy] resource.

The mapping  of  CMDH Policy Resources on LwM2M Device Management technology is addressed through the definitions of 9 specific LWM2M Objects:

- CmdhPolicy Object

- ActiveCmdhPolicy Object

- CmdhDefaults Object

- CmdhDefEcValues  Object

- CmdhDefEcParamsValues  Object

- CmdhLimits Object

- CmdhNetworkAccessRules Object

- CmdhNwAccessRule Object

- CmdhBuffer Object

These LwM2M Objects are specified in section 6.6.1 of this present document.

The Resource Type [cmdhPolicy] is a multi-instance Resource where each instance of the Resource shall map to an instance of  the LwM2M cmdhPolicy Object.

The context of this Resource is as follows

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:X |
| objectPath | /X/i |

Note : LwM2M Object ID from X to X+8 used here, will be allocated by OMNA, and will be in the range [2048 – 10240]

The attributes of an instance of [cmdhPolicy] shall be mapped to LwM2M resources of a given cmdhPolicy Object instance  as follows :

| Attribute Name of [cmdhPolicy] | Mapping to resources in LWM2M Object Instance |
| --- | --- |
| name | 0 : Name |
| cmdhDefaults | 1 : DefaultRule |
| cmdLimits | 2 : LimitRules |
| cmdhNwAccRules | 3 : NetworkAccessECRules |
| cmdhBuffer | 4 : BufferRules |

### 6.3.12.1	Resource [activeCmdhPolicy]

The Resource [activeCmdhPolicy] provides a link to the currently active set of CMDH policies, see clause D.12.1 of TS-0001 [1].

The Resource [activeCmdhPolicy] includes an attribute cmdhPolicy  which is mapped on the ActiveLink  resource of the LwM2M ActiveCmdhPolicy Object instance pointing to the active instance of the LwM2M CmdhPolicy Object.

The context of this Resource is as follows

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:X+1 |
| objectPath | /X+1/0 |

The attribute of  [activeCmdhPolicy] shall be mapped to the  resource of the LwM2M ActiveCmdhPolicy Object Instance  as follows:

| Attribute Name of [activeCmdhPolicy] | Mapping to resources in LwM2M Object Instance |
| --- | --- |
| cmdhPolicy | 0 : ActiveLink At most one <cmdhPolicy> instance shall be enabled at a time. Hence, there can only be a single instance of the activeCmdhPolicy whose cmdhPolicy attribute points to the active CMDH policy. |

### 6.3.12.2	Resource [cmdhDefaults]

The Resource [cmdhDefaults] defines default CMDH policy values, see clause D.12.2 of TS-0001 [1].

The Resource [cmdhDefaults] is a multi-instance Resource where each instance of the Resource shall map to an instance of the LwM2M cmdhDefaults Object.

The context of this Resource is as follows

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:X+2 |
| objectPath | /X+2/ i |

The attributes of an instance of [cmdhDefaults] shall be mapped to the resources of a LwM2M CmdDefaults  Object instance as follows:

| Attribute Name of [cmdhDefaults] | Mapping to resources in LwM2M Object Instance |
| --- | --- |
| cmdhDefEcValue | 0 : DefaultECRules |
| cmdhDefEcParamValues | 1 : DefaultECParamRules |

### 6.3.12.3	Resource [cmdhDefEcValues]

The Resource [cmdhDefEcValues] represents a default value for the ec (event category) parameter of an incoming request, see clause D.12.3 of TS-0001 [1].

The context of this Resource is as follows:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:X+3 |
| objectPath | /X+3/ i |

The Resource [cmdhDefEcValues] is a multi-instance Resource where each instance of the Resource shall map to an instance of the LwM2M CmdhDefEcValues Object.

The attributes of an Instance of this Resource shall be mapped  to the resources of  a LwM2M CmdhDefEcValues  Object instance  as follows:

| Attribute Name of [cmdhDefEcValues] | Mapping to resources in LwM2M Object Instance |
| --- | --- |
| order | 0 : Order |
| defECValue | 1 : DefEcValue |
| requestOrigin | 2 : RequestOrigin |
| requestContext | 3 : RequestContext |
| requestContextNotification | 4 : RequestContextNotification |
| requestCharacteristics | 5 : RequestCharacteristics |

### 6.3.12.4	Resource [cmdhEcDefParamValues]

The Resource  [cmdhEcDefParamValues] represents a specific set of default values for the CMDH related parameters rqet (request expiration timestamp), rset (result expiration timestamp), oet (operational execution time), rp (response persistence) and da (delivery aggregation) that are applicable for a given ec (event category) if these parameters are not specified in the request, see clause D.12.4 of TS-0001 [1].

The context of this Resource is as follows:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:X+4 |
| objectPath | /X+4/ i |

The Resource [cmdhEcDefParamValues] is a multi-instance Resource where each instance of the Resource shall map to an instance of the LwM2M CmdhEcDefParamValues Object.

The attributes of an instance of  [cmdhEcDefParamValues] shall be mapped to the resources of a  LwM2M  CmdhEcDefParamValues Object instance  as follows:

| Attribute Name of [cmdhEcDefParamValues] | Mapping to resources in LwM2M Object Instance |
| --- | --- |
| applicableEventCategory | 0 : ApplicableEventCategory |
| defaultRequestExpTime | 1 : DefaultRequestExpTime |
| defaultResultExpTime | 2 : DefaultResultExpTime |
| defaultOpExecTime | 3 : DefaultOpExecTime |
| default RespPersistence | 4 : DefaultRespPersistence |
| defaultDelAggregation | 5 : DefaultDelAggregation |

### 6.3.12.5	Resource [cmdhLimits]

The Resource [cmdhLimits] represents limits for CMDH related parameter values, see clause D.12.5 of TS-0001 [1].

The context of this Resource is as follows:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:X+5 |
| objectPath | /X+5/ i |

The Resource [cmdhLimits] is a multi-instance Resource where each instance of the Resource shall map to an instance of the CmdhLimits Object.

The attributes of an instance of  [cmdhLimits] shall be mapped to the resources of an instance of the LwM2M CmdhLimits  Object  as follows:

| Attribute Name of [cmdhLimits] | Mapping to resources in LwM2M CmdhLimits Object Instance |
| --- | --- |
| order | 0 : Order |
| requestOrigin | 1 : RequestOrigin |
| requestContext | 2 : RequestContext |
| requestContextNotification | 3 : RequestContextNotification |
| requestCharacteristics | 4 : RequestCharacteristics |
| limitsEventCategory | 5 : LimitsEventCategory |
| limitsRequestExpTime | 6 : LimitsRequestExpTime |
| limitsOpExecTime | 7 : LimitsOpExecTime |
| limitsRespPersistence | 8 : LimitsRespPersistence |
| limitsDelAggregation | 9 : LimitsDelAggregation |

### 6.3.12.6	Resource [cmdhNetworkAccessRules]

The Resource [cmdhNetworkAccessRules] defines the usage of underlying networks for forwarding information to other CSEs during processing of CMDH-related requests in a CSE, see clause D.12.6 of TS-0001 [1].

The context of this Resource is as follows:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:X+6 |
| objectPath | /X+6/ i |

The Resource [cmdhNetworkAccessRules] is a multi-instance Resource where each instance of the Resource shall map to an instance of  one instance of the LwM2M CmdhNetworkAccessRules Object.

The attributes of an instance of  [cmdhNetworkAccessRules] shall be mapped to the resources of  a LwM2M CmdhNetworkAccessRules Object Instance  as follows:

| Attribute Name of [cmdhNetworkAccessRules] | Mapping to resources in LwM2M Object Instance |
| --- | --- |
| applicableEventCategories | 0 : ApplicableEventCategories |
| cmdhNwAccessRule | 1 : NetworkAccessRule |

### 6.3.12.7	Resource [cmdhNwAccessRule]

The Resource [cmdhNwAccessRule] defines limits in usage of specific underlying networks for forwarding information to other CSEs during processing of CMDH-related requests, see clause D.12.7 of TS-0001 [1].

The context of this Resource is as follows:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:X+7 |
| objectPath | /X+7/ i |

The Resource [cmdhNwAccessRule] is a multi-instance Resource where each instance of the Resource shall map to an instance of the LwM2M CmdhNwAccessRule Object.

The attributes of an instance of  [cmdhNwAccessRule] shall be mapped to  the resources of  a LwM2M cmdhNwAccessRule Object Instance  as follows:

| Attribute Name of [cmdhNwAccessRule] | Mapping to resources in LwM2M Object Instance |
| --- | --- |
| targetNetwork | 0 : TargetNetwork |
| minReqVolume | 1 : MinReqVolume |
| backOffParameters | 2 : BackOffParameters |
| otherConditions | 3 : OtherConditions |
| allowedSchedule | 4 : AllowedSchedule |

### 6.3.12.8	Resource [cmdhBuffer]

The Resource [cmdhBuffer] represents limits in usage of buffers for temporarily storing information that needs to be forwarded to other CSEs during processing of CMDH-related requests in a CSE, see clause D.12.8 of TS-0001 [1].

The context of this Resource is as follows:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext-onem2m:X+8 |
| objectPath | /X+8/ i |

The Resource [cmdhBuffer] is a multi-instance Resource where each instance of the Resource shall map to an instance of the LwM2M CmdhBuffer Object.

The attributes of an instance of [cmdhBuffer] shall be mapped to the resources of an LwM2M cmdhBuffer Object Instance  as follows:

| Attribute Name of [cmdhBuffer] | Mapping to resources in LwM2M Object Instance |
| --- | --- |
| applicableEventCategory | 0 : ApplicableEventCategory |
| maxBufferSize | 1 : MaxBufferSize |
| storagePriority | 2 : StoragePriority |

## ----------------------- end of text addition 1 ---------------

## ----------------------- start of text addition 2 ---------------

## New LwM2M Objects

These LwM2M Objects are specified by oneM2M organization. They still have to be registered using the process defined by OMNA (Open Mobile Naming Authority).

The Object ID (e.g. “X”) of the LwM2M Objects specified here, will be allocated by OMNA, and will be in the range [2048 – 10240]

    - LwM2M CMDH Policy Objects

| Description The LwM2M Objects specified here are used for mapping the CMDH Policy Resources defined in oneM2M This oneM2M CMDH Policy mapping is addressed through the specification of 9 specific LwM2M Objects: CmdhPolicy Object ActiveCmdhPolicy Object CmdhDefaults CmdhDefEcValues Object CmdhDefEcParamsValues Object CmdhLimits Object CmdhNetworkAccessRules Object CmdhNwAccessRule Object CmdhBuffer Object CmdhPolicy Object Object definition Name Object ID Instances Mandatory Object URN CmdhPolicy X Multiple Optional urn:oma:lwm2m:ext-onem2m:X Resource definitions ID Name Operations Instances Mandatory Type Range or Enumeration Units Description 0 Name RW Single Mandatory String 1 DefaultRule RW Multiple Mandatory Objlink 2 LimitRules RW Multiple Mandatory Objlink 3 NetworkAccessECRules RW Multiple Mandatory Objlink 4 BufferRules RW Multiple Mandatory Objlink ActiveCmdhPolicy Object Object definition Name Object ID Instances Mandatory Object URN ActiveCmdhPolicy X+1 Single Mandatory urn:oma:lwm2m:ext-onem2M:X+1 Resource definitions |  |
| --- | --- |
| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| 0 | ActiveLink | RW | Single | Mandatory | Objlink |  |  |  |

      - CmdhDefaults  Object

Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| CmdhDefaults | X+2 | Multiple | Mandatory | urn:oma:lwm2m:ext-onem2m:X+2 |

Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | DefaultECRules | RW | Multiple | Mandatory | Objlink |  |  |  |
| 1 | DefaultECParamRules | RW | Multiple | Mandatory | Objlink |  |  |  |

      - CmdhDef ECValues Object

Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| CmdhDefECValues | X+4 | Multiple | Mandatory | urn:oma:lwm2m:ext-onem2m:X+4 |

Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | Order | RW | Single | Mandatory | Integer |  |  |  |
| 1 | DefEcValue | RW | Single | Mandatory | String |  |  |  |
| 2 | RequestOrigin | RW | Multiple | Mandatory | String |  |  |  |
| 3 | RequestContext | RW | Single | Optional | String |  |  |  |
| 4 | RequestContextNotification | RW | Single | Optional | Boolean |  |  |  |
| 5 | RequestCharacteristics | RW | Single | Optional | String |  |  |  |

      - CmdhDefaultsECParamValues Object

Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| CmdhDefECParamValues | X+4 | Multiple | Mandatory | urn:oma:lwm2m:ext-onem2m:X+4 |

Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | ApplicableEventCategory |  | Multiple | Mandatory | Integer |  |  |  |
| 1 | DefaultRequestExpTime |  | Single | Mandatory | Integer |  |  |  |
| 2 | DefaultResultExpTime |  | Single | Mandatory | Integer |  |  |  |
| 3 | DefaultOpExecTime |  | Single | Mandatory | Integer |  |  |  |
| 4 | DefaultRespPersistence |  | Single | Mandatory | Integer |  |  |  |
| 5 | DefaultDelAggregation |  | Single | Mandatory | Integer |  |  |  |

      - CmdhLimits  Object

Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| CmdhLimits | X+5 | Multiple | Mandatory | urn:oma:lwm2m:ext-onem2m:X+5 |

Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | Order | RW | Single | Mandatory | Integer |  |  |  |
| 1 | RequestOrigin | RW | Multiple | Mandatory | String |  |  |  |
| 2 | RequestContext | RW | Single | Optional | String |  |  |  |
| 3 | RequestContextNotification | RW | Single | Optional | Boolean |  |  |  |
| 4 | RequestCharacteristics | RW | Single | Optional | String |  |  |  |
| 5 | LimitsEventCategory | RW | Multiple | Mandatory | Integer |  |  |  |
| 6 | LimitsRequestExpTime | RW | Multiple | Mandatory | Integer | 2 Instances |  | Inst 0 : minTime Inst 1: maxTime |
| 7 | LimitsResultExpTime | RW | Multiple | Mandatory | Integer | 2 Instances |  | Inst 0 : minTime Inst 1: maxTime |
| 8 | LimitsOptExpTime | RW | Multiple | Mandatory | Integer | 2 Instances |  | Inst 0 : minTime Inst 1: maxTime |
| 9 | LimitsRespPersistence | RW | Multiple | Mandatory | Integer | 2 Instances |  | Inst 0 : minTime Inst 1: maxTime |
| 10 | LimitsDelAggregation | RW | Single | Mandatory | Integer |  |  |  |

Editor’s Note : By anticipation, LimitsDelAggregation  is defined here as Integer  instead of Boolean  . This has to be confirmed during TP#15 meeting

      - CmdhNetworkAccessRules  Object

Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| CmdhNetworkAccessRules | X+6 | Multiple | Mandatory | urn:oma:lwm2m:ext-onem2m:X+6 |

Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | ApplicableEventCategories | RW | Multiple | Mandatory | Integer |  |  |  |
| 1 | NetworkAccessRule | RW | Multiple | Mandatory | Objlink |  |  |  |

      - CmdhNwAccessRule  Object

Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| CmdhNwAccessRule | X+7 | Multiple | Mandatory | urn:oma:lwm2m:ext-onem2m:X+7 |

Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | TargetNetwork | RW | Multiple | Mandatory | String |  |  |  |
| 1 | MinReqVolume | RW | Single | Mandatory | Integer |  |  |  |
| 2 | BackOffParameters | RW | Multiple | Mandatory | Integer | 3 Instances | ms | 0 : BackOffTime 1: BackOffTimeIncrement 2 : MaxBackOffTime |
| 3 | OtherConditions | RW | Single | Mandatory | String |  |  |  |
| 4 | AllowedSchedule | RW | Single | Mandatory | String |  |  |  |

      - CmdhBuffer  Object

Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| CmdhBuffer | X+8 | Multiple | Mandatory | urn:oma:lwm2m:ext-onem2M:X+8 |

Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | ApplicableEventCategory | RW | Multiple | Mandatory | Integer |  |  |  |
| 1 | MaxBufferSize | RW | Single | Mandatory | Integer |  |  |  |
| 2 | StoragePriority | RW | Single | Mandatory | Integer |  |  |  |

## ------------------------ end of text addition 2 ----------------