| CHANGE REQUEST |
| --- |
| Group Name:* | MAS#15 |
| Title: * | access control mapping |
| Source:* | Huawei Technologies Co., Ltd. |
| Format:* | Physical meeting |
| Date:* | 2015-1-7 |
| Contact:* | Jiaxin Yin, Huawei Technologies, yinjiaxin@huawei.com |
| Reason for Change/s:* | The contribution is to clarify the access control mapping when performing device management |
| CR against: Release* | Release 1 |
| CR against: TS/TR* | TS-0005, ver 0.5.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The contribution clarifies the access control of DM.

### -----------------------Start of Change 1-------------------------------------------

### 5.5.4	Access Control Management

For a device under managements, the IN-CSE can have multiple DM Servers that can connect to the device. When receiving the oneM2M service layer Requests, the IN-CSE shall first authorize the Request based on the <accessControlPoilicy> resource associated with the addressed <mgmtObj> resource, Then, among those DM Servers, the IN-CSE needs to select the proper DM Server that can successfully perform the received Request based on the access rights that each DM Server has. The interaction between the IN-CSE and the DM Server can be used to discover the access rights that the DM Server has. The DM Server is agnostic of the identity or roles used in the service layer.

### -----------------------End of Change 1-------------------------------------------

### -----------------------Start of Change 2-------------------------------------------

### 5.3.10	Resource [reboot]

The Resource [reboot] is to reboot the device. Regardless of OMA DM 1.3 and OMA DM 2.0, this Resource shall be mapped to Restart Management Object (MOID: "urn:oma:mo:oma-diag:restart:1.0") that is specified in Diag Mon [ref] and Lock and Wipe Management Object (MOID: "urn:oma:mo:oma-lawmo:1.0"). The attributes of this Resource shall be mapped to Nodes in the Management Objects as follows:

| Attribute Name of [reboot] | Mapping to Nodes in Management Object |
| --- | --- |
| reboot | "<x>/Operations/Start" Node in Restart MO. The restarting level described at the "<x>/DiagMonConfig/ConfigParms/RestartLevel" Node is up to the implementation. |
| factoryReset | "<x>/Operations/FactoryReset" Node in LAWMO |

Here <x> is the interior node that acts as a placeholder for the Restart MO and the LAWMO.

### -----------------------End of Change 2-------------------------------------------

### -----------------------Start of Change 3-------------------------------------------

### 6.5.4	Access Control Management

For a device under managements, the IN-CSE can have multiple LWM2M Servers that can connect to the device. When receiving the oneM2M service layer Requests, the IN-CSE shall first authorize the Request based on the <accessControlPoilicy> resource associated with the addressed <mgmtObj> resource, Then, among those LWM2M Servers, when receiving the oneM2M service layer Requests, the IN-CSE needs to select the proper LWM2M Server that can successfully perform the received Request based on the access rights that each LWM2M Server has. The interaction between the IN-CSE and the LWM2M Server may be used to discover the access control that the LWM2M Server has for the target device. The LWM2M Server is agnostic of the identity or roles used in the service layer.

### -----------------------End of Change 3-------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?