| Input Contribution |
| --- |
| Meeting ID* | TP#16 |
| Title:* | Modeling aspects for mash-up |
| Source:* | <Junling Mao> , <China Unicom> , <maojl11@chinaunicom.cn> <Changwei Hu>, <China Unicom>, <hucw5@chinaunicom.cn> <Peng Wang>, <China Unicom>, <wangpeng@chinaunicom.cn> |
| Uploaded Date:* | 2015-03-10 |
| Document(s) Impacted* | oneM2M-TR-0007-Study_on_Abstraction_and_Semantics_Enablement |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | For discussions and adoption in the Abstraction and Semantics Technical Report. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

The mash-up capability is considered to be required in oneM2M systems, since it can facilitate the access of complicated parameters which cannot be directly measured by physical sensors and support cooperative working of multiple devices. In this contribution, we give some considerations on the modelling aspects supporting mash-up.

- Discussion

According to the current device and things aspect association model in TR 0007, the mash-up relationships can be modelled in three categories.

- Things category

In this category, the mash-up relationship will be described from the perspective of things aspect. There will be a semantic rule or ontology to state the natural relationship between the mash-up things aspect and other related things aspects, e.g. the relationship between the air aspect Air quality index (AQI) and other air aspects such as PM2.5, PM10, SO2 and NO2. This is highly related to the domain ontology of air environment.

- Devices category

In this category, the mash-up relationship will be described from the perspective of devices. There will be a semantic rule or ontology to state the relationship between the operation of the mash-up devices and the operations of other devices involved in the mash-up. Fig.1 gives an example for the mash-up modelling in device category.

Fig.1 an example for mash-up modelling in device category

- Association category

In this category, the mash-up relationship will be described from the perspective of association. There will be a semantic rule or ontology to state the association between the mash-up aspect and related devices, e.g. the association between AQI and air quality related monitoring devices such as PM2.5, PM10, SO2 and NO2 monitoring devices. This type of association is more complex than the current association in TR 0007, since it will associate with multiple devices and a mash-up logic. Fig. 2 gives an example for mash-up modelling in association category.

Fig.2 an example for mash-up modelling in association category

In Table I, we give the comparisons of above modelling methods. It can be observed that modelling in devices category is preferred for the cooperative working case, and modelling in association category is more suitable for the complicated parameter sensing case.

Table I. comparisons of mash-up relationship modelling

|  | Advantages | Weakness |
| --- | --- | --- |
| Things category | Natural expressions for the mash-up relationship Independent from the type of devices associated with thing aspects | hardly reflect the measured or impact quality may need to extend domain ontology |
| Devices category | easy for modelling the cooperative working of multiple devices flexible for reconstructing the mash-up of devices | not easy for reflecting the measured quality for the mash-up aspects impacted by the devices involved in mash-up. |
| Association category | facilitate reflecting the measured or impact quality flexible for reconstructing the mash-up of devices | not easy for modelling the cooperative working of multiple devices |

In table II, we show the relationship between above modelling categories and the works in oneM2M.

Table II. relationship between above modelling categories and works in oneM2M

|  | Things category | Devices category | Association category |
| --- | --- | --- | --- |
| Related modelling aspects | Related to things domain ontology modelling | Highly related to the modelling of virtual devices created by the mash-up of devices | Related to the modelling of association between the reources involved in mash-up and the target things apsect; (e.g. direct mash-up association between the data involved in mash-up and the target things aspect) |
| Relationship with oneM2M | Out of scope of oneM2M | In the scope of TR0007 | For future evaluation |

In summary, modelling in devices category needs to be considered first, since the virtual devices created by mash-up is already discussed in TR 0007 and we need to model this.  In addition, considering the compatibility of simultaneous modelling in above three categories  and the benefits of modelling in association category,  in future if necessary we can discuss whether to adopt the modelling in association category as supplement.

- Proposal

It is proposed to model the mash-up relationship in devices category and add the new section 8.2.2.x as the subsection of section 8.2.2 in TR 0007.

======================== Start of 1st Change ========================

### 8.2.2	Modelling of Devices and Things

#### 8.2.2.x	Modelling of mash-up devices

The basic structure for modelling Devices is described in Fig. 27 of section 8.2.2.1.In that structure, specific Device Types and successively Operation and Parameter Types are involved. The structure for modelling mash-up device (i.e. the virtual device created by mash-up) should inherit the basic structure for modelling devices, but may extend the basic structure for describing the mash-up relationship between mash-up devices and other devices involved in mash-up. A concept named Mash-up is introduced for representing the mash-up relationship.

As shown in Fig. x, the Operation of mash-up device will be linked to the Mash-up concept.  Besides Operation of mash-up device, the Mash-up concept is also associated with Operations of other devices involved in mash-up and a Mash-up logic concept.

Fig.x Example structure for modelling mash-up devices

There are two types of relations between the Mash-up concept and Operations of other devices involved in mash-up. One type indicates that the Operation plays an input role in the mash-up, i.e. the Parameter of the Operation will be an input parameter in the mash-up.  The other type indicates that the Operation plays an output role in the mash-up, i.e. the Parameter of the Operation will be an output parameter in the mash-up..

The Mash-up logic concept is used to describe the service logic used in the mash-up.  It will have a data type property (e.g. xsd: string) for logic expression to indicate the mapping relationship among the Parameters of  Operations of other devices involved in the mash-up and the Parameters of Operation of Mash-up Devices.

Based on the logic expression of Mash-up logic, the input parameters of  Operation of Mash-up Device will be mapped to set the input Parameters of Operation involved in mash-up, and the output Parameters of Operation involved in mash-up can be mapped to the set of output parameters of Operation of Mash-up Device. The Parameters of Operation that plays input role in mash-up can also be mapped to set the parameters of Operation that plays output role in mash-up.

# ======================== End of 1st Change ========================