| CHANGE REQUEST |
| --- |
| Meeting:* | MAS 17 |
| Source:* | Catalina Mladin, InterDigital Lijun Dong, InterDigital |
| Date:* | 2015-05-15 |
| Contact:* | Catalina.Mladin@InterDigital.com Lijun.Dong@InterDigital.com |
| Reason for Change/s:* | TR-007 text for 8.4.1 R01 addresses initial comments at REQ#17: re-do examples to reflect m2m domain and include all properties. |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0007V2.2.0 |
| Clauses/Sub Clauses* | Section 8 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes additional text for TR-0007 section 8.4.1 to further detail and clarify the support for common languages.

### -----------------------Start of change 1 -------------------------------------------

## 8.4	Architectural Aspects

This clause presents architectural recommendations for, or potential constraints to, the oneM2M architectural design. This clause also highlights any restrictions that the oneM2M architecture potentially places on utilisation of the analysed semantics technologies within oneM2M.

### 8.4.1	Support of common languages

RDF(S) and OWL have been introduced in section 6.1.3 as most common languages for describing ontologies.

The Resource Description Framework (RDF) is a framework for representing information on the Web. It is essentially a data-model using as building block a resource-property-value triple, called a statement.

In the example shown below, an RDF graph is used to depict the statement that Sample1 is measured on “2014-08-21”. RDF graphs are powerful for representing information, but abstract and better suited for human analysis, not for application exchange.

Figure 39 A semantic example in RDF Graph form

RDF statements could also be represented in a concrete format, such as a file or other byte stream. The most popular used expressive formats are RDF/XML and the Terse RDF Triple Language (Turtle). The figures below show the RDF statements in RDF/XML and Turtle respectively.

<rdf:RDF xmlns:rdf="http://www.w3.org/1999/02/22-rdf-syntax-ns#" xmlns:xsd ="http://www.w3.org/2001/XLMSchema#" xmlns:m2m="http://www.mydomain.org/m2m-ns"> <rdf:Description rdf:about="Sample1"> < m2m:measuredOn>"2014-08-21"^^xsd:date"</m2m:measuredOn> <m2m:unit>"mmHg"</m2m:unit> </rdf:Description> </rdf:RDF>

Figure 40 RDF Statement in RDF/XML

@prefix rdf: http://www.w3.org/1999/02/22-rdf-syntax-ns# . @prefix rdfs: http://www.w3.org/2000/01/rdf-schema# . @prefix m2m: http://www.mydomain.org/m2m-ns . m2m:Sample1 m2m:measuredOn "2014-08-21"^^xsd:date m2m:unit "mmHg"

Figure 41 RDF Statement in Turtle

Based on the RDF triples (subject, predicate and object) resources can be structured using a RDFS (RDF Schema) vocabulary. RDF use of a loose set of relations (triples) make it ideal for the integration of possibly heterogenous information on oneM2M platforms. RDF is domain-independent, so no assumptions about a particular domain of use are made. It is up to the users to define their own terminology in a schema language called RDF Schema (RDFS). RDFS defines the vocabulary used in RDF data models. In RDFS we can define the vocabulary, specify which properties apply to which kinds of objects and what values they can take, and describe the relationships between objects.

In the example above xmlns:m2m  in  is the self-defined domain name, in which the property measuredOn is defined as part of the RDFS.

Semantic technologies use a combination of a schema language and an ontology language to provide enhanced capabilities. RDFS vocabulary can be extended by the Web Ontology Language (OWL) with additional resources that can be used to build more expressive ontologies for the web.

OWL uses a predefined, reserved vocabulary to define classes and the relationships between them for specific areas of interest, At the same time, OWL introduces additional restrictions regarding the structure and contents of RDF documents in order to make processing, reasoning more computationally feasible. For example, OWL defines properties that correspond to the standard set operators: intersection, union, and complement to define Boolean combinations of classes.

The table below shows an example of using intersection to define the concept of ConstrainedDevice  is the intersection of several clasees: the Device class and three anonymous classes that put restrictions on specific paramaters such as memory, computing power and energy   . At first glance, it might appear that the OWL is equivalent to saying that ConstrainedDevicer is rdfs:subClassOf Device as well as of each of the classes setting restrictions on memory, computing power and energy . However, subClassOf statements only state that all  constrained devices  must be  dedevices and have restricted values of memory, computing power and energy . They cannot be used to infer that  an entity is a constrained device from only their being devices and their belonging to the three restricted classes , as can be done using owl:intersectionOf.

<owl:Class rdf:ID=”ConstrainedDevice”> <owl:intersectionOf rdf:parseType=”Collection”> <owl:Class rdf:about=”#Device”/> <owl:Restriction> <owl: onProperty ref:resource=”#availableMemory”/> <owl:hasValue rdf:resource=”#Amount_Limited_Memory”/> <owl:Restriction> <owl:Restriction> <owl: onProperty ref:resource=”#computingPower”/> <owl:hasValue rdf:resource=”#Amount_Limited_Computing”/> <owl:Restriction> <owl:Restriction> <owl: onProperty ref:resource=”#availableEnergy”/> <owl:hasValue rdf:resource=”#Amount_Limited_Energy”/> <owl:Restriction> </owl:intersectionOf> </owl:Class>

Figure 42 Example of owl:intersection

OWL uses the RDF and RDFS, XML schema datatypes, and OWL namespaces. The OWL vocabulary itself is defined in the namespace http://www.w3.org/2002/07/owl# and is commonly referred to by the prefix owl.

OWL allows you to use a number of predefined datatypes, most of which are defined in the XML Schema

RDF based vocabularies such as RDFS or OWL, make it easy to define inference possibilities and use expressive formats such as RDF/XML and Turtle.. As such the use of RDF and OWL as common languages within oneM2M is recommended.

### ----------------------- End of change 1 -------------------------------------------