| CHANGE REQUEST |
| --- |
| Meeting:* | MAS#17 |
| Source:* | NTT |
| Date:* | 2015-05-18 |
| Contact:* | Yoshihisa Ito, NTT, ito.yoshihisa@lab.ntt.co.jp |
| Reason for Change/s:* | Propose new description of device-specific abstract information model |
| CR against: Release* |  |
| CR against: WI* | Active <Work Item number> WI-0017 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0017 V.0.2.0 |
| Clauses/Sub Clauses* | 5.3, 2.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes charatarictics of smart meter and new chapter structure in ‘5.3.1.2 Device Sets’.

## -----------------------Start of change 1-------------------------------------------

#### 5.3.1.2	Device Sets

This section provides details on the ‘device’ for the abstract information model of the home domain. In the device sets, device-specific characteristic(s) as well common characteristic(s) are defined. Among home domain devices, the washer and the smart mater for energy management are  considered for representation.

- Washer

| Chracteristic Name | Data Type | Value | Permission | Description |
| --- | --- | --- | --- | --- |
| vendorSpecific | xs:anySimpleType | - | RW | See clause 5.3.1 where this common attribute is described. |
| deviceFirmwareID | xs:string | - | RO | See clause 5.3.1 where this common attribute is described. |
| deviceType | xs:positiveInteger | - | RO | See clause 5.3.1 where this common attribute is described. |
| deviceAlias Name | xs:positiveInteger | - | RO | See clause 5.3.1 where this common attribute is described. |
| deviceSub ModelName | xs:string | - | RO | See clause 5.3.1 where this common attribute is described. |
| nation | xs:string | - | RO | See clause 5.3.1 where this common attribute is described. |
| deviceModel Name | list | - | RO | See clause 5.3.1 where this common attribute is described. |
| deviceID | xs:string | - | RO | See clause 5.3.1 where this common attribute is described. |
| error | xs:positiveInteger | 1: door open 2: water supply 3: drainage 4: spin-dry 5: water-level 6: sensor water level 7: temperature sensor 8: motor 9: clutch 17: door lock | RO | Error status |
| mode | xs:nonNegativeInteger | 0: off 5: preparation 6: pause 20: wash preparation 23: wash 30: rinse 40: spin-dry 50: dry 60: wash off 62: on | RO | Wash status |
| state | xs:boolean | 0: off 1: on | RW | Power status |
| smart | xs:boolean | 0: off 1: on | RO | Remote control status |
| water | xs:nonNegativeInteger | 0: no choice 1: cold water 2: hot water 3: tepid water | RO | Temperature of supply water |
| total | xs:string | - | RO | Remain time + Reserve time (HHMM) |
| remain | xs:string | - | RO | Remain time (HHMM) |
| reserve | xs:string | - | RO | Reserve time (HHMM) |
| name | xs:positiveInteger | 1: standard/normal 2: wool 3: quick(speed) wash 4: bulky/bedding 6: silent 7: laundry tub dry 8: laundry tub clean 11: frugal wash 12: towel 13: functional clothing 17: double rense 18: stain(soak) 19: spin onlt 20: rinse + spin | RO | Configured washer course |
| soilLevel | xs:nonNegativeInteger | 0: no wash 1: 3 2: 6 3: 10 4: 12 5: 14 6: 17 7: 19 8: 21 9: 23 10: 25 | RO | Configured soil level |
| spinLevel | xs:nonNegativeInteger | 0: no spin-dry 1: delicate 2: low 3: medium 4: high 5: highest | RO | Configured spin level |
| rinse | xs:nonNegativeInteger | 0: 0 1: 1 2: 2 8: 3 9: 4 10: 5 | RO | Configured rinse value |
| soak | xs:nonNegativeInteger | 0: none 1: 15 minutes 2: 30 minutes 3: 45 minutes 4: 60 minutes 5: 120 minutes 6: 180 minutes | RO | Configured soak information |
| waterFlow | xs:nonNegativeInteger | 0: None 1: Strong 2: Normal 3: weak | RO | Configured water flow information |

##### Smart Meter

| Chracteristic Name | Data Type | Value | Permission | Description |
| --- | --- | --- | --- | --- |
| vendorSpecific | xs:anySimpleType | - | RW | See clause 5.3.1 where this common attribute is described. |
| deviceFirmwareID | xs:string | - | RO | See clause 5.3.1 where this common attribute is described. |
| deviceType | xs:positiveInteger | - | RO | See clause 5.3.1 where this common attribute is described. |
| deviceAlias Name | xs:positiveInteger | - | RO | See clause 5.3.1 where this common attribute is described. |
| deviceSub ModelName | xs:string | - | RO | See clause 5.3.1 where this common attribute is described. |
| nation | xs:string | - | RO | See clause 5.3.1 where this common attribute is described. |
| deviceModel Name | List | - | RO | See clause 5.3.1 where this common attribute is described. |
| deviceID | xs:string | - | RO | See clause 5.3.1 where this common attribute is described. |
| instaneous PowerConsumption | xs:double | - | RO | Measured instaneous power consumption. |
| cumulative PowerConsumption | xs:nonNegativeInteger | - | RO | Measured cumulative power consumption. |
| instaneous PowerGeneration | xs:double | - | RO | Measured instaneous power generation. |
| cumulative PowerGeneration | xs:nonNegativeInteger | - | RO | Measured instaneous power generation. |
| powerConsumption Limit | xs:double | - | RW | Cofigured power limitation. |
| objective | xs: nonNegativeInteger | 0: whole house 1: breaker 2: room 3: device | RO | Objective of meter |

## -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?