| CHANGE REQUEST |
| --- |
| Meeting:* | MAS#17 |
| Source:* | Heedong Choi, LG Electronics, heedong.choi@lge.com |
| Date:* | 2015-05-18 |
| Contact:* | Heedong Choi, LG Electronics, heedong.choi@lge.com |
| Reason for Change/s:* | Proposes a design principle of abstract information model |
| CR against: Release* |  |
| CR against: WI* | Active <Work Item number> WI-0017 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0017 V.0.2.0 |
| Clauses/Sub Clauses* | 5.3.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes additional illustrations for “abstract information model: Approach 1” with the restructure and minor editorial changes.

## -----------------------Start of change 1-------------------------------------------

## 5.3	Define Abstract and Describe Specific Abstract Information Model

This section defines plural abstract information model for the home domain devices based on the design principle.

### 5.3.1	Abstract Information Model: Approach 1

This approach is based on the ‘Design principle: Approach 1’ (section 5.2.1). That is, this section provides details on the ‘Characteristic’ and ‘Device’ for the abstract information model of the home domain. Here, the data type is defined in [i.7].

#### Common Characteristic

Since some characteristics in all home domain devices may have same values, the common characteristic sets are considered to avoid duplicating the description.

Table 5.3.1-1: Common Characteristics

| Characteristic Name | Description |
| --- | --- |
| deviceFirmwareVersion | Firmware version |
| deviceFirmwareID | Firmware ID |
| deviceType | Device type. Each device type is defined as follows: 101: refrigerator 201: washer 301: oven 401: airconditioner 501: robot cleaner 601: smart meter |
| deviceAliasName | Device alias name |
| deviceSubModelName | Device sub-model name |
| nation | Nation code |
| deviceModelName | Device model name |
| deviceID | Device ID |
| powerStatus | Power status of the device. Power status is defined as follows: 0: off 1: on |
| representedPower | Instantaneous power consumption of the device. |
| usedEnergy | Cumulative energy consumption of the device. |

#### Device Sets

In the device sets, device-specific characteristic(s) as well common characteristic(s) are defined. Among home domain devices, the washer is considered for representation.

#### 5.3.1.1	Washer

Table 5.3.1.1-1: Abstract Information Model of Washer

| Characteristic Type | Characteristic Name | Data Type | Value | Permission | Description |
| --- | --- | --- | --- | --- | --- |
| Common | deviceFirmwareID | xs:string | - | RO | See table 5.3.1-1 |
| Common | deviceFirmware Version | xs:string | - | RO | See table 5.3.1-1 |
| Common | deviceType | xs:positiveInteger | - | RO | See table 5.3.1-1 |
| Common | deviceAlias Name | xs:positiveInteger | - | RO | See table 5.3.1-1 |
| Common | deviceSub ModelName | xs:string | - | RO | See table 5.3.1-1 |
| Common | nation | xs:string | - | RO | See table 5.3.1-1 |
| Common | deviceModel Name | xs:string | - | RO | See table 5.3.1-1 |
| Common | deviceID | xs:string | - | RO | See table 5.3.1-1 |
| Common | powerStatus | xs:boolean | - | RW | See table 5.3.1-1 |
| Common | representedPower | xs:double | - | RO | See table 5.3.1-1 |
| Common | usedEnergy | xs:double | - | RO | See table 5.3.1-1 |
| Device- specific | totalTime | xs:string | - | RO | Remain time + Reserve time (HHMM) |
| Device- specific | remainTime | xs:string | - | RO | Remain time (HHMM) |
| Device- specific | reserveTime | xs:string | - | RO | Reserve time (HHMM) |
| Vendor- specific | vendorSpecific | xs:anySimpleType | - | RW | The characteristic contains vendor-specific information. |

#### 5.3.1.2	Refrigerator

Table 5.3.1.5-1: Abstract Information Model of Refrigerator

| Characteristic Type | Characteristic Name | Data Type | Value | Permission | Description |
| --- | --- | --- | --- | --- | --- |
| Common | deviceFirmwareID | xs:string | - | RO | See table 5.3.1-1 |
| Common | deviceFirmware Version | xs:string | - | RO | See table 5.3.1-1 |
| Common | deviceType | xs:positiveInteger | - | RO | See table 5.3.1-1 |
| Common | deviceAlias Name | xs:positiveInteger | - | RO | See table 5.3.1-1 |
| Common | deviceSub ModelName | xs:string | - | RO | See table 5.3.1-1 |
| Common | nation | xs:string | - | RO | See table 5.3.1-1 |
| Common | deviceModel Name | xs:string | - | RO | See table 5.3.1-1 |
| Common | deviceID | xs:string | - | RO | See table 5.3.1-1 |
| Common | powerStatus | xs:boolean | - | RW | See table 5.3.1-1 |
| Common | representedPower | xs:double | - | RO | See table 5.3.1-1 |
| Common | usedEnergy | xs:double | - | RO | See table 5.3.1-1 |
| Device- specific | freezerTemp | xs:integer | - | RW | Temperature of freezer |
| Device- specific | fridgeTemp | xs:integer | - | RW | Temperature of fridge |
| Vendor- specific | vendorSpecific | xs:anySimpleType | - | RW | The characteristic contains vendor-specific information. |

## -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?