| CHANGE REQUEST |
| --- |
| Meeting:* | MAS TP18 |
| Source:* | GEMALTO N.V |
| Date:* | 2015-07-09 |
| Contact:* | Thierry Garnier , GEMALTO N.V, Thierry.garnier@gemalto.com |
| Reason for Change/s:* | Align (OMA DM & LWM2M) TS0005 regarding Resource Names & Atributes changes in TS-0002 Minor fixes |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0005 V1.0.1 |
| Clauses/Sub Clauses* | Clause 5 & 6 and Sub Clauses |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

## ----------------------- start of text addition 1 ---------------

### 5.3.8	Resource [deviceInfo]

The Resource [deviceInfo] is to provide device related information. For OMA DM 1.3, this Resource shall be mapped to DevInfo MO (MOID: "urn:oma:mo:oma-dm-devinfo:1.1") and DevDetail MO (MOID: "urn:oma:mo:oma-dm-devdetail:1.1"). The attributes of this Resource shall be mapped to Nodes in two Management Objects as follows.

# Table 5.3.8-1 Resource [deviceInfo] mapping in OMA DM 1.3

| Attribute Name of [deviceInfo] | Mapping to Nodes in Management Object |
| --- | --- |
| deviceLabel | DevInfo/DevId |
| manufacturer | DevInfo/Man |
| model | DevInfo/Mod |
| deviceType | DevDetail/DevType |
| fwVersion | DevDetail/FwV |
| swVersion | DevDetail/SwV |
| hwVersion | DevDetail/HwV |

For OMA DM 2.0, this Resource shall be mapped to DevInfo MO (MOID: "urn:oma:mo:oma-dm-devinfo:1.2"). The attributes of this Resource shall be mapped to Nodes in the Management Object as follows.

# Table 5.3.8-2 Resource [deviceInfo] mapping in OMA DM 2.0

| Attribute Name of [deviceInfo] | Mapping to Nodes in Management Object |
| --- | --- |
| deviceLabel | <x>/DevID |
| manufacturer | <x>/Man |
| model | <x>/Mod |
| deviceType | <x>/DevType |
| fwVersion | <x>/FwV |
| swVersion | <x>/SwV |
| hwVersion | <x>/HwV |
| NOTE: Here <x> is the interior node that is the root node for the DevInfo MO. |

### 5.3.9	Resource [deviceCapability]

The Resource [deviceCapability] is to manage the device capabilities such USB, camera, etc. Regardless of OMA DM 1.3 and OMA DM 2.0, this Resource shall be mapped to Device Capability Management Object (MOID: "urn:oma:mo:oma-dcmo:1.0"). The attributes of this Resource shall be mapped to Nodes in the Management Object as follows.

# Table 5.3.9-1 Resource [deviceCapability]

| Attribute Name of [deviceCapability] | Mapping to Nodes in Management Object |
| --- | --- |
| capabilityName | <x>/Property |
| attached | <x>/Attached |
| capabilityActionStatus | This attribute is managed by the <mgmtObj> resource hosting CSE, and does not need to be mapped to OMA DM management objects. |
| enable | <x>/Operations/Enable |
| disable | <x>/Operations/Disable |
| NOTE: Here <x> is the interior node groups together the parameters of a DCMO for a particular Device Capability. |

### 5.3.10	Resource [reboot]

The Resource [reboot] is to reboot the device. Regardless of OMA DM 1.3 and OMA DM 2.0, this Resource shall be mapped to Restart Management Object (MOID: "urn:oma:mo:oma-diag:restart:1.0") that is specified in Diag Mon [ref] and Lock and Wipe Management Object (MOID: "urn:oma:mo:oma-lawmo:1.0"). The attributes of this Resource shall be mapped to Nodes in the Management Objects as follows.

# Table 5.3.10-1 Resource [reboot]

| Attribute Name of [reboot] | Mapping to Nodes in Management Object |
| --- | --- |
| reboot | "<x>/Operations/Start" Node in Restart MO. The restarting level described at the "<x>/DiagMonConfig/ConfigParms/RestartLevel" Node is up to the implementation. |
| factoryReset | "<x>/Operations/FactoryReset" Node in LAWMO |
| NOTE: Here <x> is the interior node that acts as a placeholder for the Restart MO and the LAWMO. |

### 5.3.11	Resource [eventLog]

The Resource [eventLog] is to record the event log for the device. Regardless of OMA DM 1.3 and OMA DM 2.0, this Resource shall be mapped to several Management Objects according to the logTypeId attribute of this Resource as follows:

Trap Event Logging Function Management Object (MOID: "urn:oma:mo:oma-diag:trapeventlogging:1.1") if the logTypeId attribute is set to "trap".

Trace Logs Management Object (MOID: "urn:oma:mo:oma-diag:tracelog:1.0") if the logTypeId attribute is set to "trace".

Panic Logs Management Object (MOID: "urn:oma:mo:oma-diag:paniclog:1.1") if the logTypeId attribute is set to "panic".

The attributes of this Resource shall be mapped to Nodes in above Management Objects as follows.

# Table 5.3.11-1 Resource [eventLog]

| Attribute Name of [eventLog] | Mapping to Nodes in Management Object |
| --- | --- |
| logTypeId | This attribute is not mapped to Nodes in Management Object. Instead, this attribute specifies the log type, and based on the log type, the actual Management Object mapped to this Resource is decided |
| logData | "<x>/DiagMonData/log" Node for Trap Event Logging Function MO and Trace Logs MO "<x>/DiagMonData/PanicLog" Node for Panic Logs MO |
| logStatus | "<x>/Status" Node for Trap Event Logging Function MO, Trace Logs MO and Panic Logs MO |
| logStart | "<x>/Operations/Start" Node for Trap Event Logging Function MO, Trace Logs MO and Panic Logs MO |
| logStop | "<x>/Operations/Stop" Node for Trap Event Logging Function MO, Trace Logs MO and Panic Logs MO |
| NOTE: Here <x> is the interior node that acts as a placeholder for the respective Management Objects. |

### 5.3.12	Resource [cmdhPolicy]

The Resource Type [cmdhPolicy] represents a set of rules associated with a specific CSE that govern the behaviour of that CSE regarding rejecting, buffering and sending request or response messages via the Mcc reference point. See clause D.12 of oneM2M TS-0001 [1] for a detailed high-level description of the overall structure of the [cmdhPolicy] resource, and clause D.12 of TS-0004 [2] for details on the data types of the Resource attributes.

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).  The root node of the MCMDHMO is denoted in the following by the leftmost placeholder node <x>.

The Resource Type [cmdhPolicy] is a multi-instance Resource where each instance of the Resource shall map to an instance of a <x>/cmdhPolicy/<x> node.

The attributes of an instance of [cmdhPolicy] shall be mapped to nodes of the MCMDHMO as follows.

# Table 5.3.12-1: Resource [cmdhPolicy]

| Attribute Name of [cmdhPolicy] | Mapping to Nodes in Management Object |
| --- | --- |
| name | <x>/cmdhPolicy/<x>/name |
| cmdhDefaults | <x>/cmdhPolicy/<x>/defaultRule |
| cmdhLimits | <x>/cmdhPolicy/<x>/limitRules |
| cmdhNetworkAccessRules | <x>/cmdhPolicy/<x>/networkAccessECRules |
| cmdhBuffer | <x>/cmdhPolicy/<x>/bufferRules |

#### 5.3.12.1	Resource [activeCmdhPolicy]

The Resource [activeCmdhPolicy] provides a link to the currently active set of CMDH policies, see clause D.12.1 of oneM2M TS-0001 [1] and TS-0004 [2].

The Resource [activeCmdhPolicy] includes an attribute activeCmdhPolicyLink which is mapped to a leaf node enable The value of enable shall point to the currently active instance of a <x>/cmdhPolicy node.

# Table 5.3.12.1-1: Resource [activeCmdhPolicy]

| Attribute Name of [activeCmdhPolicy] | Mapping to Nodes in Management Object |
| --- | --- |
| activeCmdhPolicyLink | <x>/activeCmdhPolicy/<x>/enable At most one <cmdhPolicy> instance shall be enabled at a time. Hence, there can only be a single instance of the activeCmdhPolicy whose enable parameter points to the active CMDH policy. |

#### 5.3.12.2	Resource [cmdhDefaults]

The Resource [cmdhDefaults] defines which CMDH related parameters will be used by default when a request or response message contains the Event Category parameter but not any other CMDH related parameters and which default Event Category parameter shall be used when none is given in the request or response, see clauses D.12.2 of oneM2M TS-0001 [1] and TS-0004 [2].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource [cmdhDefaults] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/cmdhDefaults/<x> node.

The attributes of an instance of [cmdhDefaults] shall be mapped to nodes of the MCMDHMO as follows.

# Table 5.3.12.2-1: Resource [cmdhDefaults]

| Attribute Name of [cmdhDefaults] | Mapping to Nodes in Management Object |
| --- | --- |
| cmdhDefEcValue | <x>/cmdhDefaults/<x>/defaultECRules |
| cmdhEcDefParamValues | <x>/cmdhDefaults/<x>/defaultECParamRules |

#### 5.3.12.3	Resource [cmdhDefEcValue]

The Resource [cmdhDefEcValue] represents a default value for the ec (event category) parameter of an incoming request or response when this parameter is not indicated in the message itself, see clauses D.12.3 of oneM2M TS-0001 [1] and TS-0004 [2].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource [cmdhDefEcValue] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/cmdhDefEcValue/<x> node.

The attributes of an instance of [cmdhDefEcValue] shall be mapped to nodes of the MCMDHMO as follows.

# Table 5.3.12.3-1: Resource [cmdhDefEcValue]

| Attribute Name of [cmdhDefEcValues] | Mapping to Nodes in Management Object |
| --- | --- |
| order | <x>/cmdhDefEcValue/<x>/order |
| defEcValue | <x>/cmdhDefEcValue/<x>/defEcValue |
| requestOrigin | <x>/cmdhDefEcValue/<x>/requestOrigin |
| requestContext | <x>/cmdhDefEcValue]/<x>/requestContext |
| requestContextNotification | <x>/cmdhDefEcValue]/<x>/requestContextNotification |
| requestCharacteristics | <x>/cmdhDefEcValue/<x>/requestCharacteristics |

#### 5.3.12.4	Resource [cmdhEcDefParamValues]

The Resource  [cmdhEcDefParamValues] represents a specific set of default values for the CMDH related parameters rqet (request expiration timestamp), rset (result expiration timestamp), oet (operational execution time), rp (response persistence) and da (delivery aggregation) that are applicable for a given ec (event category) if these parameters are not specified in the request, see clauses D.12.4 of oneM2M TS-0001 [1] and TS-0004 [2].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource [cmdhEcDefParamValues] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/cmdhEcDefParamValues/<x> node.

The attributes of an instance of [cmdhEcDefParamValues] shall be mapped to nodes of the MCMDHMO as follows.

# Table 5.3.12.4-1: Resource [cmdhEcDefParamValues]

| Attribute Name of [cmdhEcDefParamValues] | Mapping to Nodes in Management Object |
| --- | --- |
| applicableEventCategory | <x>/cmdhEcDefParamValues/<x>/applicableEventCategory |
| defaultRequestExpTime | <x>/cmdhEcDefParamValues/<x>/defaultRequestExpTime |
| defaultResultExpTime | <x>/cmdhEcDefParamValues/<x>/defaultResultExpTime |
| defaultOpExecTime | <x>/cmdhEcDefParamValues/<x>/defaultOpExecTime |
| defaultRespPersistence | <x>/cmdhEcDefParamValues/<x>/defaultRespPersistence |
| defaultDelAggregation | <x>/cmdhEcDefParamValues/<x>/defaultDelAggregation |

#### 5.3.12.5	Resource [cmdhLimits]

The Resource [cmdhLimits] represents limits for CMDH related parameter values  in request and response messages for a given setting of the ec parameter, see clause D.12.5 of oneM2M TS-0001 [1] and TS-0004 [2].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource [cmdhLimits] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/cmdhLimits/<x> node.

The attributes of an instance of [cmdhLimits] shall be mapped to nodes of the MCMDHMO as follows.

# Table 5.3.12.5-1: Resource [cmdhLimits]

| Attribute Name of [cmdhLimits] | Mapping to Nodes in Management Object |
| --- | --- |
| order | <x>/cmdhLimits/<x>/order |
| requestOrigin | <x>/cmdhLimits/<x>/requestOrigin |
| requestContext | <x>/cmdhLimits/<x>/requestContext |
| requestContextNotification | <x>/cmdhLimits/<x>/requestContextNotification |
| requestCharacteristics | <x>/cmdhLimits/<x>/requestCharacteristics |
| limitsEventCategory | <x>/cmdhLimits/<x>/limitsEventCategory |
| limitsRequestExpTime | <x>/cmdhLimits/<x>/limitsRequestExpTime |
| limitsResultExpTime | <x>/cmdhLimits/<x>/limitsResultExpTime |
| limitsOpExecTime | <x>/cmdhLimits/<x>/limitsOpExecTime |
| limitsRespPersistence | <x>/cmdhLimits/<x>/limitsRespPersistence |
| limitsDelAggregation | <x>/cmdhLimits/<x>/limitsDelAggregation |

## ------------------------ end of text addition 1 ----------------

## ----------------------- start of text addition 2 ---------------

# 6	OMA Lightweight M2M 1.0

## 6.1	Mapping of basic data types

oneM2M has defined the data types that describe the format of the value stored at the attribute. Those oneM2M data types are listed in the below table, and mapped to the data types specified by OMA Lightweight M2M 1.0 [5] (shortened in OMA LWM2M).

# Table 6.1-1 Basic data types

| oneM2M Data Types | Mapping to data types in OMA LWM2M | description |
| --- | --- | --- |
| xs:string | String | UTF-8 string. |
| xs:integer | Integer | ASCII signed integer 1, 2,4 or 8 bytes. |
| xs:boolean | Boolean | Data type for BooleanASCII value 0 or 1. |
| xs:float | Float | A 32 or 64-bit floating point value. The valid range of the value for a Resource SHOULD be defined. |
| xs:base64Binary | Opaque | A sequence of binary octets, the minimum and/or maximum length of the octets MAY be defined. |
| xs:dateTime | Time | Unix Time. A signed integer representing the number of seconds since Jan 1st, 1970 in the UTC time zone. |
| The mgmtLink attribute in the <mgmtObj> Resource | Objlink | The OMA LwM2M Objlink data type describes the format of a reference to an Object Instance. The mgmtLink attribute in the <mgmtObj> Resource supports the hierarchy of <mgmtObj> Resource. |

## ------------------------ end of text addition 2 ----------------

## ----------------------- start of text addition 3 ---------------

### 6.3.8	Resource [deviceInfo]

The Resource [deviceInfo] provides device related information. For OMA LWM2M, this Resource shall be mapped to the unique Instance of LWM2M Device Object (LWM2M ObjectID: 3).

The context of this Resource is the following.

# Table 6.3.8-1 Context of resource [deviceInfo]

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:3 |
| objectPath | /3/0 |

The attributes of this Resource shall be mapped to specific resources of the LWM2M Device Object Instance  as follows.

# Table 6.3.8-2 Attributes of resource [deviceInfo]

| Attribute Name of [deviceInfo] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| deviceLabel | 2 Serial Number |
| manufacturer | 0 Manufacturer name |
| model | 1 Model Number |
| deviceType | 17 The class of the device |
| fwVersion | 3 Firmware Version |
| swVersion | 19 Software Version of the device |
| hwVersion | 18 Hardware version of the device |

### 6.3.9	Resource [deviceCapability]

The Resource [deviceCapability] is to manage the device capabilities such USB, camera, etc. The Resource [deviceCapability] is mapped to the LWM2M Device Capability Management Object (urn:oma:lwm2m:oma:15 [19])

The context of this Resource is the following.

# Table 6.3.9-1 Context of resource [deviceCapability]

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:15 |
| objectPath | /15/{i} |

The attributes of this Resource shall be mapped to specific resources of the LWM2M Device Capability Management Object  as follows.

# Table 6.3.9-2 Attributes of resource [deviceCapability]

| Attribute Name of [deviceCapability] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| capabilityName | 2 Property |
| attached | 3 Attached |
| capabilityActionStatus | Has to be assigned by Management Adapter |
| enable | 5 opEnable |
| disable | 6 op Disable |

### 6.3.10	Resource [reboot]

The Resource [reboot] is used for rebooting the device. For OMA LWM2M, this Resource shall be mapped to the unique Instance of LWM2M Device Object (LWM2M ObjectID: 3).

The context of this Resource is as follows.

# Table 6.3.10-1 Context of resource [reboot]

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:3 |
| objectPath | /3/0 |

The attributes of this Resource shall be mapped to  LWM2M Device Object Instance  as follows.

# Table 6.3.10-2 Attributes of resource [reboot]

| Attribute Name of [reboot] | Mapping to resources in LWM2M Object Instance |
| --- | --- |
| reboot | 4 reboot the LWM2M Device to restore the Device from unexpected firmware failure. |
| factoryReset | 5 Perform Factory Reset : the LWM2M device return to the same configuration as at the initial deployment. |

### 6.3.11	Resource [eventLog]

The Resource [eventLog] is to record the event log for the device.

NOTE:	There is currently no defined LWM2M object yet. This mapping is not available in the present document.

### 6.3.12	Resource [cmdhPolicy]

The Resource Type [cmdhPolicy] represents a set of rules associated with a specific CSE that govern the behaviour of that CSE regarding rejecting, buffering and sending request or response messages via the Mcc reference point. See clause D.12 of TS-0001 [1] for a detailed high-level description of the overall structure of the [cmdhPolicy] resource.

The mapping  of  CMDH Policy Resources on LWM2M Device Management technology is addressed through the definitions of 9 specific LWM2M Objects:

CmdhPolicy Object

ActiveCmdhPolicy Object

CmdhDefaults Object

CmdhDefEcValue  Object

CmdhDefEcParamsValues  Object

CmdhLimits Object

CmdhNetworkAccessRules Object

CmdhNwAccessRule Object

CmdhBuffer Object

These LWM2M Objects are specified in section 6.6.1 of this present document and are registered in OMNA as LWM2M objects.

The Resource Type [cmdhPolicy] is a multi-instance Resource where each instance of the Resource shall map to an instance of  the LWM2M cmdhPolicy Object.

The context of this Resource is as follows

# Table 6.3.12-1: Context of resource [cmdhPolicy]

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext:2048 |
| objectPath | /2048/{i} |

The attributes of an instance of [cmdhPolicy] shall be mapped to LWM2M resources of a given cmdhPolicy Object instance  as follows :

# Table 6.3.12-2: Attributes of resource [cmdhPolicy]

| Attribute Name of [cmdhPolicy] | Mapping to resources in LWM2M Object Instance |
| --- | --- |
| name | 0 : Name |
| cmdhDefaults | 1 : DefaultRule |
| cmdLimits | 2 : LimitRules |
| cmdhNwAccRules | 3 : NetworkAccessECRules |
| cmdhBuffer | 4 : BufferRules |

#### 6.3.12.1	Resource [activeCmdhPolicy]

The Resource [activeCmdhPolicy] provides a link to the currently active set of CMDH policies, see clause D.12.1 of TS-0001 [1].

The Resource [activeCmdhPolicy] includes an attribute cmdhPolicy  which is mapped on the ActiveLink  resource of the LWM2M ActiveCmdhPolicy Object instance pointing to the active instance of the LWM2M CmdhPolicy Object.

The context of this Resource is as follows

# Table 6.3.12.1-1: Context of resource [activeCmdhPolicy]

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext:2049 |
| objectPath | /2049/0 |

The attribute of  [activeCmdhPolicy] shall be mapped to the  resource of the LWM2M ActiveCmdhPolicy Object Instance  as follows:

# Table 6.3.12.1-2: Attributes of resource [activeCmdhPolicy]

| Attribute Name of [activeCmdhPolicy] | Mapping to resources in LWM2M Object Instance |
| --- | --- |
| cmdhPolicy | 0 : ActiveLink At most one <cmdhPolicy> instance shall be enabled at a time. Hence, there can only be a single instance of the activeCmdhPolicy whose cmdhPolicy attribute points to the active CMDH policy. |

#### 6.3.12.2	Resource [cmdhDefaults]

The Resource [cmdhDefaults] defines default CMDH policy values, see clause D.12.2 of TS-0001 [1].

The Resource [cmdhDefaults] is a multi-instance Resource where each instance of the Resource shall map to an instance of the LWM2M cmdhDefaults Object.

The context of this Resource is as follows

# Table 6.3.12.2-1: Context of resource [cmdhDefaults]

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext:2050 |
| objectPath | /2050/{i} |

The attributes of an instance of [cmdhDefaults] shall be mapped to the resources of a LWM2M CmdDefaults  Object instance as follows:

# Table 6.3.12.2-2: Attributes of resource [cmdhDefaults]

| Attribute Name of [cmdhDefaults] | Mapping to resources in LWM2M Object Instance |
| --- | --- |
| cmdhDefEcValue | 0 : DefaultECRules |
| cmdhDefEcParamValues | 1 : DefaultECParamRules |

#### 6.3.12.3	Resource [cmdhDefEcValue]

The Resource [cmdhDefEcValue] represents a default value for the ec (event category) parameter of an incoming request, see clause D.12.3 of TS-0001 [1].

The context of this Resource is as follows:

# Table 6.3.12.3-1: Context of resource [cmdhDefEcValues]

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext:2051 |
| objectPath | /2051/{i} |

The Resource [cmdhDefEcValue] is a multi-instance Resource where each instance of the Resource shall map to an instance of the LWM2M CmdhDefEcValue Object.

The attributes of an Instance of this Resource shall be mapped  to the resources of  a LWM2M CmdhDefEcValue  Object instance  as follows:

# Table 6.3.12.3-2: Attributes of resource [cmdhDefEcValue]

| Attribute Name of [cmdhDefEcValue] | Mapping to resources in LWM2M Object Instance |
| --- | --- |
| rder | 0 : Order |
| defECValue | 1 : DefEcValue |
| requestOrigin | 2 : RequestOrigin |
| requestContext | 3 : RequestContext |
| requestContextNotification | 4 : RequestContextNotification |
| requestCharacteristics | 5 : RequestCharacteristics |

#### 6.3.12.4	Resource [cmdhEcDefParamValues]

The Resource  [cmdhEcDefParamValues] represents a specific set of default values for the CMDH related parameters rqet (request expiration timestamp), rset (result expiration timestamp), oet (operational execution time), rp (response persistence) and da (delivery aggregation) that are applicable for a given ec (event category) if these parameters are not specified in the request, see clause D.12.4 of TS-0001 [1].

The context of this Resource is as follows:

# Table 6.3.12.4-1: Context of resource [cmdhEcDefParamValues]

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext:2051 |
| objectPath | /2052/{i} |

The Resource [cmdhEcDefParamValues] is a multi-instance Resource where each instance of the Resource shall map to an instance of the LWM2M CmdhEcDefParamValues Object.

The attributes of an instance of  [cmdhEcDefParamValues] shall be mapped to the resources of a  LWM2M  CmdhEcDefParamValues Object instance  as follows:

# Table 6.3.12.4-2: Attributes of resource [cmdhEcDefParamValues]

| Attribute Name of [cmdhEcDefParamValues] | Mapping to resources in LWM2M Object Instance |
| --- | --- |
| applicableEventCategory | 0 : ApplicableEventCategory |
| defaultRequestExpTime | 1 : DefaultRequestExpTime |
| defaultResultExpTime | 2 : DefaultResultExpTime |
| defaultOpExecTime | 3 : DefaultOpExecTime |
| default RespPersistence | 4 : DefaultRespPersistence |
| defaultDelAggregation | 5 : DefaultDelAggregation |

#### 6.3.12.5	Resource [cmdhLimits]

The Resource [cmdhLimits] represents limits for CMDH related parameter values, see clause D.12.5 of TS-0001 [1].

The context of this Resource is as follows:

# Table 6.3.12.5-1: Context of resource [cmdhLimits]

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext:2053 |
| objectPath | /2053/{i} |

The Resource [cmdhLimits] is a multi-instance Resource where each instance of the Resource shall map to an instance of the CmdhLimits Object.

The attributes of an instance of  [cmdhLimits] shall be mapped to the resources of an instance of the LWM2M CmdhLimits  Object  as follows:

# Table 6.3.12.5-2: Attributes of resource [cmdhLimits]

| Attribute Name of [cmdhLimits] | Mapping to resources in LWM2M CmdhLimits Object Instance |
| --- | --- |
| order | 0 : Order |
| requestOrigin | 1 : RequestOrigin |
| requestContext | 2 : RequestContext |
| requestContextNotification | 3 : RequestContextNotification |
| requestCharacteristics | 4 : RequestCharacteristics |
| limitsEventCategory | 5 : LimitsEventCategory |
| limitsRequestExpTime | 6 : LimitsRequestExpTime |
| limitsOpExecTime | 7 : LimitsOpExecTime |
| limitsRespPersistence | 8 : LimitsRespPersistence |
| limitsDelAggregation | 9 : LimitsDelAggregation |

#### 6.3.12.6	Resource [cmdhNetworkAccessRules]

The Resource [cmdhNetworkAccessRules] defines the usage of underlying networks for forwarding information to other CSEs during processing of CMDH-related requests in a CSE, see clause D.12.6 of TS-0001 [1].

The context of this Resource is as follows:

# Table 6.3.12.6-1: Context of resource [cmdhNetworkAccessRules]

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext:2054 |
| objectPath | /2054/{i} |

The Resource [cmdhNetworkAccessRules] is a multi-instance Resource where each instance of the Resource shall map to an instance of  one instance of the LWM2M CmdhNetworkAccessRules Object.

The attributes of an instance of  [cmdhNetworkAccessRules] shall be mapped to the resources of  a LWM2M CmdhNetworkAccessRules Object Instance  as follows:

# Table 6.3.12.6-2: Attributes of resource [cmdhNetworkAccessRules]

| Attribute Name of [cmdhNetworkAccessRules] | Mapping to resources in LWM2M Object Instance |
| --- | --- |
| applicableEventCategories | 0 : ApplicableEventCategories |
| cmdhNwAccessRule | 1 : NetworkAccessRule |

#### 6.3.12.7	Resource [cmdhNwAccessRule]

The Resource [cmdhNwAccessRule] defines limits in usage of specific underlying networks for forwarding information to other CSEs during processing of CMDH-related requests, see clause D.12.7 of TS-0001 [1].

The context of this Resource is as follows:

# Table 6.3.12.7-1: Context of resource [cmdhNwAccessRule]

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext:2055 |
| objectPath | /2055/{i} |

The Resource [cmdhNwAccessRule] is a multi-instance Resource where each instance of the Resource shall map to an instance of the LWM2M CmdhNwAccessRule Object.

The attributes of an instance of  [cmdhNwAccessRule] shall be mapped to  the resources of  a LWM2M cmdhNwAccessRule Object Instance  as follows:

# Table 6.3.12.7-2: Attributes of resource [cmdhNwAccessRule]

| Attribute Name of [cmdhNwAccessRule] | Mapping to resources in LWM2M Object Instance |
| --- | --- |
| targetNetwork | 0 : TargetNetwork |
| minReqVolume | 1 : MinReqVolume |
| backOffParameters | 2 : BackOffParameters |
| otherConditions | 3 : OtherConditions |
| allowedSchedule | 4 : AllowedSchedule |

#### 6.3.12.8	Resource [cmdhBuffer]

The Resource [cmdhBuffer] represents limits in usage of buffers for temporarily storing information that needs to be forwarded to other CSEs during processing of CMDH-related requests in a CSE, see clause D.12.8 of TS-0001 [1].

The context of this Resource is as follows:

# Table 6.3.12.8-1: Context of resource [cmdhBuffer]

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:ext:2056 |
| objectPath | /2056/{i} |

The Resource [cmdhBuffer] is a multi-instance Resource where each instance of the Resource shall map to an instance of the LWM2M CmdhBuffer Object.

The attributes of an instance of [cmdhBuffer] shall be mapped to the resources of an LWM2M cmdhBuffer Object Instance  as follows:

# Table 6.3.12.8-2: Attributes of resource [cmdhBuffer]

| Attribute Name of [cmdhBuffer] | Mapping to resources in LWM2M Object Instance |
| --- | --- |
| applicableEventCategory | 0 : ApplicableEventCategory |
| maxBufferSize | 1 : MaxBufferSize |
| storagePriority | 2 : StoragePriority |

## ------------------------ end of text addition 3 ----------------

## ----------------------- start of text addition 4 ---------------

## 6.6	New LWM2M Objects

These LWM2M Objects are specified by oneM2M organization. They have to be registered using the process defined by OMNA (Open Mobile Naming Authority).

The Object ID (e.g. “X”) of the LWM2M Objects specified here, must be allocated by OMNA, and will be in the range [2048 – 10240]

### 6.6.1	LWM2M CMDH Policy Objects

The LWM2M Objects specified here are used for mapping  the CMDH Policy Resources defined in oneM2M

This oneM2M CMDH Policy mapping  is addressed through the specification of 9 specific LWM2M Objects registered in OMNA:

CmdhPolicy Object							(urn:oma:lwm2m:ext:2048)

ActiveCmdhPolicy Object					(urn:oma:lwm2m:ext:2049)

CmdhDefaults									(urn:oma:lwm2m:ext:2050)

CmdhDefEcValue  Object					(urn:oma:lwm2m:ext:2051)

CmdhDefEcParamsValues  Object			(urn:oma:lwm2m:ext:2052)

CmdhLimits Object							(urn:oma:lwm2m:ext:2053)

CmdhNetworkAccessRules Object			(urn:oma:lwm2m:ext:2054)

CmdhNwAccessRule Object					(urn:oma:lwm2m:ext:2055)

CmdhBuffer Object							(urn:oma:lwm2m:ext:2056)

#### 6.6.1.1	CmdhPolicy Object

# Table 6.6.1.1-1: Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| CmdhPolicy | 2048 | Multiple | Optional | urn:oma:lwm2m:ext:2048 |

Table 6.6.1.1-2: Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | Name | RW | Single | Mandatory | String |  |  |  |
| 1 | DefaultRule | RW | Multiple | Mandatory | Objlink |  |  |  |
| 2 | LimitRules | RW | Multiple | Mandatory | Objlink |  |  |  |
| 3 | NetworkAccessECRules | RW | Multiple | Mandatory | Objlink |  |  |  |
| 4 | BufferRules | RW | Multiple | Mandatory | Objlink |  |  |  |

#### 6.6.1.2	ActiveCmdhPolicy Object

# Table 6.6.1.2-1: Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| ActiveCmdhPolicy | 2049 | Single | Mandatory | urn:oma:lwm2m:ext:2049 |

Table 6.6.1.2-2: Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | ActiveLink | RW | Single | Mandatory | Objlink |  |  |  |

#### 6.6.1.3	CmdhDefaults  Object

# Table 6.6.1.3-1: Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| CmdhDefaults | 2050 | Multiple | Mandatory | urn:oma:lwm2m:ext:2050 |

Table 6.6.1.3-2: Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | DefaultECRules | RW | Multiple | Mandatory | Objlink |  |  |  |
| 1 | DefaultECParamRules | RW | Multiple | Mandatory | Objlink |  |  |  |

#### 6.6.1.4	CmdhDef ECValues Object

# Table 6.6.1.4-1: Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| CmdhDefECValue | 2051 | Multiple | Mandatory | urn:oma:lwm2m:ext:2051 |

Table 6.6.1.4-2: Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | Order | RW | Single | Mandatory | Integer |  |  |  |
| 1 | DefEcValue | RW | Single | Mandatory | String |  |  |  |
| 2 | RequestOrigin | RW | Multiple | Mandatory | String |  |  |  |
| 3 | RequestContext | RW | Single | Optional | String |  |  |  |
| 4 | RequestContextNotification | RW | Single | Optional | Boolean |  |  |  |
| 5 | RequestCharacteristics | RW | Single | Optional | String |  |  |  |

#### 6.6.1.5	CmdhDefaultsECParamValues Object

# Table 6.6.1.5-1: Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| CmdhDefECParamValues | 2052 | Multiple | Mandatory | urn:oma:lwm2m:ext:2052 |

Table 6.6.1.5-2: Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | ApplicableEventCategory | RW | Multiple | Mandatory | Integer |  |  |  |
| 1 | DefaultRequestExpTime | RW | Single | Mandatory | Integer |  |  |  |
| 2 | DefaultResultExpTime | RW | Single | Mandatory | Integer |  |  |  |
| 3 | DefaultOpExecTime | RW | Single | Mandatory | Integer |  |  |  |
| 4 | DefaultRespPersistence | RW | Single | Mandatory | Integer |  |  |  |
| 5 | DefaultDelAggregation | RW | Single | Mandatory | Integer |  |  |  |

#### 6.6.1.6	CmdhLimits  Object

# Table 6.6.1.6-1: Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| CmdhLimits | 2053 | Multiple | Mandatory | urn:oma:lwm2m:ext:2053 |

Table 6.6.1.6-2: Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | Order | RW | Single | Mandatory | Integer |  |  |  |
| 1 | RequestOrigin | RW | Multiple | Mandatory | String |  |  |  |
| 2 | RequestContext | RW | Single | Optional | String |  |  |  |
| 3 | RequestContextNotification | RW | Single | Optional | Boolean |  |  |  |
| 4 | RequestCharacteristics | RW | Single | Optional | String |  |  |  |
| 5 | LimitsEventCategory | RW | Multiple | Mandatory | Integer |  |  |  |
| 6 | LimitsRequestExpTime | RW | Multiple | Mandatory | Integer | 2 Instances |  | Inst 0 : minTime Inst 1: maxTime |
| 7 | LimitsResultExpTime | RW | Multiple | Mandatory | Integer | 2 Instances |  | Inst 0 : minTime Inst 1: maxTime |
| 8 | LimitsOptExpTime | RW | Multiple | Mandatory | Integer | 2 Instances |  | Inst 0 : minTime Inst 1: maxTime |
| 9 | LimitsRespPersistence | RW | Multiple | Mandatory | Integer | 2 Instances |  | Inst 0 : minTime Inst 1: maxTime |
| 10 | LimitsDelAggregation | RW | Multiple | Mandatory | Boolean |  |  |  |

#### 6.6.1.7	CmdhNetworkAccessRules  Object

# Table 6.6.1.7-1: Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| CmdhNetworkAccessRules | 2054 | Multiple | Mandatory | urn:oma:lwm2m:ext:2054 |

Table 6.6.1.7-2: Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | ApplicableEventCategories | RW | Multiple | Mandatory | Integer |  |  |  |
| 1 | NetworkAccessRule | RW | Multiple | Mandatory | Objlink |  |  |  |

#### 6.6.1.8	CmdhNwAccessRule  Object

# Table 6.6.1.8-1: Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| CmdhNwAccessRule | 2055 | Multiple | Mandatory | urn:oma:lwm2m:ext:2055 |

Table 6.6.1.8-2: Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | TargetNetwork | RW | Multiple | Mandatory | String |  |  |  |
| 1 | MinReqVolume | RW | Single | Mandatory | Integer |  |  |  |
| 2 | BackOffParameters | RW | Multiple | Mandatory | Integer | 3 Instances | ms | 0 : BackOffTime 1: BackOffTimeIncrement 2 : MaxBackOffTime |
| 3 | OtherConditions | RW | Single | Mandatory | String |  |  |  |
| 4 | AllowedSchedule | RW | Single | Mandatory | String |  |  |  |

#### 6.6.1.9	CmdhBuffer  Object

# Table 6.6.1.9-1: Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| CmdhBuffer | 2056 | Multiple | Mandatory | urn:oma:lwm2m:ext:2056 |

Table 6.6.1.9-2: Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | ApplicableEventCategory | RW | Multiple | Mandatory | Integer |  |  |  |
| 1 | MaxBufferSize | RW | Single | Mandatory | Integer |  |  |  |
| 2 | StoragePriority | RW | Single | Mandatory | Integer |  |  |  |

## ------------------------ end of text addition 4 ----------------