| CHANGE REQUEST |
| --- |
| Meeting:* | MAS#27 |
| Source:* | NTT, NTT DOCOMO |
| Date:* | 2017-02-03 |
| Contact:* | Kei Harada(harada.kei@lab.ntt.co.jp), NTT, Takafumi Yamazoe(yamazoet@nttdocomo.com), NTT DOCOMO, Takashi Yoshikawa(yoshikawatak@nttdocomo.com), NTT DOCOMO, Yoshihisa Ito(ito.yoshihisa@lab.ntt.co.jp), NTT, Hiroyuki Maeomichi(maeomichi.hiroyuki@lab.ntt.co.jp), NTT |
| Reason for Change/s:* | To add new device models to TS-0023 |
| CR against: Release* | Release-3 |
| CR against: WI* | Active <WI-0056 > MNT maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V.3.1.0 |
| Clauses/Sub Clauses* | 2.1,5.2, 5.3,5.4,5.5, 5.6, 6.3, 6.4, 6.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposed ModuleClasses and DeviceModels for the target devices those are seen in OMA Content Delivery WG’s specification. oneM2M and OMA Content Delivery WG have decided to interwork (TP-2017-0002-Comments_on_the_oneM2M_Home_Appliance_Information_Model_and_Mapping), and OMA Content Delivery WG recommended us to use their APIs. This contribution is based on their recommended APIs named OMA Device Web API- Personal Connected Healthcare (DWAPI-PCH).

Rev-1: correct some typos and grammatical mistakes.

Rev-2: reflects given comments from MAS 26.2.

Rev-3: correct some typos.

Rev-4: delete a rule about integer type (Rule 9) and a change about common property.

### -----------------------Start of change 1-------------------------------------------

### 5.2.2	Description rules for Module Classes and Device models

When the Home Appliances Information Model is described based on SDT, the following rules shall be applied:

Rule 1: CamelCase rule:

When naming each element, lowerCamelCase shall be used as the Java coding rules [2].

Rule 2: Rule for description of Action, DataPoint:

DataPoint shall be used to represent stateless operations. (e.g. powerState of binarySwitch for on/off operations).

Action shall be used when describing stateful condition, handling unknown internal state conditions (e.g. upVolume/downVolume by increasing/decreasing the audioVolume in steps, handling transactional procedures, or checking integrity using username plus password at the same time).

Rule 3: Rule for description of DataPoint and Property:

Non-functional information shall be described as a Property. Functional information shall be described as a DataPoint. (E.g. non-functional information: version, id; functional information: targetTemperature, targetVolume).

Rule 4: Definition of the Domain:

The Domain, in the case of the Home Appliance Information Model, is specified as "org.onem2m.home".

The sub-domain for Device and ModuleClass shall be specified as "org.onem2m.home.devices" and "org.onem2m.home.moduleclasses" respectively.

Rule 5: Naming rule for the element:

the name of each element should be concise and avoid repeating its parent element name; but

it may include the name of its parent element for readability. (e.g., lightDimmerUp, lightDimmerDown under lightDimmer).

Rule 6: Criteria for marking elements as optional or mandatory:

An element shall only be defined as mandatory if it's foreseen to be universally mandatory to all implementing technologies.

Rule 7: Enumeration type:

When describing the meaning of values for enumeration type elements, they may be described in another clause.

The enumeration types for Home Appliance Information Model are based on <xs:integer>, and the numeric values are interpreted as specified in clause 5.5.

Rule 8: Rule for unit  in documentation :

SI (International Systems of Units in [z]) measurement (e.g. meter, kilogram, second.) should be considered as first candidate.

Otherwise, it may be kept consistency with implementing technologies such as other SDO’s specification..

Editor's note: Popular unit in particular industrial domain should be considered  (e.g. cm for human height, calories for energy consumption in healthcare domain). It should be made coherent in the document, as possible.

Rule 9: Rule for type :

Measured and/or calculated values should be represented in float (without taking care of resolution of values).

### Editor’s note: It should be made coherent in the document, as possible. Unit shall not be fixed as a rule but be decided with correspondence to each device or module.-----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 2.1	Normative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

The following referenced documents are necessary for the application of the present document.

[1]	Home Gateway Initiative Smart Device Template.

NOTE:	Available at https://github.com/Homegateway/SmartDeviceTemplate/tree/7c890b69d9764e341ef1768c5a0e7d53a47cff5c.

[2]	Java coding rule.

[3]	oneM2M TS-0001: "Functional Architecture".

NOTE:	Available at http://www.oracle.com/technetwork/java/codeconventions-135099.html.

[z] 	ISO:80000-1: Quantities and units.

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 5.3.21	oximeter

This ModuleClass provides the capability to report the measurement of blood oxygen characteristics.

Table 5.3.21-1: DataPoints of oximeter ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| oxygenSaturation | xs:float | true | false | false | The measurement of oxygensaturation by Oximeter. The common unit is in percentage. |

### ----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 5.3.y1	sphygmomanometer

This ModuleClass provides the capability to report the measurement of blood pressure characteristics.

Table 5.3.y1-1: DataPoints of sphygmomanometer ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| diastolicPressure | xs:float | true | false | false | The measurement of diastolic pressure by sphygmomanometer. The common unit is millimetre of mercury (mmHg). |
| systolicPressure | xs:float | true | false | false | The measurement of systolic pressure by sphygmomanometer . The common unit is millimetre of mercury (mmHg). |
| meanPressure | xs:float | true | false | false | The measurement of mean arterial pressure by sphygmomanometer . The common unit is millimetre of mercury (mmHg). |

### 5.3.y2	pulsemeter

This ModuleClass provides the capability to report the measurement of pulse characteristics.

Table 5.3.y2-1: DataPoints of pulsemeter ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| pulseRate | xs:float | true | false | false | The measurement of pulserate by pulsemeter. The common unit is in beats per minute. |
| rr | xs:float | true | false | true | The measurement of RR interval by pulsemeter. The common unit is millisecond (ms). |
| energy | xs:float | true | false | true | The measurement of energy by pulsemeter. The common unit is kilocalorie per hour. |
| modality | xs: string | true | false | true | Themodality of a particularSpO2 measurement. |

### 5.3.y3	glucometer

This ModuleClass provides the capability to report the measurement of glucose characteristics.

Table 5.3.y3-1: DataPoints of glucometer ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| Concentration | xs:float | true | false | false | The measurement of concentration by Glucometer. The common unit is mg/dl. |
| hba1c | xs:float | true | false | true | The measurement of HbA1c by Glucometer. The common unit is in percentage. |
| contextExercise | xs:float | true | false | true | The measurement of context exercise by Glucometer. The common unit is in percentage. |
| contextMedication | xs:float | true | false | true | The measurement of context medication by Glucometer. The common unit is mg/dl. |
| contextCarbohydratesAmount | xs:float | true | false | true | The measurement of context carbohydrates by Glucometer. The common unit is gram (g). |
| contextCarbohydratesSource | xs:string | true | false | true | The timing of meals (e.g. Breakfast Crbohydrates). |
| contextMeal | xs:string | true | false | true | The style of meals (e.g. Casual). |
| contextLocation | xs:string | true | false | true | The body location where the Glucometer is worn (e.g. finger). |
| contextTester | xs:string | true | false | true | The test style (e.g. Self). |
| contextHealth | xs:string | true | false | true | The severity of symptoms (e.g. Minor) |

### 5.3.y4	bodyCompositionAnalyzer

This ModuleClass provides the capability to report the measurement of body composition analyzer characteristics.

Table 5.3.y4-1: DataPoints of body composition analyzer ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| bodyLength | xs:float | true | false | true | The measurement of body length by Weight scale and Body composition analyzer. The common unit is centimeter(cm). |
| Bmi | xs:float | true | false | true | The measurement of Body Mass Index (BMI) by Weight scale and Body composition analyzer. The common unit is kg/m2. |
| fatFreeMass | xs:float | true | false | true | The measurement of fat free mass by Weight scale and Body composition analyzer. The common unit is kilogram (kg). |
| softLeanMass | xs:float | true | false | true | The measurement of soft lean mass by Weight scale and Body composition analyzer. The common unit is kilogram (kg). |
| muscleMass | xs:float | true | false | true | The measurement of muscle mass by Weight scale and Body composition analyzer. The common unit is kilogram (kg). |
| basalMetabolism | xs:float | true | false | true | The measurement of basal metabolism by Weight scale and Body composition analyzer. The common unit is kilocalorie (kcal). |
| impedance | xs:float | true | false | true | The measurement of impedance by Weight scale and Body composition analyzer. The common unit is ohm. |

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5-------------------------------------------

### 5.4.x1	deviceBloodPressureMonitor

A device blood pressure is a device that can be used to monitor the blood  pressure.

Table 5.4.x1-1: Modules of deviceBloodPressureMonitor Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| sphygmomanometer | sphygmomanometer | false | See clause 5.3.y1 |
| pulsemeter | pulsemeter | false | See clause 5.3.y2 |
| battery | battery | false | See clause 5.3.4 |

### 5.4.x2	deviceGlucosemeter

A glucometer is a device that can be used to monitor the blood glucose level.

Table 5.4.x2-1: Modules of deviceGlucoseMeter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| Glucometer | glucometer | false | See clause 5.3.y3 |
| Battery | battery | false | See clause 5.3.4 |

### 5.4.x3	devicePulseOximeter

A pulseoximeter is a device that can be used to monitor the blood characteristics.

Table 5.4.x3-1: Modules of devicePulseOxiMeter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| Pulsemeter | pulsemeter | true | See clause 5.3.y2. When oximeter module doesn’t exist, pulsemeter module is mandatory. |
| oximeter | oximeter | true | See clause 5.3.21. When pulsemeter module doesn’t exist, oximeter module is mandatory. |
| battery | battery | false | See clause 5.3.4 |

### 5.4.x4	deviceThermometer

A thermometer is a device that can be used to check the body temperature.

Table 5.4.x4-1: Modules of deviceThermoMeter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| Temperature | Temperature | false | See clause 5.3.33 |
| Battery | Battery | false | See clause 5.3.4 |

### 5.4.x5	deviceWeightScaleAndBodyCompositionAnalyzer

A weight scale & body composition analyzer is a device that can be used to monitor the weight and body composition.

Table 5.4.x5-1: Modules of deviceWeightScaleAndBodyCompositionAnalyzer Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| Weight | Weight | false | See clause 5.3.40 |
| bodyCompositionAnalyzer | bodyCompositionAnalyzer | false | See clause 5.3.y4 |
| bioElectricalImpedanceAnalysis | bioElectricalImpedanceAnalysis | false | See clause 5.3.6 |
| Battery | Battery | false | See clause 5.3.4 |

### 5.4.x6	deviceHeartRateMonitor

A heart rate monitor a device that can be used to monitor the heart rate.

Table 5.4.x6-1: Modules of deviceHeartRateMonitor Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| Pulsemeter | Pulsemeter | false | See clause 5.3.y2 |
| Battery | Battery | false | See clause 5.3.4 |

### ----------------------End of change 5---------------------------------------------

### -----------------------Start of change 6-------------------------------------------

### 5.5.1	hd:deviceType

Used for DeviceType property of device models.

Table 5.5.1-1: Interpretation of deviceType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | deviceAirConditioner | See clause 5.4.1 |
| 2 | deviceClothesWasher | See clause 5.4.2 |
| 3 | deviceElectricVehicleCharger | See clause 5.4.3 |
| 4 | deviceLight | See clause 5.4.4 |
| 5 | deviceMicrogeneration | See clause 5.4.5 |
| 6 | deviceOven | See clause 5.4.6 |
| 7 | deviceRefrigerator | See clause 5.4.7 |
| 8 | deviceRobotCleaner | See clause 5.4.8 |
| 9 | deviceSmartElectricMeter | See clause 5.4.9 |
| 10 | deviceStorageBattery | See clause 5.4.10 |
| 11 | deviceTelevision | See clause 5.4.11 |
| 12 | deviceThermostat | See clause 5.4.12 |
| 13 | deviceWaterHeater | See clause 5.4.13 |
| 14 | deviceSwitch | See clause 5.4.14 |
| 15 | deviceWindowShade | See clause 5.4.15 |
| 16 | deviceDoorLock | See clause 5.4.16 |
| 17 | deviceCoffeeMachine | See clause 5.4.17 |
| x1 | deviceBloodPressureMonitor | See clause 5.4.x1 |
| x2 | deviceGlucosemeter | See clause 5.4.x2 |
| X3 | devicePulseOximeter | See clause 5.4.x3 |
| X4 | deviceThermometer | See clause 5.4.x4 |
| X5 | deviceWeightScaleAndBodyComposition Analyzer | See clause 5.4.x5 |
| X6 | deviceHeartRate Monitor | See clause 5.4.x6 |
| 0 | undefinedVendorExt | For vendor specific usage. |
| NOTE: See clause 5.4 "device Models". |

### -----------------------End of change 6---------------------------------------------

### -----------------------Start of change 7-------------------------------------------

### 6.3.2	Resource types

In protocol bindings resource type names for device models shall be translated into short names of Table 6.3.2-1.

Table 6.3.2-1: Specialization type short names (Device models)

| Resource Type Name | Short Name |
| --- | --- |
| deviceAirConditioner | deACr |
| devicePulseOximeter |  |
| deviceClothesWasher | deCWr |
| deviceCoffeeMachine |  |
| deviceDoorLock |  |
| deviceElectricVehicleCharger | dEVCr |
| deviceGlucosemeter |  |
| deviceHeartRateMonitor |  |
| deviceLight | devLt |
| deviceMicrogeneration | devMn |
| deviceOven | devOn |
| deviceRefrigerator | devRr |
| deviceRobotCleaner | deRCr |
| deviceSmartElectricMeter | dSEMr |
| deviceStorageBattery | deSBy |
| deviceSwitch |  |
| deviceTelevision | devTn |
| deviceThermostat | devTt |
| deviceWaterHeater | deWHr |
| deviceWeightScaleAndBodyCompositionAnalyzer |  |
| deviceWindowShade |  |
| devicePulseOximeter |  |
| deviceThermoMeter |  |

.

In protocol bindings resource type names for module classes shall be translated into short names of Table 6.3.2-2

Table 6.3.2-2: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| alarmSpeaker | alaSr |
| audioVideoInput | auVIt |
| audioVolume | audVe |
| Battery | batty |
| binarySwitch | binSh |
| bioElectricalImpedanceAnalysis | bEIAs |
| bodyCompositionAnalyzer |  |
| Boiler | boilr |
| Brewing |  |
| Brightness | brigs |
| Clock | clock |
| Colour | color |
| colourSaturation | colSn |
| customTemperature | cusTe |
| doorLock |  |
| doorStatus | dooSe |
| electricVehicleConnector | elVCr |
| energyConsumption | eneCn |
| energyGeneration | eneGn |
| faultDetection | fauDn |
| Foaming |  |
| freshTemperature | freTe |
| frozenTemperature | froTe |
| Glucometer |  |
| Grinder |  |
| Height | heigt |
| hotWaterSupply | hoWSy |
| Keypad | keypd |
| liquidLevel |  |
| motionSensor | motSr |
| Oximeter | oximr |
| powerSave | powS0 |
| Pulsemeter |  |
| pushButton | pusBn |
| Recorder | recor |
| Refrigeration | refrn |
| relativeHumidity | relHy |
| liquidRemaining |  |
| runMode | runMe |
| signalStrength | sigSh |
| smokeSensor | smoSr |
| sphygmomanometer |  |
| spinLevel | spiLl |
| televisionChannel | telCl |
| Temperature | tempe |
| temperatureAlarm | temAm |
| Timer | timer |
| Turbo | turbo |
| waterFlow | watFw |
| waterSensor | watSr |
| Weight | weigt |
| Wind | wind |

### -----------------------End of change 7---------------------------------------------

### -----------------------Start of change 8-------------------------------------------

### 6.4.2	Device models

The containerDefinition attribute of specializations for device models shall have the values specifien in Table 6.4.2-1.

Table 6.4.2-1: containerDefinition values of specializations for device models

| Resource Type Name | containerDefinition value |
| --- | --- |
| deviceAirConditioner | "org.onem2m.home.device.deviceAirConditioner" |
| deviceBloodPressureMonitor | "org.onem2m.home.device.deviceBloodPressureMonitor" |
| deviceClothesWasher | "org.onem2m.home.device.deviceClothesWasher" |
| deviceCoffeeMachine | "org.onem2m.home.device.deviceCoffeeMachine” |
| deviceDoorLock | "org.onem2m.home.device.deviceDoorLock" |
| deviceElectricVehicleCharger | "org.onem2m.home.device.deviceElectricVehicleCharger" |
| deviceGlucosemeter | "org.onem2m.home.device.deviceGlucosemeter" |
| deviceHeartRateMonitor | "org.onem2m.home.device.deviceHeartRateMonitor " |
| deviceLight | "org.onem2m.home.device.deviceLight" |
| deviceMicrogeneration | "org.onem2m.home.device.deviceMicrogeneration" |
| deviceOven | "org.onem2m.home.device.deviceOven" |
| deviceRefrigerator | "org.onem2m.home.device.deviceRefrigerator" |
| deviceRobotCleaner | "org.onem2m.home.device.deviceRobotCleaner" |
| deviceSmartElectricMeter | "org.onem2m.home.device.deviceSmartElectricMeter" |
| deviceStorageBattery | "org.onem2m.home.device.deviceStorageBattery" |
| deviceSwitch | "org.onem2m.home.device.deviceSwitch" |
| deviceTelevision | "org.onem2m.home.device.deviceTelevision" |
| deviceThermostat | "org.onem2m.home.device.deviceThermostat" |
| deviceWaterHeater | "org.onem2m.home.device.deviceWaterHeater" |
| deviceWeightScaleAndBodyCompositionAnalyzer | "org.onem2m.home.device.deviceWeightScaleAndBodyCompositionAnalyzer " |
| deviceWindowShade | "org.onem2m.home.device.deviceWindowShade" |
| devicePulseOximeter | "org.onem2m.home.device.devicePulseOximeter" |
| deviceThermometer | "org.onem2m.home.device.deviceThermometer" |

### 6.4.3	ModuleClasses

The containerDefinition attribute of specializations for module classes shall have the values specifien in Table 6.4.3-1.

Table 6.4.3-1: containerDefinition values of specializations for module classes

| Resource Type Name | containerDefinition value |
| --- | --- |
| alarmSpeaker | "org.onem2m.home.moduleclass.alarmSpeaker" |
| audioVideoInput | "org.onem2m.home.moduleclass.audioVideoInput" |
| audioVolume | "org.onem2m.home.moduleclass.audioVolume" |
| battery | "org.onem2m.home.moduleclass.battery" |
| binarySwitch | "org.onem2m.home.moduleclass.binarySwitch" |
| bioElectricalImpedanceAnalysis | "org.onem2m.home.moduleclass.bioElectricalImpedanceAnalysis" |
| bodyCompositionAnalyzer | "org.onem2m.home.moduleclass. bodyCompositionAnalyzer " |
| boiler | "org.onem2m.home.moduleclass.boiler" |
| brewing | "org.onem2m.home.moduleclass.brewing” |
| brightness | "org.onem2m.home.moduleclass.brightness" |
| clock | "org.onem2m.home.moduleclass.clock" |
| colour | "org.onem2m.home.moduleclass.colour" |
| colourSaturation | "org.onem2m.home.moduleclass.colourSaturation" |
| customTemperature | "org.onem2m.home.moduleclass.customTemperature" |
| doorLock | "org.onem2m.home.moduleclass.doorLock" |
| doorStatus | "org.onem2m.home.moduleclass.doorStatus" |
| electricVehicleConnector | "org.onem2m.home.moduleclass.electricVehicleConnector" |
| energyConsumption | "org.onem2m.home.moduleclass.energyConsumption" |
| energyGeneration | "org.onem2m.home.moduleclass.energyGeneration" |
| faultDetection | "org.onem2m.home.moduleclass.faultDetection" |
| foaming | "org.onem2m.home.moduleclass.foaming” |
| freshTemperature | "org.onem2m.home.moduleclass.freshTemperature" |
| frozenTemperature | "org.onem2m.home.moduleclass.frozenTemperature" |
| glucometer | "org.onem2m.home.moduleclass.glucometer" |
| grinder | "org.onem2m.home.moduleclass.grinder” |
| height | "org.onem2m.home.moduleclass.height" |
| hotWaterSupply | "org.onem2m.home.moduleclass.hotWaterSupply" |
| keypad | "org.onem2m.home.moduleclass.keypad" |
| liquidLevel | "org.onem2m.home.moduleclass.liquidLevel” |
| liquidRemaining | "org.onem2m.home.moduleclass.liquidRemaining” |
| motionSensor | "org.onem2m.home.moduleclass.motionSensor" |
| oximeter | "org.onem2m.home.moduleclass.oximeter" |
| powerSave | "org.onem2m.home.moduleclass.powerSave" |
| pulsemeter | "org.onem2m.home.moduleclass.pulsemeter" |
| pushButton | "org.onem2m.home.moduleclass.pushButton" |
| recorder | "org.onem2m.home.moduleclass.recorder" |
| refrigeration | "org.onem2m.home.moduleclass.refrigeration" |
| relativeHumidity | "org.onem2m.home.moduleclass.relativeHumidity" |
| rinseLevel | "org.onem2m.home.moduleclass.rinseLevel" |
| runMode | "org.onem2m.home.moduleclass.runMode" |
| signalStrength | "org.onem2m.home.moduleclass.signalStrength" |
| smokeSensor | "org.onem2m.home.moduleclass.smokeSensor " |
| sphygmomanometer | "org.onem2m.home.moduleclass.sphygmomanometer" |
| spinLevel | "org.onem2m.home.moduleclass.spinLevel" |
| televisionChannel | "org.onem2m.home.moduleclass.televisionChannel" |
| temperature | "org.onem2m.home.moduleclass.temperature" |
| temperatureAlarm | "org.onem2m.home.moduleclass.temperatureAlarm" |
| timer | "org.onem2m.home.moduleclass.timer" |
| turbo | "org.onem2m.home.moduleclass.turbo" |
| waterFlow | "org.onem2m.home.moduleclass.waterFlow" |
| waterSensor | "org.onem2m.home.moduleclass.waterSensor" |
| weight | "org.onem2m.home.moduleclass.weight" |
| wind | "org.onem2m.home.moduleclass.wind" |

### -----------------------End of change 8---------------------------------------------

### -----------------------Start of change 9-------------------------------------------

### 6.5.2	XSD definitions for Device models

The XSD definitions for Device models are listed in Table 6.5.2-1.

Table 6.5.2-1: Data type definition of Device models

| Device model | File Name | Note |
| --- | --- | --- |
| deviceAirConditioner | HD-deviceAirConditioner-v<TS-version>.xsd |  |
| deviceBloodPressureMonitor | HD-deviceBloodPressureMonitor-v<TS-version>.xsd |  |
| deviceClothesWasher | HD-deviceClothesWasher-v<TS-version>.xsd |  |
| deviceCoffeeMachine | HD-deviceCoffeeMachine-v<TS-version>.xsd |  |
| deviceDoorLock | HD-deviceDoorLock-v<TS-version>.xsd |  |
| deviceElectricVehicleCharger | HD-deviceElectricVehicleCharger-v<TS-version>.xsd |  |
| deviceGlucosemeter | HD-deviceGlucosemeter-v<TS-version>.xsd |  |
| deviceHeartRateMonitor | HD- deviceHeartRateMonitor -v<TS-version>.xsd |  |
| deviceLight | HD-deviceLight-v<TS-version>.xsd |  |
| deviceMicrogeneration | HD-deviceMicrogeneration-v<TS-version>.xsd |  |
| deviceOven | HD-deviceOven-v<TS-version>.xsd |  |
| deviceRefrigerator | HD-deviceRefrigerator-v<TS-version>.xsd |  |
| deviceRobotCleaner | HD-deviceRobotCleaner-v<TS-version>.xsd |  |
| deviceStorageBattery | HD-deviceStroageBattery-v<TS-version>.xsd |  |
| deviceSmartElectricMeter | HD-deviceSmartElectricMeter-v<TS-version>.xsd |  |
| deviceSwitch | HD-deviceSwitch-v<TS-version>.xsd |  |
| deviceTelevision | HD-deviceTelevision-v<TS-version>.xsd |  |
| deviceThermostat | HD-deviceThermostat-v<TS-version>.xsd |  |
| deviceWaterHeater | HD-deviceWaterHeater-v<TS-version>.xsd |  |
| deviceWeightScaleAndBodyCompositionAnalyzer | HD-deviceWeightScaleAndBodyCompositionAnalyzer -v<TS-version>.xsd |  |
| deviceWindowShade | HD-deviceWindowShade-v<TS-version>.xsd |  |
| devicePulseOximeter | HD-devicePulseOximeter-v<TS-version>.xsd |  |
| deviceThermometer | HD-deviceThermometer-v<TS-version>.xsd |  |
| NOTE: The string '<TS-version>' shall be intepreted as the version of the present document. |

### 6.5.3	XSD definitions for ModuleClass

The XSD definitions for ModuleClass are listed in Table 6.5.3-1.

Table 6.5.3-1: Data type definition of ModuleClasses

| ModuleClass ID | File Name | Note |
| --- | --- | --- |
| alarmSpeaker | HD-mod-alarmSpeaker-v<TS-version>.xsd |  |
| audioVideoInput | HD-mod-audioVideoInput-v<TS-version>.xsd |  |
| audioVolume | HD-mod-audioVolume-v<TS-version>.xsd |  |
| battery | HD-mod-battery-v<TS-version>.xsd |  |
| binarySwitch | HD-mod-binarySwitch-v<TS-version>.xsd |  |
| bioElectricalImpedanceAnalysis | HD-mod-bioElectricalImpedanceAnalysis-v<TS-version>.xsd |  |
| bodyCompositionAnalyzer | HD-mod- bodyCompositionAnalyzer-v<TS-version>.xsd |  |
| boiler | HD-mod-boiler-v<TS-version>.xsd |  |
| brewing | HD-mod- brewing -v<TS-version>.xsd |  |
| brightness | HD-mod-brightness-v<TS-version>.xsd |  |
| clock | HD-mod-clock-v<TS-version>.xsd |  |
| colour | HD-mod-colour-v<TS-version>.xsd |  |
| colourSaturation | HD-mod-colourSaturation-v<TS-version>.xsd |  |
| doorLock | HD-mod-doorLock-v<TS-version>.xsd |  |
| doorStatus | HD-mod-doorStatus-v<TS-version>.xsd |  |
| electricVehicleConnector | HD-mod-electricVehicleConnector-v<TS-version>.xsd |  |
| energyConsumption | HD-mod-energyConsumption-v<TS-version>.xsd |  |
| energyGeneration | HD-mod-energyGeneration-v<TS-version>.xsd |  |
| faultDetection | HD-mod-faultDetection-v<TS-version>.xsd |  |
| foaming | HD-mod- foaming -v<TS-version>.xsd |  |
| glucometer | HD-mod-glucometer-v<TS-version>.xsd |  |
| grinder | HD-mod- grinder -v<TS-version>.xsd |  |
| height | HD-mod-height-v<TS-version>.xsd |  |
| hotWaterSupply | HD-mod-hotWaterSupply-v<TS-version>.xsd |  |
| keypad | HD-mod-keypad-v<TS-version>.xsd |  |
| liquidLevel | HD-mod- liquidLevel -v<TS-version>.xsd |  |
| liquidRemaining | HD-mod- liquidRemaining -v<TS-version>.xsd |  |
| motionSensor | HD-mod-motionSensor-v<TS-version>.xsd |  |
| oximeter | HD-mod-oximeter-v<TS-version>.xsd |  |
| powerSave | HD-mod-powerSave-v<TS-version>.xsd |  |
| pulsemeter | HD-mod- pulsemeter-v<TS-version>.xsd |  |
| pushButton | HD-mod-pushButton-v<TS-version>.xsd |  |
| recorder | HD-mod-recorder-v<TS-version>.xsd |  |
| refrigeration | HD-mod-refrigeration-v<TS-version>.xsd |  |
| relativeHumidity | HD-mod-relativeHumidity-v<TS-version>.xsd |  |
| rinseLevel | HD-mod-rinseLevel-v<TS-version>.xsd |  |
| runMode | HD-mod-runMode-v<TS-version>.xsd |  |
| signalStrength | HD-mod-signalStrength-v<TS-version>.xsd |  |
| smokeSensor | HD-mod-smokeSensor-v<TS-version>.xsd |  |
| sphygmomanometer | HD-mod-sphygmomanometer-v<TS-version>.xsd |  |
| spinLevel | HD-mod-spinLevel-v<TS-version>.xsd |  |
| televisionChannel | HD-mod- HD-mod--v<TS-version>.xsd |  |
| temperature | HD-mod-temperature-v<TS-version>.xsd |  |
| temperatureAlarm | HD-mod-temperatureAlarm-v<TS-version>.xsd |  |
| timer | HD-mod-timer-v<TS-version>.xsd |  |
| turbo | HD-mod-turbo-v<TS-version>.xsd |  |
| waterFlow | HD-mod-waterFlow-v<TS-version>.xsd |  |
| waterSensor | HD-mod-waterSensor-v<TS-version>.xsd |  |
| weight | HD-mod-weight-v<TS-version>.xsd |  |
| wind | HD-mod-wind-v<TS-version>.xsd |  |
| NOTE: The string '<TS-version>' shall be intepreted as the version of the present document. |

### -----------------------End of change 9---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?