| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#27 |
| Source:* | Dongjoo Kim (dongjoo7.kim@lge.com) |
| Date:* | 2017-2-15 |
| Reason for Change/s:* | This CR requests some changes and additions of module classes for washer device model so as to enhance interoperability with external proximal IoT technologies and make the model be in better shape. |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <WI-0056> MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.1.0 |
| Clauses * | 5.3, 5.4, 5.5, 6.3, 6.4, 6.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR requests to modify and add some module classes, enumeration definition and deviceClothesWasher device model in order to make the models related to the washer model clearer and more useful based on information models of real product and external proximal technology.

[Modification]

- runMode ( runState

  - expression change from “Mode” to “State” for clarification

  - distinguishing between jobState and machineState

- deviceClothesWasher

  - some module classes are modified or added in accordance with this CR

  - temperature, liquidLevel, waterFlow, spinLevel are removed since they are implicitely included in washingCourse and washingCourseOption module classes, which are newly proposed in this CR.

- clause 6

  - short names

  - container definitions

  - xsd definitions

[Addition]

- operationMode module class
: with this module, an user can start or pause the operation of the appliance.

- remoteControl module class
: this module is set by user locally and it fundamentally enables or disables remote accessibility

- washingCourse module class
: this module provides supporting washing courses such as normal, quick, delicates/handwash or wool, and a user can monitor or control the current course.

- washingCourseOption module class
: this module gives some additional options for user to adjust pre-set courses. the options are water temperature, dry time, spin repeat and etc.

- necessary enumeration types are added

### -----------------------Start of change 1-------------------------------------------

### 5.3.28	runState

This ModuleClasses provides capabilities to control and monitor the job state and machine state of appliances.

Table 5.3.28-1: DataPoints of runState ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentMachineState | hd:machineState | true | true | false | Currently active machine state. |
| machineStates | list of hd:machineState | true | false | false | List of possible machine states the device supports (see clause 5.5.x) |
| currentJobState | hd:jobState | true | true | false | Currently active job state. The value of this property shall be idle unless the value of currentMachineState property is active |
| jobStates | list of hd:jobState | true | false | false | List of possible job states the device supports (see clause 5.5.7) |
| progressPercentage | float | true | false | true | Indication of current progress in percentage |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 5.5.x	hd:machineState

Used for currentMachineState and machineStates DataPoints of runState ModuleClass.

Table 5.5.x-1: Interpretation of machineState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | idle | Machine is ready to operate |
| 2 | active | Machine is operating its functions |
| 3 | reserved | Reservation is made by user |
| 4 | paused | Operation is paused by user |
| 5 | cancelled | Operation is cancelled by user |
| 6 | stopped | Operation is stopped/aborted by some other reasons |
| 7 | complete | Operation is complete |
| 8 | error | Error has occurred |
| 9 | diagnostic | Machine reports diagnostic information to the server |
| 10 | test | Particular functions run for test |
| NOTE: See clause 5.3.28 "runState". |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 5.5.7	hd:jobStates

Used for currentJobState and jobStates DataPoints of runState ModuleClass.

Table 5.5.7-1: Interpretation of jobState

| Value | Interpretation | Note |
| --- | --- | --- |
| 0~99 | - | Reserved for vendor extension |
| 100~199 | - | Reserved for deviceAirConditioner |
| 200 | idle | This value is for deviceClothesWasher and indicates idle state. |
| 201 | preWash | This value is for deviceClothesWasher and indicates pre-washing state. pre-wash is a cold water cycle that runs prior to the main wash cycle. It is used for heavily soiled laundy. |
| 202 | wash | This value is for deviceClothesWasher and indicates washing state. |
| 203 | rinse | This value is for deviceClothesWasher and indicates rinsing state. |
| 204 | spin | This value is for deviceClothesWasher and indicates spinning state. |
| 205 | dry | This value is for deviceClothesWasher and indicates drying state. |
| 206 | airDry | This value is for deviceClothesWasher and indicates air-drying state. In airDry state, a rotating wheel circulates air to get fresh air used to dry laundry. |
| 207 | wrinkleProof | This value is for deviceClothesWasher and indicates wrinkleProof state. |
| 208 | soak | This value is for deviceClothesWasher and indicates soak state. |
| 209~299 | - | Reserved for deviceClothesWasher |
| 300~399 | - | Reserved for deviceElectricVehicleCharger |
| 400~499 | - | Reserved for deviceLight |
| 500~599 | - | Reserved for deviceMicrogeneration |
| 600 | warmingUp | This value is for deviceOven and indicates warmingUp state. |
| 601 | cooking | This value is for deviceOven and indicates cooking state. |
| 602 | cooling | This value is for deviceOven and indicates cooling state. |
| 603~699 | - | Reserved for deviceOven |
| 700~799 | - | Reserved for deviceRefrigerator |
| 800 | charging | This value is for deviceRobotCleaner and indicates charging state. |
| 801 | homing | This value is for deviceRobotCleaner and indicates homing state. |
| 802 | docking | This value is for deviceRobotCleaner and indicates docking state. |
| 803~899 | - | Reserved for deviceRobotCleaner |
| 900~999 | - | Reserved for deviceSmartElectricMeter |
| 1000~1099 | - | Reserved for deviceStorageBattery |
| 1100~1199 | - | Reserved for deviceTelevision |
| 1200 | antifreeze | This mode sets the thermostat to a minimum temperature to avoid home system to freeze when the habitants are not there for a long time |
| 1201 | manual | This mode allows for direct change of the temperature indication for the thermostat by the user. |
| 1202 | eco | This is to set the thermostat to the economic mode |
| 1203 | program | The program mode is used to set the thermostat to a predefined mode |
| 1204~1299 | - | Reserved for deviceThermostat |
| 1300~1399 | - | Reserved for deviceWaterHeater |
| 1400~1499 | - | Reserved for deviceCoffeeMachine |
| NOTE: See clause 5.3.28 "runstate". |

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 5.3.x	operationMode

This ModuleClasses provides capabilities to control or monitor the operation mode of appliances.

Table 5.3.x-1: DataPoints of operationMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| startPause | boolean | true | true | false | True triggers an operation, and False pauses the operation. |

### -----------------------End of change 4-------------------------------------------

### -----------------------Start of change 5-------------------------------------------

### 5.3.x	remoteControlEnable

This ModuleClasses provides capabilities to monitor the remote controllability of the appliance.

Table 5.3.x-1: DataPoints of remoteControlEnable ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| remoteControlEnabled | boolean | true | false | false | This datapoint is set by user locally and it fundamentally enables or disables remote controllability. True means it allows remote access, and False means it does not. In False case, however, it still allows to monitor relevant resources. |

### -----------------------End of change 5-------------------------------------------

### -----------------------Start of change 6-------------------------------------------

### 5.3.x	washingCourse

This ModuleClasses provides capabilities to control and monitor the washing course of washer.

Table 5.3.x-1: DataPoints of smartReady ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentWashingCourseName | string | true | true | true | Currently active course name in human readable language |
| currentWashingCourse | hd:washingCourse | true | true | false | Currently active course. |
| washingCourses | list of hd:washingCourse | true | false | false | Supported courses by washer. |

### -----------------------End of change 6-------------------------------------------

### -----------------------Start of change 7-------------------------------------------

### 5.5.x	hd:washingCourse

Used for currentWashingCourse and washingCourses DataPoints of washingCourse ModuleClass. Washing options such as water temperature and spin speed are decided to pre-set values upon selected washing course. Manufacturers can define their own courses by setting this value to 99.

Table 5.5.x-1: Interpretation of washingCourse

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | normal |  |
| 2 | smallLoad |  |
| 3 | delicate |  |
| 4 | comforter |  |
| 5 | expressWash |  |
| 6 | cleanWash |  |
| 7 | kidsWear |  |
| 8 | workoutWears |  |
| 0 | vendorSpecific |  |
| NOTE: See clause 5.3xxxxxx |

### -----------------------End of change 7-------------------------------------------

### -----------------------Start of change 8-------------------------------------------

### 5.3.x	washingCourseOption

This ModuleClasses provides capabilities to control and monitor the washing course options of washer.

Table 5.3.x-1: DataPoints of smartReady ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| washTemp | hd:generalTemperature | true | true | true | Option for temperature of water |
| soilLevel | hd:generalLevel | true | true | true | Option for washing level |
| spinSpeed | hd:generalSpeed | true | true | true | Option for spin-dry speed |
| preWash | boolean | true | true | true | Option for pre-wash |
| speedWash | boolean | true | true | true | Option for speed wash |
| steamTreat | boolean | true | true | true | Option for steam treat |
| coldWash | boolean | true | true | true | Option for cold wash |
| extraRinse | boolean | true | true | true | Option for extra rinse |

### -----------------------End of change 8-------------------------------------------

### -----------------------Start of change 9-------------------------------------------

### 5.5.x	hd:generalTemperature

Used for washTemp DataPoint of washingCourseOption ModuleClass.

Table 5.5.x-1: Interpretation of generalTemperature

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | cold | Actual temperature is set by manufacturer |
| 2 | warm |  |
| 3 | hot |  |
| NOTE: See clause 5.3xxxxxx |

### -----------------------End of change 9-------------------------------------------

### -----------------------Start of change 10-------------------------------------------

### 5.5.x	hd:generalLevel

Used for soilLevel DataPoint of washingCourseOption ModuleClass.

Table 5.5.x-1: Interpretation of level

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | light |  |
| 2 | normal |  |
| 3 | heavy |  |
| NOTE: See clause 5.3xxxxxx |

### -----------------------End of change 10-------------------------------------------

### -----------------------Start of change 11-------------------------------------------

### 5.5.x	hd:generalSpeed

Used for spinSpeed DataPoint of washingCourseOption ModuleClass.

Table 5.5.x-1: Interpretation of speed

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | low |  |
| 2 | medium |  |
| 3 | high |  |
| 4 | extraHigh |  |
| NOTE: See clause 5.3xxxxxx |

### -----------------------End of change 11-------------------------------------------

### -----------------------Start of change 12-------------------------------------------

### 5.4.2	deviceClothesWasher

A clothes washer is a home appliance that is used to wash laundry, such as clothing and sheets. This information model provides capabilities to interact with specific functions and resources of clothes washers.

Table 5.4.2-1: Modules of deviceClothesWasher Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.5 |
| operationMode | operationMode | false | See clause 5.3.x |
| runstate | runstate | false | See clause 5.3.28 |
| washingCourse | washingCourse | false | See clause 5.3.x |
| washingCourseOption | washingCourseOption | true | See clause 5.3.x |
| remoteControl | remoteControl | true | See clause 5.3.x |
| timer | timer | true | See clause 5.3.35 |

### -----------------------End of change 12-------------------------------------------

### -----------------------Start of change 13-------------------------------------------

### 6.3.2	Resource types

Table 6.3.2-2: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| alarmSpeaker | alaSr |
| audioVideoInput | auVIt |
| audioVolume | audVe |
| battery | batty |
| binarySwitch | binSh |
| bioElectricalImpedanceAnalysis | bEIAs |
| boiler | boilr |
| brewing |  |
| brightness | brigs |
| clock | clock |
| colour | color |
| colourSaturation | colSn |
| customTemperature | cusTe |
| doorStatus | dooSe |
| electricVehicleConnector | elVCr |
| energyConsumption | eneCn |
| energyGeneration | eneGn |
| faultDetection | fauDn |
| foaming |  |
| freshTemperature | freTe |
| frozenTemperature | froTe |
| grinder |  |
| height | heigt |
| hotWaterSupply | hoWSy |
| keypad | keypd |
| liquidLevel |  |
| motionSensor | motSr |
| operationMode |  |
| oximeter | oximr |
| powerSave | powS0 |
| pushButton | pusBn |
| recorder | recor |
| refrigeration | refrn |
| relativeHumidity | relHy |
| liquidRemaining |  |
| runState |  |
| signalStrength | sigSh |
| remoteControl |  |
| smokeSensor | smoSr |
| spinLevel | spiLl |
| televisionChannel | telCl |
| temperature | tempe |
| temperatureAlarm | temAm |
| timer | timer |
| turbo | turbo |
| washingCourse |  |
| washingCourseOption |  |
| waterFlow | watFw |
| waterSensor | watSr |
| weight | weigt |
| wind | wind |

Table 6.3.3-2: Resource attribute short names (ModuleClass data points) (1/2)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| absoluteEnergyConsumption | energyConsumption | abECn |
| absoluteStartTime | timer | abSTe |
| absoluteStopTime | timer | abST0 |
| alarm | motionSensor, smokeSensor, temperatureAlarm, waterSensor | alarm |
| alarmStatus | alarmSpeaker | alaSs |
| availableChannels | televisionChannel | avaCs |
| bath | hotWaterSupply | bath |
| batteryThreshold | battery | batTd |
| blue | colour | blue |
| bone | bioelectricalImpedanceAnalysis | bone |
| brightness | brightness | brigs |
| capacity | battery | capay |
| channelId | televisionChannel | chaId |
| charging | battery | charg |
| coarseness | grinder |  |
| code | faultDetection | code |
| coldWash | washingCourceOption |  |
| colourSaturation | colourSaturation | colSn |
| cupsNumber | brewing |  |
| current | energyConsumption | currt |
| currentDate | clock | curDe |
| currentJobState | runState |  |
| currentMachingState | runState |  |
| currentWashingCourse | washingCource |  |
| currentTemperature | temperature | curT0 |
| currentTime | clock | curTe |
| defrost | refrigeration | defrt |
| description | faultDetection | descn |
| desiredHumidity | relativeHumidity | desHy |
| detectedTime | smokeSensor | detTe |
| diastolicPressure | oximeter | diaPe |
| directionAuto | wind | dirAo |
| directionDown | wind | dirDn |
| directionLeft | wind | dirLt |
| directionRight | wind | dirRt |
| directionUp | wind | dirUp |
| discharging | battery | discg |
| doorState | doorStatus | dooSe |
| duration | recorder | duran |
| estimatedTimeToEnd | timer | eTTEd |
| extraRinse | washingCourceOption |  |
| fat | bioElectricalImpedanceAnalysis | fat |
| filterLifetime | refrigeration | filLe |
| frequency | energyConsumption | freqy |
| foamingStrength | foaming |  |
| grainsRemaining | grinder |  |
| green | colour | green |
| height | height | heigt |
| inputSourceID | audioVideoInput | inSId |
| jobStates | runState |  |
| kcal | bioElectricalImpedanceAnalysis | kcal |
| keepWarm | brewing |  |
| keyNumber | keypad | keyNr |
| level | battery | level |
| light | alarmSpeaker | light |
| liquidLevel | liquidLevel | liqLl |
| liquidRemaining | liquidRemaining |  |
| lowBattery | battery | lowBy |
| lqi | signalStrength | lqi |
| machineStates | runState |  |
| maxValue | audioVolume, temperature | maxVe |
| minValue | temperature | minVe |
| multiplyingFactors | energyConsumption, energyGeneration | mulFs |
| muscle | bioElectricalImpedanceAnalysis | musce |
| muteEnabled | audioVolume | mutEd |
| openAlarm | doorStatus | opeAm |
| openDuration | doorStatus | opeDn |
| oxygenSaturation | oximeter | oxySn |

Table 6.3.3-3: Resource attribute short names (ModuleClass data points) (2/2)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| power | energyConsumption | power |
| powerGenerationData | energyGeneration | poGDa |
| powerSaveEnabled | powerSave | poSEd |
| powerState | binarySwitch | powSe |
| preWash | washingCourceOption |  |
| previousChannel | televisionChannel | preCl |
| progressPercentage | runState |  |
| pulseRate | oximeter | pulRe |
| pushed | pushButton | pusBn |
| rapidCool | refrigeration | rapCl |
| rapidFreeze | refrigeration | rapFe |
| red | colour | red |
| referenceTimer | timer | refTr |
| relativeHumidity | relativeHumidity | relHy |
| resistance | bioElectricalImpedanceAnalysis | resie |
| rinseLevel | rinseLevel | rinLl |
| roundingEnergyConsumption | energyConsumption | roECn |
| roundingEnergyGeneration | energyGeneration | roEGn |
| rssi | signalStrength | rssi |
| runningTime | timer | runTe |
| sensitivity | motionSensor | sensy |
| significantDigits | energyConsumption, energyGeneration | sigDs |
| silentTime | motionSensor | silTe |
| remoteControlEnabled | remoteControl |  |
| soilLevel | washingCourceOption |  |
| speedWash | washingCourceOption |  |
| spinSpeed | washingCourceOption |  |
| startPause | operationMode |  |
| status | boiler, electricVehicleConnector, faultDetection, hotWaterSupply, brewing | stats |
| steamTreat | washingCourceOption |  |
| stepValue | audioVolume, temperature | steVe |
| strength | spinLevel, waterFlow, wind, brewing | streh |
| supportedInputSources | audioVideoInput | suISs |
| systolicPressure | oximeter | sysPe |
| targetDuration | timer | tarDn |
| targetTemperature | temperature | tarTe |
| targetTimeToStart | timer | tTTSt |
| targetTimeToStop | timer | tTTSp |
| temperature | temperatureAlarm | tempe |
| temperatureThreshhold | temperatureAlarm | temTd |
| tone | alarmSpeaker | tone |
| turboEnabled | turbo | turEd |
| unit | temperature | unit |
| useGrinder | grinder |  |
| visceraFat | bioElectricalImpedanceAnalysis | visFt |
| voltage | energyConsumption | volte |
| volumePercentage | audioVolume | volPe |
| washingCourses | washingCourse |  |
| washTemp | washingCourceOption |  |
| water | bioElectricalImpedanceAnalysis | water |
| weight | weight | weigt |

### -----------------------End of change 13-------------------------------------------

### -----------------------Start of change 14-------------------------------------------

### 6.4.3	ModuleClasses

The containerDefinition attribute of specializations for module classes shall have the values specifien in Table 6.4.3-1.

Table 6.4.3-1: containerDefinition values of specializations for module classes

| Resource Type Name | containerDefinition value |
| --- | --- |
| alarmSpeaker | "org.onem2m.home.moduleclass.alarmSpeaker" |
| audioVideoInput | "org.onem2m.home.moduleclass.audioVideoInput" |
| audioVolume | "org.onem2m.home.moduleclass.audioVolume" |
| battery | "org.onem2m.home.moduleclass.battery" |
| binarySwitch | "org.onem2m.home.moduleclass.binarySwitch" |
| bioElectricalImpedanceAnalysis | "org.onem2m.home.moduleclass.bioElectricalImpedanceAnalysis" |
| boiler | "org.onem2m.home.moduleclass.boiler" |
| brewing | "org.onem2m.home.moduleclass.brewing” |
| brightness | "org.onem2m.home.moduleclass.brightness" |
| clock | "org.onem2m.home.moduleclass.clock" |
| colour | "org.onem2m.home.moduleclass.colour" |
| colourSaturation | "org.onem2m.home.moduleclass.colourSaturation" |
| customTemperature | "org.onem2m.home.moduleclass.customTemperature" |
| doorStatus | "org.onem2m.home.moduleclass.doorStatus" |
| electricVehicleConnector | "org.onem2m.home.moduleclass.electricVehicleConnector" |
| energyConsumption | "org.onem2m.home.moduleclass.energyConsumption" |
| energyGeneration | "org.onem2m.home.moduleclass.energyGeneration" |
| faultDetection | "org.onem2m.home.moduleclass.faultDetection" |
| foaming | "org.onem2m.home.moduleclass.foaming” |
| freshTemperature | "org.onem2m.home.moduleclass.freshTemperature" |
| frozenTemperature | "org.onem2m.home.moduleclass.frozenTemperature" |
| grinder | "org.onem2m.home.moduleclass.grinder” |
| height | "org.onem2m.home.moduleclass.height" |
| hotWaterSupply | "org.onem2m.home.moduleclass.hotWaterSupply" |
| keypad | "org.onem2m.home.moduleclass.keypad" |
| liquidLevel | "org.onem2m.home.moduleclass.liquidLevel” |
| liquidRemaining | "org.onem2m.home.moduleclass.liquidRemaining” |
| motionSensor | "org.onem2m.home.moduleclass.motionSensor" |
| operationMode | "org.onem2m.home.moduleclass.operationMode" |
| oximeter | "org.onem2m.home.moduleclass.oximeter" |
| powerSave | "org.onem2m.home.moduleclass.powerSave" |
| pushButton | "org.onem2m.home.moduleclass.pushButton" |
| recorder | "org.onem2m.home.moduleclass.recorder" |
| refrigeration | "org.onem2m.home.moduleclass.refrigeration" |
| relativeHumidity | "org.onem2m.home.moduleclass.relativeHumidity" |
| rinseLevel | "org.onem2m.home.moduleclass.rinseLevel" |
| runState | "org.onem2m.home.moduleclass.runState " |
| signalStrength | "org.onem2m.home.moduleclass.signalStrength" |
| remoteControl | "org.onem2m.home.moduleclass.remoteControl" |
| smokeSensor | "org.onem2m.home.moduleclass.smokeSensor " |
| spinLevel | "org.onem2m.home.moduleclass.spinLevel" |
| televisionChannel | "org.onem2m.home.moduleclass.televisionChannel" |
| temperature | "org.onem2m.home.moduleclass.temperature" |
| temperatureAlarm | "org.onem2m.home.moduleclass.temperatureAlarm" |
| timer | "org.onem2m.home.moduleclass.timer" |
| turbo | "org.onem2m.home.moduleclass.turbo" |
| washingCourse | "org.onem2m.home.moduleclass.washingCourse" |
| washingCourseOption | "org.onem2m.home.moduleclass.washingCourseOption" |
| waterFlow | "org.onem2m.home.moduleclass.waterFlow" |
| waterSensor | "org.onem2m.home.moduleclass.waterSensor" |
| weight | "org.onem2m.home.moduleclass.weight" |
| wind | "org.onem2m.home.moduleclass.wind" |

### -----------------------End of change 14-------------------------------------------

### -----------------------Start of change 15-------------------------------------------

### 6.5.3	XSD definitions for ModuleClass

The XSD definitions for ModuleClass are listed in Table 6.5.3-1.

Table 6.5.3-1: XSD definition of ModuleClasses

| ModuleClass ID | File Name | Note |
| --- | --- | --- |
| alarmSpeaker | HD-mod-alarmSpeaker-v<TS-version>.xsd |  |
| audioVideoInput | HD-mod-audioVideoInput-v<TS-version>.xsd |  |
| audioVolume | HD-mod-audioVolume-v<TS-version>.xsd |  |
| battery | HD-mod-battery-v<TS-version>.xsd |  |
| binarySwitch | HD-mod-binarySwitch-v<TS-version>.xsd |  |
| bioElectricalImpedanceAnalysis | HD-mod-bioElectricalImpedanceAnalysis-v<TS-version>.xsd |  |
| boiler | HD-mod-boiler-v<TS-version>.xsd |  |
| brewing | HD-mod- brewing -v<TS-version>.xsd |  |
| brightness | HD-mod-brightness-v<TS-version>.xsd |  |
| clock | HD-mod-clock-v<TS-version>.xsd |  |
| colour | HD-mod-colour-v<TS-version>.xsd |  |
| colourSaturation | HD-mod-colourSaturation-v<TS-version>.xsd |  |
| doorStatus | HD-mod-doorStatus-v<TS-version>.xsd |  |
| electricVehicleConnector | HD-mod-electricVehicleConnector-v<TS-version>.xsd |  |
| energyConsumption | HD-mod-energyConsumption-v<TS-version>.xsd |  |
| energyGeneration | HD-mod-energyGeneration-v<TS-version>.xsd |  |
| faultDetection | HD-mod-faultDetection-v<TS-version>.xsd |  |
| foaming | HD-mod- foaming -v<TS-version>.xsd |  |
| grinder | HD-mod- grinder -v<TS-version>.xsd |  |
| height | HD-mod-height-v<TS-version>.xsd |  |
| hotWaterSupply | HD-mod-hotWaterSupply-v<TS-version>.xsd |  |
| keypad | HD-mod-keypad-v<TS-version>.xsd |  |
| liquidLevel | HD-mod- liquidLevel -v<TS-version>.xsd |  |
| liquidRemaining | HD-mod- liquidRemaining -v<TS-version>.xsd |  |
| motionSensor | HD-mod-motionSensor-v<TS-version>.xsd |  |
| operationMode | HD-mod- operationMode-v<TS-version>.xsd |  |
| oximeter | HD-mod-oximeter-v<TS-version>.xsd |  |
| powerSave | HD-mod-powerSave-v<TS-version>.xsd |  |
| pushButton | HD-mod-pushButton-v<TS-version>.xsd |  |
| recorder | HD-mod-recorder-v<TS-version>.xsd |  |
| refrigeration | HD-mod-refrigeration-v<TS-version>.xsd |  |
| relativeHumidity | HD-mod-relativeHumidity-v<TS-version>.xsd |  |
| rinseLevel | HD-mod-rinseLevel-v<TS-version>.xsd |  |
| runState | HD-mod-runState-v<TS-version>.xsd |  |
| signalStrength | HD-mod-signalStrength-v<TS-version>.xsd |  |
| remoteControl | HD-mod- remoteControl-v<TS-version>.xsd |  |
| smokeSensor | HD-mod-smokeSensor-v<TS-version>.xsd |  |
| spinLevel | HD-mod-spinLevel-v<TS-version>.xsd |  |
| televisionChannel | HD-mod- HD-mod--v<TS-version>.xsd |  |
| temperature | HD-mod-temperature-v<TS-version>.xsd |  |
| temperatureAlarm | HD-mod-temperatureAlarm-v<TS-version>.xsd |  |
| timer | HD-mod-timer-v<TS-version>.xsd |  |
| turbo | HD-mod-turbo-v<TS-version>.xsd |  |
| washingCourse | HD-mod-washingCourse-v<TS-version>.xsd |  |
| washingCourseOption | HD-mod-washingCourseOption-v<TS-version>.xsd |  |
| waterFlow | HD-mod-waterFlow-v<TS-version>.xsd |  |
| waterSensor | HD-mod-waterSensor-v<TS-version>.xsd |  |
| weight | HD-mod-weight-v<TS-version>.xsd |  |
| wind | HD-mod-wind-v<TS-version>.xsd |  |
| NOTE: The string '<TS-version>' shall be intepreted as the version of the present document. |

### -----------------------End of change 15-------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?