| CHANGE REQUEST |
| --- |
| Meeting:* | MAS27 |
| Source:* | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2017-02-13 |
| Contact:* | As above |
| Reason for Change/s:* | Corrects mgmtLink in [registration] to refer to an [authenticationProfile] instance, in order to align with MAS-2017-0005Rxx |
| CR against: Release* | Release 2.x |
| CR against: WI* | Active WI-0030 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0022 and 0.9.0 |
| Clauses/Sub Clauses* | 7.1.2.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

Corrects description of [registration] resource to align with MAS-2017-0005Rxx:

- mgmtLink in [registration] is changed to refer to [authenticationProfile].

- Note 1 in Table 7.1.2.1-2 has also been updated to align with offline discussion between Shingo Fujimoto (FUJITSU), Tim Carey (NOKIA) and Phil Hawkes (QUALCOMM).

- The text following Table 7.1.2.1-2  is no longer applicable and has been deleted.

The CR, as shown, does not account for the re-organization proposed in MAS-2017-0023. If MAS-2017-0023, is agreed, then the changes would be easiely integrated.

R01:  Replaced the figure with the corrected on as given in agreed CR MAS-2017-0023.

### ----------------------- Start of change 1 -------------------------------

#### Introduction

This specialization of <mgmtObj> is used to convey the service layer configuration information needed to register an AE or CSE with a Registrar CSE.

Figure 7.1.2.1-1: Structure of [registration] resource

Table 7.1.2.1-1: Data Type Definition of [registration]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| registration | DCFG-registration-v1_0.xsd |  |

Table 7.1.2.1-2: Resource specific attributes of [registration]

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| mgmtDefinition | M | NP | See clause 7.4.15of oneM2M TS-0004 [4]. | "registration" |
| objectIDs | O | NP | See clause 7.4.15 of oneM2M TS-0004 [4]. |  |
| objectPaths | O | NP | See clause 7.4.15 of oneM2M TS-0004 [4]. |  |
| description | O | O | See clause 7.4.15 of oneM2M TS-0004 [4]. |  |
| originatorID | O | O | m2m:ID | CSE-ID of the CSE hosted on the ASN/MN or the AE-ID of an AE hosted on an ASN/MN or ADN node. If the setting is for a CSE, then this attribute shall be present. |
| poA | M | O | xs:anyURI | The point of access URI of the Registrar CSE. Note; protocol binding is determined from the protocol schema in this URI. |
| appID | O | O | m2m:ID | The APP_ID of an AE. This attribute shall only be present when this resource is used for the registration of an AE. |
| externalID | O | O | m2m:externalID | The M2M-Ext-ID of the ASN/MN CSE. This attribute can be present when the originatorID is a CSE-ID and the CSE uses the dynamic registration defined in clause 7.1.10 Trigger Recipient Identifier of TS-0001 [2]. |
| triggerRecipientID | O | O | m2m:triggerRecipientID | The Trigger-Recipient-ID of the ASN/MN CSE. This attribute can be present when the originatorID is a CSE-ID and the CSE uses the dynamic registration defined in clause 7.1.10 Trigger Recipient Identifier of TS-0001 [2]. |
| mgmtLink | O | O | m2m:mgmtLinkRef | 1 link to a [authenticationProfile] resource instance. See Note 1. |
| NOTE 1: The SUID in the linked [authenticationProfile] instance constrains the security framework to be used with the Authentication Profile. The security frameworks used with the [registration] resource are Security Association Establishment Frameworks (SAEF). The entity composing a [registration] instance is expected to confirm that the linked Authentication Profile contains a SUID corresponding to an SAEF. The SAEF SUIDs are the values 12, 22, 32 or 42 as defined in oneM2M TS-0004 [4]. |

#### 7.1.2.2 Resource specific procedure on CRUD operations

### ----------------------- End of change 1 -------------------------------

# Comments

Should this be authProfileRef ?