| Input Contribution |
| --- |
| Meeting ID* | MAS27.2 |
| Title:* | Adding_the_Mapping_clause_to_TS-0023 |
| Source:* | Kei Harada(harada.kei@lab.ntt.co.jp), NTT, Hiroyuki Maeomichi(maeomichi.hiroyuki@lab.ntt.co.jp), NTT, Takashi Yoshikawa(yoshikawatak@nttdocomo.com), NTT DOCOMO, |
| Uploaded Date:* | 2017-03-03 |
| Document(s) Impacted* | TS-0023 Rel-3 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Adding the new clause about mapping to TS-0023 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution proposed to create new clause in 7.0 Mapping with Other Information Models from External Organizations to clarify the mapping with non-oneM2M data model.

### -----------------------Start of change 1-------------------------------------------

# Contents

1	Scope	6

2	References	6

2.1	Normative references	6

2.2	Informative references	6

3	Definitions	6

4	Conventions	7

5	Home Appliance Information Model	7

5.1	Introduction	7

5.2	Design Principle of the Home Appliance Information Model	7

5.2.1	Basic design principle of information modelling	7

5.2.2	Description rules for Module Classes and Device models	8

5.3	ModuleClasses	9

5.3.1	alarmSpeaker	9

5.3.2	audioVideoInput	9

5.3.3	audioVolume	9

5.3.4	battery	10

5.3.5	binarySwitch	10

5.3.6	bioElectricalImpedanceAnalysis	11

5.3.7	boiler	11

5.3.8	brightness	11

5.3.9	clock	12

5.3.10	colour	12

5.3.11	colourSaturation	12

5.3.12	doorStatus	12

5.3.13	electricVehicleConnector	12

5.3.14	energyConsumption	13

5.3.15	energyGeneration	13

5.3.16	faultDetection	14

5.3.17	height	14

5.3.18	hotWaterSupply	14

5.3.19	keypad	14

5.3.20	motionSensor	15

5.3.21	oximeter	15

5.3.22	powerSave	15

5.3.23	pushButton	15

5.3.24	recorder	15

5.3.25	refrigeration	16

5.3.26	relativeHumidity	16

5.3.27	openLevel	16

5.3.28	runState	17

5.3.29	signalStrength	17

5.3.30	smokeSensor	18

5.3.31	spinLevel	18

5.3.32	televisionChannel	18

5.3.33	temperature	18

5.3.34	temperatureAlarm	19

5.3.35	timer	19

5.3.36	turbo	20

5.3.37	waterFlow	20

5.3.38	liquidLevel	21

5.3.39	waterSensor	21

5.3.40	weight	21

5.3.41	wind	21

5.3.42	doorLock	22

5.3.43	liquidRemaining	22

5.3.44	foaming	22

5.3.45	grinder	22

5.3.46	brewing	23

5.3.47	sphygmomanometer	23

5.3.48	pulsemeter	23

5.3.49	glucometer	24

5.3.50	bodyCompositionAnalyzer	24

5.3.51	operationMode	25

5.3.52	remoteControlEnable	25

5.3.53	washingCourse	25

5.3.54	washingCourseOption	26

5.4	Device models	26

5.4.1	deviceAirConditioner	26

5.4.2	deviceClothesWasher	26

5.4.3	deviceElectricVehicleCharger	27

5.4.4	deviceLight	27

5.4.5	deviceMicrogeneration	27

5.4.6	deviceOven	27

5.4.7	deviceRefrigerator	28

5.4.8	deviceRobotCleaner	28

5.4.9	deviceSmartElectricMeter	28

5.4.10	deviceStorageBattery	29

5.4.11	deviceTelevision	29

5.4.12	deviceThermostat	29

5.4.13	deviceWaterHeater	29

5.4.14	deviceSwitch	30

5.4.15	deviceWindowShade	30

5.4.16	deviceDoorLock	30

5.4.17	deviceCoffeeMachine	30

5.4.18	deviceBloodPressureMonitor	30

5.4.19	deviceGlucosemeter	31

5.4.20	devicePulseOximeter	31

5.4.21	deviceThermometer	31

5.4.22	deviceWeightScaleAndBodyCompositionAnalyzer	31

5.4.23	deviceHeartRateMonitor	32

5.5	Enumeration type definitions	32

5.5.1	hd:deviceType	32

5.5.2	hd:supportedInputSources	32

5.5.3	hd:liquidLevel	33

5.5.4	hd:spinLevelStrength	33

5.5.5	hd:doorState	33

5.5.6	hd:tone	34

5.5.7	hd:jobStates	34

5.5.8	hd:alertColourCode	35

5.5.9	hd:waterFlowStrength	35

5.5.10	hd:windStrength	35

5.5.11	hd:grainsLevel	35

5.5.12	hd:foamStrength	36

5.5.13	hd:tasteStrength	36

5.5.14	hd:grindCoarseness	36

5.5.15	hd:machineState	36

5.5.16	hd:washingCourse	37

5.5.17	hd:generalTemperature	37

5.5.18	hd:generalLevel	37

5.5.19	hd:generalSpeed	38

5.6	Universal and Common Properties for Device models	38

6	The Principle of Resource Mapping for Home Appliance Information Model	38

6.1	Introduction	38

6.2	The Resource Mapping Rules	38

6.2.1	Introduction	38

6.2.2	Resource mapping for Device model	38

6.2.3	Resource mapping for ModuleClass	39

6.2.4	Resource mapping for Action	39

6.2.5	Resource mapping for Property	39

6.2.6	Resource mapping for DataPoint	40

6.3	Short names	40

6.3.1	Introduction	40

6.3.2	Resource types	40

6.3.3	Resource attributes for properties and data points	42

6.4	containerDefinition values	45

6.4.1	Introduction	45

6.4.2	Device models	45

6.4.3	ModuleClasses	45

6.4.4	Actions	46

6.5	XSD definitions	46

6.5.1	Introduction	46

6.5.2	XSD definitions for Device models	47

6.5.3	XSD definitions for ModuleClass	47

6.5.4	XSD definitions for Action	48

7	Mapping with Other Information Models from External Organizations	49

7.1	 OMA DWAPI-PCH

7.1.1	data point

7.1.2	module class

7.1.3	device model

7.1.4	data type

7.1.5	property

7.2	AllJoyn

7.2.1	data point

7.2.2	module class

7.2.3	device model

7.2.4	data type

7.2.5	property

7.3	OIC

7.3.1	data point

7.3.2	module class

7.3.3	device model

7.3.4	data type

7.3.5	property

7.4	ECHONET

7.4.1	data point

7.4.2	module class

7.4.3	device model

7.4.4	data type

7.4.5	property

8	Ontology for the Home Appliance Information Model aligned with oneM2M Base Ontology	49

Annex A (informative):  Resource Mapping Examples	51

A.1	Introduction	51

A.2	Example for Device model ‘deviceAirConditioner'	51

A.3	Example of ModuleClass 'binarySwitch'	53

A.4	Example of Action 'toggle'	54

History	54

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

# 7	Mapping with Other Information Models from External Organizations

This clause is intended to specify how the Home Appliance Information Model (HAIM) defined in the clause 5 of the present document can be mapped with existing external models from AllJoyn, OIC, ECHONET, OMA DWAPI-PCH etc. The mapping is to enable the interworking between the oneM2M system  and external technologies at the information model level. This means a oneM2M native application which understand only oneM2M standardized HAIM can interact with non-oneM2M home appliances of different technologies in a consistent way without knowing the technology specific details. An IPE is responsible for translating the HAIM to/from technology specific information model bidirectionally following the mapping specification in this clause. Using HAIM as a bridge, home appliances and applications of different technologies can also interact with each other via the oneM2M system (with IPEs).

7.1	OMA DWAPI-PCH

introduction about OMA DWAPI-PCH data model.

7.1.1	data point

use the table same as the TS-0005 Management Enablrmrnt(OMA) clause 5.

Table 7.1.1 OMA DWAPI-PCH

| oneM2M data point | Mapping to data object in OMA DWAPI-PCH | Description |
| --- | --- | --- |
| (ex.) diastolicPressure | (ex.)diastlic | (ex.)The measurement of diastolic pressure by sphygmomanometer. The common unit is millimetre of mercury (mmHg). |

7.1.2	module class

use the table same as the TS-0005 Management Enablrmrnt(OMA) clause 5.

Table 7.1.2 OMA DWAPI-PCH

| oneM2M module class | Mapping to data object in OMA DWAPI-PCH | Description |
| --- | --- | --- |
| (ex.)spygmomanometer | (ex.)Blood Pressure Monitor | (ex.)This ModuleClass provides the capability to report the measurement of blood pressure characteristics. |

7.1.3	device model

use the table same as the TS-0005 Management Enablrmrnt(OMA) clause 5.

Table 7.1.3 OMA DWAPI-PCH

| oneM2M device model | Mapping to data object in OMA DWAPI-PCH | Description |
| --- | --- | --- |
| (ex.)deviceBloodPressureMonitor | (ex.)Blood Pressure Monitor | (ex.)A device blood pressure is a device that can be used to monitor the blood pressure. |

7.1.4	data type

use the table same as the TS-0005 Management Enablrmrnt(OMA) clause 5.

Table 7.1.4 OMA DWAPI-PCH

| oneM2M data type | Mapping to data type in OMA DWAPI-PCH | Description |
| --- | --- | --- |
| (ex.)xs: integer | (ex.)int | (ex.)Data type for 32-bit signed integer |

7.1.5	property

use the table same as the TS-0005 Management Enablrmrnt(OMA) clause 5.

Table 7.1.5 OMA DWAPI-PCH

| oneM2M universal/common property | Mapping to data point in OMA DWAPI-PCH | Description |
| --- | --- | --- |
| (ex.)deviceLabel | (ex.)serialNumber | (ex.) Unique device label assigned by the manufacturer. The uniqueness may be global or only valid within a certain domain (e.g. vendor-wise or for a certain deviceType). This attribute is a specialization of [objectAttribute] attribute. It’s typically used as e.g. device serial number. |

## 7.2	AllJoyn

## introduction about AllJoyn data model.

## 7.2.1	data point

## 7.2.2	module class

## 7.2.3	device model

## 7.2.4	data type

## 7.3.5	property

## 7.3	OIC

introduction about OIC data model.

## 7.3.1	data point

## 7.3.2	module class

## 7.3.3	device model

## 7.3.4	data type

## 7.3.5	property

## 7.4	ECHONET

introduction about ECHONET data model.

## 7.4.1	data point

## 7.4.2	module class

## 7.4.3	device model

## 7.4.4	data type

## 7.4.5	property

### -----------------------End of change 2-------------------------------------------