| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC#28 |
| Source:* | NTT, NTT DOCOMO |
| Date:* | 2017-03-30 |
| Contact:* | Kei Harada(harada.kei@lab.ntt.co.jp), NTT, Hiroyuki Maeomichi(maeomichi.hiroyuki@lab.ntt.co.jp), NTT, Yoshihisa Ito(ito.yoshihisa@lab.ntt.co.jp), NTT, Takashi Yoshikawa(yoshikawatak@nttdocomo.com), NTT DOCOMO |
| Reason for Change/s:* | To add the contents to clause 7.0. |
| CR against: Release* | R3 |
| CR against: WI* | Active <WI-0056> MNT maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.2.0 |
| Clauses * | 7.0 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | TS-0023 |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposed to add contents to 7.0 Mapping with Other Information Models from External Organizations to clarify the mapping with non-oneM2M data model.

Rev-1: Add the annex B.

Rev-2: Reconstruct the clause.

Rev-3: Reconstruct the clause and tables.

### -----------------------Start of change 1-------------------------------------------

# Contents

1	Scope	6

2	References	6

2.1	Normative references	6

2.2	Informative references	6

3	Definitions	6

4	Conventions	7

5	Home Appliance Information Model	7

5.1	Introduction	7

5.2	Design Principle of the Home Appliance Information Model	7

5.2.1	Basic design principle of information modelling	7

5.2.2	Description rules for Module Classes and Device models	8

5.3	ModuleClasses	9

5.3.1	alarmSpeaker	9

5.3.2	audioVideoInput	9

5.3.3	audioVolume	9

5.3.4	battery	10

5.3.5	binarySwitch	10

5.3.6	bioElectricalImpedanceAnalysis	11

5.3.7	boiler	11

5.3.8	brightness	11

5.3.9	clock	12

5.3.10	colour	12

5.3.11	colourSaturation	12

5.3.12	doorStatus	12

5.3.13	electricVehicleConnector	12

5.3.14	energyConsumption	13

5.3.15	energyGeneration	13

5.3.16	faultDetection	14

5.3.17	height	14

5.3.18	hotWaterSupply	14

5.3.19	keypad	14

5.3.20	motionSensor	15

5.3.21	oximeter	15

5.3.22	powerSave	15

5.3.23	pushButton	15

5.3.24	recorder	15

5.3.25	refrigeration	16

5.3.26	relativeHumidity	16

5.3.27	openLevel	16

5.3.28	runState	17

5.3.29	signalStrength	17

5.3.30	smokeSensor	18

5.3.31	spinLevel	18

5.3.32	televisionChannel	18

5.3.33	temperature	18

5.3.34	temperatureAlarm	19

5.3.35	timer	19

5.3.36	turbo	20

5.3.37	waterFlow	20

5.3.38	liquidLevel	21

5.3.39	waterSensor	21

5.3.40	weight	21

5.3.41	wind	21

5.3.42	doorLock	22

5.3.43	liquidRemaining	22

5.3.44	foaming	22

5.3.45	grinder	22

5.3.46	brewing	23

5.3.47	sphygmomanometer	23

5.3.48	pulsemeter	23

5.3.49	glucometer	24

5.3.50	bodyCompositionAnalyzer	24

5.3.51	operationMode	25

5.3.52	remoteControlEnable	25

5.3.53	washingCourse	25

5.3.54	washingCourseOption	26

5.4	Device models	26

5.4.1	deviceAirConditioner	26

5.4.2	deviceClothesWasher	26

5.4.3	deviceElectricVehicleCharger	27

5.4.4	deviceLight	27

5.4.5	deviceMicrogeneration	27

5.4.6	deviceOven	27

5.4.7	deviceRefrigerator	28

5.4.8	deviceRobotCleaner	28

5.4.9	deviceSmartElectricMeter	28

5.4.10	deviceStorageBattery	29

5.4.11	deviceTelevision	29

5.4.12	deviceThermostat	29

5.4.13	deviceWaterHeater	29

5.4.14	deviceSwitch	30

5.4.15	deviceWindowShade	30

5.4.16	deviceDoorLock	30

5.4.17	deviceCoffeeMachine	30

5.4.18	deviceBloodPressureMonitor	30

5.4.19	deviceGlucosemeter	31

5.4.20	devicePulseOximeter	31

5.4.21	deviceThermometer	31

5.4.22	deviceWeightScaleAndBodyCompositionAnalyzer	31

5.4.23	deviceHeartRateMonitor	32

5.5	Enumeration type definitions	32

5.5.1	hd:deviceType	32

5.5.2	hd:supportedInputSources	32

5.5.3	hd:liquidLevel	33

5.5.4	hd:spinLevelStrength	33

5.5.5	hd:doorState	33

5.5.6	hd:tone	34

5.5.7	hd:jobStates	34

5.5.8	hd:alertColourCode	35

5.5.9	hd:waterFlowStrength	35

5.5.10	hd:windStrength	35

5.5.11	hd:grainsLevel	35

5.5.12	hd:foamStrength	36

5.5.13	hd:tasteStrength	36

5.5.14	hd:grindCoarseness	36

5.5.15	hd:machineState	36

5.5.16	hd:washingCourse	37

5.5.17	hd:generalTemperature	37

5.5.18	hd:generalLevel	37

5.5.19	hd:generalSpeed	38

5.6	Universal and Common Properties for Device models	38

6	The Principle of Resource Mapping for Home Appliance Information Model	38

6.1	Introduction	38

6.2	The Resource Mapping Rules	38

6.2.1	Introduction	38

6.2.2	Resource mapping for Device model	38

6.2.3	Resource mapping for ModuleClass	39

6.2.4	Resource mapping for Action	39

6.2.5	Resource mapping for Property	39

6.2.6	Resource mapping for DataPoint	40

6.3	Short names	40

6.3.1	Introduction	40

6.3.2	Resource types	40

6.3.3	Resource attributes for properties and data points	42

6.4	containerDefinition values	45

6.4.1	Introduction	45

6.4.2	Device models	45

6.4.3	ModuleClasses	45

6.4.4	Actions	46

6.5	XSD definitions	46

6.5.1	Introduction	46

6.5.2	XSD definitions for Device models	47

6.5.3	XSD definitions for ModuleClass	47

6.5.4	XSD definitions for Action	48

7	Mapping with Other Information Models from External Organizations	49

7.1	 OMA GotAPI(DWAPI-PCH) 	507.1.1   Device Models	xx

7.1.1.1   deviceBloodPressureMonitor 	xx

7.1.1.2	   deviceGlucosemeter 	xx

7.1.1.3	   devicePulseOximeter 	xx

7.1.1.4	   deviceThermometer 	xx

7.1.1.5	   deviceWeightScaleAndBodyCompositionAnalyzer 	xx

7.1.1.6	   deviceHeartRateMonitor 	xx

7.1.2   Data Types 	xx

7.2	OCF	xx

7.3	ECHONET	xx8	Ontology for the Home Appliance Information Model aligned with oneM2M Base Ontology	49

Annex A (informative):  Resource Mapping Examples	51

A.1	Introduction	51

A.2	Example for Device model ‘deviceAirConditioner'	51

A.3	Example of ModuleClass 'binarySwitch'	53

A.4	Example of Action 'toggle'	54

Annex B (informative):  Introduction of External Organizations Data Model	55

B.1	OMA GotAPI(DWAPI-PCH)	55

B.2	OCF	xx

B.2	ECHONET	xx

History	54

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

## 2.1	Normative references

The following referenced documents are necessary, partially or totally, for the application of the present document. Their use in the context of this TS is specified by the normative statements that are referring back to this clause

[1]	Home Gateway Initiative Smart Device Template.

NOTE:	Available at https://github.com/Homegateway/SmartDeviceTemplate/tree/7c890b69d9764e341ef1768c5a0e7d53a47cff5c.

[2]	Java coding rule.

[3]	oneM2M TS-0001: "Functional Architecture".

[4]	oneM2M TS-0004: “Service Layer Core Protocol Specification”

[5]	oneM2M TS-0005: ”Management Enablement (OMA)”.

[6]	ISO:80000-1: Quantities and units

NOTE:	Available at http://www.oracle.com/technetwork/java/codeconventions-135099.html.

[7]	Open Mobile AllianceTM: “OMA-ER-Device_WebAPIs-V1_0-20160419-C”.

NOTE:	Available at

[8]	Open Mobile AllianceTM: “OMA-TS-Blood_Pressure_Monitor_APIs-V1_0-20160419-C”.

NOTE:	Available at

[9]	Open Mobile AllianceTM: “OMA-TS-Glucometer_APIs-V1_0-20160419-C”.

NOTE:	Available at

[10]	Open Mobile AllianceTM: “OMA-TS-Heart_Rate_Monitor_APIs-V1_0-20160419-C”.

NOTE:	Available at

[11]	Open Mobile AllianceTM: “OMA-TS-Pulse_Oximeter_APIs-V1_0-20160419-C”.

NOTE:	Available at

[12]	Open Mobile AllianceTM: “OMA-TS-Thermometer_APIs-V1_0-20160419-C”.

NOTE:	Available at

[13]	Open Mobile AllianceTM: “OMA-TS-Weight_Scale_Body_Composition_Analyzer_APIs-V1_0-20160419-C”.

NOTE:	Available at

[14]	W3C Recommendation: “XML Schema Part 2: Datatypes”, 02 May 2001.

NOTE:	Available at http://www.w3.org/XML/Schema/.

### -----------------------End of change 2-------------------------------------------

-----------------------Start of change 3-------------------------------------------

# 7	Mapping with Other Information Models from External Organizations

This clause specifies how the Home Appliance Information Model (HAIM) defined in the clause 5 of the present document can be mapped with existing external models from , OCF, ECHONET, OMA GotAPI etc. and introduction of these models is written in annex B. The mapping shall be  to enable the interworking between the oneM2M system and external technologies at the information model level. This means a oneM2M native application which understand only oneM2M standardized HAIM shall be able to  interact with non-oneM2M home appliances of different technologies in a consistent way without knowing the technology specific details. An IPE shall be  responsible for translating the HAIM to/from technology specific information model bidirectionally following the mapping specification in this clause. Using HAIM as a bridge, home appliances and applications of different technologies shall be able to  also interact with each other via the oneM2M system (with IPEs).

7.1	OMA GotAPI(DWAPI-PCH)

This section is intended to specify the mapping relationship between HAIM and OMA DWAPI-PCH with tables.

## 7.1.1	Device Models

## 7.1.1.1	 deviceBloodPressureMonitor

DeviceBloodPressureMonitoer of HAIM shall be mapped to Blood Pressure Monitor of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.1.1 Map of deviceBloodPressureMonitor of oneM2M HAIM to OMA DWAPI-PCH

| Module Class | data points of oneM2M HAIM | data objects of OMA DW-PCH | Description |
| --- | --- | --- | --- |
| sphygmomanometer | diastolicPressure | diastolic | See clause 5.3.47 |
|  | systolicPressure | systolic |  |
|  | meanPressure | mean |  |
| pulsemeter | pulseRate | pulse | See clause 5.3.48 |
| battery | level | batteryLevel | See clause 5.3.4. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |

## 7.1.1.2  	deviceGlucosemeter

DeviceGlucometer of HAIM shall be mapped to Glucometer of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.1.2 Map of deviceGlucometer of oneM2M HAIM to OMA DWAPI-PCH

| Module Class | data points of oneM2M HAIM | data objects of OMA DW-PCH | Description |
| --- | --- | --- | --- |
| glucometer | concentration | concentration | See clause 5.3.49 |
|  | hba1c | hba1c |  |
|  | contextExercise | contextExercise |  |
|  | contextMedication | contextMedication |  |
|  | contextCarbohydratesAmount | contextCarbohydrates |  |
|  | contextCarbohydratesSource | contextCarbohydrates |  |
|  | contextMeal | contextMeal |  |
|  | contextLocation | contextLocation |  |
|  | contextTester | contextTester |  |
|  | contextHealth | contextHealth |  |
| battery | level | batteryLevel | See clause 5.3.4. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |

## 7.1.1.3  	devicePulseOximeter

DevicePulseOximeter of HAIM shall be mapped to Pulse Oximeter of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.1.3 Map of devicePulseOximeter of oneM2M HAIM to OMA DWAPI-PCH

| Module Class | data points of oneM2M HAIM | data objects of OMA DW-PCH | Description |
| --- | --- | --- | --- |
| pulsemeter | modality | spo2, pulse | See clause 5.3.48. When oximeter module doesn’t exist, pulsemeter module is mandatory. |
| oximeter | modality | spo2, pulse | See clause 5.3.21. When pulsemeter module doesn’t exist, oximeter module is mandatory. |
| battery | level | batteryLevel | See clause 5.3.4. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |

## 7.1.1.4  deviceThermometer

DeviceTermometer of HAIM shall be mapped to Thermometer of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.1.4 Map of deviceThermometer of oneM2M HAIM to OMA DWAPI-PCH

| Module Class | data points of oneM2M HAIM | data objects of OMA DW-PCH | Description |
| --- | --- | --- | --- |
| temperature | unit | temperature | See clause 5.3.33 |
| battery | level | batteryLevel | See clause 5.3.4. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |

## 7.1.1.5  deviceWeightScaleAndBodyCompositionAnalyzer

DeviceWeightScaleAdBodyCompositionAnalyzer of HAIM shall be mapped to Weight Scale Body Composition Analyzer of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.1.5 Map of deviceWeightScaleAdBodyCompositionAnalyzer of oneM2M HAIM to OMA DWAPI-PCH

| Module Class | data points of oneM2M HAIM | data objects of OMA DW-PCH | Description |
| --- | --- | --- | --- |
| bodyCompositionAnalyzer | bodyLength | bodyLength | See clause 5.3.50 |
|  | Bmi | bmi |  |
|  | fatFreeMass | fatFreeMass |  |
|  | softLeanMass | softLeanMass |  |
|  | muscleMass | muscleMass |  |
|  | basalMetabolism | basalMetabolism |  |
|  | impedance | impedance |  |
| weight | weight | bodyMass | See clause 5.3.40 |
| bioElectricalImpedanceAnalysis | water | bodyWater | See clause 5.3.6 |
|  | fat | bodyFat |  |
|  | muscle | musclePercentage |  |
| battery | level | batteryLevel | See clause 5.3.4. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |

7.1.1.6  deviceHeartRateMonitor

DeviceHeartRateMonitor of HAIM shall be mapped to Heart Rate Monitor of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.1.6 Map of deviceHeartRateMonitor of oneM2M HAIM to OMA DWAPI-PCH

| Module Class | data points of oneM2M HAIM | data objects of OMA DW-PCH | Description |
| --- | --- | --- | --- |
| pulsemeter | pulseRate | rate | See clause 5.3.48 |
|  | rr | rr |  |
|  | energy | energy |  |
| battery | level | batteryLevel | See clause 5.3.4. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |

7.1.2	data type

Data types of oneM2M HAIM and OMA DWAPI-PCH shall be mapped each other on the basis of the following table.

Table 7.1.2 Map of data types between oneM2M and OMA DWAPI-PCH

| oneM2M data type | Mapping to data type in OMA DWAPI-PCH | Description |
| --- | --- | --- |
| xs:integer | int, Number | Data type for 32-bit signed integer. |
| xs:string | String, Array | Data type for text. The length limitation should be considered for the mapping. |
| xs:float | Float | Data type for a single precision 32-bit floating point type as defined in XML Schema 1.0 [14] as the float primitive type. |
| xs:Boolean | Boolean | Data type for Boolean. |

### ----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

Annex B (informative): 
Introduction of Extarnal Organizations Data Model

## B.1	OMA Got API(DWAPI-PCH)

OMA GotAPI(OMA Generic Open Terminal API Framework) provides the framework to enable applications and multitype devices through GotAPI Servers and Extension Plug-Ins [6]. When APIs are implemented in Extension Plug-Ins under the GotAPI framework, these APIs are called as OMA Device WebAPIs Enabler. In case of healthcare devices, these APIs are called as OMA DWAPI-PCH(Device WebAPIs for Personal Connected Healthcare).

Healthcare devices can be a one of the smart home devices so OMA DWWAPI-PCH can have relationship with oneM2M SDT.

## B.2	OCF

### B.3	ECHONET

### -----------------------End of change 4-------------------------------------------