| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#28 |
| Source:* | Dongjoo Kim (dongjoo7.kim@lge.com) |
| Date:* | 2017-3-27 |
| Reason for Change/s:* | Enhancement of the air conditioner data model. |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <WI-0056> MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.2.0 |
| Clauses * | 5.3, 5.4, 5.5, 6.3, 6.4, 6.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The present document proposes to improve deviceAirConditioner data model based on the real product.

### -----------------------Start of change 1-------------------------------------------

### 5.4.1	deviceAirConditioner

An air conditioner is a home appliance used to alter the properties of air (primarily temperature and humidity) to more comfortable conditions. This air conditioner information model provides capabilities to control and monitor air conditioner specific functions and resources.

Table 5.4.1-1: Modules of deviceAirConditioner Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.5 |
| runState | runState | true | See clause 5.3.28 |
| airConJobMode | airConJobMode | true | See clause 5.3.xx |
| airConOperationMode | operationMode | true | See clause 5.3.51 This module instance is used to trigger airCon operation that is pre-set in airConJobMode. If this data point is not present, then the airconditioner job mode can be triggered by setting the “airConJobMode”. |
| airCleanOperationMode | operationMode | true | See clause 5.3.51 This module instance is used to trigger airClean operation. |
| temperature | temperature | true | See clause 5.3.33 |
| timer | timer | true | See clause 5.3.35 |
| turbo | turbo | true | See clause 5.3.36 |
| wind | wind | true | See clause 5.3.41 |
| powerSave | powerSave | true | See clause 5.3.22 |
| airQualitySensor | airQualitySensor | true | See clause 5.3.x |
| filterInfo | filterInfo | true | See clause 5.3.x |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 5.3.28	runState

This ModuleClasses provides capabilities to control and monitor machine state of appliances.

Table 5.3.28-1: DataPoints of runState ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentMachineState | hd:machineState | true | true | false | Currently active machine state. |
| machineStates | list of hd:machineState | true | false | false | List of possible machine states the device supports (see clause 5.5.15) |
| progressPercentage | float | true | false | true | Indication of current progress in percentage |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 5.5.x	hd:airConJobMode

Used for currentJobMode and jobModes DataPoints of airConJobMode ModuleClass.

Table 5.5.x-1: Interpretation of hd:airConJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | cool | This value is for deviceAirConditioner and indicates cool mode. |
| 2 | airDry | This value is for deviceAirConditioner and indicates air dry mode. |
| 3 | fan | This value is for deviceAirConditioner and indicates fan mode. |
| 4 | AI | This value is for deviceAirConditioner and indicates artificial intelligence mode. |
| 5 | heat | This value is for deviceAirConditioner and indicates heat mode. |
| 6 | airClean | This value is for deviceAirConditioner and indicates air clean mode. |
| 7 | ACO | This value is for deviceAirConditioner and indicates Auto Change Over mode. |
| 8 | aroma | This value is for deviceAirConditioner and indicates aroma mode. |
| NOTE: See clause 5.3.xx "airConJobMode". Negative values are reserved for vendor specific modes. |

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 5.5.10	hd:windStrength

Used for DataPoints indicating strength of wind.

Table 5.5.10-1: Interpretation of windStrength

| Value | Interpretation | Note |
| --- | --- | --- |
| 0 | zero | No wind |
| 1 | minimum | Minimum strength |
| 2 | low | Lower than medium |
| 3 | medium | Medium strength |
| 4 | high | Higher than medium |
| 5 | maximum | Maximum strength |
| 6 | auto | Automatically changing |
| NOTE: See clause 5.3.41 "wind". |

### -----------------------End of change 4-------------------------------------------

### -----------------------Start of change 6-------------------------------------------

### 5.3.x	airQualitySensor

This ModuleClass is for monitoring sensor that shows air quality.

Table 5.3.x-1: DataPoints of airQualitySense ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| sensorPM1 | xs:integer | true | false | true | Concentration of Particle Matter under 1㎛. Minimum value is 0, and maximum is 1000. |
| sensorPM2 | xs:integer | true | false | true | Concentration of Particle Matter under 2.5㎛. Minimum value is 0, and maximum is 1000. |
| sensorPM10 | xs:integer | true | false | true | Concentration of Particle Matter under 10㎛. Minimum value is 0, and maximum is 1000. |
| sensorOdor | xs:integer | true | false | true | Concentration of odor that reflects air pollution. Minimum value is 0, and maximum is 1000. |
| sensorHumidity | xs:integer | true | false | true | Measured humidity. Minimum value is 0, and maximum is 100. |
| monitoringEnabled | xs:boolean | true | true | true | 1 allows monitoring this resource whereas 0 does not. |
| CO2 | xs:integer | true | false | true | This value indicates ppm(parts per million) |

### -----------------------End of change 6-------------------------------------------

### -----------------------Start of change 7-------------------------------------------

### 5.3.x	filterInfo

This ModuleClass is for monitoring filter information of a device.

Table 5.3.x-1: DataPoints of filterInfo ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| usedTime | xs:integer | true | false | false | Cumulative used time in second of a filter |
| needsReplacement | xs:boolean | true | false | true | This value indicates that the filter needs to be replaced. |

### -----------------------End of change 7-------------------------------------------

### -----------------------Start of change 8-------------------------------------------

### 6.3.2	Resource types

Table 6.3.2-2: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| alarmSpeaker | alaSr |
| audioVideoInput | auVIt |
| audioVolume | audVe |
| battery | batty |
| binarySwitch | binSh |
| bioElectricalImpedanceAnalysis | bEIAs |
| boiler | boilr |
| brewing |  |
| brightness | brigs |
| clock | clock |
| colour | color |
| colourSaturation | colSn |
| customTemperature | cusTe |
| doorStatus | dooSe |
| electricVehicleConnector | elVCr |
| energyConsumption | eneCn |
| energyGeneration | eneGn |
| faultDetection | fauDn |
| foaming |  |
| freshTemperature | freTe |
| frozenTemperature | froTe |
| grinder |  |
| height | heigt |
| hotWaterSupply | hoWSy |
| keypad | keypd |
| liquidLevel |  |
| motionSensor | motSr |
| oximeter | oximr |
| powerSave | powS0 |
| pushButton | pusBn |
| recorder | recor |
| refrigeration | refrn |
| relativeHumidity | relHy |
| liquidRemaining |  |
| runState |  |
| signalStrength | sigSh |
| smokeSensor | smoSr |
| spinLevel | spiLl |
| televisionChannel | telCl |
| temperature | tempe |
| temperatureAlarm | temAm |
| timer | timer |
| turbo | turbo |
| waterFlow | watFw |
| waterSensor | watSr |
| weight | weigt |
| wind | wind |
| bodyCompositionAnalyzer |  |
| glucometer |  |
| pulsemeter |  |
| sphygmomanometer |  |
| operationMode |  |
| remoteControl |  |
| washingCourse |  |
| washingCourseOption |  |
| airQualitySensor |  |
| filterInfo |  |

### -----------------------End of change 8-------------------------------------------

### -----------------------Start of change 9-------------------------------------------

### 6.4.3	ModuleClasses

The containerDefinition attribute of specializations for module classes shall have the values specifien in Table 6.4.3-1.

Table 6.4.3-1: containerDefinition values of specializations for module classes

| Resource Type Name | containerDefinition value |
| --- | --- |
| alarmSpeaker | "org.onem2m.home.moduleclass.alarmSpeaker" |
| audioVideoInput | "org.onem2m.home.moduleclass.audioVideoInput" |
| audioVolume | "org.onem2m.home.moduleclass.audioVolume" |
| battery | "org.onem2m.home.moduleclass.battery" |
| binarySwitch | "org.onem2m.home.moduleclass.binarySwitch" |
| bioElectricalImpedanceAnalysis | "org.onem2m.home.moduleclass.bioElectricalImpedanceAnalysis" |
| boiler | "org.onem2m.home.moduleclass.boiler" |
| brewing | "org.onem2m.home.moduleclass.brewing” |
| brightness | "org.onem2m.home.moduleclass.brightness" |
| clock | "org.onem2m.home.moduleclass.clock" |
| colour | "org.onem2m.home.moduleclass.colour" |
| colourSaturation | "org.onem2m.home.moduleclass.colourSaturation" |
| customTemperature | "org.onem2m.home.moduleclass.customTemperature" |
| doorStatus | "org.onem2m.home.moduleclass.doorStatus" |
| electricVehicleConnector | "org.onem2m.home.moduleclass.electricVehicleConnector" |
| energyConsumption | "org.onem2m.home.moduleclass.energyConsumption" |
| energyGeneration | "org.onem2m.home.moduleclass.energyGeneration" |
| faultDetection | "org.onem2m.home.moduleclass.faultDetection" |
| foaming | "org.onem2m.home.moduleclass.foaming” |
| freshTemperature | "org.onem2m.home.moduleclass.freshTemperature" |
| frozenTemperature | "org.onem2m.home.moduleclass.frozenTemperature" |
| grinder | "org.onem2m.home.moduleclass.grinder” |
| height | "org.onem2m.home.moduleclass.height" |
| hotWaterSupply | "org.onem2m.home.moduleclass.hotWaterSupply" |
| keypad | "org.onem2m.home.moduleclass.keypad" |
| liquidLevel | "org.onem2m.home.moduleclass.liquidLevel” |
| liquidRemaining | "org.onem2m.home.moduleclass.liquidRemaining” |
| motionSensor | "org.onem2m.home.moduleclass.motionSensor" |
| oximeter | "org.onem2m.home.moduleclass.oximeter" |
| powerSave | "org.onem2m.home.moduleclass.powerSave" |
| pushButton | "org.onem2m.home.moduleclass.pushButton" |
| recorder | "org.onem2m.home.moduleclass.recorder" |
| refrigeration | "org.onem2m.home.moduleclass.refrigeration" |
| relativeHumidity | "org.onem2m.home.moduleclass.relativeHumidity" |
| rinseLevel | "org.onem2m.home.moduleclass.rinseLevel" |
| runState | "org.onem2m.home.moduleclass.runState" |
| signalStrength | "org.onem2m.home.moduleclass.signalStrength" |
| smokeSensor | "org.onem2m.home.moduleclass.smokeSensor " |
| spinLevel | "org.onem2m.home.moduleclass.spinLevel" |
| televisionChannel | "org.onem2m.home.moduleclass.televisionChannel" |
| temperature | "org.onem2m.home.moduleclass.temperature" |
| temperatureAlarm | "org.onem2m.home.moduleclass.temperatureAlarm" |
| timer | "org.onem2m.home.moduleclass.timer" |
| turbo | "org.onem2m.home.moduleclass.turbo" |
| waterFlow | "org.onem2m.home.moduleclass.waterFlow" |
| waterSensor | "org.onem2m.home.moduleclass.waterSensor" |
| weight | "org.onem2m.home.moduleclass.weight" |
| wind | "org.onem2m.home.moduleclass.wind" |
| bodyCompositionAnalyzer | "org.onem2m.home.moduleclass.bodyCompositionAnalyzer " |
| glucometer | "org.onem2m.home.moduleclass.glucometer " |
| pulsemeter | "org.onem2m.home.moduleclass.pulsemeter " |
| sphygmomanometer | "org.onem2m.home.moduleclass.sphygmomanometer " |
| operationMode | "org.onem2m.home.moduleclass.operationMode" |
| remoteControl | "org.onem2m.home.moduleclass.remoteControl" |
| washingCourse | "org.onem2m.home.moduleclass.washingCourse" |
| washingCourseOption | "org.onem2m.home.moduleclass.washingCourseOption" |
| airQualitySensor | "org.onem2m.home.moduleclass.airQualitySensor" |
| filterInfo | "org.onem2m.home.moduleclass.filterInfo" |

### -----------------------End of change 9-------------------------------------------

### -----------------------Start of change 10-------------------------------------------

### 6.5.3	XSD definitions for ModuleClass

The XSD definitions for ModuleClass are listed in Table 6.5.3-1.

Table 6.5.3-1: XSD definition of ModuleClasses

| ModuleClass ID | File Name | Note |
| --- | --- | --- |
| alarmSpeaker | HD-mod-alarmSpeaker-v<TS-version>.xsd |  |
| audioVideoInput | HD-mod-audioVideoInput-v<TS-version>.xsd |  |
| audioVolume | HD-mod-audioVolume-v<TS-version>.xsd |  |
| battery | HD-mod-battery-v<TS-version>.xsd |  |
| binarySwitch | HD-mod-binarySwitch-v<TS-version>.xsd |  |
| bioElectricalImpedanceAnalysis | HD-mod-bioElectricalImpedanceAnalysis-v<TS-version>.xsd |  |
| boiler | HD-mod-boiler-v<TS-version>.xsd |  |
| brewing | HD-mod- brewing -v<TS-version>.xsd |  |
| brightness | HD-mod-brightness-v<TS-version>.xsd |  |
| clock | HD-mod-clock-v<TS-version>.xsd |  |
| colour | HD-mod-colour-v<TS-version>.xsd |  |
| colourSaturation | HD-mod-colourSaturation-v<TS-version>.xsd |  |
| doorStatus | HD-mod-doorStatus-v<TS-version>.xsd |  |
| electricVehicleConnector | HD-mod-electricVehicleConnector-v<TS-version>.xsd |  |
| energyConsumption | HD-mod-energyConsumption-v<TS-version>.xsd |  |
| energyGeneration | HD-mod-energyGeneration-v<TS-version>.xsd |  |
| faultDetection | HD-mod-faultDetection-v<TS-version>.xsd |  |
| foaming | HD-mod- foaming -v<TS-version>.xsd |  |
| grinder | HD-mod- grinder -v<TS-version>.xsd |  |
| height | HD-mod-height-v<TS-version>.xsd |  |
| hotWaterSupply | HD-mod-hotWaterSupply-v<TS-version>.xsd |  |
| keypad | HD-mod-keypad-v<TS-version>.xsd |  |
| liquidLevel | HD-mod- liquidLevel -v<TS-version>.xsd |  |
| liquidRemaining | HD-mod- liquidRemaining -v<TS-version>.xsd |  |
| motionSensor | HD-mod-motionSensor-v<TS-version>.xsd |  |
| oximeter | HD-mod-oximeter-v<TS-version>.xsd |  |
| powerSave | HD-mod-powerSave-v<TS-version>.xsd |  |
| pushButton | HD-mod-pushButton-v<TS-version>.xsd |  |
| recorder | HD-mod-recorder-v<TS-version>.xsd |  |
| refrigeration | HD-mod-refrigeration-v<TS-version>.xsd |  |
| relativeHumidity | HD-mod-relativeHumidity-v<TS-version>.xsd |  |
| rinseLevel | HD-mod-rinseLevel-v<TS-version>.xsd |  |
| runState | HD-mod-runState-v<TS-version>.xsd |  |
| signalStrength | HD-mod-signalStrength-v<TS-version>.xsd |  |
| smokeSensor | HD-mod-smokeSensor-v<TS-version>.xsd |  |
| spinLevel | HD-mod-spinLevel-v<TS-version>.xsd |  |
| televisionChannel | HD-mod- HD-mod--v<TS-version>.xsd |  |
| temperature | HD-mod-temperature-v<TS-version>.xsd |  |
| temperatureAlarm | HD-mod-temperatureAlarm-v<TS-version>.xsd |  |
| timer | HD-mod-timer-v<TS-version>.xsd |  |
| turbo | HD-mod-turbo-v<TS-version>.xsd |  |
| waterFlow | HD-mod-waterFlow-v<TS-version>.xsd |  |
| waterSensor | HD-mod-waterSensor-v<TS-version>.xsd |  |
| weight | HD-mod-weight-v<TS-version>.xsd |  |
| wind | HD-mod-wind-v<TS-version>.xsd |  |
| bodyCompositionAnalyzer | HD-mod- bodyCompositionAnalyzer -v<TS-version>.xsd |  |
| glucometer | HD-mod- glucometer -v<TS-version>.xsd |  |
| pulsemeter | HD-mod- pulsemeter -v<TS-version>.xsd |  |
| sphygmomanometer | HD-mod- sphygmomanometer -v<TS-version>.xsd |  |
| operationMode | HD-mod- operationMode-v<TS-version>.xsd |  |
| remoteControl | HD-mod- remoteControl-v<TS-version>.xsd |  |
| washingCourse | HD-mod-washingCourse-v<TS-version>.xsd |  |
| washingCourseOption | HD-mod-washingCourseOption-v<TS-version>.xsd |  |
| airQualitySensor | HD-mod-airQualitySensor-v<TS-version>.xsd |  |
| filterInfo | HD-mod-filterInfo-v<TS-version>.xsd |  |
| NOTE: The string '<TS-version>' shall be intepreted as the version of the present document. |

### -----------------------End of change 10-------------------------------------------

### -----------------------Start of change 11-------------------------------------------

### 5.3.x	airConJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of air conditioner.

Table 5.3.xx-1: DataPoints of airConJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd:airConJobMode | true | true | false | Currently active job mode. |
| currentJobModeName | xs:string | true | false | true | Name of current job mode in string. This can be used when currentJobMode is vendor-specific. |
| jobModes | list of hd: airConJobMode | true | false | false | List of possible job states the device supports (see clause 5.5.x) |

### -----------------------End of change 11-------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?