| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#28 |
| Source:* | Dongjoo Kim (dongjoo7.kim@lge.com) |
| Date:* | 2017-3-27 |
| Reason for Change/s:* | This CR request to add a devicePrinter data model. |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <WI-0056> MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.2.0 |
| Clauses * | 5.4.4, 5.5.7, 6.3.2, 6.4.2, 6.5.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The present CR requests to add a printer device model which does not exist in the current HAIM specification. This model is proposed with binarySwitch and runState module classes.

### -----------------------Start of change 1-------------------------------------------

### 5.4.x	devicePrinter

A printer is a device that is used to monitor or control the state of a printing device.

Table 5.4.x -1: Modules of devicePrinter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.5 |
| runState | runState | true | See clause 5.3.28 |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 5.5.7	hd:jobStates

Used for currentJobState and jobStates DataPoints of runState ModuleClass.

Table 5.5.7-1: Interpretation of jobState

| Value | Interpretation | Note |
| --- | --- | --- |
| 0~99 |  | Reserved for future use |
| 100~199 |  | Reserved for deviceAirConditioner |
| 200 | idle | This value is for deviceClothesWasher and indicates idle state. |
| 201 | preWash | This value is for deviceClothesWasher and indicates pre-washing state. pre-wash is a cold water cycle that runs prior to the main wash cycle. It is used for heavily soiled laundy. |
| 202 | wash | This value is for deviceClothesWasher and indicates washing state. |
| 203 | rinse | This value is for deviceClothesWasher and indicates rinsing state. |
| 204 | spin | This value is for deviceClothesWasher and indicates spinning state. |
| 205 | dry | This value is for deviceClothesWasher and indicates drying state. |
| 206 | airDry | This value is for deviceClothesWasher and indicates air-drying state. In airDry state, a rotating wheel circulates air to get fresh air used to dry laundry. |
| 207 | wrinkleProof | This value is for deviceClothesWasher and indicates wrinkleProof state. |
| 208 | soak | This value is for deviceClothesWasher and indicates soak state. |
| 209~299 |  | Reserved for deviceClothesWasher |
| 300~399 |  | Reserved for deviceElectricVehicleCharger |
| 400~499 |  | Reserved for deviceLight |
| 500~599 |  | Reserved for deviceMicrogeneration |
| 600 | warmingUp | This value is for deviceOven and indicates warmingUp state. |
| 601 | cooking | This value is for deviceOven and indicates cooking state. |
| 602 | cooling | This value is for deviceOven and indicates cooling state. |
| 603~699 |  | Reserved for deviceOven |
| 700~799 |  | Reserved for deviceRefrigerator |
| 800 | charging | This value is for deviceRobotCleaner and indicates charging state. |
| 801 | homing | This value is for deviceRobotCleaner and indicates homing state. |
| 802 | docking | This value is for deviceRobotCleaner and indicates docking state. |
| 803~899 |  | Reserved for deviceRobotCleaner |
| 900~999 |  | Reserved for deviceSmartElectricMeter |
| 1000~1099 |  | Reserved for deviceStorageBattery |
| 1100~1199 |  | Reserved for deviceTelevision |
| 1200 | antifreeze | This mode sets the thermostat to a minimum temperature to avoid home system to freeze when the habitants are not there for a long time |
| 1201 | manual | This mode allows for direct change of the temperature indication for the thermostat by the user. |
| 1202 | eco | This is to set the thermostat to the economic mode |
| 1203 | program | The program mode is used to set the thermostat to a predefined mode |
| 1204~1299 |  | Reserved for deviceThermostat |
| 1300~1399 |  | Reserved for deviceWaterHeater |
| 1400~1499 |  | Reserved for deviceCoffeeMachine |
| 1500 | idle | This value is for devicePrinter and indicates idle state. |
| 1501 | pending | This value is for devicePrinter and indicates pending state. |
| 1502 | printing | This value is for devicePrinter and indicates printing state. |
| 1503~1599 |  | Reserved for devicePrinter |
| NOTE: See clause 5.3.28 "runstate". |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 6.3.2	Resource types

In protocol bindings resource type names for device models shall be translated into short names of Table 6.3.2-1.

Table 6.3.2-1: Specialization type short names (Device models)

| Resource Type Name | Short Name |
| --- | --- |
| deviceAirConditioner | deACr |
| deviceClothesWasher | deCWr |
| deviceCoffeeMachine |  |
| deviceElectricVehicleCharger | dEVCr |
| deviceLight | devLt |
| deviceMicrogeneration | devMn |
| deviceOven | devOn |
| deviceRefrigerator | devRr |
| deviceRobotCleaner | deRCr |
| deviceSmartElectricMeter | dSEMr |
| deviceStorageBattery | deSBy |
| deviceTelevision | devTn |
| deviceThermostat | devTt |
| deviceWaterHeater | deWHr |
| devicePulseOximeter |  |
| deviceGlucosemeter |  |
| deviceHeartRateMonitor |  |
| deviceWeightScaleAndBodyCompositionAnalyzer |  |
| devicePulseOximeter |  |
| deviceThermoMeter |  |
| devicePrinter |  |

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 6.4.2	Device models

The containerDefinition attribute of specializations for device models shall have the values specifien in Table 6.4.2-1.

Table 6.4.2-1: containerDefinition values of specializations for device models

| Resource Type Name | containerDefinition value |
| --- | --- |
| deviceAirConditioner | "org.onem2m.home.device.deviceAirConditioner" |
| deviceClothesWasher | "org.onem2m.home.device.deviceClothesWasher" |
| deviceCoffeeMachine | "org.onem2m.home.device.deviceCoffeeMachine” |
| deviceElectricVehicleCharger | "org.onem2m.home.device.deviceElectricVehicleCharger" |
| deviceLight | "org.onem2m.home.device.deviceLight" |
| deviceMicrogeneration | "org.onem2m.home.device.deviceMicrogeneration" |
| deviceOven | "org.onem2m.home.device.deviceOven" |
| deviceRefrigerator | "org.onem2m.home.device.deviceRefrigerator" |
| deviceRobotCleaner | "org.onem2m.home.device.deviceRobotCleaner" |
| deviceSmartElectricMeter | "org.onem2m.home.device.deviceSmartElectricMeter" |
| deviceStorageBattery | "org.onem2m.home.device.deviceStorageBattery" |
| deviceTelevision | "org.onem2m.home.device.deviceTelevision" |
| deviceThermostat | "org.onem2m.home.device.deviceThermostat" |
| deviceWaterHeater | "org.onem2m.home.device.deviceWaterHeater" |
| devicePulseOximeter | "org.onem2m.home.device.devicePulseOximeter" |
| deviceGlucosemeter | "org.onem2m.home.device.deviceGlucosemeter" |
| deviceHeartRateMonitor | "org.onem2m.home.device.deviceHeartRateMonitor" |
| deviceWeightScaleAndBodyCompositionAnalyzer | "org.onem2m.home.device.deviceWeightScaleAndBodyCompositionAnalyzer" |
| devicePulseOximeter | "org.onem2m.home.device.devicePulseOximeter" |
| deviceThermoMeter | "org.onem2m.home.device.deviceThermoMeter" |
| devicePrinter | "org.onem2m.home.device.devicePrinter" |

### -----------------------End of change 4-------------------------------------------

### -----------------------Start of change 5-------------------------------------------

### 6.5.2	XSD definitions for Device models

The XSD definitions for Device models are listed in Table 6.5.2-1.

Table 6.5.2-1: XSD definition of Device models

| Device model | File Name | Note |
| --- | --- | --- |
| deviceAirConditioner | HD-deviceAirConditioner-v<TS-version>.xsd |  |
| deviceClothesWasher | HD-deviceClothesWasher-v<TS-version>.xsd |  |
| deviceCoffeeMachine | HD-deviceCoffeeMachine-v<TS-version>.xsd |  |
| deviceElectricVehicleCharger | HD-deviceElectricVehicleCharger-v<TS-version>.xsd |  |
| deviceLight | HD-deviceLight-v<TS-version>.xsd |  |
| deviceMicrogeneration | HD-deviceMicrogeneration-v<TS-version>.xsd |  |
| deviceOven | HD-deviceOven-v<TS-version>.xsd |  |
| deviceRefrigerator | HD-deviceRefrigerator-v<TS-version>.xsd |  |
| deviceRobotCleaner | HD-deviceRobotCleaner-v<TS-version>.xsd |  |
| deviceStorageBattery | HD-deviceStroageBattery-v<TS-version>.xsd |  |
| deviceSmartElectricMeter | HD-deviceSmartElectricMeter-v<TS-version>.xsd |  |
| deviceTelevision | HD-deviceTelevision-v<TS-version>.xsd |  |
| deviceThermostat | HD-deviceThermostat-v<TS-version>.xsd |  |
| deviceWaterHeater | HD-deviceWaterHeater-v<TS-version>.xsd |  |
| devicePulseOximeter | HD-devicePulseOximeter -v<TS-version>.xsd |  |
| deviceGlucosemeter | HD-deviceGlucosemeter -v<TS-version>.xsd |  |
| deviceHeartRateMonitor | HD-deviceHeartRateMonitor -v<TS-version>.xsd |  |
| deviceWeightScaleAndBodyCompositionAnalyzer | HD-deviceWeightScaleAndBodyCompositionAnalyzer -v<TS-version>.xsd |  |
| devicePulseOximeter | HD-devicePulseOximeter -v<TS-version>.xsd |  |
| deviceThermoMeter | HD-deviceThermoMeter -v<TS-version>.xsd |  |
| devicePrinter | "org.onem2m.home.device.devicPrinter" |  |
| NOTE: The string '<TS-version>' shall be intepreted as the version of the present document. |

### -----------------------End of change 5-------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?